## Slide 1: 3 - FUNDAMENTALS OF TOXICOLOGY

## Slide 2: 3. FUNDAMENTALS OF TOXICOLOGY
    Toxicology is the study of the adverse effects of substances on living organisms.
    Historically toxicology was the art and science of poisoning.
    It is today a discipline which makes use of information developed by a wide range of chemical, physical, biological and medical sciences in order to predict the likely adverse effects on man of an ever‑increasing range of substances to which he is exposed.

## Slide 3: 3. FUNDAMENTALS OF TOXICOLOGY
Toxicity is the innate ability of substances to injure living things.
Hazard assessment is the prediction of the toxic effects that will be evident under defined conditions of exposure.
Risk assessment is the prediction of the probability that defined toxic effects will occur under defined conditions of exposure in a single person or a defined population.

## Slide 4: 3. FUNDAMENTALS OF TOXICOLOGY
Substance covers a wide range of materials including single chemical compounds or mixtures of these, simple or complex naturally occurring or synthetically produced substances and micro‑organisms.
Substances may be chemically pure or contain additives or impurities and may be in the form of solids, liquids, gases, dusts, fibres, fumes or aerosols.
Some (e.g. fumes, dusts and aerosols) may be difficult to identify.
They may be materials used or which arise during maintenance or repair of plants or buildings or they may be formed or used during research, development or testing.

## Slide 5: 3. FUNDAMENTALS OF TOXICOLOGY
    "All substances are poisons, there is none which is not a poison. The right dose differentiates a poison and a remedy" – Paracelsus (1525).

## Slide 6: 3. FUNDAMENTALS OF TOXICOLOGY
  The toxic effects of a substance depend upon:
  Its physical form.
  The dose.
  The route of entry.
  Its absorption, distribution, metabolism and excretion.

## Slide 7: 3. FUNDAMENTALS OF TOXICOLOGY
Solids | When ground or crushed, dusts result and can be inhaled, ingested or contaminate the skin
Liquids | Can be swallowed or contaminate the skin
Gases | Can be swallowed or contaminate the skin
Vapours | 
Fumes | 
Mists | 
Aerosols | 

## Slide 8: 3. FUNDAMENTALS OF TOXICOLOGY
    Dose = Exposure x Time
Dose is the product of concentration of the substance and duration of exposure to it. In simple terms it may be described as:
However in industrial circumstances both the exposure and time can vary greatly. For example, a very high concentration for a short time may be lethal (e.g. alcohol) while prolonged exposure to smaller amounts does little harm. The dose is the same in both cases.

## Slide 9: 3. FUNDAMENTALS OF TOXICOLOGY
Ingestion: Ingestion is the least significant route of entry in industry while in environmental toxicology it is the most.
Inhalation: In the lung there are no similar mechanisms for selective uptake. Particles less than 10 micron in diameter may reach the alveoli. If soluble, approximately 40% are then absorbed. Inhalation accounts for 90% or so of industrial poisoning.
The Skin: In the skin there is again no selective uptake. Fat-soluble compounds are absorbed readily as are organic solvents.
Route of entry / absorption

## Slide 10: 3. FUNDAMENTALS OF TOXICOLOGY
Distribution
Once substances have entered the body they can distributed around the body through the blood supply.
They may concentrate differentially in the organs.

## Slide 11: 3. FUNDAMENTALS OF TOXICOLOGY
Metabolism
Substances which are distributed through the body then tend to be metabolised.
The main site of metabolism is the liver, although the kidneys, lungs and skin can metabolise some chemicals.
Metabolism can convert a toxic substance to a non-toxic one and vice versa.

## Slide 12: 3. FUNDAMENTALS OF TOXICOLOGY
Excretion
This takes place via;
  Kidneys
  Bile,
  Lungs,
  Gastric juices,
  Breast milk,
  Skin (iron).
The more rapidly excretion takes place the less likely is a toxin to damage the body.
Excretion products are often used to monitor work exposure.

## Slide 13: Material Safety Data Sheets

## Slide 14: Material Safety Data Sheets
Much of the work involved in accessing workplace hazards can be carried out by accessing Materials Safety Data Sheets (MSDS), sometimes also called Safety Data Sheets (SDS). The MSDS is a standard way of communicating toxicology and other relevant information about substances.
In many countries it is a legal requirement or common practice that a company supplies an MSDS for each of the products that they sell.

## Slide 15: Material Safety Data Sheets
Composition/Data on components: This gives details of the different chemicals contained within the material. It will often list the Chemical Abstracts Service (CAS) number for each chemical is contains. The CAS number is a unique number which is assigned to most of the chemicals used in industry.
Identification of substance: This includes the trade name, as well as manufacturer/supplier details. It may also give emergency information such as contact names and telephone numbers.
The content of the MSDS will vary depending upon local legislative requirements but is likely to contain the following information:

## Slide 16: Material Safety Data Sheets
Hazards identification: The material will be classified under a number of categories and described with pictograms.
First aid measures: Advice about how to deal with workers who have been exposed under different circumstances.
Fire fighting measures: Dos and don’ts of fire extinguishing e.g. what type of fire extinguisher to use.
Accidental release measures: The procedures to be followed in case of accidental release of the chemical, including methods to be used to clean up spills.
Handling and storage: Giving information on the precautions such as flammables cabinets and temperature limitations.

## Slide 17: Material Safety Data Sheets
Exposure controls and personal protection: Outlines requirements such as Personal Protective Equipment and ventilation.
Physical and chemical properties: e.g. the form (solid/liquid/gas), colour, odour, melting and boiling points.
Stability and reactivity: Properties such as thermal decomposition and conditions to be avoided.
Toxicological information: Details such as acute and chromic effects on man and animals.
Ecological information: How the material might affect the environment if it is released beyond the workplace.
Disposal considerations: Any special requirements associated with disposal of the material.

## Slide 18: Material Safety Data Sheets
Transport information: generally as a list of codes indicating the dangers associated with the chemical.
Regulations: Relevant legislation for the country in which the material is used.
Other information: Any information which is relevant.