## Slide 1: 4 - EXAMPLES OF HAZARDOUS SUBSTANCES/PROCESSES

## Slide 2: SILICA
Crystalline silica or quartz (SiO2) is the most widely occurring of all minerals and it is found in most rocks.
Sand on beaches
Inhalation can give rise to silicosis = Pulmonary fibrosis
  Dust concentration in the atmosphere;
  Percentage of free silica in the dust, and the
  Duration of exposure.
Silica is encountered during many processes which use minerals e.g. quarrying and mining, brick, tile and refractory manufacture, pottery and ceramic, sandblasting, Glass manufacture.

## Slide 3: SILICA
Silica released during stone cutting activities
Source: HSE
Source: HSE

## Slide 4: SILICA
Silica released during Quarrying activities
Source: Wikimedia Commons
Source: Wikimedia Commons

## Slide 5: MACHINE MADE MINERAL FIBRE MMMF
Machine Made Mineral Fibres (MMMF) include ceramic fibers, special purpose fibers and continuous filament fibers.
The material is normally made from molten glass, rock or slag.
The material exhibits good resistance to heat and chemicals and can be woven.
Cause irritations of the skin and eyes, and that at excessively dusty conditions they lead to irritation of the upper respiratory tract.
While most skin becomes resistant after a transitory period, some people need to take precautions to protect their skin and a small number need to move to other work.
Studies in which non-asbestos mineral fibres were implanted into the chests of laboratory animals have shown that mesothelioma tumours result
Inhalation studies on animals have not led to clinically significant fibrosis.

## Slide 6: MACHINE MADE MINERAL FIBRE MMMF
Silica released during the relining of a Kiln
Source: Steve Bailey
Source: Steve Bailey

## Slide 7: WELDING
Source: Wikimedia Commons
Source: Wikimedia Commons
Source: Wikimedia Commons

## Slide 8: WELDING FUME
Mixtures of airborne gases and fine particles.
The degree of risk will depend on: the composition of the fume, the quantity of fume in the air which is breathed, the duration of exposure.

## Slide 9: WELDING FUME
The main health effects are:
Irritation of the Respiratory Tract
Metal Fume Fever
Systemic Poisoning
Long Term or Chronic Effects

## Slide 10: MANUAL METAL ARC WELDING
Source: Wikimedia Commons

## Slide 11: TIG WELDING
Source: Wikimedia Commons

## Slide 12: EXAMPLES OF HAZARDOUS SUBSTANCES/PROCESSES
Isocyanates can be liquids or solids at room temperature and are mainly used in the production of polyurethanes, foams, adhesives, varnishes and paints.
They are irritating to the skin and mucous membranes. However, the most serious problems associated with exposure to isocyanates are those affecting the respiratory system. Isocyanates are widely recognised as one of the commonest causes of occupational asthma. After varying exposure to isocyanates workers may respond to extremely low concentrations and this is known as sensitisation.

## Slide 13: Isocyanates
Exposure to Isocyanates as well as solvent vapours during paint spraying
Source: HSE

## Slide 14: WOOD DUST
Sanding of wood creates dust
Gluing of wood veneers
Source: Wikimedia Commons
Source: Wikimedia Commons

## Slide 15: WOOD DUST
Wood dust is produced whenever the machining or cutting of wood takes place.
The hazards associated with wood dusts are mainly from inhalation and skin contact.
Gives rise to many different symptoms, the nature of which depends on the quantity, and composition of the wood.
  Dermatitis
  Conjunctival irritation
  irritation of the upper respiratory tract.
  Concern over the progression of the nasal irritation into nasal cancer.

## Slide 16: Pharmaceuticals
Potent compounds.
Mostly in the form of dusts but some liquids/solvents
  Allergic reactions
  Vitamin deficiency
  Fungal infections
  Nitroglycerin
  Tranquilizers.

## Slide 17: Pharmaceuticals
Powder is fed through an open chute into a tablet press.
Manual feeding of powder from drum to open mixer.
Source: Steve Bailey
Source: Steve Bailey

## Slide 18: Pharmaceuticals
A plastic sack of powdered material about to be charged to a reactor through a hopper inserted in the port.
Source: Steve Bailey

## Slide 19: Petroleum Products
Lubricating Oils:
  Irritant
  Defatting of Skin
  Inhalation of oil mists and vapours may cause irritation of the eyes, nose and throat.
  Most formulations contain chemical additives of variable composition with different hazardous properties
Gasoline
  Skin irritant
  Defatting of Skin
  Toxic additives e.g. tetraethyl lead
Gas oils, fuel oils
  Skin irritant
Benzene
  Defatting of Skin
  Dermatitis on repeated exposure
  nervous system depression
  Repeated exposure damages blood
  Prolonged exposure to high concentrations cause a type of leukaemia (cancer of the blood)

## Slide 20: Petroleum Products
Lubricating Oils
Source: Steve Bailey

## Slide 21: Petroleum Products
Tanker delivery of volatile solvents
Source: Steve Bailey

## Slide 22: Mining – Mineral & Metal Extraction
Mining of coal, metal ores and other minerals is undertaken extensively around the world.
Historically mine workers have suffered higher incidences of ill health than workers in other heavy industry sectors.
  Pneumoconiosis
  Emphysema.

## Slide 23: Mining – Mineral & Metal Extraction
Coal miner in Xingtai, China 2008
Child coal miners - drivers and mules USA 1907

## Slide 24: Mining – Mineral & Metal Extraction
Different Minerals Present Different Hazards

## Slide 25: Mining – Mineral & Metal Extraction
Open-pit copper mine New Mexico
Boddington Gold Mine, Western Australia.

## Slide 26: Metal Use and Refining
Source: Adrian Hirst
    Casting of Bronze containing Copper and Tin

## Slide 27: Metal Use and Refining
Tungsten Carbide Tool containing Cobalt
Tools formed by Sintering Powdered metal.
Exposure can occur during manufacture or sharpening of the tool.

## Slide 28: Chromium
Steel-grey, hard metal element, which will take on a high lustre.
Alloying and Electroplating
It is capable of having a number of valent states
  Hazards dependant on compound it forms:
  Dermal irritation, ulceration and allergic dermatitis.
  Pulmonary irritation,
  Nasal septum perforation,
  Cancer.

## Slide 29: Chromium
Source: Steve Bailey
Source: Steve Bailey
Electroplating Tanks

## Slide 30: LEAD
Soft malleable metal with good anticorrosive properties.
Used extensively in the construction industry as well as in the production of batteries, bullets and weights.
Its various compounds are toxic
  Acute effects are rare, as lead is mainly a cumulative chronic poison
  Some organo lead compounds can be quickly absorbed through the skin and affect the brain causing death in some cases.
  Chronic effects are observed with the slow accumulation of lead in the body often being deposited in the bones.
  Chronic effects range from stomach pains to lethargy and anaemia, ultimately causing death.
  It can give rise to brain damage especially to the young and unborn.

## Slide 31: LEAD
Recycling lead in a lead-acid battery recovery facility
Source: Wikimedia Commons

## Slide 32: EXAMPLES OF HAZARDOUS SUBSTANCES/PROCESSES
There are numerous substances that are Hazardous to Health
They can be Used in a wide variety of ways
In order to take any action with regards to Hazardous substances it is first necessary to:
  Understand the Industrial Process
  Understand the hazards associated with the materials used/generated.