## Slide 1: BASIC PRINCIPLES IN OCCUPATIONAL HYGIENE
Day 2

## Slide 2: 5 - ASSESSMENT OF HEALTH RISKS

## Slide 3: Hazard and Risk
A hazard is something that can cause harm if not controlled.
The outcome is the harm that results from an uncontrolled hazard.
A risk is a combination of the probability that a particular outcome will occur and the severity of the harm involved.

## Slide 4: ASSESSMENT OF HEALTH RISKS
Primary reason for conducting a workplace assessment is to assess the risk(s) to the health of employees.
Where a less than satisfactory situation is indicated there will be an additional requirement:
  To specify steps to achieve adequate control.
  To identify any other action that is required.

## Slide 5: 5 - ASSESSMENT OF HEALTH RISKS

## Slide 6: Define the Extent of the Assessment
Define the process or activity which is being assessed.
Assessment Unit:
  Person
  Activity
  Task
  Substance
  Machine
Number and Type of Hazards
  Hazardous Substance
  Noise
  Vibration
  Safety.

## Slide 7: Gather Information
The nature of the process or operation, e.g. continuous or batch, indoor or outdoor.
The substances used and produced (chemical, biological) plus other agents (noise, radiation) and factors (ergonomic) present.
The form of the substances (gases, vapours etc.) and other agents.
An understanding of the effect(s) of the relevant agents/factors (chemical, physical, biological, ergonomic) on the body.
A knowledge of the types of job carried out (e.g. operator, maintenance, supervisory, laboratory)
Exposure estimates.
The types and extent of occupational exposures.

## Slide 8: Gather Information
Work/shift pattern.
The recommended operating practices and precautionary measures (incl. engineering control).
Worker health experiences
The existence of inventories/registers of substances, non‑chemical agents (e.g. noise and radiation sources)
The availability of relevant sources of information can also be of considerable advantage, e.g.
  Material safety data sheets (MSDSs).
  Manufacturers' labelling.
  Regulatory documentation.
  Other published (e.g. national, company, trade association, technical) and unpublished sources.

## Slide 9: Assess the Health Risk(s)
Assessment = Subjective but informed decision on the level of risk
This requires:
  Full information
  Competent Person
Assessment is not the same as ‘measurement’ or ‘monitoring’.
Measurements can contribute to an assessment.

## Slide 10: Workplace Monitoring
It may be necessary to obtain some monitoring data.
The aim is to assist in ensuring the health protection of employees
  Sampling strategy adopted should be appropriate to the reason for the type of survey to be conducted.

## Slide 11: Identify Actions
Where the assessment indicates a risk to health, it is necessary to specify the steps to be taken to achieve effective control.
This is an important, integral part of the assessment, which is NOT deemed to have been completed without this aspect being addressed.

## Slide 12: Record The Assessment
Demonstrates compliance
Helps with the assessment process
Helps drive the actions
Helps the review process.

## Slide 13: Carry Out Actions
It is important to ensure that recommendations from any assessment are implemented properly.
Many assessments fail to control exposure because the actions are not implemented.

## Slide 14: Review The Assessment
The initial assessment should not be regarded as being relevant forever.
Periodic re-assessments should be undertaken regularly and in any event whenever it is suspected that the assessment is no longer valid.
  Significant changes to:
    The substances/agents involved and/or their sources.
    The plant, e.g. modified engineering control.
    The process or method of work.
    The volume or rate of production.
  Adverse results from:
    Personal exposure monitoring.
    Health surveillance monitoring (e.g. eudiometry, biological monitoring).
    Monitoring of process control (e.g. fugitive emissions).
  Cases of occupational disease.
  New information.

## Slide 15: Expert Systems and Control Banding
There are a number of expert systems which have been developed to assist employers in undertaking health risk assessments.
These systems all use an approach called “Control Banding”.
Control banding involves the following steps.
  Hazard Classification
  Assessment of exposure potential
  Selection of control approach.

## Slide 16: The ILO Toolkit – an example of control banding approaches

## Slide 17
The ILO Toolkit – an example of control banding approaches

## Slide 18
Example of COSHH Essentials Control Approach Sheet

## Slide 19: RISK ASSESSEMENTS

## Slide 20
Paint Spraying

## Slide 21
Grain Sack Filling

## Slide 22
Stone Cutting

## Slide 23
Sack Emptying

## Slide 24
Soldering