## Slide 1: BASIC PRINCIPLES IN OCCUPATIONAL HYGIENE
Day 2

## Slide 2: Physical States

## Slide 3: Physical States
Vapour - the gaseous state of a substance which is liquid at 25°C and 760 mm Hg (STP).
Mist - liquid particles, large size generally produced by bubbling, splashing or boiling of a liquid.
Fume - Solid particles produced by condensation from a liquid or a reaction between two gases. The particle size of a fume <1 micron (µm) diameter anything larger is considered a dust particle.
Dust - particles of solid material in the broad size range of 1 micron to 1 millimetre diameter. Anything of a larger particle size is considered to be grit and will be too heavy to remain airborne.
Aerosol - general term for the dispersions of solid or liquid particles of microscopic size in a gaseous medium e.g. fog, smoke etc. although commonly used to term fine liquid spray (e.g. ‘aerosol can’).
Fibre – Solid particulate which are long and thin i.e. have a high aspect ratio of length to breadth.

## Slide 4: Sampling Techniques
Appropriate for the purpose of the measurement.
‘Monitoring’ or ‘Sampling’ - the use of valid and suitable techniques to derive a quantitative estimate of the Personal Exposure.
Only validated monitoring methods should be used.
  HSE, NIOSH or Other National Standards
  May be legislation/country specific
Personal Exposures.
Static Sampling.

## Slide 5: Types of Sampling
Grab
Short term
Long term
Continuous

## Slide 6: Grab Sampling

## Slide 7: Short Term Sampling

## Slide 8: Long Term Sampling

## Slide 9: Continuous Monitoring

## Slide 10: Bulk Sampling
Taken and analysed for identification purposes.
Not possible to relate the results to the airborne concentrations.
Can be use to show spread of contamination.

## Slide 11: Sampling for Particulates

## Slide 12: Particle Size
Source: Adrian Hirst

## Slide 13: Particle size
Total inhalable dust is the fraction of airborne material which enters the nose and mouth during breathing and is therefore liable to deposition anywhere in the respiratory tract. The particle sizes of total inhalable dust are up to 100 microns.
Respirable dust is that fraction that penetrates to the deep lung where gas exchange takes place. The particle sizes of respirable dust are up to 10 microns.

## Slide 14: Elements of a Sampling System
Sampling train
Pump
Filter
Sampling Head / Size Separator.
Source: SKC

## Slide 15: Sampling Head / Size Seperator
IOM Head
Total Inhalable Dust
Cyclone
Respirable Dust
Source: SKC

## Slide 16: Samples Collected for Welding Fume
Source: Adrian Hirst

## Slide 17: Calculation of Exposure
Concentration (mg/m3) = Weight gain (g) .
Flow rate (litre/min) x Time (min)
OR
= Weight gain (mg)
Flow rate (litre/min) x Time (min) x 1000

## Slide 18: Weight (mass) Gain
Source: Wikimedia Commons
Notes: <number>
Need a better photo of a balance that weights down to 10ug

## Slide 19: Flow rate
Source: Adrian Hirst

## Slide 20: Flow rate
Source: Adrian Hirst

## Slide 21: Calculation of Exposure
Concentration (mg/m3) = Weight gain (mg) .
Flow rate (litre/min) x Time (min) x 1000

## Slide 22: Calculation of Personal Exposure
Time of sample: 09:12 to 15:45
Flow Rate of Pump = 2.0 litres per minute
Weight of Filter before exposure: 25.82 mg
Weight of Filter after exposure: 27.21 mg
What is the Personal Exposure?

## Slide 23: Calculation of Personal Exposure
Time of sample: 09:12 to 15:45 = 5 hours and 33 minutes = 333 mins
Sample Volume = Flow Rate of Pump x Time
Sample Volume = 2.0 lpm x 333 mins
Sample Volume = 666 litres
Sample Volume = 0.666 m3
Mass of material on filter = 27.21 – 25.82 mg
Mass of material on filter = 1.39 mg
Personal Exposure = 1.39 mg / 0.666 m3
Personal Exposure = 2.09 mg/m3

## Slide 24: Sampling for Gases and Vapours
Active Sampling - i.e. by means of a mechanic/sampling pump method.
  Sorbent Tubes
Passive Sampling

## Slide 25: Sorbent Tubes
Source: Adrian Hirst

## Slide 26: Passive Samplers
Source: 3M
Source: SKC

## Slide 27: Equipment used for Taking Grab Sample
Source: Drager
Indicator Tubes

## Slide 28: Equipment used for Taking Grab Sample
Sample Bags
Source: SKC

## Slide 29: Equipment used for Taking Grab Sample
Equipment Type | Mode of Operation | Advantages | Disadvantages
Detector Tubes | Chemical reaction produces colour change | Instant result, easy to use | Not very accurate, often tubes are non-specific
Gas sampling bags, syringes and containers | Pumps used to fill a bag or container to be sent for analysis | Simple, light, cheap | No concentration effect, losses can occur. Not instant.
Paper tapes/ impregnated filters | Air drawn through paper impregnated with chemical reagents producing a colour change | Direct reading, can be used for other sampling techniques | Stain can fade. Personal samplers bulky. Non-specific
Electrochemical Detectors | Substance interacts with electrochemical detector cell | Direct reading, simple, lightweight. Also used for other sampling techniques | Expensive, calibration required, non-specific
Gold Film Mercury Vapour Analyser | Mercury vapour increases resistance of gold film sensor | Simple, lightweight specific | Expensive, requires regular cleaning and calibration

## Slide 30: Equipment used for taking short and long term Samples
Source: SKC
Source: 3M

## Slide 31: Equipment used for taking short and long term Samples
Equipment Type | Mode of Operation | Advantages | Disadvantages
Pumped samplers with solid sorbent traps e.g. charcoal or tenax | Air is drawn through a tube on which the substances of interest are collected | Accurate, reliable, used in many official methods | Needs complex analysis systems, result not instant.
Diffusive Samplers | Contaminant diffuses through a membrane onto a sorbent bed of filter material. | Small, robust, cheap, acceptable to operators | May require validation in field conditions. Needs complex analysis systems. Result not instant.
Bubblers/ Impingers | Air is bubbled through a solvent or reactive solution | Solution obtained can be analysed directly. | Wearer carries a glass vial. Devices bulky, losses can occur

## Slide 32: Equipment used for continuous Sampling
SKC Real Time Dust Monitor
Mini RAE 3000 Portable PID

## Slide 33: Equipment used for continuous Sampling
Equipment Type | Mode of Operation | Advantages | Disadvantages
Flame Ionisation e.g. organic vapour analyser (OVA) or total vapour analyser (TVA) | Combustion of organics in an air / hydrogen flame produces ions – sensed by electrodes and converted into a voltage signal | Portable Usually intrinsically safe | Limited on range and specificity of contaminants
Infrared e.g. Miran Analyser | Absorption of IR radiation used to measure the concentration of substance | Semi-portable, Limited in the compounds it can detect | Bulky, non-intrinsically safe
Ultraviolet | Absorbance of ultraviolet | Portable | Interferences, calibration, not intrinsically safe

## Slide 34: Fixed Position Sampling
Normally personal samples taken.
Fixed Position Samples useful to
  Provide information about contamination from fixed sources
  Assess effectiveness of control measures e.g. local exhaust ventilation.
Care has to be exercised in interpreting the results.
Fixed position samples cannot be used to establish personal exposures or be compared to hygiene standards.

## Slide 35: Sampling Methods
Validated methods of sampling and analysis should be used e.g. HSE, NIOSH
National Standards may specify particular methods.

## Slide 36: Sampling Strategies
Most sampling done to assess personal exposure, but also done to:
  Identification of airborne contaminants
  Identify leaks and spillages
  Assessment of the Effectiveness of Control Measures
Strategy employed needs to be varied depending upon the aims of the survey.

## Slide 37: Sampling Records
Full details of the sampling performed should be recorded and retained.
  When the monitoring was done
  Who and where was monitored
  Details of the equipment used
  The operations in progress at the time of the survey
In most countries records of monitoring should be available to employees or their representatives.

## Slide 38: Sample Handling
Inappropriate handling and transport of sampled materials may give rise to losses or contamination.
  The type of container used
  Temperature
  Sunlight
  Time before analysis
  Contamination.
Advice can usually be obtained from the laboratory undertaking the analysis.

## Slide 39: Collected Sample for Analysis

## Slide 40: Methods of Analysis
There are numerous analytical techniques available for the analysis of airborne contaminants.
  Organic Vapours - gas chromatograph (GC) complete with a flame ionisation detection (FID).
  Inorganic Gases - GC/thermal conductivity methods, photometric and microcoulometry, chemiluminescence.
  Organic Particulate Matter - high pressure liquid chromatography (HPLC), infra-red (IR) or ultraviolet (UV) spectrometery.
  Metals and their Compounds – ICP, Atomic Absorption (AA).
  Mineral Dusts – Microscopy, gravimetery, x-ray diffraction.
Calibration and Quality Control
  Schemes - WASP or RICE (both UK) or PAT (US).
  Accreditation - UKAS (UK) or NATA (Australia).