## Slide 1: HYGIENE STANDARDS AND OCCUPATIONAL EXPOSURE LIMITS

## Slide 2: Hygiene Standards or Occupational Exposure Limits (OELs)
They are not an index of toxicity
They do not represent a fine demarcation between good and bad practice.
They are based on the current best available information and are liable to change.
If there is not a hygiene standard set for a chemical substance, it does not mean that substance is safe.
Good occupational hygiene practice is to keep airborne contaminants to as low a level as possible, not to just below the relevant hygiene standard(s).
They apply to occupational exposure of adults. They are not applicable to environmental exposure where more susceptible groups exist e.g. pregnant women, children, infirm.
For chemicals they generally relate to airborne concentrations i.e. they only take into account the inhalation route of entry.
They generally refer to single substances, although some guidance may be given on mixed exposures.

## Slide 3: Setting of Hygiene Standards and Exposure Limits
There are three main types of hygiene standards:-
  Chemical agents such as gases, vapours, fumes, mists, dusts and aerosols.
  Physical agents such as noise, vibration, heat, cold and radiation (ionising and non‑ionising)
  Biological exposure indices.

## Slide 4: Setting of Hygiene Standards and Exposure Limits
When setting hygiene standards for hazardous agents, the effects the agents might have on the body have to be considered namely:-
  Contact
  Local toxic effects at the site of contact (skin, eye, respiratory tract etc.)
  Absorption
  Transport, Metabolism, Storage
  Systemic toxic effects, remote from the site of contact (any organ system e.g. blood, bone, nervous system, kidney etc.)
  Excretion
  Acute toxicity i.e. the adverse effects occur within a short time of exposure to a single dose, or to multiple doses over 24 hours or less e.g. irritation, asphyxiation, narcosis
  Chronic toxicity.

## Slide 5: Setting of Hygiene Standards and Exposure Limits
The data for setting hygiene standards includes the use of:
  Animal studies
  Human research and experience
  Epidemiology (the statistical study of disease patterns in groups of individuals)
  Analogy.

## Slide 6: Hygiene Standards for Chemical Agents
Limit | Country / Union
TLV – Threshold Limit Value | USA
MAK - Maximale Arbeitsplatz-Konzentration | Germany
MAC | Russia
WEL – Workplace Exposure Limit | United Kingdom
IOELVs (Indicative Occupational Exposure Limit Value) | Europe
OES – Occupational Exposure Standards | Australia
WES – Workplace Exposure Standards | New Zealand
Only a few countries have organisations with the appropriate resources for setting limits. Most countries base limits on the following:

## Slide 7: Quantifying Airborne Concentrations of Chemical Agents
Airborne contaminants can be quantified in several ways;
By volume - atmospheric concentration in parts per million (ppm)
By weight - milligrams of substance per cubic metre of air (mg.m-3).

## Slide 8: Milligrams per cubic metre (mg m-3)
mg = mg/m3 = mg m-3
m3

## Slide 9: Quantifying Airborne Concentrations of Chemical Agents
There is a correlation between ppm and mg.m-3:
Conc by weight (mg.m-3) = Conc by volume (ppm) x Molecular weight (g)
24.06
at 20°C and 760 mm Hg (1 atmosphere pressure)

## Slide 10: Quantifying Airborne Concentrations of Chemical Agents
Can you rearrange this equation to convert ppm to mg.m-3 ?
Conc by weight (mg.m-3) = Conc by volume (ppm) x Molecular weight (g)
24.06
Conc by volume (ppm) = ?

## Slide 11: Quantifying Airborne Concentrations of Chemical Agents
Can you rearrange this equation to convert ppm to mg.m-3 ?
Conc by weight (mg.m-3) = Conc by volume (ppm) x Molecular weight (g)
24.06
Conc by volume (ppm) = Conc by weight (mg.m-3) x 24.06
Molecular weight (g)

## Slide 12: Categories of Exposure Limits
Long Term Exposure Limits are expressed as a Time Weighted Average (TWA) normally over an eight hour period. This allows for exposures to vary through the working day so long as the average exposure does not exceed the limit.
Short Term Exposure Limit (STEL) normally over a 15 minute period are used when exposure for short periods of time occurs.
Ceiling Limits are sometimes used and are concentrations that should not be exceeded during any part of the working exposure.
"Skin" Notation - Substances can have a contributing exposure effect by the cutaneous route (including mucous membranes and eyes).

## Slide 13: Effects of Mixed Exposures
Synergistic substances: known cases of synergism are considerably less common than the other types of behaviour in mixed exposures.
Additive substances: where there is reason to believe that the effects of the constituents are additive, and where the WELS are based on the same health effects, the mixed exposure should be assessed using a formula.
Independent substances: where no synergistic or additive effects are known or considered likely, the constituents can be regarded as acting independently and the measures needed to achieve adequate control assessed for each separately.

## Slide 14: Calculation of exposure with regard to the specified reference periods
The 8-hour reference period
Exposures treated as equivalent to a single uniform exposure for 8 hours (the 8-hour time-weighted average (TWA) exposure).
Represented mathematically by:
C1 x T1 + C2 x T2 + ……. Cn x Tn
8
Where:
C1 is the occupational exposure
T1 is the associated exposure time in hours in any 24-hour period.

## Slide 15: Calculation of exposure with regard to the specified reference periods
The 8-hour reference period - Example 1
The operator works for 7h 20min on a process in which he is exposed to a substance hazardous to health. The average exposure during that period is measured as
0.12 mg m-3.
The 8-hour TWA therefore is:
7h 20min (7.33 h) at 0.12 mg m-3
40min (0.67h) at 0 mg m-3
That is:
(0.12 x 7.33) + (0 x 0.67) = 0.11 mg m-3
8

## Slide 16: Calculation of exposure with regard to the specified reference periods
The 8-hour reference period - Example 2
The operator works for 6h 00min on a process in which he is exposed to a substance hazardous to health. The average exposure during that period is measured as 0.5 mg m-3. The operator then works for a further 1 hour in which he is exposed to 1.5 mg m-3.
What is the 8-hour TWA ?

## Slide 17: Calculation of exposure with regard to the specified reference periods
The 8-hour reference period - Example 2
The operator works for 6h 00min on a process in which he is exposed to a substance hazardous to health. The average exposure during that period is measured as 0.5 mg.m-3. The operator then works for a further 1 hour in which he is exposed to 1.5 mg.m-3.
What is the 8-hour TWA therefore is:
6h 00min (6.00 h) at 0.5 mg m-3
1h 00min (1.00 h) at 1.5 mg m-3
1h 00min (1.00 h) at 0.0 mg m-3
That is:
(0.5 x 6.00) + (1.5 x 1.00) + (0 x 1.00) = 0.69 mg m-3
8

## Slide 18: The short-term reference period
Exposure should be recorded as the average over the specified short-term reference period (usually 15 minutes) and should normally be determined by sampling over that period.
If the exposure period is less than 15 minutes, the sampling result should be averaged over 15 minutes. For example, if a 5 minute sample produces a level of 150 ppm and is immediately followed by a period of zero exposure then the 15-minute average exposure will be 50 ppm.
That is: 5 x 150 = 50 ppm
15

## Slide 19: Biological Monitoring Guidance Values
Complimentary technique to air monitoring.
Biological monitoring is the measurement and assessment of hazardous substances or their metabolites in tissues, excreta or expired air in exposed workers.
Measurements reflect absorption of a substance by all routes.
Particularly useful where exposure is by routes other than inhalation
In most cases limits for Biological Monitoring are not statutory.
Biological monitoring undertaken needs to be conducted on a voluntary basis (i.e. with the fully informed consent of all concerned).