## Slide 1: BASIC PRINCIPLES IN OCCUPATIONAL HYGIENE
Day 3

## Slide 2: 11 - ASBESTOS

## Slide 3: Asbestos
“the evil effects of asbestos dust” … “sharp, glass-like, jagged nature of the particles … effects have been found to be injurious”
- The Chief Factory Inspectors Report UK (1898)

## Slide 4: Types of Asbestos

## Slide 5: What is Asbestos?
A naturally occurring, mined, fibrous silicate mineral with various compositions & structures
Used extensively as a heat insulator & fire resistant material
Numerous different forms. Present as sheet; board; rope; or mixed with plaster.
Notes: <number>

## Slide 6: Asbestos Mines
Notes: <number>

## Slide 7: Mined Asbestos
Notes: <number>

## Slide 8: What are Fibres?
Long & thin structures
Defined by their aspect ratio [width: length]
Can be man made, mineral, animal, vegetable
Asbestos is a fibre but not all fibres are asbestos [E.g.. Mineral wool, cotton, wool, carbon fibres].
Notes: <number>

## Slide 9
WHO fibre
L > 5m
D < 3 m
L/D (aspect ratio) > 3:1
WHO fibre as measured
Fibres up to 100m long have been found in the deep lung.
Notes: <number>

## Slide 10: Properties of Asbestos
Fire resistance
Mechanical strength
Chemical resistance
Thermal insulation.

## Slide 11: Uses of Asbestos
Source: HSE
Fire Blanket
Ceiling Tile
Soffits
Pipe Insulation
String
Paper
Cement Sheets
Gasket

## Slide 12: Uses of Asbestos
Product | Type of Asbestos | Approximate Content (%)
Cement Materials e.g. corrugated sheets, water tanks, pipes, prefabricated building components | Chrysotile (occasionally incorporating Crocidolite or Amosite) | 10 - 20
Fire-resistant Insulating Board | Amosite (occasionally incorporating chrysotile or crocidolite | 15 - 40
Thermal, insulation, lagging, incl. pipe and vessel insulation. | Amosite, chrysotile & crocidolite | 1 - 55
Sprayed coatings e.g. applied to structural beams and ceilings as fire protection/and/or acoustic and thermal insulation | Amosite, chrysotile & crocidolite | 60 - 90
Textiles e.g. heat resistant gloves, fire-blankets, fire-protective clothing & insulation mattresses. | Chrysotile (occasionally Crocidolite) | 85 - 100
Jointings & packings e.g. gaskets. | Chrysotile (occasionally Crocidolite) | 25 - 85
Friction materials e.g. automotive brake & clutch lining. | Chrysotile | 30 - 70
Floor tiles. | Chrysotile | 5 - 7
Filler & Reinforcements e.g. in felts, millboards, papers, underseals, mastics, adhesives. | Chrysotile (occasionally Crocidolite for some applications) | 1 - 10
Reinforced thermo-setting plastics & battery cases. | Chrysotile, crocidolite & amosite | 5 - 20

## Slide 13: Airborne Asbestos Fibres
Activity | f/ml
Dry removal of lagging | upto 100
Drilling of asbestos insulation board | upto 10
Hand sawing of asbestos insulation board | upto 10
Drilling of asbestos cement | upto 1
Hand sawing of asbestos cement | upto 1
Use of a circular saw | upto 20

## Slide 14: Asbestos Register
Record the use/presence of all asbestos and asbestos-containing materials at work sites.
Record the location of all asbestos materials on site.
Ensure that the condition of asbestos-containing materials are frequently inspected and any necessary remedial action is instigated.
Ensure that any work with asbestos or asbestos-containing materials is carried out in an approved manner.
Minimise the acquisition and use of materials or equipment, which may contain asbestos.

## Slide 15: REMEDIAL TREATMENT OF ASBESTOS REMOVAL
Damaged and friable, i.e. in an easily crumbled condition, thereby having a potential for releasing airborne fibres.
Expected to deteriorate in future.
If it is likely that they will be disturbed during maintenance, construction or demolition.
Asbestos-containing materials should be removed if they are:

## Slide 16
Wrapping the outer surface with, for example, canvas or aluminium.
Sealing with an encapsulant that seals the fibres together.
REMEDIAL TREATMENT OF ASBESTOS REPAIR / ENCAPSULATION