## Slide 1: BASIC PRINCIPLES IN OCCUPATIONAL HYGIENE
Day 3

## Slide 2: 13 - NOISE

## Slide 3: NOISE
Noise is unwanted sound.
Known for many years as a cause of hearing loss in industry.
Sound is the sensation that is perceived by the human or animal brain as a result of longitudinal vibrations of molecules of the air impinging on the ear.
Sounds are actually pressure waves caused by a vibrating body, which radiate from the source.

## Slide 4: The Ear
Cochlea
External Ear
Middle Ear
Source: Wikimedia Commons

## Slide 5: Audible Sound
Two key features of sound are frequency and intensity.
The number of pressure waves/vibrations per second is known as the frequency, and is expressed in the unit Hertz (Hz)
The more fluctuations per second the higher the pitch of the sound
By intensity (I) we mean the amplitude (size) of the pressure waves and is defined as the average amount of energy passing through a unit area in unit time (Wm2).

## Slide 6: Decibels, Pascals Watts/metre2
Source: Canadian Centre for Occupational Health and Safety

## Slide 7: Health Effects of Excessive Noise
Noise Induced Hearing Loss (NIHL), a cumulative effect from repeated exposure and it is due to damage to the hair cells of the cochlea in the inner ear.
Tinnitus - Noise heard in the ear without external cause, frequently accompanies deafness.
Temporary Threshold Shift (TTS) - Damage to the hair cells of the inner ear which can impair hearing temporarily, resulting from exposure to high noise levels.
Physical damage to the eardrum and ossicles induced by excessively high noises e.g. explosions.
Annoyance/stress, which is difficult to measure and quantify, but may cause psychological effects such as poor concentration, irritability and stress.

## Slide 8: Addition of Sound Levels
When two sounds are being emitted at the same time their total combined intensity is not the numerical sum of the decibel levels of each sound.
For accurate calculations they must be added as logarithms – usually using a calculator.
Alternatively a reasonable approximation of additions of decibel levels can be made.
Difference in dB (A) | Add to the Higher
0 or 1 | 3
2 or 3 | 2
4 to 9 | 1
10 or more | 0

## Slide 9: Addition of Sound Levels
Doubling of the Pressure increases noise levels by 3dB

## Slide 10: Frequency Analysis
Source: Castle Group

## Slide 11: Decibel Weightings
As the human ear is more sensitive to certain frequencies than others, it is possible to make allowances for that in the electronic circuitry of a sound level meter.
Certain frequencies are suppressed whilst others are enhanced in order to approximate to the response of the human ear.
Known as weighting and there are A, B, C and D weightings available for various purposes. The one that has been adopted for a workplace spectrum is given in dB(A).

## Slide 12: Decibel Weightings
Source: Wikimedia Commons

## Slide 13: Equivalent Continuous Sound Level (Leq)
Leq can be defined as the steady sound pressure level, which over a period of time has the same energy content and consequently the same hearing damage potential as the actual fluctuating noise.
Source: Adrian Hirst

## Slide 14: Noise Dose
Duration per Day (hours) | European Limit (Leq ) dB(A)
16 | 82
8 | 85
4 | 88
2 | 91
1 | 94
30 min | 97
15 min | 100
7.5 min | 103
3.75 min | 106

## Slide 15: Noise Limits
European Limits:
Lower exposure action values: a daily or weekly personal noise exposure of 80dB (A-weighted) and a peak sound pressure of 135dB (C-weighted).
Upper exposure action values: a daily or weekly personal noise exposure of 85dB (A-weighted) and a peak sound pressure of 137 dB (C-weighted).
Exposure limit values: a daily or weekly personal noise exposure of 87dB (A-weighted) and a peak sound pressure of 140dB (C-weighted).
Other Limits
In the USA a more complex set of criteria is used which correlates dose with sound pressure level and time. This is known as a 5 dB doubling concept and is largely discredited outside of the USA.

## Slide 16: Assessment of Workplace Noise
Source: Wikmedia Commons
Noise Meter
Noise Dosimeter

## Slide 18: Control of Workplace Noise
Reduction of noise at source - best achieved at the design stage
Enclosure of noisy equipment - although heat dissipation and access for maintenance can be a problem.
Screening of noisy equipment from the worker and/or increased separation of the worker from the noise source(s)
Absorption of sound by the cladding of appropriate surfaces with sound absorbent material where reverberation can be a problem.

## Slide 19: Protection of Personnel at Risk
Provision of Noise Refuges in designated areas.
Alteration of the Work Pattern.
Use of Personal Hearing Protection Devices, e.g. ear muffs, ear plugs.
Source: Wikmedia Commons