## Slide 1: BASIC PRINCIPLES IN OCCUPATIONAL HYGIENE
Day 4

## Slide 2: 17 - IONIZING RADIATION

## Slide 3: Nature
It is possible to explain many atomic scale phenomena by assuming that all atoms are made up of three fundamental particles. These are called electrons, protons and neutrons.
The simplest atomic combination is formed by one electron and one proton ‑ the hydrogen atom.
In general, however, a number of negatively charged electrons rotate in certain allowed orbits around a central nucleus which is composed of an equal number of positively charged protons and some neutrons.

## Slide 4: Hydrogen Isotopes

## Slide 5: Different Types of Ionising Radiation
Type | Symbol | Nature | Charge | Relative Mass | Range in Air | Penetration
alpha |  | particulate (helium nucleus) | + + | 4 | 0.4 - 2 cm | None
beta |  | particulate (electron) | - | 1/1800 | 5-20 cm | Slight
neutron | n | particulate (neutron) | 0 | 1 | long | High
gamma |  | electro-magnetic | 0 | 0 | v.long | High
x-ray |  | electro-magnetic | 0 | 0 | v.long | High

## Slide 6: Radionuclides
Ionising radiation is emitted from unstable nuclei which are decaying, with the emission of energy.
These are known as radioactive nuclei (radionuclides).
The trefoil symbol is used to indicate radioactive material.
A radionuclide loses its radioactivity by decay.

## Slide 7: Units of Ionising Radiation
Most countries now use the International System of Units (abbreviated SI from the French le Système International d'Unités) which is the modern form of the metric system.
The US continues to use an older system for some regulatory purposes.

## Slide 8: Units for Measuring Radiation – Part 1
Activity (Becquerel)
The SI unit of for the activity of a radioactive material is the becquerel (Bq), where one Becquerel = 1 disintegration per second.
The traditional unit of activity has been the Curie (Ci), where one Curie = 3.7 x 1010 disintegration's per second.

## Slide 9: Units for Measuring Radiation – Part 2
Absorbed Dose (Gray)
This is a measurement of the energy imparted to matter by ionising radiation per unit mass of the material. The SI unit of absorbed dose is the gray (Gy), which is equal to an energy absorption of 1 joule/Kg.
The traditional unit of absorbed dose is the rad, where 1 Gray = 100 rads.

## Slide 10: Units for Measuring Radiation – Part 3
Dose Equivalent (Sievert)
Equal absorbed doses may not always give rise to equal risks of any biological effect. The relative biological effectiveness of a particular absorbed dose may be affected by the type of radiation or the radiation conditions. Accordingly the equivalent dose can be expressed as:
  Dose equivalent (Sievert) = Absorbed dose (Gray) x Modifying Factor.
  The modifying factor depends on both the 'quality' of the radiation (which is 1.0 for the lower energy radiations but rises to 20 for high energy fission fragments) and the part of the body affected.
  The traditional unit is the rem where 1 sievert = 100 rem.

## Slide 11: External Radiation
 Minimal hazard
 Skin and eyes at risk
 Whole body at risk (penetrating radiation)
The effects of external exposure can be summarised as:

## Slide 12: Internal Radiation
 Very serious hazard
 Serious hazard
 Not normally applicable
The internal effects of exposure are:

## Slide 13: Levels of Radiation
Cosmic radiation which increases with height above sea level
The material which your home is made from.
Time spent on aircraft
Smoking
Medical x–rays
Other lifestyle factors.
The Los Alamos National Laboratory in the US provides an online tool which enables you to calculate your annual radiation dose. This takes into account:

## Slide 14: Biological Effects of Ionising Radiation
Acute Effects | Chronic Effects
Erythema | Cancer
Blood change | Hereditary defects
Sterility | 
Death | 

## Slide 15: Uses of Radiation – Part 1
Industrial
Gauges - radiation (, , , neutrons) can be used to measure thickness, density and moisture level
Industrial Radiography - checking the integrity of welds (, )
Laboratory analytical techniques - X-ray diffraction and fluorescence
Tracers - Radionuclides are used in yield determination, wear tests, water and oil reservoir investigations.

## Slide 16: Uses of Radiation – Part 1
Medical
Diagnostic X-rays
Medical imaging - radionuclides are sometimes used as markers.
Cancer treatment - using radionuclides to destroy tumours.

## Slide 17: Measurement of Radiation – Part 1
Emitted radiation: Geiger counters and scintillation counters can be used to measure the levels of radiation from particular sources. The devices are often specific to the type of radiation being measured.

## Slide 18: Measurement of Radiation – Part 2
Radiation dose: Various devices can be used to measure personal dose. It is important to differentiate between internal dose (that which a person takes into their body by routes such as breathing) and external dose (received simply by virtue of being in an environment where radiation is present).

## Slide 19: Radiological Protection – Part 1
Time: Limiting or minimizing the amount of time to which people are exposed to radiation will reduce the dose which they receive.
Distance: Radiation intensity decreases sharply with distance, according to an inverse square law. In addition even air attenuates alpha and beta radiation.

## Slide 20: Radiological Protection – Part 2
Shielding: Alpha particles may be completely stopped by a sheet of paper, beta particles by aluminum shielding. Gamma rays can only be reduced by much more substantial barriers. Barriers composed of lead, concrete or water give effective protection from energetic particles such as gamma rays and neutrons. Some radioactive materials are stored or handled underwater or by remote control in rooms constructed of thick concrete or lined with lead.

## Slide 21: Radiological Protection – Part 3
Containment: Radioactive materials may be used in "sealed sources" to prevent them spreading. The use of small working spaces, segregated areas and controlled ventilation are also used to contain the release of radioactive materials

## Slide 22: Radiological Protection

## Slide 23: Health Surveillance
Completion of a questionaire
A blood test
Urine test
Blood Pressure check
Height and Weight Check
General discussion about health.
Employees working in controlled areas would typically be subjected to: