## Slide 1: BASIC PRINCIPLES IN OCCUPATIONAL HYGIENE
Day 4

## Slide 2: LIGHTING AND NON-IONIZING RADIATION

## Slide 3: LIGHTING AND NON-IONIZING RADIATION
Electromagnetic waves are produced by the motion of electrically charged particles.
These waves are also called "electromagnetic radiation" because they radiate from the electrically charged particles.
They travel through empty space as well as through air and can penetrate some other substances.
Radio waves, microwaves, visible light, and x rays are all examples of electromagnetic waves.

## Slide 4: LIGHTING AND NON-IONIZING RADIATION
As with sound energy, Electromagnetic Radiation can be described in terms of its frequency (or wavelength) and its intensity.
f  1

Where:  = wavelength
f = frequency
The frequency (Hz) is inversely proportional to the wavelength (nm), so higher frequencies have shorter wavelengths:

## Slide 5: The Electromagnetic Spectrum

## Slide 6
Non - Ionizing
Ionizing

## Slide 7: Non-ionising and Ionising radiation
The distinction between non-ionising and ionising radiation is simply one of associated energy.
For the ionising region of the electromagnetic spectrum, the energy incident upon a material is large enough to remove an electron from an atom orbit to produce ionisation.

## Slide 8: Ultraviolet (UV) Radiation
UV is invisible radiation produced naturally by the sun (solar radiation) and artificially in industry via arcs (e.g. welding) operating at high temperatures.
Eyes and skin are particularly vulnerable.
Sunburn, blistering of the skin.
Premature ageing and thickening (keratosis) of the skin.
Skin cancer.
Conjunctivitis.

## Slide 9: Infrared (IR) Radiation
IR radiation is emitted by hot bodies, e.g. furnaces and gas torches.
Its primary effect is heating of surface tissues.
Excessive exposure to radiant heat will produce immediate discomfort and therefore a suitable warning of impending damage is provided, usually before burning can occur.

## Slide 10: Laser Radiation
LASER = 'Light Amplification by Stimulated Emission of Radiation'.
Concentrated beam of non‑ionising radiation
  Of a single wavelength or a narrow wavelength band
  In the visible and infrared region of the electromagnetic spectrum
Hazardous due to concentrated intensity.
Damage eyes from repairable burns to permanent blindness.
Cataract formation may also occur.
Lasers have widespread use, e.g. in communications, construction, medical applications, research, surveying.

## Slide 11: Laser Classifications
Class 1 | Safe | 
Class 1M | Safe provided optical instruments are not used. | 
Class 2 | Visible lasers. Safe for accidental exposure. | 
Class 2M | Visible lasers. Safe for accidental exposure providing optical instruments are not used. | 
Class 3R | Not safe. Low risk. | 
Class 3B | Hazardous. Viewing of diffuse reflection is safe. | 
Class 4 | Hazardous. Viewing of diffuse reflection is also hazardous. Fire risk. | 
Warning label for Class 2 and higher

## Slide 12: Microwave Radiation
Microwaves are produced by molecular vibration in solid bodies.
The primary effect on the body is thermal - burning of the skin and eyes.
Prolonged exposure to low level microwave radiation has been linked with headaches, sleeplessness, irritability, fatigue and memory loss.
Microwaves are widely used in applications like wireless computing and mobile phone networks.
Much public concern has been raised about the possibility of serious long-term health effects such as cancer. As yet, research has failed to demonstrate such a link conclusively.

## Slide 13
Visible
400 to 700 nm

## Slide 14: LIGHTING
In terms of occupational hygiene we are concerned with the subjective feeling of visual comfort, and good illumination which is described in terms of the quantity and quality of the lighting.
Quantity - this is the amount of illumination on the task. It is measured in lux and must be sufficient for the worker to undertake the task.
Quality - is the suitability of the illumination, for example the distribution of brightness in a visual environment, the colour of light, its direction, diffusion and the degree of glare.

## Slide 15: Evaluation of Illumination
Light meter (often termed a 'Lux' meter).
Colour corrected to respond to the human eye.

## Slide 16: Glare
Any brightness within the field of vision that causes discomfort, annoyance, interference with vision, or eye fatigue.
  Disability glare
  Discomfort glare
  Reflected glare