## Slide 1: BASIC PRINCIPLES IN OCCUPATIONAL HYGIENE
Day 4

## Slide 2: 18 - ERGONOMICS

## Slide 3: Common Activities
manual handling of loads;
tasks involving repetitive actions;
the use of display screen equipment, such as when working with computers.
Some common activities where ergonomics
are important are:

## Slide 4: Different Work Places

## Slide 5: Evaluation of Ergonomics Factors in the Workplace
It should address:
Hardware
Software
Visual workspace
Organisation
Physical workspace
Individual characteristics

## Slide 6: Manual Handling Assessment
It should address four critical factors:
The task
The load
The working environment
The capabilities of the individual.

## Slide 7: THE BACK

## Slide 8: Simple Assessment Procedure
Is the operation essential? Can it be avoided?
Consider the shape, size, weight and special difficulties of a load.
How is it handled?
Where is it moved from and to and how often? Repetitive bending, twisting movements increase the risk, as does lifting with extended reach.
Does the working environment add to the risk of injury?
Are floors slippery, uneven?
Is the environment cramped, hot or badly lit?
Are the task and the workplace adapted to the individual? At its simplest this may simply involve considering working heights of benches, tables, stillage sizes and so on.
Consider possible remedial measures, eg. it may be possible to use mechanical aids or breakdown the load, or the task may be re‑arranged.

## Slide 10: Information and Instruction
Where it is reasonably practicable to do so, employees involved in manual handling operations should be provided with precise information about the weight of each load, and about the heaviest side of any load whose centre of gravity is not positioned centrally.

## Slide 11: Training
A suitable training programme should address:
How potentially hazardous loads may be recognised;
How to deal with unfamiliar loads;
Good handling techniques, including the proper use of handling aids;
The proper use of personal protective equipment;
Features of the working environment that contribute to safety;
The importance of good housekeeping;
Factors affecting individual capability, including fitness and health.

## Slide 12: Repetitive Tasks
Tasks that involve repeated movements can lead to disorders of the muscles, joints and tendons, even when the individual actions do not involve excessive load or force.

## Slide 14: Display screen equipment (DSE)
Many types of computerised equipment used in laboratories, factories, offices and home working incorporate a display screen and some kind of data entry device such as a keyboard or mouse.

## Slide 15: Postural Problems
These range from fatigue or soreness in the arm, hand and shoulder areas to chronic soft tissue disorders like carpal tunnel syndrome - inflammation of the sheath surrounding the tendons that flex the fingers.

## Slide 16: Visual Problems

## Slide 17: Fatigue and Stress
Many symptoms described by display screen users reflect stresses arising from the user's task. They may be secondary to upper limb or visual problems but they are more likely to be caused by poor job design or work organisation, lack of control of the work by the user, under-utilisation of skills, high-speed repetitive working or social isolation.