## Slide 1
M502
Thermal Environment
Day 1
Notes: <number>

## Slide 2: Emergency Procedures
(Insert appropriate procedures)

## Slide 3
(Lecturers Introductions)

## Slide 4: Group Introductions
In 30 seconds-
Tell us who you are:
Where you work:
What your role is:

## Slide 5: Course Aims
To provide participants with a sound understanding of the of the effects of the thermal environment on people and the means of assessing and controlling the risks associated with thermal stress

## Slide 6: Course Learning Outcomes
Participants will be able to:
  Identify sources of thermal stress within the working environment
  Understand the nature of thermal strain on the body
  Make assessments of the thermal environment through appropriate measurement and other means

## Slide 7: Course Learning Outcomes (Cont)
Participants will be able to:
  Evaluate the likely risk from exposure to thermal stress
  Suggest appropriate control approaches for the thermal environment

## Slide 8: Topics to be Discussed
The Thermal Spectrum
Principles
Effects of temperature extremes
Thermal comfort
Evaluation of hot & cold environments
Thermal surveys
Control of hot & cold environments
Approaches to Risk Assessment

## Slide 9: Today’s Learning Outcomes
Thermal Spectrum
  To understand the range of thermal environments that humans work within
Principles
  Understand the basic physiological responses of the body to hot & cold environments
  Understand the processes for heat production & exchange

## Slide 10: Today’s Learning Outcomes (cont)
Effects of Temperature Extremes
  Understand the effects of hot & cold environments
Thermal Surveys
  Understand the principles of measuring major environmental factors
  Review different monitoring strategies
  Understand some approaches to establishing the degree of risk resulting from a thermal survey

## Slide 11: Work Groups
Each participant will be assigned a work group for the duration of the course
The work groups are expected to work as a team when evaluating in cases studies and practical sessions
Notes: <number>

## Slide 12: Thermal Spectrum
Source: University of Wollongong

## Slide 13: Thermal Spectrum
Energy from the sun is fundamental to life in all its forms
  Humans, plants, animals & organisms
Evolution has decided that humans are warm-blooded and their biochemistry functions within a narrow operating temperature range

## Slide 14: Thermal Spectrum (cont)
Humans can be considered as homeotherms and attempt to maintain the body temperature near 37oC
A deviation of a few degrees can have serious consequences

## Slide 15: Thermal Spectrum (cont)
In order to maintain the core body temperature within acceptable limits there is a need to understand and control those factors which may influence this process
As there is significant variability within humans the application of any measurement index or control approach may not be appropriate to all

## Slide 16: Work in Extreme Temperatures
Humans work in extremes of heat or cold on a daily basis
  Oil production in Alaska & Middle East
  Mining in the Arctic regions of Canada & the high temperatures of Central Africa & Australia

## Slide 17: Work in Extreme Temperatures (cont)
Other examples of work in extreme conditions
  Refrigerated areas like cool rooms & freezers
  High radiant energy areas e.g. foundries, steel plants, glass plants, coke ovens, brick plants & smelters
  Outdoor areas where there is exposure to the sun or wind chill
  Military activities

## Slide 18: Work in Moderate Temperatures
Work in areas of extreme temperatures is associated with increased awareness with the local conditions & control methods
This is not apparent in more temperate climates
Hotter than normal conditions can affect whole production facilities through heat induced illness

## Slide 19: Work in Moderate Temperatures (cont)
Reasons for these events include:
  Thermoregulation of the body is normally within very narrow range & time is needed to adjust to an increase in that range
  Workforce may have more at risk persons e.g. obese, elderly, unfit
  Workplace not designed for significant variation in temperatures

## Slide 20: Work in Moderate Temperatures (cont)
Activities in moderate temperatures where thermal stress may be an issue
  Rubber vulcanising plants
  Bakeries
  Commercial kitchens
  Laundries
  Food canneries
  Boiler rooms
  Fire fighting activities

## Slide 21: Case Study 1 - Bakery
Break up into groups and review the case study (located in appendix 2)
20 minutes has been allocated for this review
A group discussion will be conducted after the exercise

## Slide 22: Case Study 1 - Bakery
Source: University
of Wollongong

## Slide 23: Principles

## Slide 24: Principles
Heat Stress
  Net heat load from the combined contributions of work (metabolic load), environmental factors (air temperature, movement, humidity, radiant load) & clothing requirements

## Slide 25: Principles (cont)
Heat Strain
The overall physiological response resulting from heat stress

## Slide 26: Relationship - Heat Stress & Heat Strain
Source: WHO 1969

## Slide 27: Homeostasis
Process by which the body keeps its internal environment (e.g. temperature, blood pressure, pH, blood gases) stable by modulating physical functions & behavior

## Slide 28: Homeostasis (cont)
Dynamic equilibrium in which continuous changes are occurring
Process is controlled by a part of the brain called the hypothalamus which adjusts
  Breathing & metabolic rates
  Blood vessel dilation
  Blood sugar levels
  in response to changes caused by factors such as ambient temperature, hormones & disease

## Slide 29: Typical Body Temperatures (Tc)
46.5°C Highest recorded survivable core temperature
43°C Tissue damage (brain, liver)
41°C Cessation of sweating
39°C The threshold of hyperthermia
36.8°C Normal core temperature

## Slide 30: Typical Body Temperatures (cont)
35°C The threshold of hypothermia
33°C Impaired muscle function, introversion, loss of mental alertness
30°C Cessation of shivering and then unconsciousness
28°C Possible ventricular fibrillation

## Slide 31: Typical Body Temperatures (cont)
26°C Bradycardia and Bradypnoea
24°C Possible death without rewarming
14.4°C Lowest recorded core temperature for a survivor of accidental hypothermia

## Slide 32
36.4
36.6
36.7
36.8
36.9
37.0
37.1
37.2
37.3
37.4
36.3
36.2
36.1
36.0
35.9
0
10
20
30
40
50
60
Number of people
Core temperature (oC)
Mean
1 SD
2 SD
2 SD
1 SD
Source : Taylor 2005- reproduced with permission
Tc of 276 Healthy Resting Adults
Notes: <number>

## Slide 33: Variation of Tc in Humans
Variation occurs not only between humans but within humans
  Tc may be 0.5-1.0oC higher in evening due to inherent circadian temperature rhythm
  Ovulation in women causes Tc to rise by 0.1-0.4 oC

## Slide 34: Skin Temperature
Temperature gradient from skin surface to the superficial layers of muscle
Varies according to the external temperature , region of body surface & rate of heat conductance from core to shell
Determines rate & direction of heat flow in body

## Slide 35: Variation in Skin Temperature
Thermally comfortable individual may have following skin temperature variations (o C)
  Toes = 25
  Upper arms & legs = 31
  Forehead = 34
  Core = 37

## Slide 36: Human Thermal Regulation
Behavioral change
  Clothing
  Changing posture
  Movement
  Shelter
  Personal protective equipment
Physiological systems
  Hypothalamus

## Slide 37: Feedback Control of Body Temperature

## Slide 38: Physiological Responses to Hot Environments
Vasodilatation (vasodilation)
Sweating
Electrolyte changes
Dehydration
Heart rate
Respiration rate
Other effects

## Slide 39: Vasodilatation (Vasodilation)
Venous blood returns to the heart near the skin hence increasing the availability of heat loss from the skin to the environment

## Slide 40: Sweating
As body temperature increases, sweat is secreted over the body to allow cooling via evaporation
Eccrine sweat glands perform the thermoregulatory function and there are 2-4 million such glands distributed over the entire body surface
Major method of maintaining Tc in hot conditions

## Slide 41: Electrolyte Changes
Sweating can significantly reduce electrolytes
Many organs depend on ionic gradients across cell membranes to support electrical activity
Failure to maintain electrolyte levels often results in muscle cramps & gastrointestinal disturbances

## Slide 42: Dehydration
Sweating is a natural process to control Tc but it sacrifices body fluid to cool the skin temperature
For people working in hot environments the maximum daily sweat rate can approach 10-15 litres/day

## Slide 43: Dehydration (cont)
Consequences of dehydration
  Reduced blood volume
  Impaired cardiovascular stability
  Reduced physical & cognitive performance
  Reduced muscle & general endurance
  Elevated thermal strain
  Reduced heat tolerance
  Reduction in benefits of heat adaption
  Increased risk of heat illness

## Slide 44: Heart Rate
Heart rate increases with
  work rate in order to allow an increase in blood flow to working muscles
  vasodilatation in order to allow an increase blood flow to skin for heat loss
In hot environments, competition between muscle and skin for blood can cause exhaustion

## Slide 45: Respiration Rate
Heat can be lost to the environment via evaporation of moisture in the respiratory tract

## Slide 46: Other Physiological Effects
Prickly heat
  skin rash from continued exposure to humid heat and the skin remaining wet due to unevaporated sweat
Fatigue
  Heat stress can contribute to increased levels of fatigue and vice versa

## Slide 47: Physiological Responses to Cold Environments
Vasoconstriction
Shivering
Piloerection
Cold diuresis
Respiration
Heart rate
Dehydration
Psychological
Other effects

## Slide 48: Vasoconstriction
Reaction of the body to reduce heat loss
Constriction of the superficial veins in the limbs so that blood from the skin returns along the venal comitans close to the artery thus gaining heat to return to the body core

## Slide 49: Shivering
Designed to increase the metabolic heat production within the body as an offset to a Tc decrease
In very cold environments (or cold water immersion) shivering can reduce fall in Tc but can also increase heat loss to the environment

## Slide 50: Piloerection
Occurs when skin becomes cold
Hairs stand on end so as to maintain a layer of still air between body & environment to reduce heat loss

## Slide 51: Cold Diuresis
Constriction of all skin blood vessels forces large amount of blood to body core
Causes rapid increase in blood pressure & to compensate kidneys quickly removes fluid from blood stream to stabilise BP
Resultant effect is need to urinate

## Slide 52: Respiration
Heat loss is via respiratory tract. Depends on:
  Temperature & humidity of atmosphere
  Respiratory ventilation rate
Cold may induce broncospasm and in some people may lead to exercise-induced asthma

## Slide 53: Heart Rate
Hypothermia can lead to an increased level of cardiovascular strain
Vasoconstriction leads to increased BP which can lead to increased levels of angina attacks, coronary & cerebral thrombosis
Persons with abnormal heart function at greater risk of heart attack in cold conditions

## Slide 54: Dehydration
Loss of heat occurs via moisture loss in the respiratory tract
Cold diuresis also results in loss of excessive fluids

## Slide 55: Other Physiological Effects
Local cold injury (freezing or non-freezing)
  Frostbite
  Trenchfoot
Cold allergy
  Occurs on removal from cold with widespread vasodilatation over the body, headache & hypertension
Paralysis of facial nerve
  Results from cold airstream on side of face (rare)

## Slide 56: Psychological Responses
Personal behavior can be influenced by thermal stress
Underlying mechanisms between thermal environments and psychological responses are not understood

## Slide 57: Basic Thermodynamics
1st law of thermodynamics
Simply stated:
  Energy cannot be created or destroyed. It can only be transformed from one state to another

## Slide 58: Basic Thermodynamics (cont)
2nd law of thermodynamics
Simply stated:
  Energy spontaneously tends to flow from being concentrated in one place to becoming diffused or dispersed
  Example: Hot object cooling by loss of energy (heat) to its surroundings

## Slide 59: External Heat Sources
Sun
  Fundamental source of heat for all life
  Temperature 5500oc
  Heat to top of earths atmosphere at rate of 1370 Wm-2
  Heat to earths surface at rate of 800-1000Wm-2
  Energy transposed from one form to another in accordance with laws of thermodynamics
  Air temperature & radiant temperature are the two major sources of heat which can impose thermal loads on humans

## Slide 60: Internal Heat Sources
Humans are homoeothermic (warm-blooded) and generate heat derived from food & oxygen
Humans are inefficient mechanisms and approximately 80% of energy is lost as heat and must be removed
Heat energy released is distributed around the body mainly by the blood

## Slide 61: Heat Balance Equation
Given that Tc must be maintained around 37oC this suggest that a heat balance exists between the body and its environment
Heat processes in this heat balance
  Heat generation in the body
  Heat transfer
  Heat storage

## Slide 62: Heat Balance Equation
M - W = E  R  C  K  S
    M = rate of metabolic heat production
    W = external work performed by the body
    K = conductive heat loss or gain
    C = convective heat loss or gain
    R = radiant heat loss or gain
    E = evaporative heat loss
    S = heat gained or lost by the body
Notes: <number>

## Slide 63: Heat Balance Equation (cont)
M is always positive
W + or – work leaving or entering the system
S + heat storage or – heat loss
K,C,R + ve = heat gain and – ve = heat loss
E is always negative
For body to be in heat balance (Tc constant) the rate of heat storage is zero

## Slide 64: Other Equations
Using the heat balance equation it is possible to derive other equations for
  Heat loss at the skin
  Evaporative heat loss from the skin
  Heat loss from respiration

## Slide 65: Metabolic Heat Production
Metabolism
  involves the combustion of foodstuffs (carbohydrates, fats & proteins) to carbon dioxide & water using oxygen
  is very inefficient (0-25%)
Metabolic rate (M)
  is the total energy produced (heat + work) measured indirectly from the rate of O2 consumption

## Slide 66: Metabolic Heat Production (cont)
HEAT ENERGY 75 - 100%
EXTERNAL WORK ENERGY 0 -25%
Food + O2 CO2 + H2O

## Slide 67: Typical Values of Metabolic Heat Prod.
Class | Metabolic Rate (M) Wm-2 | Examples
0 (Resting) | M<65 | Resting
1 (Low) | 65 <M <130 | Sitting, standing
2 (Moderate) | 130 <M <200 | Sustained hand & arm work
3 (High) | 200 <M <260 | Intense arm & trunk work
4 (Very high) | M >260 | Very intense activity

## Slide 68: Metabolic Rates by Occupation

## Slide 69: Non Evaporative Heat Transfer
Conduction
Convection
Radiation

## Slide 70: Conduction
  Heat is transferred by conduction between a body and surface with which it is in contact
  Amount of heat transferred is dependent on the temperature difference, the surface areas in contact and the conductance

## Slide 71: Conduction (cont)
  Transfer of heat by conduction not usually significant for humans working in hot environments
  Concept important when considering the insulation provided by protective clothing or insulation on hot surfaces

## Slide 72: Conduction (cont)
  Typical thermal conductivity values (k)
  in Wm-1oC-1
      Air 0.024 (at 0oC)
      Asbestos 0.13
      Wood 0.2
      Cork 0.42
      Water 0.57 (at 0oC)
      Steel 46
      Copper 380

## Slide 73: Convection
  Heat transfer will occur between a person and the boundary layer of air next to them
  If surface temperature is higher than surrounding air, the heated air close to the surface moves upwards and replaced by cold air
  Rate of heat loss or gain depends on temperature difference and surface area

## Slide 74: Convection (cont)
Natural convection
  relative air velocity < 0.1 m/s
Forced convection
  higher heat loss or gain at higher air velocities

## Slide 75: Radiation
Radiant heat is electromagnetic radiation
  Will travel through space until intercepted by an object
  Energy will be absorbed to appear as ‘heat’
  Infra-red radiation (wavelengths between 760 nm & 1 mm)

## Slide 76: Radiation (cont)
  Amount of radiant heat emitted is dependent on the absolute temperature and emissivity R = σ . e . T4
  Where
  σ is the Stefan-Boltzmann constant
  e is the emissivity of the surface and
  T is the temperature in 0 K

## Slide 77: Radiation (cont)
Emissivity
  Materials have different emissivities
    Expressed as a ratio to a theoretical perfect ‘black-body’ which has an emissivity of 1.0
Notes: <number>

## Slide 78: Radiation (cont)
    Lower emissivity materials produce lower intensity radiation
      Important in the choice of materials used as barriers / screens in the control of radiant heat
    Materials with high emissitivity are also good absorbers of radiant heat

## Slide 79: Heat Transfer
Typical emissivity values
  Aluminium – oxidised 0.1
  Stainless steel – polished 0.1
  Rusted iron 0.85
  Brick 0.93
  Black body 1.0
  (generally bright, shiny surfaces have lower emissivity's than dark or dull surfaces)
  Skin and normal clothing typically have fairly high emissivity
Notes: <number>

## Slide 80: Evaporative Heat Loss
  Heat loss only - amount of heat loss is dependent on rate of evaporation of water
    For humans the main mechanism is evaporation of water (sweat) from the skin but also evaporation of water from respiratory passages can occur

## Slide 81: Evaporative Heat Loss (cont)
    Sweating goes on continuously – even in
    comfortable conditions about 30 g sweat
    evaporate every hour – termed insensible
    perspiration – we are unaware of it
    Under more thermal stress the skin
    becomes wetted and we are aware of it –
    sensible perspiration

## Slide 82: Acclimatisation
Physiological or behavioral changes that reduce the strain caused by stressful changes in the natural environment
Acclimatised persons are able to adapt to heat and tolerate higher ambient temperatures

## Slide 83: Acclimatisation (cont)
Should take place gradually over 7-10 days
Fit person acclimatise more readily than unfit persons
Acclimatisation declines after exposure is reduced and is lost after about 30 days of non exposure

## Slide 84: Acclimatisation (cont)
Acclimatisation in cold climates not as well understood as in hot climates
Evidence of local acclimatisation to cold of the hands & fingers in some groups (fishermen, Eskimos)

## Slide 85
Effects of Temperature Extremes

## Slide 86: Effects of Excessive Heat Strain – Hot Environments
Narrow core temperature band 36.8 – 37.2 °C
Core temperature remains constant when there is equilibrium between internal heat production and heat loss from the surface of the body

## Slide 87: Human heat balance equation
M  W  K  C  R - E = S
    M = rate of metabolic heat production
    W = external work performed by the body
    K = conductive heat loss or gain
    C = convective heat loss or gain
    R = radiant heat loss or gain
    E = evaporative heat loss
    S = heat gained or lost by the body
    W and K are usually small so a simplified form is often used:
M  C  R - E = S

## Slide 88: Heat stress & heat strain
Heat Stress
The combined effect of external thermal environment and internal metabolic heat production constitutes the thermal stress on the body.
Heat Strain
The levels of activity required in response to the thermal stress by systems such as cardiovascular, thermoregulatory, respiratory, renal and endocrine constitute the thermal strain.

## Slide 89: Heat Stroke
State of thermoregulatory failure
Life threatening
Characterised by:
  Hot dry skin
  Rapidly rising body temperature
  Collapse
  Loss of consciousness
  Convulsions
If deep body temp exceeds 40°C danger of heat stroke is imminent

## Slide 90: Heat Stroke (cont)
Treatment
Medical emergency & can lead to death
While waiting for medical help
Remove & lay in cool shaded area, remove & loosen clothing

## Slide 91: Heat Stroke (cont)
Immediate cooling necessary to reduce core to< 39°C
eg Spray with cool water and fan to evapourate, ice packs on extremities
If conscious, give sips of cool water
Monitor airway & breathing

## Slide 92: Heat Exhaustion
While serious, less severe than heat stroke
Inadequate fluid replacement
Characterised by
  Clammy, moist skin
  Weakness or extreme fatigue
  Nausea
  Headache
  No excessive increase in body temperature
  Low blood pressure and weak pulse
  Without prompt treatment collapse may occur

## Slide 93: Heat Exhaustion (cont)
Treatment
Remove & lay in cool shaded area, remove & loosen clothing
Initiate active cooling
e.g. Spray with cool water and fan to evaporate
If conscious allow casualty to slowly drink cool water
Observe

## Slide 94: Heat Syncope (fainting)
Exposure of fluid deficient persons to hot environment can cause major shift of blood supply to skin vessels for heat dissipation
This can result in inadequate supply of blood to brain and consequent fainting.
Onset of heat collapse is rapid and unpredictable

## Slide 95: Heat Syncope or Fainting (cont)
Treatment
Remove and lay in cool shaded area
If conscious allow casualty to slowly drink cool water
Observe

## Slide 96: Heat Cramps
Caused by performing hard work in a hot
environment.
Characterised by:
Painful muscle spasm
Electrolyte imbalance caused by sweating
Can be caused by both too much and too little salt

## Slide 97: Heat Cramps (cont)
Thirst cannot be relied on as a guide to the need for water
Water must be taken every 15 – 20 minutes in hot environments

## Slide 98: Heat Cramps (cont)
Treatment
Under extreme conditions working loss of sodium can occur & need to be replaced
Individuals need to be encouraged to maintain a balanced electrolyte intake, with meals if possible.

## Slide 99: Prickly Heat (heat rash)
Occurs as a result of continued exposure to humid heat with skin remaining continuously wet from un-evapourated sweat
Characterised by:
Clogged sweat glands
Itchy skin
Reduced sweating

## Slide 100: Prickly Heat or Heat Rash (cont)
Treatment
Keeping the skin cool & dry
Mild drying lotions
Keep skin clean to avoid infections

## Slide 101: Possible Other Effects
Reproductive
Increased risk of malformation of the unborn foetus during the first trimester of pregnancy may occur if a female’s core temperature exceeds 39°C for extended periods (evidence not conclusive).
Chronic
Chronic long-term effects (eg higher incidence of kidney stones) are not conclusive.

## Slide 102: Effects of Excessive Heat Strain – Cold Environments
Factors which contribute to cold stress include:
Cold temperatures
High or cold winds
Dampness
Cold water
Inadequate protection

## Slide 103: Cold Occupational Environments
Air Temp°C | Example of such an Environment
- 90 | Lowest temperature at south pole base - Vostock
- 55 | Cold store for fish meat and production of frozen, dried products
- 40 | “Normal” temperature at polar base
- 28 | Cold store for frozen products
20 to – 10 | Average January temp of S. Canada, N. Scandinavia and Central Russia
-10 to 0 | Average January temp of N.USA, S. Scandinavia, Central Europe, parts of Middle and Far East, Central & N. Japan

## Slide 104: Frostbite
Medical condition damage caused to skin & other tissues
Likely to occur in body parts farthest from heart & in those with a lot of surface area exposed to the cold
Discoloration of skin, burning sensations, even intense pain
Skin can look burnt
Can lead to gangrene &
amputation
Source: BP International

## Slide 105: Trenchfoot
Trench foot or immersion foot – prolonged exposure of feet to damp and cold
Does not require freezing temperatures – up to 16°C
Feet swell, may involve blisters & infections
Can lead to gangrene & amputation

## Slide 106: Hypothermia
Hypothermia refers to any condition in which the temperature of the body drops below the level required for normal metabolism and/or bodily functions to take place

## Slide 107: Signs & Symptoms
Mild hypothermia
36.5 - 32°C
Shivering
Lack of coordination, stumbling, fumbling hands
Slurred speech
Memory loss
Pale, cold skin

## Slide 108: Signs & Symptoms (cont)
Moderate hypothermia
32 - 30°C
Shivering stops
Unable to walk or stand
Confused or irrational

## Slide 109: Signs & Symptoms (cont)
Severe hypothermia
30 – 25.5°C
Severe muscle stiffness
Very sleepy or unconscious
Ice cold skin
Death

## Slide 110: Progressive Clinical Signs of Hypothermia
Tc °C | Clinical signs
37.6 | Normal rectal temp
36 | Metabolic rate increases to compensate for heat loss
33 | Severe hypothermia
30 - 29 | Progressive loss of consciousness, blood pressure hard to detect, shivering ceases
26 | Victim seldom conscious
22 - 21 | Maximum risk of ventricular fibrillation
18 | Lowest accidental hypothermia victim to recover

## Slide 111: Predisposing Factors – Heat Stress
Age
Age as such not necessarily the important feature
Condition rather than physical debilitations associated with age
Personal factors of health & level of fitness rather than age itself

## Slide 112: Predisposing Factors (cont)
Gender
Matched (cardio vascular fitness levels) groups – no difference in tolerance levels males & females
General health
Some medical conditions can contribute
  eg Past histories of heat related illnesses
  Cardiovascular conditions & diabetes affects blood flow
  Skin disorders (sunburn, psoriases) inhibit sweating

## Slide 113: Predisposing Factors (cont)
Excess body fat
  Insulator
  Greater expenditure of energy to move around
  Often indicates an inactive lifestyle
Lack of sleep / fatigue

## Slide 114: Predisposing Factors (cont)
State of hydration
Typically workers do
not drink enough water
Cool water
250 ml every 15 minutes
Urine colour charts helpful
Source: BHP Billiton-reproduced with permission

## Slide 115: Predisposing Factors (cont)
Alcohol, Caffeine & Diet
Alcohol & caffeine consumption (even night before) should be discouraged before hot work
Alcohol & caffeine are diuretics & contribute to dehydration
Carbonated drinks may cause bloating
High protein meals – water lost in excreting nitrogenous waste

## Slide 116: Predisposing Factors (cont)
Nicotine use
Using nicotine tightens blood vessels & hence those in the skin cannot widen to let heated blood reach the surface to release heat
Medications
Should be confirmed by a medical practitioner that they do NOT affect body’s ability to regulate temperature

## Slide 117: Predisposing Factors (cont)
Medications known to affect the bodies ability to regulate temperature
Diuretics
Tranqilisers
Antidepressants
Antihistamines
Others

## Slide 118: Predisposing Factors (cont)
Acclimatisation
Recommended for new workers
Physiological adaptation which occurs with repeated exposure to hot environments

## Slide 119: Predisposing Factors (cont)
Heart rate decreases, sweating increase, sweat becomes more dilute & body temp will be lower
Varies among workers
Approx 7 days required for full acclimatisation
After a weeks absence need to reacclimatise usually 3 or 4 days

## Slide 120: Predisposing Factors (cont)
Protective clothing & other protective equipment
Often impedes sweat evaporation & heat loss
Liquid/vapour/air permeable versus impermeable

## Slide 121: Predisposing Factors (cont)
Slightly loose fitting allows good ventilation & air circulation
The higher the insulation factor the more difficult to dissipate heat
Air cooled helmets & suits

## Slide 122: Thermal Surveys
Source ;University of Wollongong, BP International & Quest Inc-with permission)

## Slide 123: Thermal Surveys
Measurement equipment
  Air temperature
  Radiant temperature
  Humidity
  Air movement
  Composite integrating meters
  Personal monitoring

## Slide 124: Thermal Surveys (cont)
Survey
  Data collection
  Monitoring strategies
Assessment of degree of risk
  Recording of results
  Assessment of risk
  Outcomes of surveys

## Slide 125: Air Temperature
Definition
  Temperature of air surrounding the body which is representative of that aspect of the the surroundings which determines heat flow between the human body and the air

## Slide 126: Air Temperature
Temperature scales
  Celsius (centigrade) scale o C
  Fahrenheit scale o F
  Kelvin scale K

## Slide 127: Temperature Scales (cont)
0 o C = 32 o F
100 o C = 212 o F
Kelvin scale starts at absolute zero
0oc = 273 K
20oc = 293 K
100OC = 373 K

## Slide 128: Measurement of Air Temperature
Mercury-in-glass thermometer
Thermocouple
Platinum resistance thermometer
Thermistor
All techniques must be appropriately calibrated

## Slide 129: Mean Radiant Temperature
Definition
  Temperature of a uniform enclosure within which a small black sphere at the test point would have the same radiation exchange as it does with the real environment

## Slide 130: Mean Radiant Temperature (cont)
In practice radiant energy is measured using a globe thermometer
  This absorbs heat from all sources and gives an integrated measure
Mean radiant temperature of environment can be determined by
  calculation (very complex)
  by using a nomogram (different nomograms for different diameter globes)
Notes: <number>

## Slide 131: The Globe Thermometer
Normal bulb thermometer
  at centre of matt black copper painted hollow sphere
  thermometer sealed into the sphere
150 mm diameter spheres are the most accurate but takes about 20 minutes to equilibrate
40 mm diameter sphere is less accurate but only takes about 10 minutes to equilibrate
Notes: <number>

## Slide 132: Black Globe Thermometer
Source: BP International

## Slide 133: Humidity
Air contains a certain amount of water vapour
Higher air temperature
  more water vapour can be contained in the air
Lower air temperature
  less water vapour can be contained in the air
Notes: <number>

## Slide 134: Humidity (cont)
If the air contains as much water vapour as it can at a certain temperature it is termed saturated
If air containing water vapour is cooled a temperature is reached at which the air is saturated and water will condense out. This is the dew point.

## Slide 135: Humidity (cont)
The amount of water vapour in air at a certain temperature expressed as a percentage of the amount of water vapour the air at that temperature could contain when saturated is termed the relative humidity
Notes: <number>

## Slide 136: Dry & Wet Bulb Thermometers
Water evaporating from a surface reduces the temperature of the surface
If the bulb of a thermometer is covered by a damp fabric sleeve water evaporating causes a lower reading - this is termed the wet bulb temperature
Notes: <number>

## Slide 137: Dry & Wet Bulb Thermometers (cont)
The difference between dry bulb temperature and wet bulb temperature can be used to determine relative humidity
At 100% relative humidity no evaporation takes place so the dry bulb temperature and wet bulb temperature will be the same

## Slide 138: Measuring Relative Humidity
Whirling hygrometer
  one dry bulb thermometer
  one wet bulb thermometer - bulb covered with wick dipped into distilled water reservoir
  air flow (> 4 metres / sec) achieved by ‘whirling’
  read wet bulb temperature first, then dry bulb
Notes: <number>

## Slide 139: Whirling (Sling) Hygrometer
Source; University of Wollongong

## Slide 140: Calculation of Relative Humidity
Direct calculation from formulae
Slide rule for particular instruments
Psychrometric charts
  Charts that inter-relate
  vapour pressure (water content)
  relative humidity
  dry bulb temperature
  wet bulb temperature
Notes: <number>

## Slide 141: Psychrometric Charts
Source Ellis 1972

## Slide 142: Air Movement
Air movements varies in time & direction.
Mean air velocity over the body integrated over all directions & over exposure time of interest

## Slide 143: Measurement of Air Velocity
Vane anemometer
  Directional & not accurate at low velocities
Hot-wire anemometer
  Directional & inaccurate at low velocities
Kata thermometer
  Omni-directional but not suited to conditions where large or rapid variations in air movement occur

## Slide 144: Vane Anemometer
Source; University of Wollongong

## Slide 145: Hot-wire Anemometer
Source; University of Wollongong

## Slide 146: Kata Thermometer
Source: BP International

## Slide 147: Kata Thermometer (cont)
Principle of operation
  thermometer with large bulb
  two marks on stem (3K apart)
  heated so that fluid is above higher mark
  fixed in monitoring position
  allowed to cool
  time for fluid to cool to lower mark noted
Notes: <number>

## Slide 148: Kata Thermometer (cont)
Rate of cooling dependent on
  air speed
  air temperature
  radiant heat sources
Variables in Kata thermometer
  3 temperature range models available
  silvered or unsilvered bulb
Notes: <number>

## Slide 149: Kata Thermometer (cont)
Precautions in use
  choose silvered / unsilvered - why?
  heat carefully (often using hot water)
  ensure bulb thoroughly dried - why?
  fix stationary in sampling position - why?
  repeat measurements 3 times
Notes: <number>

## Slide 150: Kata Thermometer (cont)
Advantages
  omnidirectional - takes account of air movement from all directions
  averages over a reasonable time period
  determines very low average air speeds
Disadvantages
  fragile
  time consuming
Notes: <number>

## Slide 151: Kata Thermometer (cont)
Determining air speed
  use appropriate nomogram
  nomograms inter-relate
    Kata factor
    dry bulb temperature
    cooling time
  to give air speed in metres per second
Notes: <number>

## Slide 152: Nomogram for Kata Thermometer
Source: Ellis 1972

## Slide 153: Portable Instrumentation
Basic models have ability to measure dry bulb , wet bulb & globe bulb
More modern instruments can measure humidity & air velocity
Some instruments can measure & store a vast amount of data which can be downloaded to a software programme
Sensors require calibration

## Slide 154: Thermal Environment Monitor
Source: Quest Technologies-Reproduced with permission

## Slide 155: Personal Monitoring
Measure physiological indicators of heat strain rather than environmental conditions
Usually monitor factors such as heart rate, body temperature, skin temperature
Limitations of instrumentation need to be understood & care needs to be exercised with interpretation of data

## Slide 156: Typical Personal Hest Stress Monitor
Source: Quest Technologies-reproduced with permission

## Slide 157: Surveys
Basic data required for most assessments:
  Air temperature
  Mean radiant temperature
  Humidity
  Air movement
  Metabolic work rate
  Clothing

## Slide 158: Data for Complex Surveys
Air temperature gradients
Surface temperature measurements
Plane radiant temperature
Local air movement
Changing humidity conditions
Variations in clothing & activity
Physiological measurements

## Slide 159: Other Data that is Required
Exposure period
Confined space work requirements
Task complexity
Distance to rest area
Distance to drinking water
Respiratory protection
Medication being taken by workers

## Slide 160: Other Data that is Required (cont)
Chronic medical conditions
Acute infections
Acclimatisation level
Obesity
Age
Fitness level
Consumption of alcohol in last 24 hours
Vaccinations in some countries (Rabies)

## Slide 161: Monitoring Strategies
No preferred monitoring strategy as it is dictated by conditions
Approaches include
  OSHA technical manual
  Malchaire et al
  AIOH
  South African Department of Minerals & Energy

## Slide 162: OSHA Technical Manual (1995)
Employer & employee interviews
Walkaround inspection
Workload assessment
Sampling of environmental conditions

## Slide 163: Malchaire et al (1999)
Four stage model:
1) Detection of risk factors
2) Review of climatic & working conditions over entire year
3) Analysis phase using information from stages 1 & 2
4) For extremely complex situations involve further expertise

## Slide 164: AIOH (2003)
Modification of Malchaire:
Basic heat stress risk assessment using a simple index (WBGT)
2) If 1 indicates issue initiate a more complex evaluation of situation & general environment
3) If calculated allowable exposure time is <30 mins or high level PPE is involved employ physiological monitoring

## Slide 165: South African DME (2002)
Requirement for operator to categorise the thermal environment
Steps include
  Subdivide into measurement areas
  Subdivide measurement areas in activity areas
  Evaluate the risk in each
  Analyse data to categorise each activity area
  Adopt strategies comensate with risk level in each activity area

## Slide 166: Assessment of Risk – AIHA (Hot)
Preliminary review
Select a heat index
Select instruments
Measure the thermal environment
Calculate the selected index

## Slide 167: Assessment of Risk – AIHA (Hot)
Estimate the metabolic heat load
Evaluate recommended exposure limits
Determine thermal components
Modification of hot work exposures
Re-evaluate workplace exposures after modifications

## Slide 168: Assessment of Risk – AIHA (Cold)
Preliminary review
Decide the type of analysis
Measure the thermal environment
Determine the WCI

## Slide 169: Assessment of Risk – AIHA (Cold)
Estimate metabolic heat load
Determine insulation required
Modification of cold work exposure

## Slide 170: Outcome of Surveys
Environmental control measures (hot conditions)
  Insulation of hot surfaces & pipe work
  Shielding of radiant heat sources
  Plant maintenance
  Increased ventilation, air movement & local cooling

## Slide 171: Outcome of Surveys (cont)
  Personnel selection & monitoring (hot conditions)
    Level of fitness & obesity
    Chronic illness
    Minor illnesses
    Prior history of heat stress

## Slide 172: Outcome of Surveys (cont)
Work-Rest regimes
  Work at very high temperatures may be permitted for short periods followed by a period of rest
  The body can accumulate a certain amount of heat before Tc reaches an unacceptable level

## Slide 173: Outcome of Surveys (cont)
Clothing
  At extremes of hot or cold temperatures, clothing (PPE) appropriate to the prevailing conditions must be worn
  Selection of clothing must be undertaken with caution to ensure adverse effects are not inadvertently introduced

## Slide 174: Review of Today’s Learning Outcomes
Thermal Spectrum
  To understand the range of thermal environments that humans work within
Principles
  Understand the basic physiological responses of the body to hot & cold environments
  Understand the processes for heat production & exchange

## Slide 175: Today’s Learning Outcomes (cont)
Effects of Temperature Extremes
  Understand the effects of hot & cold environments
Thermal Surveys
  Understand the principles of measuring major environmental factors
  Review different monitoring strategies
  Understand some approaches to establishing the degree of risk resulting from a thermal survey