## Slide 1
M502
Thermal Environment
Day 2
Notes: <number>

## Slide 2: Today’s Learning Outcomes
Review of Overnight Questions
Thermal Comfort
  Understand the concepts of thermal comfort & the relationship between environmental & personal factors
Evaluation of Hot Environments
  Review the common approaches for evaluating hot environments
  Understand the limitations of the various indices

## Slide 3: Today’s Learning Outcomes (cont)
Control of Hot Environments
  Review the various factors that can be used to control hot environments
Practical Session
  Understand how to use basic thermal environment monitoring equipment

## Slide 4
Thermal Comfort

## Slide 5: Thermal Comfort
Definition : Parsons (2003)
“That condition of mind which expresses satisfaction
with the thermal environment.”
Also used also by:
ASHRAE
ISO 7730 – Thermal Comfort

## Slide 6: Thermal Comfort (cont)
What is the interaction of the basic parameters of
environmental factors of:
Air temperature
Radiant temperature
Air velocity
Humidity
Plus personal factors of:
Metabolic heat generated by human activity
Clothing worn i.e. insulation

## Slide 7: Why it Can be Important?
It is subjective
Varies from person to person
Seems to be related to job satisfaction or dissatisfaction
Employer – employee relations
Affects morale
Other psychological factors

## Slide 8: Subjective Scales

## Slide 9: Subjective Scales (Cont)
ASHRAE Psycho-Physical Scale | 
Cold | -3
Cool | -2
Slightly cool | -1
Neutral | 0
Slightly warm | +1
Warm | +2
Hot | +3
Source; Fanger 1972

## Slide 10: Indoor Environments
Thermal comfort studies
In Hot Climates
Emphasis on how to cool the indoor environment for thermal comfort by
  Increased air movement
  Air conditioning - air temp & humidity
In Cold climates
  Warmth and freshness
  Not much consideration on humidity

## Slide 11: Thermal Comfort (cont)
Fanger
Three conditions for a person to be in thermal comfort:
Body in heat balance
Sweat rate is within comfort limits
Mean skin temp within comfort limits
Fanger Comfort Equation

## Slide 12: Fanger Comfort Equation
M – W = (C + R + Esk) + (Cres + Eres)
“skin” “breathing”
M = metabolic rate
W = Work
C = Heat transfer by convection from clothing surface
R = Heat transfer by radiation from clothing surface
Esk = Evaporative convective heat exchange
Cres= Respiratory convective heat exchange
Eres= Respiratory evaporative heat exchange

## Slide 13: Predicted Mean Vote (PMV)
An index that predicts the value of the mean votes of a large group of persons on the thermal sensation scale (ASHRAE Psycho-Physical)

## Slide 14
ASHRAE Psycho-Physical Scale | 
Cold | -3
Cool | -2
Slightly cool | -1
Neutral | 0
Slightly warm | +1
Warm | +2
Hot | +3
Source; Fanger 1972

## Slide 15: PMV (cont)
Determination of the PMV:
From the equation – using a computer
Directly from Annex in ISO 7730:2005 where tables of PMV values are given for different combinations of activity, clothing, operative temperature and relative humidity
By direct measurement using an integrating sensor

## Slide 16: Predicted Percentage Dissatisfied (PPD)
An index that predicts the percentage of thermally
dissatisfied people.
The percentage of a large group of
people voting hot, warm, cool or cold on the ISO
seven point thermal sensation scale

## Slide 17: Graph PPD as a Function PMV
Source;: Fanger 1972

## Slide 18: ISO 7730:2005
“Ergonomics of the thermal environment – Analytical
determination and interpretation of thermal comfort
using calculation of the PMV and PPD indices and local
thermal comfort criteria”

## Slide 19: Local Thermal Discomfort
Most common causes:
Draught
Thermal radiation asymmetry
Vertical air temperature differences
Floor temperatures

## Slide 20: Local Thermal Discomfort (cont)
Draught: Unwanted local cooling of the body
Dependent on the velocity, the fluctuations in velocity & the air temperature
Calculations provided in ISO 7730
(mean air velocity < 0.5 m/sec)

## Slide 21: Local Thermal Discomfort (cont)
Thermal radiation asymmetry
Warm ceilings & cold windows are the most uncomfortable
Warm walls & cold ceilings seemed to be less uncomfortable
Calculations provided in ISO 7730
(windows < 10°C warm ceiling < 5°C)

## Slide 22: Local Thermal Discomfort (cont)
Vertical air temperature difference
Generally unpleasant to be warm around the head while being cold at the feet
Calculations provided in ISO 7730
(< 3°C between head & ankles )

## Slide 23: Local Thermal Discomfort (cont)
Floor temperature
Depends on the thermal conductivity & specific heat of the floor material
Depends on footwear
Calculations provided in ISO 7730
(between 19 - 26°C)

## Slide 24: Controls for Thermal Comfort
Factors likely to influence thermal conditions within a
space or building include:
Building fabric
  Poor or inadequate thermal insulation
  Single window glazing versus double glazing
  Use of heat emitters to reduce cold down draughts

## Slide 25: Controls for Thermal Comfort (cont)
  Building fabric(cont)
  Solar gain through windows
    Solar control glass
    Internal blinds
    External shutters
  Poor sealing
  Internal partitioning

## Slide 26: Use of Shutters to Reduce Solar Load
Source: University of Wollongong

## Slide 27: Controls For Thermal Comfort (cont)
Heating systems designed & functioning correctly
  Output from central boiler plant
  Position of heat emitters can assist in counteracting discomfort
  Poor siting can lead to radiation asymmetry & draughts
  Noise (e.g. from fans) can be an annoyance
  Heat output from emitters needs to be controlled:
  can be simple or complex

## Slide 28: Controls For Thermal Comfort(cont)
Ventilation Systems (heating) when assessing:
  Identify air input grills, check volume flow, velocity, circulation & distribution of supply air
  Supply air temperature
  Air temperature gradients
  Air volumes
  Ensure local adjustments do not “flow on”
  Low levels of humidity may result in winter heating

## Slide 29: Controls For Thermal Comfort(cont)
Air conditioning, heating, cooling & humidity control
Building systems complex & sophisticated
  What is principle of operation?
  Check for over or under capacity
  Temp and velocity of air leaving grills
  Is humidity controlled?

## Slide 30: Controls For Thermal Comfort (cont)
Control systems (heating, cooling, humidity & airflow)
  What is mode of control?
  Are sensors suitably positioned? Are they responding to air or surface temperatures?
  Are sensors set at appropriate control values?

## Slide 31: Controls For Thermal Comfort (cont)
Control systems (heating, cooling, humidity & airflow)
  Control may be fully automatic, local or operated by individuals
  The type of control may influence “perceived” comfort
  Check functioning & calibration of sensors
  Plant may be controlled by an Energy / Building Management System – check functional logic

## Slide 32: Controls For Thermal Comfort (cont)
Plant maintenance
  Plant should be fully documented
  Maintenance & condition monitoring records should be kept
  Expert advice may be required

## Slide 33: Case Study 2
Industrial Relations and Thermal Comfort

## Slide 34: The Issues
Complaints from pilots operating Dash 8 aircraft in tropical regions of excessive cockpit temperatures
Significant industrial issue with pilots lodging list of demands

## Slide 35: The Workplace
Dash 8 aircraft built in Canada
Operating at remote airports in tropical climate
No auxiliary power units (APU)
Notes: Auxiliary power units are a small turbine located in the aircraft tail which supplies power when the aircraft is on the ground for air-conditioning and other functions.
<number>

## Slide 36: Dash 8 Aircraft
Source: University of Wollongong
Notes: Dash 8 Aircraft are built by a subsidiary of Boeing in Canada and typically operate on regional routes where short take-off and landing performance is often required. The aircraft in the slide is identical to those sampled and carries about 36 passengers 2 pilots and 1 cabin attendent
<number>

## Slide 37: Dash 8 Cockpit Window
Source: University of Wollongong
Notes: Note the wrap around windows of the cockpit. This given an avenue for increased solar load if the aircraft is parked into the sun.
<number>

## Slide 38: Discussions with Airline
Some aircraft have APU’s and others don’t
Upgrade of all aircraft would cost $6-10m
Negotiated agreement that Chief pilot would fly plane with co-pilot being union representative while evaluation undertaken by hygienist

## Slide 39: Data Collection
Collected data on flight deck over three days on 4 different aircraft
Quest Temp 15 Heat Stress Monitor
TSI VelociCalc Plus Air Velocity Meter
TSI Air Quality Monitor (Humidity)

## Slide 40: Measured or Calculated
Dry Bulb Temperature
Wet Bulb Temperature
Globe Temperature
WBGT
Effective Temperature
Relative Humidity
Air Flow

## Slide 41: Airflows on Flight Deck
Aircraft 1 0 - 0.5 m/s
Aircraft 2 0 - 1.05 m/s
Aircraft 3 0 - 0.25 m/s
Aircraft 4 0 - 0.2 m/s
All airflows measured in pilots normal seated position
Notes: No reason could be found for the higher than other aircraft airflow on aircraft 2. One suggestion was that it was a newer plane but manufactured to the same design as the others.
<number>

## Slide 42: Results (T = Tropical)
Aircraft | Location | Out.T oC | RH % | ET oC | WBGT oC | Weather
1 | Port A | - | 55 | 28 | 27.8 | Sunny
 | Cruise | - | 37 | 21 | 20.1 | -
 | Port B (T) | 25 | 73 | 27 | 27.1 | O/cast
 | Port C (T) | 27 | 72 | 25 | 25.2 | O/cast
 | Port D (T) | 27 | 77 | 25.5 | 25.6 | T storm

## Slide 43: Results (T = Tropical)
Aircraft | Location | Out.T oC | RH % | ET oC | WBGT oC | Weather
2 | Port E (T) | 32 | 67 | 30.5 | 30.7 | Sunny & humid
 | Port D (T) | 30 | 67 | 29 | 29.1 | Sunny
 | Port C (T) | 25 | 65 | 25 | 25.2 | O/cast
 | Port B (T) | 26 | 62 | 23 | 24 | Sunny
 | Cruise | - | 40 | 15 | 15.1 | -
Notes: Note the drop in humidity during cruise which was the major portion of the flight
<number>

## Slide 44: Results (T = Tropical)
Aircraft | Location | Out.T oC | RH % | ET oC | WBGT oC | Weather
3 | Port A | 25 | 59 | 24 | 24 | O/cast
 | Cruise | - | 30 | 18 | 18 | -
 | Port F (T) | 25 | 54 | 22 | 21 | O/cast
 | Port B (T) | 28 | 55 | 27.5 | 27.2 | Sunny

## Slide 45: Results (T = Tropical)
Aircraft | Location | Out.T oC | RH % | ET oC | WBGT oC | Weather
4 | Port A | 28 | 47 | 25 | 24.2 | Sunny
 | Cruise | - | 32 | 22 | 22.4 | -
 | Port G (T) | 26 | 58 | 23 | 22.1 | O/cast
 | Port H(T) | 27 | 59 | 24 | 23.9 | Rain

## Slide 46: Limits for Aircraft
ASHRAE (American Society of Heating, Refrigeration and Airconditioning Engineers)
  Air Transportation Subcommittee (passengers only)
Notes: No limits could be found for pilots of aircraft. ASHRAE do have some for passengers
<number>

## Slide 47: Limits for Aircraft (cont)
Boeing
  Max ET of 97oF (36.1oC)
  1 hr ET limit of 93oF (33.9oC)
WHO
  Performance and productivity decrease as ET exceeds 30oC
Notes: Boeing values were for the construction of aircraft and not Dash 8 craft. WHO report from the 1980’s suggested a drop in performance (especially difficult tasks) as ET > 30oC Flying a commercial aircraft requires considerable concentration especially in tropical areas where storms are a common occurence
<number>

## Slide 48: Summary
Possible for WHO guideline to be exceeded
Exceedances of very short duration
Validity of performance loss above 30oC ET difficult to confirm
Airflows on flight deck variable but low

## Slide 49: Summary (cont)
Air for pilots also used to cool avionics therefore usually warm
Instrument panel adds up to 2oC radiant heat
Parking bays (in relation to sun) influences temperature on flight deck
Ground power units developed to run air -conditioning
Notes: The design of the ventilation was based on cooling the avionics equipment behind the pilots control panel rather than ventilating the cockpit. Significant radiant heat was generated from the instrument panel.
Parking aircraft into the sun at tropical terminals added considerable solar load. Reluctance to change parking pattern due to safety and passenger comfort reasons.
<number>

## Slide 50: Ground Power Unit
Source: University of Wollongong
Notes: Final solution was to develop portable power units so aircraft air conditioning could be run while the aircraft was stationary loading or unloading passengers.
<number>

## Slide 51: Key Learnings
Issue is more one of comfort rather than health risk
Heat stress is commonly used in industrial situations
Flying the routes highlighted the issue of parking of aircraft into the sun
Irritation can be an issue which has flow on effects
Notes: Issue of parking of aircraft at tropical airports would not have been highlighted unless investigating officer had flown routes.
<number>

## Slide 52
Evaluation of Hot Environments

## Slide 53: Heat Stress Indices
Definition:
A heat stress index is a single number that attempts to incorporate the effects of basic parameters in any thermal environment
It aims to correlate the number with thermal strain experienced by the exposed worker

## Slide 54: Heat Stress v Heat Strain
Heat stress is the total heat load on the body from all
sources
Heat strain relates to the physiological responses of
the imposed stress

## Slide 55: List of Common Indices
Empirical (derived from people’s observations or physiological effects)
Effective Temperature (ET)
Corrected Effective Temperature (CET)
Predicted 4-hour Sweat Rate (P4SR)
Wet Bulb Globe Temperature (WBGT)

## Slide 56: List of Common Indices (cont)
Theoretical or rational indices (based on the heat balance equation)
Heat Stress Index (HSI)
Required Sweat Rate (SWreq)
Predicted Heat Strain (PHS)
Thermal Work Limit (TWL)

## Slide 57: Effective Temperature (ET)
Developed as a comfort scale
Combines effects of:
  Air temperature
  Humidity
  Air movement
Two charts produced:
  One for persons naked to waist - Basic ET
  One for normally clothed – Normal ET

## Slide 58: Effective Temperature (ET)
Example:
Dry bulb 30°C, wet bulb 20°C,
Air vel 2.0 m/sec.
BET = 21°C
This means man naked to waist will sense env. of DB 30°C, WB 20°C & vel. 2.0 m/s as equivalent to 21°C dry bulb temp of still & saturated air (i.e. BET).
Source: BJIM Vol29 1972-with permission

## Slide 59: Effective Temperature
Nomogram for normal
effective temperature
Source: BJIM Vol 29 – with permission

## Slide 60: Corrected Effective Temperature (CET)
ET was limited - did not take into account radiant heat
Modified to form Corrected ET
150 mm diameter globe used to
measure radiant heat in lieu of dry bulb
Source: BP International Ltd

## Slide 61: ET & CET
Still used as a comfort index where humidity high &
radiant temperature low
eg underground mines
ET & CET make limited allowance for effects of clothing & no allowance for level of activity
Notes: <number>

## Slide 62: Predicted 4 Hour Sweat Rate (P4SR)
Uses a nomogram to predict the quantity of sweat
given off by fit, young, acclimatised men exposed to
the environment for 4 hours
P4SR takes into account all the environmental factors plus the personal factors of metabolic rate and clothing
A disadvantage – covers only a moderate range of physical activity

## Slide 63: P4SR (cont)
To obtain index
  If tg ≠ ta, increase wet bulb by 0.4 (tg – ta) °C
  If metabolic rate M > 63Wm-2, increase wet bulb by amount from nomogram or from Table 7.1 in Student Manual
  If person clothed, increase wet bulb by 1.5Iclo (°C)
  Use the chart to obtain Basic 4-hour sweat rate
  Calc P4SR = B4SR + 0.37Iclo + (0.012 + 0.001 Iclo) (M – 63)

## Slide 64: Nomogram for P4SR
Source: BJIM Vol 29 – with permission

## Slide 65: P4SR (cont)
Outside prescriptive zone (e.g. P4SR > 5 litres) sweat
rate was not a good indicator of strain
A number of limits proposed
  Absolute maximum of 4.5 litres &
  Maximum of 3 litres for regular exposure

## Slide 66: Wet Bulb Globe Temperature (WBGT)
Probably most widely used index
WBGT combines effects of 4 thermal components
affecting heat stress:
  Air temperature
  Humidity
  Air velocity
  Radiation
  As measured by the dry bulb, natural wet bulb and globe
  temperatures
Source: Quest technologies-reproduced with permission

## Slide 67: WBGT (cont)
With direct exposure to sunlight
WBGTout = 0.7NWB + 0.2GT + 0.1DB
Without direct exposure to sunlight ie inside
WBGTin = 0.7NWB + 0.3GT
where NWB = Natural wet bulb
GT = Globe temperature
DB = Dry bulb (air) temperature

## Slide 68: WBGT (cont)
NIOSH & ISO 7243
WBGT index adopted by both NIOSH and into
ISO 7243 “Hot environments – Estimation of the heat stress on the working man, based on the WBGT index.”
ACGIH 2007
WBGT used as their first order index of the environmental contribution to heat stress

## Slide 69: WBGT (cont)
ACGIH Screening Criteria for TLV® and Action Limit
WBGT is only a index of the environment
Screening criteria adjusted for by reference to Tables for contributions of:
  Work demands
  Clothing
  State of acclimatisation

## Slide 70: WBGT (cont)
ACGIH Screening Criteria for TLV® and Action Limit
Source: ACGIH –Reproduced with permission

## Slide 71: Heat Stress Index (HSI)
Based on heat exchange
Is a comparison of evaporation required to maintain heat balance (Ereq) with maximum evaporation that could be achieved (Emax)
HSI = Ereq / Emax x 100
Allowable exposure time = 2440 / (Ereq – Emax) minutes

## Slide 72: HSI (cont)
Ereq = M – R – C
Emax = 7.0v0.6(56 – pa) clothed
= 11.7v0.6(56 – pa) unclothed
M = Metabolic rate
R = Radiant heat loss
= 4.4(35 – tr) clothed
= 7.3(35 – tr) unclothed
C = Convective heat loss
= 4.6v0.6(35 – ta) clothed
= 7.6v0.6(35 – ta) unclothed
pa = water vapour pressure
tr = mean radiant temp
ta = dry bulb (air) temp

## Slide 73: Interpretation of HSI Values
HSI | Effect of 8 hour exposure
0 | No thermal strain
10-30 | Mild to moderate strain, little effect physical work, possible effect on skilled work
40-60 | Severe heat strain, threat to health unless physically fit, acclimatisation required
70-90 | Very severe heat strain, need to be medically selected, adequate water & salt intake assured
100 | Maximum strain tolerated daily by fit acclimatised young men
>100 | Exposure time limited by rise in deep body temp

## Slide 74: HSI (cont)
HSI application by following example
A hot metal worker is exposed to the following
conditions:
ta = 30°C, twb = 20°C, tr = 45°C, v = 0.5m/sec, M = 165Wm-2
Calculate his HSI and interpret the results

## Slide 75: HSI Example
C = 15.17 Wm-2
R = - 44 Wm-2
E req = 194 Wm-2
E max = 183 Wm-2
HSI = 194 ∕ 183 x 100 = 106 (exposure time limited by rise in deep body temperature)
AET = 2440 ∕ (194-183) = 222 minutes

## Slide 76: Required Sweat Rate (SWreq)
From further theoretical & practical development of HSI
Comprehensive, complex & considers many factors.
Adopted ISO 7933:1989 – “Hot environments Analytical
Determination & interpretation of thermal stress using
calculation of required sweat rate”
Calculated from dry bulb temp, wet bulb temp,
humidity, air velocity, globe temp, thermal insulation,
property of clothing, metabolic work rate & posture

## Slide 77: SWreq (cont)
Typically data entered spread sheet & calculated by
Computer (> 1 hour manually).
Following example illustrates the computer application:
A worker is standing & exposed to following conditions:
ta = 35°C, twb = 30°C, tr = 35°C, v = 1.0 m/sec, Iclo = 0.5,
M = 165 Wm-2.

## Slide 78: Swreq (Example cont)
The worker is standing. Using the programme an excessive body temperature increase would occur after the following time (mins)
Criterion Level of acclimatisation
Yes No
Danger 98 65
Alarm 82 54

## Slide 79: Predicted Heat Strain (PHS)
Methods for calculating SWreq further developed by
Malchaire et al. in the revised
ISO 7993:2004 Ergonomics of the thermal environment
– Analytical determination & interpretation of heat
stress using calculation of the predicted heat strain”
Program to calculate PHS can be downloaded from
Malchaire’s web site:
http://www.md.ucl.ac.be/hytr/new/en/

## Slide 80: Thermal Work Limit (TWL)
Developed in Australia by Brake & Bates (2002) for application in underground mine situations & adapted to all situations by Miller & Bates (2007)
“The limiting (or maximum) sustainable metabolic rate
that euhydrated, acclimatised individuals can maintain
in a specific thermal environment, within a safe deep
body core temperature (<38.2°C) & sweat rate (1.2kg/hr)”

## Slide 81: Thermal Work Limit (cont)
Designed for self paced workers & does not rely on
estimates of actual metabolic rates
Work areas evaluated using dry bulb, wet bulb & globe temperatures plus air movement , atmospheric pressure & clothing to predict a safe maximum continuously sustainable metabolic rate for the conditions (Wm-2)

## Slide 82: TWL (cont)
Recommended guidelines for TWL limits have been produced
  Based on hierarchy of controls
  Include approaches such as
    Engineering
    Procedural
    PPE

## Slide 83: TWL (cont)-Recommended TWL Limits & Interventions for Self Paced Work
Source : Brake 2002 – Reproduced with permission

## Slide 84: Instrumentation to Measure TWL
Source: Romteck Pty Ltd – reproduced with permission

## Slide 85: Summary of Empirical Indices

## Slide 86: Summary of Rational Indices

## Slide 87: Direct Physiological Measurements
ISO 9886:2004
Body core temperature
Skin temperature
Heart rate
Body-mass loss

## Slide 88: Body Core Temperature
Oesophagus
Rectum
Gastrointestinal tract
Mouth
Tympanum
Auditory canal
Urine temperature

## Slide 89: Body Core Temperature (cont)
ISO Limits
Hot Environments - Slow heat storage (ie increase of
about 1°C in more than an hour)
Limit set at increase of 1.0°C or 38.0°C whichever comes first where :
  Core measured intermittently whatever technique used
  Auditory canal or tympanic temps measured
  In absence competent medical personnel
  Where no other physiological parameter measured

## Slide 90: Body Core Temperature (cont)
ISO Limits
Hot Environments - Rapid heat storage (ie increase by
about 1°C in less than 1 hour) same limits apply as well
as when rectal or abdominal temps are used
When oesophageal & heart rate measured continuously higher limits can be tolerated ie (1.4°C or 38.5°C whichever comes first)

## Slide 91: Body Core Temperature (cont)
Still temperatures above 38.5°C may be tolerated BUT with many conditions:
  Medically screened
  Acclimatised
  Continuous medical surveillance
  Oesophageal temp continuously monitored
  Other parameters eg heart rate simultaneously monitored
  If exposure can be stopped if intolerant symptoms appear
  Worker can leave as pleases
Any core increase above 39°C is NOT recommended

## Slide 92: Body Core Temperature (cont)
ISO Limits
Cold Environments
Only oesophageal, rectal & intra-abdominal temps are relevant
Lower limit fixed at 36.0°C
  When temps monitored intermittently
  When exp to be repeated same day
Exceptional circumstances for short periods IF
  Medically screened
  Local skin temps measured & limits respected
  Worker can leave as pleases

## Slide 93: Skin Temperature
Varies widely over the surface of the body
Distinction between:
  Local at specific point
  Mean – not measured directly, but “averaged”
Influenced by:
  Thermal exchanges of conduction, convection, radiation & evaporation
  Variations of blood flow & of temp of arterial blood at points of the body

## Slide 94: Skin Temperature (cont)
ISO Limits
Concern only the threshold of pain
Hot environments
  Maximum local skin temp is 43°C
Cold Environments
  Minimum local skin temp is 15°C, in particular for the extremities

## Slide 95: Heart Rate
Guide to stress on the body
When Tc increases, circulation is adjusted to move
blood around to dissipate heat – increase in pulse rate
Number of recommendations for heart rate as indicator
of strain:
ISO 9986
ACGIH
Heart rate recovery approach

## Slide 96: Heart Rate (cont)
ISO 9986
Increase in heart rate ≈ 33 bpm / per degree rise of core temperature
Ideally !! max value of person – 20 by individual test,
Heart Rate Limit HRL = 185 – 0.65 x Age
Heart Rate Limit sustained HRL,sustained = 180 - age

## Slide 97: Heart Rate (cont)
Where ACGIH TLVs are exceeded or if water vapour
impermeable clothing worn
Exposure should be discontinued if:
  Sustained (several mins) heart rate in excess of 180 bpm (180 – age) (normal cardiac performance)
  Body core temp > 38.5°C for medically selected & acclimatised > 38°C for unselected & unacclimatised
  Recovery heart rate after 1 minute peak work > 110 bpm
  Symptoms of sudden & severe fatigue, nausea, dizziness & light headedness

## Slide 98: Heart Rate (cont)
ACGIH cont:
Example
Sustained heart rate for a 40 year old person would be
140 bpm.
These values represent an equivalent cardiovascular
demand of working at about 75% of maximum aerobic
capacity

## Slide 99: Heart Rate (cont)
Heart rate recovery approach - Brouha’s
At end of work cycle:
P1 pulse rate counted from 30 – 60 seconds
P2 pulse rate counted from 90 – 120 seconds
P3 pulse rate counted from 150 – 180 seconds

## Slide 100: Heart Rate (cont)
Heart rate recovery approach (cont):
IF P3 < 90 bpm job situation satisfactory
IF P3 ≤ 90 bpm & P1 – P3 < 10bpm
work level is high, but little likelihood of increase in body temperature
IF P3 > 90 bpm & P1 – P3 < 10 bpm
the stress (work & heat) is too high and action is need to redesign the work

## Slide 101: Body- Mass Loss
Sweat loss can be considered as an index of strain
includes:
  Sweat that evaporates at surface of skin
  Fraction dripping from body
  Accumulation in the clothing
ISO 7933
Sweat rate should be limited to 1.0 litre/hour for non acclimatised and up to 1.25 for acclimatised
Total body-water balance limit set at 5% of body mass to avoid dehydration

## Slide 102
Control of Hot Environments

## Slide 103: Personal Factors Mitigating Against “hot” Work
Severity of heat related disorders from personal
factors can be reduced:
Obesity
Medication
Age
State of acclimatisation

## Slide 104: Obesity
People overweight/unfit are more likely
to experience ill effects
Physical fitness leads to increased
blood volume & cardiovascular
capabilities
Larger the person, the greater the
energy required to do task & hence
higher metabolic heat production

## Slide 105: Obesity (cont)
Healthy life style considerations:
Diet
Exercise
Wellness programs
Stop smoking campaigns

## Slide 106: Medication
Many therapeutic & social drugs can impact on
person’s tolerance to heat
Effects can include:
  Inhibit sweating
  Create cardiac disturbances
  Cause dehydration
  Decrease cardiac output
  Affect ability to recognise temperature increases
  Increase body temp

## Slide 107: Medication (cont)
Any worker taking medication should receive medical clearance before being expose to hot conditions
Sick workers, especially with a fever are more at risk before body temp is regulated to higher than normal
Any disease that may affect cardiovascular or kidney function or state of hydration (eg diarrhoea results in dehydration) may impact on heat tolerance

## Slide 108: Age
Physical condition rather than debilitations often associated with age more important
“Old & fit” versus “young & unfit”
Observed declines in thermal
tolerance with age may be related
to decreased physical capacity rather
than ageing as such

## Slide 109: Age (cont)
Some physical disabilities associated with ageing can reduce a persons’ response to heat stress.
Anything that affects the circulatory system and its ability to distribute heat in the body and bring it to the surface of the skin, as do compromised abilities to maintain full hydration.

## Slide 110: State of Acclimatisation
The body adapts in a number of ways:
Increase in amount of sweat – evaporative cooling
Earlier onset of sweating – reduces prior heat build up
More dilute sweat – reduces electrolyte losses
Increased skin blood flow – greater convective heat transfer between deep body & skin

## Slide 111: State of Acclimatisation (cont)
Reduction of heart rate at any given work rate, lowers cardiovascular strain
Greater use of fats as fuel during heavy work, saves carbohydrates for when very high rates of energy production needed
Reduction in skin & deep body temp at any given work rate, maintains a larger heat storage reservoir, can work at a higher rate

## Slide 112: State of Acclimatisation (cont)
These work together to:
Reduce deep body temp
Reduce skin temp
Provide a greater reserve for emergency or prolonged hot work

## Slide 113: State of Acclimatisation (cont)
How long does it take ?
Very rapidly
After about 2 hours/day consecutively for a week
Diminishes after a 7-10 days away from job & need to be reestablished on return to work if away for significant period

## Slide 114: Engineering Controls
Control the source:
Insulation
Radiant heat
Radiant heat barriers

## Slide 115: Engineering Controls (cont)
Ventilation
Removal or dilution of hot/humid air & replacement cooler drier air - most efficient method
  Forced mechanical
  Forced draft
  Exhausted
  Push – pull systems
  combination of forced & exhausted

## Slide 116: Engineering Controls (cont)
  Natural ventilation
  Utilise open doors,
  windows, roof louvers
  Thermal up-draughts
  above molten metal

## Slide 117: Engineering Controls (cont)
  Increasing air movement
  Increasing air velocity increases rate of heat loss from body
  by both evaporation & convection
  Rule of thumb:
  if wet bulb is below 36°C,
  increasing air velocity is beneficial
  if above 36°C it is detrimental

## Slide 118: Engineering Controls (cont)
Artificial cooling
  No advantage in using ambient air if temps the same
  Evaporative coolers reduce air temp by spraying water into air stream or passing it over a wetted element
  Large mechanical chillers can be used for jobs such as “hot” furnace entry

## Slide 119: Administration Controls
Worker selection
Ethical/moral issues must be considered on a case by case basis
  e.g. exposing known pregnant women or people with known cardiac conditions to high heat strain
Selecting workers on obvious factors seems reasonable
Observe workers to see who is most tolerant
Personal monitoring desirable, but not always practical

## Slide 120: Administration Controls (cont)
Worker training:
  Mechanisms of heat exposure
  Potential heat exposure situations
  Recognition of predisposing factors
  Importance of fluid intake
  The nature of acclimatisation
  Effects of alcohol & drugs in hot environments

## Slide 121: Administration Controls (cont)
Worker training (cont)
  Early recognition of symptoms of heat illness
  Prevention of heat illness
  First aid treatment of heat related illness
  Self assessment
  Management & control
  Medical surveillance programs

## Slide 122: Administration Controls (cont)
Scheduling of work
  Time of season of year
  Time of day – especially outdoor work
  Outdoor work should be done where practical in the cooler months

## Slide 123: Administration Controls (cont)
Work-rest intervals
  Often recommended in ISO 7243 (WBGT) and by the ACGIH WBGT based TLV
  If required to wear protective clothing must be removed during rest breaks to properly cool down
  Rest periods should be spent in a cool place with plenty of cool water for fluid replacement

## Slide 124: Administration Controls (cont)
Fluid replacement
  Is critical during hot & arduous work
  Well balanced diet & plenty of non
  alcoholic beverages in day/night preceding
  Should avoid diuretic drinks & drink 500 ml prior to work
  During work try & drink as much & as frequently as possible

## Slide 125: Administration Controls (cont)
Fluid replacement (cont)
  Workers should be provided cool drinks that appeal to them fluids can contain 40-80 g/L sugar and 0.5 to 0.7 g/L of sodium
  Workers should be encouraged to rehydrate between work shifts
  Body weight should be monitored at start and end of each shift to ensure progressive dehydration not occurring

## Slide 126: Personal Protective Clothing & Equipment
Clothing
Can have adverse effects by insulating body & reducing evaporative heat loss
Impervious clothing impedes heat loss
Can contribute to heat storage
if has a high insulation factor Iclo
Dark colours absorb heat
Reflective materials can be used

## Slide 127: PPE (cont)
Air circulating systems
Vortex cooling tube
Balance of air volumes
& temperature important
Breathing quality air required
Liquid circulating systems
Chilled liquid (water) pumped through capillaries in cooling suit by battery pump or remote cooling unit

## Slide 128: PPE (cont)
Ice cooling systems
Traditionally ice placed
in pockets of insulating garment.
Phase change materials now being used
Reflective systems
To reduce radiant heat load

## Slide 129: AIHA Checklist
  Are adequate supplies of palatable cool drinking water available?
  What is the major source of heat & how can it be mitigated?
  If radiant shielding (includes shade) is possible, is it in the right place?

## Slide 130: AIHA Checklist (cont)
  Is temperature monitoring equipment available?
  Are work guidelines appropriate to the situation?
  Are first aid supplies available & appropriate?
  Has an appropriate work rate been determined?
  Have supervisors been instructed to remove workers at first sign of problems?

## Slide 131: AIHA Checklist (cont)
  Are the workers properly acclimatised?
  Is a cool rest area available?
  Are workers & supervisors trained in recognising symptoms & providing first aid treatment?
  Is there a means of calling emergency support & do workers know how & when to call?

## Slide 132: AIHA Checklist (cont)
  Is clothing appropriate?
  Is the air velocity as high as practical?
  Are workers well hydrated at the beginning of work?
  Is spot cooling available?
  Is microclimate cooling (eg cool vests) available as needed?

## Slide 133: AIHA Checklist (cont)
  Have workers who might be pregnant, have cardiovascular problems, previous heat injuries, on problematic medications & who have fever, been protected from elevated internal body temperature?
  Have workers been reminded of appropriate safety pre cautions?

## Slide 134: Hot Surfaces
When human skin comes into contact with a hot solid
surface, burns may occur.
Local vasodilation & sweating
Pain
Burns

## Slide 135: Factors
Burns occur & depend on:
  Temperature of surface
  Material of surface
  Period of contact
  Structure of surface
  Sensitivity of person (e.g. adult or child)

## Slide 136: Touching a Surface
Intentional or unintentional?
0.5 sec is minimum applicable contact period for
unintentional touching

## Slide 137: Skin Burns
At temperatures above 43°C
If below 43°C, should be no discomfort or pain
sensation or damage
Local skin temperatures only
If whole body say 42°C – serious breakdown of
thermoregulation
Number of skin burn classifications based on skin
layers

## Slide 138: Solid Surfaces
Metals “hotter” than wood
Factors include:
Number of layers of skin
Surface roughness
Wet or dry
Surface temperature
Thermal conductivity
Specific heat
Density
Material thickness
Surface cleanliness

## Slide 139: ISO 13732-1:2006
ISO 13732-1: 2006 “Ergonomics of the thermal
environment – Methods for the assessment of human
responses to contact with surfaces – Hot surfaces”

## Slide 140: Burn Thresholds
“Temperature values of hot surfaces of products which,
when in contact with the skin leads to burns”
Between 0.5 seconds to 10 seconds
Between 10 seconds and 1 minute
Between 1 min and longer (8 hr and longer)

## Slide 141: Burn Thresholds (cont)
Hot, smooth surface made of bare (uncoated) metal
Coated metals
Ceramics, glass & stone materials
Plastics
Wood

## Slide 142: Relevance of 43°C
43°C value for 8 hour and longer ONLY for:
Minor part of body (<10%)
Minor part of head (<10%)
If touching area not only local or if hot surface is touched by vital areas of face (e.g. airways) severe injuries can occur even if surface temperature does not exceed 43°C

## Slide 143: Assessment of Risks of Burning
Identification of hot, touchable surfaces
Task analysis
Measurement of surface temperature
Choice of applicable burn threshold value
Comparison of surface temp & threshold temp
Determination of the risk of burning
Repetition of the assessment if changes

## Slide 144: Protective Measures
Engineering measures
  Reduction of surface temps, insulation, guards, surface structuring e.g. fins
Organisational methods
  Warning signs & signals, training and technical/process documentation
Personal protective measures
  e.g. wearing of gloves, aprons etc

## Slide 145: Practical Session
Break up into work groups
Four (4) exercises to be completed
25 minutes on each exercise and then rotate to the next exercise until all 4 are completed

## Slide 146: Practical Session (cont)
Exercises
Airflow measurement
2) Humidity measurement
3) Radiant heat measurement
4) Thermal monitor use

## Slide 147: Review of Today’s Learning Outcomes
Review of Overnight Questions
Thermal Comfort
  Understand the concepts of thermal comfort & the relationship between environmental & personal factors
Evaluation of Hot Environments
  Review the common approaches for evaluating hot environments
  Understand the limitations of the various indices

## Slide 148: Review of Today’s Learning Outcomes (cont)
Control of Hot Environments
  Review the various factors that can be used to control hot environments
Practical Session
  Understand how to use basic thermal environment monitoring equipment