## Slide 1
M502
Thermal Environment
Day 3
Notes: <number>

## Slide 2: Today’s Learning Outcomes
Case Studies (hot environments)
  Discuss various case studies to highlight various aspects of hot environments
Evaluation & Control of Cold Environments
  Understand the principles by with thermal stress in cold environments can be evaluated
  Review the approaches to controlling worker exposure to thermal stress in cold environments

## Slide 3: Today’s Learning Outcomes (cont)
Approaches to Risk Assessment
  Review approaches adopted in various parts of the world
Case Studies (cold environments)
  Discuss various case studies to highlight various aspects of cold environments

## Slide 4: Case Studies
Hot Environments

## Slide 5: Case Study 3
Heat Stress & Heat Strain during Sheep Shearing
Derived from :
Dr R Gun
AIOH Conference 1987

## Slide 6: The Situation
Large part of world wool industry is based on sheep properties in arid regions
Sheep are shorn in late summer when temperatures are frequently 40oC
Work is physically demanding and shearers are paid by number of sheep shorn per day. A single shearer will shear several hundred sheep per day
Notes: This case study is based in part on a research project conducted in an arid climate in the 1980’s. The work environment is typically a tin shed with no air-conditioning. Shearers are paid on a per sheep basis and thus rest breaks are limited.
<number>

## Slide 7: The Study
Carried out over 13 working days & consisted of 60 persons
Hourly measurements were made of the thermal environment
Simultaneous hourly measurements made of physiological variables

## Slide 8: Thermal Environment Measurements
Air temperature
Radiant temperature
Humidity
Air speed
Insulation value of clothing
Metabolic load

## Slide 9: Physiological Measurements
Rectal temperature (Tc)
Recovery pulse (P60 seconds & P180 seconds)
Daily sweat loss
Notes: It is understood (but could not be confirmed) that rectal thermometers were used.
<number>

## Slide 10: Other Recorded Information
Age of individual workers
Body fat
Number of days worked in previous week
Alcohol intake the previous night
Percentage dehydration

## Slide 11: Criteria For Heat Strain Used in Study
Hourly core temperature >38oC on more than 2 occasions OR
Hourly 60 second recovery pulse rate (P60) >110 beats/minute on more than 2 occasions OR
Hourly 180 second recovery pulse rate (P180) >100 beats/minute on more than 2 occasions
Notes: This is the criteria that was used to assess heat strain in the project.
<number>

## Slide 12: Results
Air temperatures ranged from 20oC in the mornings to >30oC in afternoons with some afternoons >40oC
Mean WBGT of last 4 hours of measurements in day (afternoon when air temperature highest) ranged from 16.1oC to 29oC
Rectal temperature & recovery pulse rate increased during the day. P60 appears to be determinate criteria

## Slide 13: Results (cont)
Percentage of workers exhibiting heat strain increased quickly between 26.3-29oC WBGT
All cases of heat strain were found to be clustered in 7 of 13 days studied. These were the 7 hottest days of the study
Multivariate analysis of personal variables (e.g. body fat, age, alcohol) indicated that these variables did not influence the relationship between heat stress & heat strain

## Slide 14: Shearers Mean Tc versus Time of Day
Notes: The graph shows a rise in core temp at the start of the day followed by a dip at lunchtime (but not back to the start of day core temp). As the day heats up the core temp continues to rise placing shearers at risk of heat strain
<number>

## Slide 15: % Workers with Heat Strain v PM WBGT (o C)
Notes: A comparison of heat strain v time of day WBGT shows that as the WBGT increases so does the % of workers with heat strain as per the project criteria. This is certainly not unexpected.
<number>

## Slide 16: Conclusions
Sustained Tc at or above 38oC or P60 above 110/minute or P180 above 100/minute indicate sheep shearing workers are not fully compensating against heat stress
Such levels of strain are unlikely to occur if mean afternoon WBGT <26.3oC
Engineering controls should be introduced to limit the mean afternoon WBGT <26.3oC
Notes: Engineering controls are usually primitive. In most case this may be a fan but when the ambient temperature is high in the afternoon this is detremental.
<number>

## Slide 17: What Do You Think?
Is this study an accurate representation of heat strain in sheep shearers?
What controls could be introduced to prevent heat strain in workers in these temperature & working conditions?
Notes: It most probably is as these are usually transient workforces and little research has been done in this area.
Obviously the common approaches of increased fluid intake, work rest regimes could be easily introduced. Long term engineering controls are not likely as the facility is only used once per year for 7-10 days.
<number>

## Slide 18: Case Study 4
Thermal Limits of Men in Moderate to Heavy Work in Tropical Farming
Source:
P. Nag, A. Nag & S. Ashtekar
Industrial Health 2007,45 107-117
Reproduced with permission

## Slide 19: The Situation
Farmers in tropical climates are typically exposed to high heat loads during the summer months
The farmers have inherent health issues such as malaria & anemia
26 young male farmers (26 + 3 yrs) studied under controlled conditions
Notes: The controlled conditions were achieved through the use of a walk in climatic chamber.
<number>

## Slide 20: Summer Conditions
WBGT 34.4 – 42.2 oC
Air speed 0.4 – 0.6 ms-1
Metabolic work rate ranged from light to moderately heavy to heavy physical work

## Slide 21: Measured Factors
Body core temperature
Skin temperatures (forehead, trunk, upper arm, hand, thigh & feet)
Metabolic rate
Heart rate
Sweating responses (net change in body weight)

## Slide 22: Measured Experimental Conditions
Ambient temperature 38-50 oC
Wet bulb temperature 27-42 oC
Globe temperature 41-51 oC
Metabolic rates > 275 Wm-2
Clothing insulation 0.3 clo
Notes: Note the high ambient temperatures and high WGBT. The globe temperature is also extremely high indicating significant solar load.
<number>

## Slide 23: Results
Sweat rates increased with environmental heat load
Body core temperature increased with environmental heat load to dangerous levels
Heart rates increased with environmental heat load
Core temperature, heart rate & sweat rate influenced by work severity (i.e. heavy physical work v moderately heavy work)

## Slide 24: Sweat Loss V WBGT
Notes: <number>

## Slide 25: Body Core Temperature v WBGT
Notes: Note the elevated core temperatures. Farmers are under excessive heat strain.
<number>

## Slide 26: Conclusions
Millions of farmers working in tropical climates are at risk of heat strain due to high environmental heat load & physical activity performed
In Eastern India in 1998-1999 11% of the total number of farm accidents resulting in fatalities was from heat stroke
Notes: The authors suggest that some farm accidents (11%) could in fact be due to excessive heat strain. The data suggests that this is a likely outcome. Given the total number of accidents involved this would be an incredible number of persons.
<number>

## Slide 27: What Do You Think?
Is this study realistic?
How could the number of fatalities be reduced?
Notes: Probably. The authors seemed to match conditions very carefully.
Education would be the first starting point.
<number>

## Slide 28: Case Study 5
Physiological Strain of Miners at Hot Working Places in German Coal Mines
Source:
B. Kalkowsky & B Kampmann
Industrial Health 2006,44 465-473
Reproduced with permission

## Slide 29: The Situation
Percentage of shifts in studied coal mines classified as “hot working conditions” has increased to >50% in last 10 years
Rapid increase in hot conditions due to increasing mine depth and increasing mechanisation
Notes: The rise in hot mines is due to increased depth of coal seams and the increasing size of machinery (and thus heat) to extract coal.
<number>

## Slide 30: The Study
Involved 38 miners over 125 shifts
Monitored continuously for heart rate & rectal temperature
Body mass & food/fluid intake measured before & after each shift
Other factors recorded: age, work experience, work conditions, work load, environmental conditions

## Slide 31: Legal Requirements
A working place is deemed as “hot” if:
  If air temperature exceeds 28oC
  Basic effective temperature (BET) exceeds 25 oC
Controls are:
  Reduction in hours worked as BET increases
  Work ceases at a BET of 30oC
  Medical checks every 2 years
  Acclimatisation over 14 day period

## Slide 32: Typical Underground Mining Equipment
Source: BHP Billiton Illawarra Coal – reproduced with permission
Notes: The photograph on the left is a typical continuous miner used to develop the various roadways underground. The machine on the right is the major production equipment commonly used in coal mines around the world. The long wall shearer (far right of photograph) moves backwards and forwards across the coal face slicing off the coal as it goes. Long wall faces are 200-450m wide and 1-4 km long.
<number>

## Slide 33: Results : Environmental Conditions
Dry bulb temperature 31.2 oC (21.6-36.3)
Wet bulb temperature 28.2 oC (20.0-30.0)
Wind velocity 1.8ms-1 (0.2-6.0)
BET 26.3 (16.6-32.2)
WBGT 29.1 (20.5-33.7)

## Slide 34: Results (cont)
Heart rate follows cardiovascular activity
Core temperature stabilises around 38.3 oC
Heart rates have considerable variability due to different fitness levels, time of day but no overall increase with environmental heat load

## Slide 35: Results (cont)
Significant increase in sweat loss with increasing environmental heat load
Sweat losses were not replaced during the shift (50-60% replaced thus net deficit of 40-50%)

## Slide 36: Typical Miners Core Temperature & Heart Rate
Notes: Note steady core temperature during the day suggesting self pacing.
<number>

## Slide 37: Typical Miners Core Temperature & Heart Rate During Various Activities
Notes: Note increase in heart rate with activity.
<number>

## Slide 38: Conclusions
Heart rate & core temperature did not increase with thermal load yet sweat rate did increase
Miners are “self pacing” to keep level of strain at an appropriate level
Miners have a net water deficit per shift

## Slide 39: What Do You Think?
What recommendation would you make?
What factors need to be encouraged and practiced to maintain the current situation?
Notes: Try and get them to drink small amounts but less often.
<number>

## Slide 40: Case Study 6
Evaluating Heat Stress for Blast Furnace Operators: An Approach to the “Hot Topic”
for Port Kembla Steelworks
Source : S. Jones, K. Burton & I. Tague
AIOH Conference Proceedings 2005
(Reproduced with permission)

## Slide 41: The Process
Molten iron produced in a blast furnace
“Tapping” of the
molten iron at a
temperature of
approximately
1550°C
Notes: Iron is produced in a blast furnace where iron ore is mixed with coke and limestone and heated under a reducing atmosphere.
<number>

## Slide 42: The Process (cont)
Flows through
cast house floor
into ladles for
transport to the
steelmaking
department for
further processing
Area monitoring - Timbering
Notes: The molten iron flows from the blast furnace into ladles on rail cars which are then transported. As the molten metal cools it forms a crust which restricts flow and thus this must be dislodged via the use of timber poles “timbering”
<number>

## Slide 43: The Situation
Operator concerns in regard to a proposal for significant work re-organisation
Monitoring conducted over 3 monitoring periods within 12 months
Each blast furnace has 6 operators per 12 hour shift operating in rotating teams of 2 or 3

## Slide 44: The Situation (cont)
Each team monitors a single cast which last 2.5 hrs and all work is self-paced
After the cast each team cleans up for about 30 min but then rests for next two casts (5 hours)
The proposed re-organisation would require operators to do inspections in current rest periods
Notes: Note the significant rest period between casts (tapping of the blast furnace)
<number>

## Slide 45: Physiological Monitoring
Physiological data collected using Questemp QTIII personal heat stress monitor programmed according to amount of clothing worn & age
Continuous monitoring of heart rate (bpm) and skin temperature

## Slide 46: Physiological Monitoring (cont)
Recording of tasks by an occupational hygienist in attendance at all times
Tympanic membrane temperature measured pre & post casting
Blood pressure & body weight measure pre & post shift. Detailed medical questionnaire

## Slide 47: Environmental Monitoring
Questemp°15 - Area Heat Stress Monitor used to measure temperatures at approximately head, abdomen & feet
Measurements of natural wet bulb, ambient, globe temperatures were weighted as per AIOH guideline to determine WBGT index
Air velocity
Metabolic workloads estimated from AIOH guidelines

## Slide 48
Physiological Monitoring Data
Hot metal worker during the shift
Notes: Note increasing heart rate and core temp with activity. Maximum core temperature reached was 37.6 oC
<number>

## Slide 49: Monitoring Programme
57 operators monitored over 29 x 12 hour shifts
Monitoring pre & post re-organisation and in very hot summer months to confirm findings
Using environmental data the Predicted Heat Strain Index was calculated using the computer programme of Malchaire et al

## Slide 50: Malchaire’s Model Results
PHS MODEL: Based on 75kg person 1.8m high who is acclimatised (A) or not acclimatised (NA)
A NA
Total water loss (g): 4649 4649
Rectal temperature at the
end of the phase (o C): 37.5 37.5
Interpretation (PHS) : rectal temperature of 38 o C is not exceeded for (A) or (NA)
Notes: Note how close the physiological monitoring was to Malchaire’s prediction.
<number>

## Slide 51: Malchaire’s Model Results (cont)
Maximal water loss (g)
5625 g for a mean subject: N.A.: not exceeded
A.: not exceeded
3750 g for 95% of the subjects: N.A.: reached at minute 531
A.: reached at minute 531
To protect 95% of the subjects, the work N.A. A.
must be stopped before : (in minutes) 531 531
Notes: 531 minutes (8.9 hours) is well in excess of the period of time that they work on the process of tapping the blast furnace. Little risk of heat strain.
<number>

## Slide 52: Results
Calculations of PHS from Malchaire et al:
  Maximum allowable rectal temp NOT exceeded
  Results should NOT cause heat related illness
Thirst reported by majority operators:
Generally low fluid intake – average 2 - 3 litres
Body weight loss up to 2 kg
No significant symptoms or signs of heat strain

## Slide 53: Results (cont)
Some physical activities associated with high heart rates
Elevated WBGTs at some particular locations & tasks
Monitoring of work practices highlighted some behavioral changes which would affect a decrease in heat exposure for operators

## Slide 54: Conclusions
Methodology was acceptable to all stakeholders
Physiological data collection was the most valuable in interpreting results
Behavioral factors added unnecessary heat load to cast house operators

## Slide 55: What Do You Think?
If you were presented with a similar situation would you use this approach?
What is the factor was identified which was adding unnecessary heat load to these workers?
What methods are used to reduce radiant heat in these conditions?
Notes: Yes. Behavioral practices eg standing in a position of high radiant heat load when it could be avoided. Barriers,PPE
<number>

## Slide 56: Evaluation of Cold Environments
Source: M Taylor – reproduced with permission
Notes: Photo taken in alaska showing the difficulty of working in such an environment
<number>

## Slide 57: Evaluation of Cold Environments
Wind chill index & equivalent chilling temperature
Required clothing insulation index
ACGIH TLV standards
Use of cold stress indices

## Slide 58: Wind Chill Index
Can be described as the cooling power of the atmosphere
Originally derived from the freezing time of 250g of water in a plastic cylinder suspended freely in variable atmospheric conditions whose temperature and wind velocity were known

## Slide 59: Assessing Cold Stress
Wind chill index (WCI)
  combines effects of air temperature and air movement
  has limitations - makes no allowance for different clothing or other heat loss mechanisms
  rather subjective
  however useful to identify conditions with risk of cold injury to exposed skin
  most widely used index for cold stress
Notes: <number>

## Slide 60: Equivalent Chilling Temperature
The temperature under calm wind (<1.8ms-1) which would provide cooling of the skin (i.e. the same WCI) equivalent to that found with other combinations of temperature and wind

## Slide 61: WCI, ECT & Effect on Exposed Flesh
Source: University of Wollongong
Notes: <number>

## Slide 62: Required Clothing Insulation Index (IREQ)
IREQ first developed in 1984 and is the resultant clothing insulation required to maintain the body in thermal equilibrium under steady state conditions when sweating is absent and peripheral vasoconstriction is present
Expresses cold stress in terms of general body cooling and insulation required to maintain thermal balance

## Slide 63: IREQ (cont)
IREQ min
  Highest admissible cooling level
IREQ neutral
  No or minimal cooling of the human body
  Thus for a given situation need to select a clothing
  ensemble which has insulation values above IREQ
  min and below IREQ neutral

## Slide 64: Duration Limited Exposures (DLE)
If the selected clothing insulation values are less than IREQ min exposure has to be time limited to prevent progressive body cooling
Possible to calculate allowable exposure times (DLE) and after exposure a recovery time (RT) to restore the bodies normal heat balance

## Slide 65: IREQ at Varying Levels of Activity
Source: AIHA 2003 – reproduced with permission

## Slide 66: IREQ (cont)
Complex index requiring significant knowledge, expertise & information
Requires computer programme to calculate indices
Usefulness of the IREQ in practical applications is yet to be determined

## Slide 67: ACGIH TLV Standards
Based on the prevention of Tc falling below 36 oC and prevention of cold injury to extremities
Based on workload & wind speed for properly clothed workers in cold environments
Presented as work/warm-up schedules
Notes: <number>

## Slide 68: Work/warm-up Schedule for 4 Hour Shift
Source: ACGIH 2007 – Reproduced with permission

## Slide 69: ACGIH Equivalent Chilling Temperature
ACGIH also recommend the use of equivalent chilling temperature for control of injury to exposed skin
Simple chart links tch to duration of exposure for exposed skin to potential danger

## Slide 70: ACGIH Wind Chill Chart
Source: ACGIH 2007 – reproduced with permission

## Slide 71: Use of Cold Stress Indices
No one index accounts for all possible variables
All indices have limitations in their ability to predict human response to the environment
Most appropriate approach is to control & manage risk factors present in each situation

## Slide 72: Control of Cold Environments
Personal factors
Engineering controls
Management tools
Clothing

## Slide 73: Personal Factors
Screening of workers for diseases
  Heart disease
  Respiratory disease
  Cold allergy
  Raynaud’s phenomenon
Medication which may interfere with normal body temperature regulation or reduces tolerance to cold

## Slide 74: List of Screening Factors
British refrigerated food industry confederation
  Heart or circulation problems
  Diabetes
  Thyroid problems
  Blood disorders
  Kidney or urine disorders
  Arthritis or bone disease
  Any infection

## Slide 75: List of Screening Factors (cont)
British refrigerated food industry confederation
  Lung function problems or asthma
  Chronic gastro-enteritis , diarrhoea or vomiting
  Neurological malfunction
  Psychological problems
  Eyesight or hearing difficulties
  Prescribed medication

## Slide 76: Engineering Controls
Reduce exposure to wind
  Wind barriers : have been found effective outdoors or in freezer rooms to control circulated air
  Refuges : access to warm conditions and warm drinks during rest

## Slide 77: Engineering Controls (cont)
Insulation of metal handles :avoid metal tools
Provision of local heating :hot air jets, radiant heating
Use of mechanical aids
Design of equipment so gloves/mittens do not need to be removed to operate
Design of workplaces so operators are not required to sit or stand for long periods
Reducing air velocity in cool rooms & chillers while workers are inside

## Slide 78: Management Controls
Monitoring (ACGIH 2007)
  Appropriate monitoring of thermal parameters
  If DB < -1oC measure temperature at least every 4 hours
  If wind speed > 2ms-1 in indoor workplaces record every 4 hours
  In outdoor situations measure wind speed with temperature
  whenever air temperature < -1oC
  Calculate the equivalent chilling temperature in all cases where air measurements are required

## Slide 79: Work-Rest Regimes
Developed by Saskatchewan department of Labour in Canada
Adopted by the ACGIH as TLV limits
  Applies for a 4 hour shift for moderate to heavy work with warm up breaks of 10 minutes in a warm location

## Slide 80: Work-Rest Regimes (cont)
Example
  Conditions of -35 o C at wind speed of 8 km/hr a worker should have a maximum work period of 40 minutes with 4 breaks in a 4 hour period
  If work is light moderate worker should have a maximum work period of 30 minutes with 5 breaks in 4 hour period (i.e. apply scale at one step lower than for moderate to heavy work)

## Slide 81: Work/warm-up Schedule for 4 Hour Shift
Source: ACGIH 2007 – Reproduced with permission

## Slide 82: Other Managerial Controls
Education
  Symptoms of over exposure to cold
  Clothing habits
  Safe work practices in cold conditions
  Physical fitness requirements
  Emergency procedures
Medical screening
  Respiratory or cardiac condition
  Medications which interfere with thermoregulation

## Slide 83: Other Managerial Controls (cont)
Acclimatisation
  Recommended for new workers and those returning from extended leave
Instructions
  Training on symptoms of cold stress, emergency procedures & preventative measures
Supervision
  Monitoring for signs of cold stress
  Work in extreme cold should be in pairs or groups

## Slide 84: Other Managerial Controls (cont)
Self-reporting of illness
  Encourage reporting medical factors that may influence susceptibility to cold
Self-paced working
  Encourage self pacing of work rates so that heavy sweating does not occur
  Encourage co-worker observation

## Slide 85: Other Managerial Controls (cont)
Health Life-styles
  A good diet and physical conditioning help protect against abnormal cold
  Fatigue increases vulnerability to cold
Administrative controls
  Arrange work so sitting or standing for long periods is minimised
  Long shifts and excessive overtime should be avoided

## Slide 86: Clothing
In absence of shelter most important means of protection against cold
Insulation of clothing due to air trapped between layers of clothing & in fibrous structure
Insulation proportional to:
  Thickness of trapped air
  Capacity to trap air
  Compressibility to trap air
Needs to be windproof

## Slide 87: Clothing (cont)
Whole body protection required in cold air or cold water immersion to prevent onset of hypothermia
Efficiently waterproofed clothing is essential in cold wet environments due to rapid cooling by combined evaporation & wind chill
Serious disadvantage of impermeable clothing is that water vapour cannot escape from the skin surface & will condense and eliminate insulation of trapped air

## Slide 88: Clothing (cont)
Apart from protection against wet conditions impermeable clothing is useful in cold, dry conditions where people are not very active
For severe work the outer layer should be water repellent but capable of allowing vapour movement. Need to change if it become wet
Extremities & head must be protected

## Slide 89: Intrinsic Clothing Insulation (Icl)
Icl is a property of the clothing itself and represents the resistance to heat transfer between the skin and the clothing surface
Units are m2 oC W-1 but in 1941 the clo unit was introduced

## Slide 90: Definition of clo
1.0 clo is the insulation provided by clothing sufficient to allow a person to be comfortable when sitting in still air at a temperature of 21 o C
1.0 clo equivalent to a Icl of 0.155 m2 oC W-1

## Slide 91: Intrinsic Clothing Insulation Values
Clothing Ensemble | Icl (clo)
Nude | 0
Shorts only | 0.1
Light summer clothing | 0.5
Typical indoor clothing | 1.0
Heavy business type suit | 1.5
Business clothes, overcoat plus hat | 2.0
Polar weather suit | 3 to 4

## Slide 92: Selection & Use of PPE
Clothing
  Use multiple layers
  Inner layer should be to remove moisture from skin. Underwear made from polyesters or polypropylene suitable for this purpose. Fishnet underwear good for this purpose
  Outer layers should be easy to open or remove to prevent excessive sweating
  Outer layer should be waterproof in wet conditions

## Slide 93: Selection & Use of PPE (cont)
Clothing (cont)
  50% of body heat can be lost through the head. Wool knit cap or liner under a hard hat can reduce this loss
  Dirt fills air cells in fibres of clothing & destroys insulation properties
  Clothing should be kept dry. Remove snow before entering heated shelters
  Depending upon dexterity level required use gloves, 4oC for light work & below minus 7oC for moderate work. All work below minus 17oC use mittens

## Slide 94: Selection & Use of PPE (cont)
Footwear
  Felt-lined, rubber bottomed, leather-topped boots with removable insoles are best suited to heavy work in cold since leather is porous
  For work in water waterproof boots must be worn but care must be taken as insulating materials & socks will become wet as moisture cannot escape

## Slide 95: Selection & Use of PPE (cont)
Socks
  One pair thick bulky socks or 2 pairs (inner of “wick” type material plus thicker outer)
  Use correct thickness for boots so as to ensure compression does not occur (loss of insulation)
Face & eye
  In extremely cold conditions where face protection is used eye protection must be separated from nose & mouth to prevent exhaled moisture fogging glasses

## Slide 96: Working in Cold Conditions
Source: M Taylor – reproduced with permission
Notes: Alaska 26 February 2007 temperature -42OC
<number>

## Slide 97: Working in Cold Conditions
Source: M Taylor – Reproduced with permission
Notes: Note the mobile warm up cabins in the background
<number>

## Slide 98: Working in Cold Conditions
Source: M Taylor – reproduced with permission
Notes: Note the difficult ergonomic situation
<number>

## Slide 99: Working in Cold Conditions
Source: M Taylor – Reproduced with permission

## Slide 100: AIHA Checklist for Working in Cold Areas
Appropriate training
Emergency medical support
Appropriate clothing
Emergency warming
Facilities to dry clothing
Windbreaks positioned correctly

## Slide 101: AIHA Checklist for Working in Cold Areas
Instructions to supervisors
Hand & foot warmers
Modification of work rates so as to ensure very heavy work is not followed by light work
Spot warming
Warm appropriate drinks

## Slide 102
Risk Assessment & the Thermal Environment

## Slide 103: Approaches to Risk Assessment
AIOH Approach
Republic of South Africa DME Code of Practice
ACGIH Thermal Stress TLV’s
Quantitative v Qualitative Approaches
Physiological Assessments

## Slide 104: AIOH Tiered Approach
Use the basic Thermal Risk Assessment Form
Screening for clothing that does not allow air and water vapour movement
Detailed analysis
Heat strain

## Slide 105: AIOH - Thermal Risk Assessment Form
Assessment points
If less than 28 points, risk of thermal conditions low, NO branch of flow chart can be taken
If 28 points or more, further analysis is required
If > 60 points the need for immediate implementation of controls

## Slide 106: AIOH - Screening for Clothing
Clothing that does NOT allow air & water vapour
Movement
Even if ambient conditions considered cool &
Assessment points “Low Risk” if workers required to
wear clothing that does NOT allow air & water vapour
movement the NO branch of flow chart should be taken

## Slide 107: AIOH - Detailed Analysis
The thermal risk assessment form is an initial
screening step.
If no data for environmental conditions & clothing, the
NO branch in flow chart is taken ie physiological
monitoring
PHS
TWL

## Slide 108: AIOH - PHS & TWL
If suggested values do not exceed the criteria, the NO
branch of the flow chart can be taken
If the exposure exceeds the limits the YES branch leads
to reassessment of job specific controls.
If these are not available, the NO branch leads to
physiological monitoring as the only alternative to demonstrate adequate protection is being provided

## Slide 109: AIOH - Heat Strain
AIOH recommend removal from heat exposure if:
Heart Rate Limit = 185 – 0.65 x Age (ISO 9886)
Thermal Heart Rate increase > 30 bpm per 1oC Tc increase
Recovery HR at 1 min after peak effort > 124 bpm

## Slide 110: AIOH - Heat Strain (cont)
Body core temp
  > 38.5°C medically selected & acclimatised
  > 38°C unselected & unacclimatised
Symptoms of sudden & severe fatigue, nausea, dizziness & lightheadedness

## Slide 111: Basic Thermal Risk Assessment Form
Source; AIOH 2003 – Reproduced with permission

## Slide 112: AIOH Heat Stress Management Flow Chart
Source; AIOH 2003 – Reproduced with permission

## Slide 113: South African DME Code of Practice
Mandatory for each mine to prepare & implement a code of practice for thermal stress
Components
  Risk assessment & control
  Monitoring programme
  Hierarchy of controls
  Medical surveillance
  Reporting & reviewing

## Slide 114: South African DME Code of Practice

## Slide 115: South African DME Code of Practice
Occupational hygiene
  Risk assessment
  Categorisation of the thermal environments
  Thermal stress management
  Measurement methodology
  Thermal stress monitoring
  Reporting & recording

## Slide 116: South African DME Code of Practice
Medical surveillance
  Initial examination
  Periodic examination
  Exit examination

## Slide 117: ACGIH Thermal Stress TLVs®
To maintain core body temperature within +1°C of
  normal (37°C) temperature
Their guidance represents conditions under which it is believed that nearly all heat acclimatised, adequately hydrated, unmedicated, healthy workers may be repeatedly exposed without adverse health effects
WBGT based

## Slide 118: ACGIH - Decision Making Process
Process outlined in their flow chart should be started if:
A qualitative exposure assessment indicates possibility of heat stress
There are reports of discomfort due to heat stress
Professional judgement indicates heat stress conditions

## Slide 119: ACGIH Chart for Evaluating Heat Stress & Strain
Source: ACGIH – reproduced with permission

## Slide 120: ACGIH TLVs® & Action Limits
Source: ACGIH – reproduced with permission

## Slide 121: Clothing Adjustment Factors
Source: ACGIH – reproduced with permission

## Slide 122: Screening Threshold Based on WBGT
Source: ACGIH – reproduced with permission

## Slide 123: Metabolic Rate Categories
Source: ACGIH – reproduced with permission

## Slide 124: ACGIH – Detailed Analysis
If required second level analysis such ISO 7933 PHS
If this data not available the NO branch in the flow chart is taken & goes to physiological monitoring
If data is available & does not exceed Action Limit for unacclimatised workers then NO branch taken

## Slide 125: ACGIH – Detailed Analysis (cont)
If Action Limit exceeded but TLV® for acclimatised workers are not exceed then implement general controls
If exposure exceeds TLV® for acclimatised workers the YES branch leads to physiological monitoring

## Slide 126: ACGIH Guidelines for Limiting Heat Strain
ACGIH recommend removal from heat exposure if:
Sustained (several mins) Heart Rate > (180 bpm – age)
Body core temp > 38.5°C for med selected & acclim
> 38°C in unselected & unacclimatised
Recovery HR after 1 min peak effort > 120 bpm
Symptoms of sudden & severe fatigue, nausea, dizziness or lightheadedness

## Slide 127: ACGIH Heat Stress Management & Controls
General Controls
Provide accurate verbal & written instructions & annual training programs
Encourage drinking small volumes of cool palatable water or other acceptable fluid about every 20 mins
Permit self limitation of exposures & use a buddy system

## Slide 128: ACGIH Heat Stress Management & Controls
An individual may be at greater risk of heat related
disorders if:
Profuse sweating is sustained over hours
Weight loss over a shift > 1.5% body weight
24-hour urinary sodium excretion is < 50 mmoles

## Slide 129: ACGIH Heat Stress Management & Controls
Counsel & monitor those on medications & those who abuse or are recovering from abuse of alcohol or other intoxicants
Encourage healthy life style, ideal body weight & electrolyte balance
Consider pre-placement medical screening
Monitor the heat stress conditions & reports of heat related disorders

## Slide 130: ACGIH Heat Stress Management & Controls
Job Specific Controls
Consider engineering controls that reduce metabolic rate, provide general air movement, reduce process heat & water vapour release, & shield radiant heat sources etc
Consider administrative controls that set acceptable exposure times, allow sufficient recovery & limit physiological strain

## Slide 131: ACGIH Heat Stress Management & Controls
Consider personal protection that is demonstrated effective for the specific work practices & conditions at the location
NEVER IGNORE ANYONE’S SIGNS OR SYMPTOMS OF HEAT RELATED DISORDERS

## Slide 132: Quantitative & Qualitative Approaches
Quantitative (measurement)
  Provides a more accurate estimate of an individual’s strain
  Gives greater level of confidence in relation to the impact on an individual
  Requires significant technical expertise
  Requires equipment some of which is expensive
  Time consuming if all individuals are evaluated

## Slide 133: Quantitative & Qualitative Approaches (cont)
Qualitative (risk assessment)
  Widely adopted as a screening process
  Process dependent on available information
  Requires limited technical expertise
  Usually applied to groups rather than individuals
  Significant health issues may go un-noticed due to lack of technical expertise
  Risk assessments do not solve problems only the actions arising from the process

## Slide 134: Physiological Assessments
Means by which to identify “at risk” people
Factors to consider when assessing suitability for work in hot environments
  Weight & physical fitness
  Age
  Medical disorders
  Medications
  Previous heat intolerance

## Slide 135: Individual Employee Risk Profile
Developed as a management tool in South African gold & platinum mines
Elements
  Medical contraindications
  Age
  Obesity
  Inherent heat intolerance
  Strenuous work
  History of heat disorders

## Slide 136: Individual Employee Risk Profile
Approach recommended to assess risk
  Profile with no more of one of the above risk factors generally acceptable
  Presence of any two factors viewed with concern and should not be condoned unless situation can be mitigated
  More than two risk factors is unacceptable

## Slide 137: Employee Risk Profile Matrix
Source: SIMRAC-Reproduced with permission

## Slide 138: Global Approach to Assessing Workers
Review of 121 cases of heat stroke in South African mines found that in 87% two or more risk factors were present yet worker had not been identified as “at risk” and allowed to work
No standardisation of schemes to assess “at risk” workers within global industry-individual companies developing own specific company guidelines

## Slide 139: Case Studies
Cold Environments

## Slide 140: Case Study 7
Cold Exposure During Helicopter Rescue Operations in the Western Alps
Source:
T. Kupper, J Steffgen & P Jansing
Annals of Occupational Hygiene Vol 47, No 1, 7-16, 2003
Reproduced with permission

## Slide 141: The Situation
Study to assess the risk of personnel exposed to cold environments during alpine rescue operations with their quickly changing conditions
1082 rescue operations over a 15 month period was reviewed

## Slide 142: Typical Alpine Rescue
Notes: Photographs of a typical rescue taken from source paper. Note the rescuer outside the helicopter
<number>

## Slide 143: Data Collection
Due to aircraft and operational conditions it was not possible to collect precise environmental or physiological data
Used meteorological data, accidents location & duration of exposure to estimate exposure to cold
Using above approach two models produced; mean & worst case conditions
Clothing insulation was calculated using ISO 11079 :
IREQ (min) & IREQ (neutral)

## Slide 144: Equivalent Chill Temperature (oC)

## Slide 145: Wind Speed
Most operations performed at 3-6 m/s
Some operations took place at > 20 m/s

## Slide 146: Results
Mean exposure time was 15 minutes but ranged up to 850 minutes
Insulation recommended by ISO 11079 was sufficient in 40.2% (IREQ (min) ) of rescues in summer but it was only sufficient in 0.3% (IREQ (min) ) in winter rescues
Notes: Most rescues were completed in very quick time but several took much longer. In one rescue the helicopter and crew had to overnight on the alps. The crew was not prepared for such a stay.
<number>

## Slide 147: Conclusions
The typical clothing ensemble used by rescuers has a combined insulation of 2.0 clo which is insufficient in a considerable number of operations
Cases of shivering are commonly reported but cases of moderate or severe hypothermia are rare
Quickly changing conditions within the helicopter to outside make suitable clothing ensembles difficult to find

## Slide 148: Conclusions (cont)
Winching operations are a major source of thermal stress for rescuers as they are standing outside the helicopter while the patient is being transported to a safe landing area (patient inside thermal bag)
Cold weather injuries within rescuers are grossly under reported as they are not considered occupational accidents
Medical assessments of rescuers are limited

## Slide 149: Recommendations
Additional clothing should be carried for long duration rescues
Medical assessments to exclude rescuers with medical conditions that may increase risk of cold injuries should be introduced
Procedures to protect rescuers during winching operations should be adopted

## Slide 150: What Do You Think?
Why are cases of shivering common but cases of hypothermia rare?
What procedures could be adopted to minimise the risk of frostbite to the face of rescuers immediately after winching operations?
Notes: Because the rescuers clothes are designed mainly for the hot cabin of the helicopter and thus when they are outside for a longer than expected period they start to shiver. These outside periods are short in duration and thus hypothermia is rare.
It was suggested that the rescuer turn his back to the wind so that the hood on his clothing offered some protection from wind blast.
<number>

## Slide 151: Case Study 8
Cold Stress During in Cold-Storage Depots
Derived from:
H Strasser & K Kluth
IEA World Conference 2006

## Slide 152: The Situation
Cold storage workers are exposed to cold temperatures (-24oC) for periods up to 90 minutes
Following a warm up period of 20 minutes the workers return to the cold room for another period. This process is repeated throughout the day
Heavy manual handling of the groceries was a major requirement of workers performing this task

## Slide 153: Measurements
30 subjects were assessed for exposure to cold
Heart rate & blood pressure
Core body temperature was estimated via ear canal temperatures
Temperature of the sole of the foot
Workers rated their personal degree of cold sensation in various body regions

## Slide 154: Results
The range of the majority of subjects tympanic temperatures in both warm and cold conditions is generally narrow (< 1 oC)
One person had a range of 2oC
More variation in foot temperatures than core temperatures
Average decrease in foot temperature with cold was 3.5 oC

## Slide 155: Results (cont)
Results of personal rating of cold sensation indicated few workers experienced any problems with arms, legs, ears & upper torso
Ratings of cold sensation were moderately high for nose, mouth & hands
Ratings of sensation were high in most workers for the fingers, feet & toes

## Slide 156: Conclusions
The use of appropriate protective clothing compensates in the majority of cases for any physiological strain from the cold
The workers requirement to undertake physical activity is a benefit provided an individuals physiological performance capacity is not exceeded
Numerous changes in body posture & hand / arm movement appear to improve circulation

## Slide 157: What Do You Think?
What should be done to ensure that workers who are doing very heavy physical work do not have an increased risk of cold injuries?
How could the sensation of cold in the workers extremities be reduced?
Notes: When they have rest periods they replace wet clothing with dry. Use of improved gloves and footwear
<number>

## Slide 158: Case Study 9
Food Handling in a Moderately Cold Facility
Derived from:
Human Thermal Environments 2nd Edn

## Slide 159: The Situation
Food is delivered to the handling area in refrigerated trucks at 2 oC
The food had already been cooked & chilled at the factory prior to delivery
The food is unloaded through a sealed area into a chilled area (2 oC)where it is divided into meal size portions. Fans continually push cool air into the area
immediately above the work space

## Slide 160: The Situation (cont)
Staff are located at workstations along a conveyor belt and the food is served from large containers onto plates which are on trays but still within the chilled area
The trays are loaded into closed trolleys which contain heaters so that the food is heated to the correct serving temperature at the point of delivery
The process of takes workers 1 hour per meal during which all workers are in an environment at 2oC

## Slide 161: The Situation (cont)
After completing the dispensing of food workers had a hot drink before completing other duties
Some workers cleaned the dispensing area while others went outside the chilled area to wash up & clean
Activities outside the area required removing some clothes and other workers performing cleaning inside the chilled area also removed some clothes as they felt hot

## Slide 162: Data Collection
The process involves 50 persons the majority of which are female
Workplaces were monitored for environmental parameters (air speed, humidity, ambient & globe temperature)
The metabolic heat production was established at 70 Wm-2 for the light arm work involved
Estimated insulation value of 2.3 clo was obtained for the clothing ensemble normally worn

## Slide 163: Results
Air temperature ranged between 1 & 3 oC
No radiant effects were present
Humidity was close to 100%
Air speed was 0.2-1.2 ms-1
Wind chill index was 783 Wm-2
IREQ calculations indicated a maximum work time of 2.2 hr at 1.6 oC & 1.2ms-1
Turning off the fans during the dispensing of food improved comfort levels significantly

## Slide 164: Conclusions
Environment cold but no risk of damage to extremities
A change in activity (cleaning v dispensing) resulted in undergarments becoming wet
A more suitable range of clothing (easily removed & replaced) would encourage workers to remove & replace layers for different activities

## Slide 165: What Do You Think?
Are there some other recommendations that could have been made?
Notes: Relocation of the fans or at least turning them off during dispensing of food.
<number>

## Slide 166: Today’s Learning Outcomes
Case Studies (hot environments)
  Discuss various case studies to highlight various aspects of hot environments
Evaluation & Control of Cold Environments
  Understand the principles by with thermal stress in cold environments can be evaluated
  Review the approaches to controlling worker exposure to thermal stress in cold environments

## Slide 167: Today’s Learning Outcomes (cont)
Case Studies (cold environments)
  Discuss various case studies to highlight various aspects of cold environments
Approaches to Risk Assessment
  Review approaches adopted in various parts of the world