## Slide 1
M502
Thermal Environment
Day 4
Notes: <number>

## Slide 2: Today’s Learning Outcomes
Case Studies
  Discuss various case studies to highlight various risk assessment approaches
  Discuss a number of other scenarios which highlight thermal stress issues
Student Exercises
  Undertake a number of exercises to reinforce the learning's contained in the lectures

## Slide 3: Case Studies
Risk Assessment & Other Approaches

## Slide 4: Case Study 10
Heat Stress Scenario’s
Source: Ross Di Corletto
(Reproduced with permission)

## Slide 5: Scenario 1
Descaling of a large sealed circular sedimentation vessel
Hard scale, on horizontal surfaces, vertical and sloping walls must be removed using pneumatic jackhammers. Activity is for approximately 120 minutes
One high velocity axial fan on the top of the vessel
A large access hatch on the roof of the vessel and a small hatch on the bottom have been opened
Notes: <number>
Scenario 1
An operator is involved in the descaling of a large sealed circular sedimentation vessel measuring approximately 20 metres in diameter and 10 metres deep. The deposit, which is high in silica and iron resulting in a hard scale, is attached to horizontal surfaces, vertical and sloping walls must be removed using pneumatic jackhammers. One high velocity axial fan has been positioned on the top of the vessel acting as an exhaust fan and a large access hatch on the roof of the vessel and a small hatch on the bottom have been opened.

## Slide 6: De-scaling of a Sedimentation Tank
Size of Tank: 20m in diameter & 10m high
Ventilation is via an axial fan sucking air into the vessel from an access hat on the top and a small hatch at the bottom

## Slide 7: Basic Risk Assessment of Scenario 1
Notes: <number>

## Slide 8: Stage 2 Assessment
Additional Monitoring
  dry bulb,
  wet bulb,
  globe temperature,
  air velocity,
  humidity,
  metabolic load and
  clothing.
  posture
Rational Index
Notes: <number>
The Stage 2 assessment necessitates additional ‘specialist’ monitoring to ensure that the additional basic thermal parameters are measured, that is dry bulb, wet bulb, globe temperature, air velocity, humidity, metabolic load and clothing. This information is then utilised in a more comprehensive rational heat stress index, such as the ISO 7933 Predicted Heat Strain or equivalent (eg. TWL). While such indices are complex and involve upwards of 30 formulae to arrive at the final result, there are computer programs readily available to perform the calculations. One such program has been developed by Professor Jacques Malchaire, and is available from his website at http://www.md.ucl.ac.be/hytr/Download/PrevHeaten.htm.
Also available for use at this stage is a heat stress risk assessment checklist (see Documentation appendix), which identifies additional hazards that should also be considered at this point.
Have a copy of the Risk Assessment Checklist as an OH available.

## Slide 9: Monitored Parameters for Scenario 1
Dry Bulb = 28.2°C
Globe = 28.9°C
Relative Humidity = 85%
Air Velocity = 0.2 ms-1
Metabolic Load = 165 Wm-2
Posture = Standing
Clothing is a single layer disposable cotton overalls with an insulation factor of 0.8 clo
Acclimatised worker
Notes: <number>
In this situation the results were as follows:
Dry Bulb = 28.2
Globe = 28.9
Relative Humidity = 85%
Air Velocity = 0.2 m/s
Metabolic Load = 165 W/m2
Clothing is single layer cotton long sleeve shirt & trousers. (0.8 clo) The thermal insulation rating for the clothing ensemble being worn can be obtained from ISO standards[i]
Posture is Standing
[i] International Organisation for Standardization (ISO): Ergonomics of the Thermal Environment - Estimation of the Thermal Insulation and Evaporative Resistance of a Clothing Ensemble. ISO 9920. ISO, Geneva (1995).

## Slide 10: Malchaire’s Website http://www.md.ucl.ac.be/hytr/new/en/
Download the HYTR Programs and use the PHS program
Notes: <number>
The Predicted Heat Strain (ISO 7933) PHS program may be downloaded from the above website. Make sure when it is installed that you select the correct language.

## Slide 11: Predicted Heat Strain
Notes: <number>
The figure above illustrates the the use of the Malchaire Predicted Heat Strain (PHS) program and how it appears.

## Slide 12: Predicted Core Temperature Graph
Notes: <number>
This is also corroborated in the view of the core temperature graph which shows an initial climb but then stabilises at approximately 37.2C.

## Slide 13: Scenario 2
A worker is involved in the removal of asbestos lagging from a hot vessel
Task will last approx 2 hours
The task has been undertaken in an encapsulating bubble
Notes: <number>
Scenario 2
In a second scenario a worker is involved in the removal of asbestos lagging from hot pipework, which will last approximately 2 hours. To avoid contamination of the nearby work area the task has been undertaken in an encapsulating bubble. It is obvious that the work environment in this situation is quite hostile as employees are quite distressed.
In such a situation it is not necessary to go through the process of utilising the basic thermal risk assessment as it is obvious there is a problem.

## Slide 14: Monitored Parameters
Dry Bulb = 46.9°C
Globe = 54.3°C
Relative Humidity = 22.6%
Air Velocity = 0.2 ms-1
Metabolic Load = 200 Wm-2
Posture = Standing
Clothing is a single layer disposable cotton overalls with an insulation factor of 0.8 clo
Acclimatised worker
Notes: <number>
Proceeding directly to stage 2 monitoring results are as follows:
Dry Bulb = 46.9
Globe = 54.3
Relative Humidity = 22.6%
Air Velocity = 0.2 m/s
Metabolic Load = 200 W/m2
Posture = Standing
Clothing is a single layer disposable cotton overalls with an insulation factor of 0.8 clo,
Our worker is acclimatised.

## Slide 15: Predicted Core Temperature Graph
Notes: <number>
This is graphically illustrated on this diagram where the core temperature climbs uninterrupted to 39.3 C for the acclimatised worker. This is obviously unacceptable as it will place the individual at a serious risk.

## Slide 16: If a 30 Minute Rest Break is Taken
Notes: <number>
Assume that it has been decided that a 30 minute rest break in an air conditioned room is taken. How does this affect the recovery pattern?

## Slide 17: Predicted Strain
Notes: <number>
The diagram above does show a marked reduction in the core temperature but even after 30 minutes rest in the air-conditioned room the core temperature is still above the WHO 38ºC.
So what should be done?
The rest break should be taken earlier at approximately 45 minutes into the work cycle and could be reduced to 15 minutes.

## Slide 18: Upon Return to Work
Notes: <number>
As we can see in this diagram, it has effectively reduced the strain on the employee. Caution should be exercised however as at this point they have not recovered to their baseline level and if the individual returns to the same work environment there is a potential that they may exceed the limits.

## Slide 19: Scenario 3
If our previous situation is repeated but our asbestos removalists are now taken out of the normal overalls and placed in impervious disposables.
We now have a situation whereby physiological monitoring must be undertaken.
Notes: <number>
If our situation above is repeated but our asbestos removalists are now taken out of the normal overalls and placed in impervious disposables we now have a situation whereby physiological monitoring must be undertaken.

## Slide 20: Physiological Monitoring
Source: University of Wollongong
Notes: <number>

## Slide 21: Physiological Monitoring
Notes: <number>
The figure above gives an example of a time history graph of the heart rate for an asbestos removalist involved in an asbestos strip in conditions outlined in scenario 2 and wearing Tyvek barrier disposable overalls.
Between 1100 and 1200 was spent setting up the task. At 1200 the employee entered the bubble and began wetting down and removing the asbestos. It can be seen that the heart rate begins to climb significantly at 1235 he leaves the bubble, showers and rests in a shaded area. At 1300 he re-enters and exits at 1335, showering and resting. Again his heart rate climbs and is sustained for a significant period.

## Slide 22: Brouha’s Recovery Rate
The worker is allowed to rest and the heart rate is measured from
  30 to 60 seconds (P1),
  90 to 120 seconds (P2), and
  150 to 180 seconds (P3).
Notes: <number>
In Brouha’s method the worker is allowed to rest and the heart rate is measured from 30 to 60 seconds (P1), 90 to 120 seconds (P2), and 150 to 180 seconds (P3). At 180 seconds, the temperature is recorded. The data collection facility of the HS3800 collects the heart rate at 60 second intervals hence this method was modified to suit such that;
P1 = the average of 0 to 60 seconds
P2 = the average of 60 to 120 seconds, and
P3 = the average of 120 to 180 seconds.

## Slide 23: Brouha’s Recovery Rate (cont)
Method was modified to suit the personal monitor (HS3800) such that;
  P1 = the average of 0 to 60 seconds
  P2 = the average of 60 to 120 seconds, and
  P3 = the average of 120 to 180 seconds.

## Slide 24: Heart Rate Recovery Criteria
P3 < 90 bpm situation satisfactory
P3 ≤ 90 & P1 - P3 < 10
  High metabolic load but not significant increase in body temperature
P3 > 90 & P1 - P3 < 10
  Excessive strain, insufficient recovery, hence modification of work patterns is required.
Notes: <number>

## Slide 25: Recovery Rate
Notes: <number>
Figure 3 is a zoomed graph of a rest period taken in order to calculate the recovery rate utilising a modified Brouha’s method[i].
[i] Di Corleto, R., “The Evaluation of heat Stress Indices using Physiological Comparisons in an Alumina Refinery in a Sub Tropical Climate” Masters Thesis Report. Deakin University 1998.

## Slide 26: Recovery Rate Calculations
P1 = 172 bpm, and
P3 = 163 bpm, hence
172 – 163 = 9 bpm,
This indicates the individual, is under excessive strain.
Notes: <number>
In this example our worker had a P1 of 172 bpm and P3 of 163 bpm hence,
172 – 163 = 9 bpm, which indicates the individual, is under excessive strain.
This was also supported by his surrogate core temperature was recorded at 38.5 C.
This individual was obviously under significant stress and the task required modification and addition of controls.

## Slide 27: Other Physiological Parameters
‘Heart Rate Limit = 185 - 0.65A’ (where A = Age in years); or
‘Thermal Heart Rate’ increase is greater than 30 bpm; or
Recovery heart rate at one minute after a peak work effort is greater than 124 bpm; or
Notes: <number>
Excessive heat strain may be marked by one or more of the following measures, and an individual's exposure to heat stress should be discontinued when any of the following occur:
Heart Rate Limit = 185 - 0.65A’ (see ISO 9886), where A = Age in years; or
‘Thermal Heart Rate’ increase is greater than 30 bpm. Consult Documentation for details of ISO 9886[i] (1992) - Evaluation of thermal strain by physiological measurements; or
 Recovery heart rate at one minute after a peak work effort is greater than 124 bpm; Based on the technique developed by Brouha analysis, “..it can be seen that the 99.6F (37.6C) criterion line for oral temperature intersects the upper confidence limit at a P1 value of about 124 bpm. In effect, this says that 95% of the times that one finds a P1 value of 124, the oral temperature will be at or below 99.6 F (37.6C).
Body core temperature is greater than 38.5oC (101.3oF) for medically selected and acclimatised personnel; or greater than 38oC (100.4oF) in unselected, unacclimatised workers.
Work undertaken by Donoghue[ii] et al has indicated an increased risk to heat exhaustion at when SG levels exceed 1.015
[i] International Organization for Standardization (ISO): Ergonomics - Evaluation of Thermal Strain by Physiological Measurements. ISO 9886. Geneva 1992(E).
[1] Donoghue, A. M., Sinclair, M. J., Bates, G. P., “Heat Exhaustion in a deep underground metalliferous mine.” Occ & Env Medicine, March 2000, Vol 57, No 3, pp 165-174

## Slide 28: Other Physiological Parameters (cont)
Body core temperature is
   38.5oC (101.3oF) for medically selected and acclimatised personnel; or
   38oC (100.4oF) in unselected, unacclimatised workers;
Specific Gravity of Urine >1.015

## Slide 29: What Do You Think?
Are these approaches acceptable?

## Slide 30: Case Study 11
Suspected Heat Stroke Case
Source: South African Department of Mines
News Flash – February 2002

## Slide 31: The Situation
Two operators diamond drilling in an underground mine in South Africa
The assistant drill operator was busy helping the drill operator when he exhibited symptoms of shivering & disorientation
The drill operator walked his assistant to the main return airway
The drill operator left him alone to get help

## Slide 32: Drill Working Underground
Notes: This is a typical drill used in the underground metaliferrous mining industry. There is no indication in the report if this was the type of equipment being used.
<number>

## Slide 33: The Situation (cont)
When the supervisor arrived he decided to arrange transport to the surface and left to make those arrangements
When the drill operator started to depart the ill person became aggressive & attacked the drill operator
The ill person was subdued, tied to a stretcher & transported to the surface and then to hospital
He died at hospital

## Slide 34: Inspectors Findings
First aid not administered to person
No paramedic assistance was provided to person while being transported to hospital
Area had been temporarily abandoned due to rock fall and operations had just recommenced in area

## Slide 35: Inspectors Findings (cont)
No risk assessment conducted in work area prior to commencing work
Wet bulb was within 10C of legal limit (32.5oC)
Dry bulb was within 20C of legal limit (37oC)
Deceased worker was an inexperienced employee

## Slide 36: Inspectors Recommendations
Conduct a risk assessment to determine if employees are trained to identify the symptoms and treatment of heat disorders
An adjusted monitoring programme of thermal conditions should be implemented as prevailing conditions are close to the upper limits

## Slide 37: What Do You Think?
Is this a case of heat stroke?
Where did the system fail?
Are the inspectors recommendations adequate?

## Slide 38: Case Study 12
Suspected Heat Stroke Case
Source: South African Department of Mines
News Flash – May 2007

## Slide 39: The Situation
An employee was found to be missing at roll call after day shift prior to a blast in an underground mine in South Africa
Search parties located the now deceased missing person at 10.00 am the following day
Deceased person located in a temporarily abandoned area of the mine

## Slide 40: Investigation Findings
Deceased person was a drill operator but as he could not locate his rock drill machine on that morning did not carryout any drilling activities
Was working alone with no assistants
Had been seen by several mine personnel at various locations looking for his drill machine location

## Slide 41: Investigation Findings (cont)
Last time he was seen was at 2.00 pm on the day he went missing
Area where he was eventually found was abandoned in late 2006
A temporary barricade of wooden planks & plastic curtaining was erected to prevent hot air entering the workings above and to also restrict entry of persons to the abandoned area

## Slide 42: Investigation Findings (cont)
Location where the deceased was found had a temperature of >400C and there was no ventilation
No harmful gases could be detected after the event
Deceased worked was experienced (25 years) but had not been working in the section for 18 months

## Slide 43: Recommendations
Standards for barriers to be improved
Control of working gang to be improved: to include discipline, communication, reporting system

## Slide 44: What Do You Think?
How did this tragedy happen?
Are the recommendations adequate?
How could this situation been avoided?

## Slide 45: Case Study 13
Collapse of Air Force Flight Surgeon
Source: Thomas E Kupferer
(Reproduced with permission)

## Slide 46: The Situation
Air Force flight surgeon collapsed while responding to an emergency out on the flight line
Subsequent investigation established that this person had been resident in the country (S E Asian tropical climate) for 6 months

## Slide 47: The Situation (cont)
Flight surgeon had worked in an air conditioned medical facility
He had taken his meals, slept and passed his spare time in air conditioned quarters

## Slide 48: What Do You Think?
Why did the flight surgeon collapse when performing only mildly demanding tasks on the flight line?

## Slide 49: Case Study 14
Frost Bite & Frost Nip experienced by Soldiers
Source: Penny Goodstein
(Reproduced with permission)

## Slide 50: The Situation
Soldiers exercising and working in cold climate
As a result of above activities some soldiers removed their balaclavas and/or gloves due to becoming too hot
As a result of this action some of the soldiers experienced frost nip or frost bite

## Slide 51: What Do You Think?
Could this situation have been prevented?
If so what steps could have been taken to do so?

## Slide 52: Calculation & Assessment Exercises
Break up into groups and attempt the various exercises
Seek guidance from lecturers (if required)

## Slide 53: Calculation Exercises
Heat Stress – 5 calculations
  Relative humidity
  CET
  P4SR
  WBGT
  HSI
Cold Stress – 3 calculations
  WCI
  Effective Chilling Temperature
  Work-warm up schedule

## Slide 54: Student Assessment Exercises
Hot environments – coke ovens refractory replacement
Cold environments – hiking trip in the alps
Risk assessment – Fitter (mechanic) working on a dozer
Thermal comfort – shopping centre

## Slide 55: Empty Coke Oven
Source: BlueScope Steel-reproduced with permission
Notes: Raw coal is converted to coke by heating it to high temperatures in the absence of air in individual coke ovens in a battery of ovens.
<number>

## Slide 56: Exercise 1 - Coke Ovens Battery
Source: BlueScope Steel-reproduced with permission
Notes: The coke oven is a refractory brick lined cavity measuring approximately 17 m long, 5 m high and 450mm wide. The oven is heated from either side by gas fired heating chambers which are heated to approximately 1200°C to allow the conversion of coal to coke. Typically there are approximately 50 ovens in a modern battery
<number>

## Slide 57: Refractory Worker in Typical PPE
Source: BlueScope Steel-reproduced with permission
Notes: Over time damage occurs to the refractory linings of the ovens and repairs need to be undertaken to prolong the efficient production life of the batteries.
The process involves the oven to be repaired being taken out of service and while the oven is still red hot, refractory brickwork walls and floors are progressively removed by hand, working inwards to a distance of approximately 5 metres. Once all the damaged brickwork is removed the oven is rebricked and returned to service
This and the following two slides show the restricted area that operators have to work. Note the PPE worn by the person in this slide
<number>

## Slide 58: Hot Brickwork Inside an Oven
Source: BlueScope Steel-reproduced with permission
Notes: Note the cage to stop falling hot bricks
<number>

## Slide 59: Refractory Brickwork to be Removed
Source: BlueScope Steel-reproduced with permission
Notes: Note all the rubble in the bottom of the oven that must be removed.
<number>

## Slide 60: Group Exercise
Read the scenario and answer the question:
What investigations & recommendations would you suggest?

## Slide 61: Group Exercise (cont)
Read the scenario’s for exercises 2 , 3 & 4 and answer the questions
Note: Some questions will involve calculations

## Slide 62: Review of Today’s Learning Outcomes
Case Studies (risk assessment)
  Discuss various case studies to highlight various risk assessment approaches
Student Exercises
  Undertake a number of exercises to reinforce the learning's contained in the lectures