## Slide 1
M503
Noise - Measurement & Its Effects
Day 1
Notes: <number>

## Slide 2: Course Aims
To provide participants with an understanding of
  Appreciation of nature of noise hazards in the workplace and the effects of noise on people
  Identification and risk assessment of noise
  Understanding of hearing and risks of hearing loss
  Significance of data in relation to exposure standards
  Possible noise control mechanisms

## Slide 3: Course Learning Outcomes
Participants will be able to:
  Describe the consequences to health and well being of excessive noise exposure;
  Understand the measurement (including dosimetry) of noise in relation to current standards;
  Conduct surveys in the workplace to assess risks from noise;

## Slide 4: Course Learning Outcomes (cont)
  Advise on the need and means of control, including personal protective equipment;
  Appreciate and advise on environmental noise assessment and concerns; and
  Understand current standards and good practice in these fields.

## Slide 5: Topics to be Discussed
Sound physical properties and human effect
Risk Assessment and Noise Surveys
Noise Controls
Education and Training requirements
Audiometry and Hearing Disorders
Assessment
Environmental Noise
Presentation of results

## Slide 6: Today’s Learning Outcomes
Understand Sound
  Physics, descriptors and propagation
  Human response
Be familiar with Risk Assessment and Noise Surveys Instrumentation

## Slide 7: Work Groups
Each participant will be assigned a work group for the duration of the course
The work groups are expected to work as a team when evaluating cases studies and undertaking practical sessions

## Slide 8: Discussion Topics
Sound Propagation
Properties of Sound
Sound Pressure, Power, and Intensity
Levels and Decibels
The Decibel Scale and Use of Levels
Common Sound Levels

## Slide 9: Discussion Topics (cont)
Quantifying Sound Levels
Decibel Addition, Subtraction, and Averaging
Directivity of Sound Propagation
Frequency Characteristics of Sound
Weighted Sound Levels

## Slide 10: Discussion Topics (cont)
The Human Audible Range of Hearing and Loudness
Relationship between Sound Pressure Level and Sound Power level
Time-Varying Noise Sources
The Ear and its Response to Sound

## Slide 11: 2. INTRODUCTION TO SOUND

## Slide 12: Sound Propagation
Sound is a fluctuation in pressure above and below the ambient pressure of a medium that has elasticity and viscosity.
The medium may be a solid, liquid, or gas.
Sound is also defined as the auditory sensation evoked by these oscillations in pressure

## Slide 13: Pound Propagation (cont)
For workplace noise, air is the medium.
The word “noise” is often used to describe unwanted sound, but it is also often used interchangeably with sound as in “sound source” or “noise source”.

## Slide 14: Sound Propagation (cont)
A vibrating tuning fork sets air molecules into motion, which results in positive (compression) and negative (rarefaction) excursions around atmospheric pressure.

## Slide 15: Sound Propagation (cont)
What other cause mechanisms are there?
  Any vibrating machine part
  Vibrating vocal chords
  Pulsating air pressure at an escape point
  Vibrating guitar string

## Slide 16: Sound Propagation (cont)
Type of wave?
Longitudinal or
Transverse

## Slide 17: Properties of Sound
Amplitude
Period
Frequency
Speed
Wavelength

## Slide 18: Properties of Sound (cont)
Amplitude
For a simple sine wave it is easy

## Slide 19: Properties of Sound (cont)
Period (T)
is the time it takes to complete one full cycle
Frequency (f)
is the number of times per second a complete
wave passes a point. The number of cycles per
second is termed Hertz (Hz).
The period and the frequency are simply related
by the following equation
T = 1/f (seconds)

## Slide 20: Properties of Sound (cont)
Speed (c)
of sound in air is governed by density and air pressure which in turn relates to temperature and elevation above sea level.
The speed of sound in air is approximately 343 m/s. Sound travels about 1 kilometre in 3 seconds.

## Slide 21: Properties of Sound (cont)
Wavelength (λ)
is the length of one complete cycle, and is
measured in metres (m).
It is related to the frequency (f) and speed of
sound (c) by:
Wavelength (λ) = c/f metres

## Slide 22: Properties of Sound (cont)
Wavelength in air at standard atmospheric conditions
Frequency | Wavelength
100 Hz | 3.44 m
1000 Hz | 0.34 m
1,000 Hz | 34.4 mm
10,000 Hz | 3.4mm

## Slide 23: Properties of Sound (cont)
There is more than one way to measure Amplitude:

## Slide 24: Properties of Sound (cont)
There is more than one way to measure
Amplitude:
The peak value occurs only for a very short time
period and so may not be very closely related to
the subjective impression of the sound.
While an average may be more appropriate, due to
the symmetrical shape of the pressure wave the
times the amplitude is positive equals the times
the amplitude is negative and so the resultant
‘average’ is zero

## Slide 25: Properties of Sound (cont)
We need an "average" which takes into account the magnitude of the sound pressure fluctuations but not their direction (positive and negative).
The one most commonly used is the root-mean square (or RMS) sound pressure.

## Slide 26: Properties of Sound (cont)

## Slide 27: Properties of Sound (cont)
SLMs have electronic circuits which convert the microphone signal to an RMS sound pressure.
The RMS pressure is used because it can be related to the average intensity of the sound and to the loudness of the sound. For a pure (simple sine wave) tone it can be shown that the peak pressure and the RMS pressure are simply related:

## Slide 28: Properties of Sound (cont)
pRMS = ppeak = 0.707 x ppeak
√2
For more complex signals, there is no simple relationship between the two.

## Slide 29: Properties of Sound (cont)
Peak is however important to measure
In particular for loud impulsive noise, such as gunfire, explosions or punch presses.
The Crest Factor is the ratio of the peak amplitude of a waveform to the RMS value.
Short intense impulses will have high values of crest factor.

## Slide 30: Poperties of Sound (cont)
Power
Intensity
Pressure

## Slide 31: Power
  Sound power is defined as the total sound energy generated by the source per unit of time.
  Sound power is expressed in units of watts (W).

## Slide 32: Power (cont)
  It is important to keep in mind that for all practical situations the sound power of a source output is constant regardless of its location (i.e. inside versus outside).
  Conversely, the sound intensity and sound pressure will change as a function of the environment in which it is located.

## Slide 33: Intensity
  Defined as sound power per unit area
  (Watts/m2)
  Sound intensity is a vector quantity

## Slide 34: Intensity (cont)
  A point sound source will radiate sound power evenly in all directions, assuming there are no reflective surfaces present. As the power spreads spherically from its origin, the surface area in increases and so the power per unit area decreases.
  The total power remains the same, but the enclosing area is increasing, which results in a decrease in the sound intensity. This is known as the inverse-square law.

## Slide 35: Power and Intensity

## Slide 36: Intensity
  Surface area of sphere = 4 r 2
  At 1 metre from source power will be spread over a sphere whose surface area is 4 x1
  At 2 metres this will be 4 x 4 ie 4 times as large and thus the Intensity will be one quarter.

## Slide 37: Intensity (cont)
  At 3 metres the surface will be 32 = 9 times bigger, therefore as the distance from source spreads the energy per unit area diminishes.
  Sound intensity is a vector quantity

## Slide 38: Properties of Sound (cont)
Pressure
  The variation of pressure superimposed on the atmospheric pressure within the sonic range is called the sound pressure.

## Slide 39: Pressure
  Sound pressure is expressed as force per unit area, and the unit is the Pascal (Pa).
  Keep in mind sound pressure is the “effect” of a disturbance. The actual “cause” of the disturbance, and the resulting reaction effect, is due to the driving force or sound power

## Slide 40
What are these Alexander Graham Bells anyway ?
decibel = 20log ( p /po )

## Slide 41: Levels and Decibels
The Decibel Scale and Use of Levels
  Level is used as understood in the term “water level” i.e. height relative to something else, say the riverbank.
  The softest sounds heard about 0.000,000,000,001 watts/m2
  Saturn rocket at lift-off is greater than 100,000,000 watts/m2

## Slide 42: Levels and Decibels (cont)
The Decibel Scale and Use of Levels
  This kind of huge range is not uncommon and the solution is similar, squeeze it down by only looking at the indices. i.e. Use logarithms
  The unit is the Bel
  But that is big so we use 1/10 of a Bel or a decibel dB

## Slide 43: Levels and Decibels (cont)
In air, the expression for each acoustical property is:
Sound Intensity Level:
Sound Power Level:

## Slide 44: Levels and Decibels (cont)
Sound Pressure Level:
The “L” in each expression stands for “Level,” and the I, W, and p terms
represent intensity, power, and pressure, respectively

## Slide 45: Levels and Decibels (cont)
The reference quantities are related to human hearing as they nominally correspond to the threshold of hearing at 1000 Hz:
  Reference intensity (Iref) = 10-12 w/m2
  Reference power (Wref) = 10-12 w
  Reference pressure (pref) = 2 x 10-5 N/m2, or 20 µPa

## Slide 46: Levels and Decibels (cont)
W, I & p are mathematically related
and p2 is inversely proportional to r2 (

## Slide 47
Common Sound Levels

## Slide 48: Quantifying Sound Levels
  The study of human perception to sound is called Psychoacoustics.
  Perception of relative changes in sound intensity.
  The ear does not respond linearly to changes in sound level

## Slide 49: Quantifying Sound Levels
1 dB change barely perceptible to person with excellent hearing
3 dB difference would be just perceptible to the average listener
5 dB change clearly noticeable
10 dB increase typically perceived as twice as loud.

## Slide 50: Decibel Addition, Subtraction, and Averaging
Addition is a simple sum
Adding; 89.0dB plus 85.0dB plus 90.0dB
10log [ 1089/10 + 1085/10 + 1090/10] = 92 dB

## Slide 51: Decibel Addition, by Table
Numerical difference between levels LP1 and LP2 (dB) | Amount to be added to the higher of LP1 or LP2 (dB)*
0 | 3.0
1 | 2.5
2 | 2.1
3 | 1.8
4 | 1.5
5 | 1.2
6 | 1.0
7 | 0.8
8 | 0.6
9 | 0.5
10 | 0.4
greater than10 | 0.0 for all practical purposes

## Slide 52: Decibel Addition, by Table
Example – Adding; 89.0dB 85.0dB, and 90.0dB.
Step 1: Ordering these from low to high
85.0, 89.0, and 90.0
Step 2: Difference between 85 and 89 is 4 dB. From column 2 in the table the value to add to the higher level is 1.5 dB
so the total for these two levels is 89 + 1.5 = 90.5 dB.

## Slide 53: Decibel Addition, by Table
Step 3: Now combine the 90.5 dB with the 90 dB.
Difference is 0.5 dB so from the table the amount to be added falls between 3 and 2.5. Interpolating between these the amount to be added is 2.8
So 90.5 + 2.5 gives a total of 93.3 dB
This is the total sound level for the three sounds.

## Slide 54: Overall Sound Level from Frequency Spectrum
Frequency, (Hz) | 63 | 125 | 250 | 500 | 1000 | 2000 | 4000
SPL (dB re 20µPa) | 95 | 72 | 85 | 80 | 86 | 82 | 79
Rearranging in ascending order | 72 | 79 | 80 | 82 | 85 | 86 | 95
Difference |  | 7 | 0.2 | 1 | 0.5 | 2 | 4.9
Add |  | 0.8 | 3 | 2.5 | 2.5 | 2.1 | 1.2
Cum. level dB |  | 79.8 | 83 | 85.5 | 88 | 90.1 | 96.2

## Slide 55: Decibel Addition simplified table
Difference in levels | Amount to add to the higher level
0, 1 | +3
2,3 | +2
4,5,6,7,8,9 | +1
10 and greater | 0
This can be used for quick calculations when all that is needed is a general understanding of the overall level

## Slide 56: Subtraction of sound levels
This can be done using the equation
Subtracting; 85 from 90dB.
10log [ 1090/10 - 1085/10] = 88.3dB
Alternatively the table for addition of dB can be used in an iterative manner

## Slide 57: Decibel Subtraction using Table
Example – 96.0 dB minus 94.0dB.
  Step 1: 94 dB plus X dB has to combine for a total of 96 dB, ie the total noise level becomes 2 dB greater.
  Step 2: From Table, if the difference in levels was 2 dB then the amount to add is +2.1 dB. So if X was 92 db then 94 plus 92 would lead to a total of 96 dB.

## Slide 58: Decibel Subtraction by Interpolating Table
  Step 3: therefore X must be 92 as no other number will suit.
  A value for X less than 92 would lead to a
  total less than 96 dB. Similarly a value for X
  greater than 92 would lead to a total less
  than 96 dB.

## Slide 59: The equation to determine the average sound level for a number of measurements of a source is:
Averaging; 81, 86, 82 and 84dB.
10log 1/4[ 1081/10 + 1086/10 + 1082/10 + 1084/10] = 83.7dB

## Slide 60: Directivity of Sound Propagation

## Slide 61: Directivity of Sound Propagation
  Comparison of Directivity Factor and Directivity Index
Source Location | Directivity Factor | Directivity Index (dB)
Suspended in space | 1 | 0
On floor of large room | 2 | 3
At intersection of one wall and floor | 4 | 6
In the corner of a room | 8 | 9

## Slide 62: Frequency Characteristics of Sound
Workplace sounds are not simple sine
waves
They comprise of a broad spectrum of
frequencies, which can to be divided into
smaller bandwidths to assist the analysis
for risk assessment, noise control,
evaluation of hearing protection etc.

## Slide 63: Frequency Characteristics of Sound
For this purpose, the sound level meter
may contain a filter set to measure the
select bandwidths of concern or a
frequency analyser can be used. The
most common bandwidths are
  octave bands
  third octave bands

## Slide 64: Frequency Characteristics of Sound
Due to the human ears response Octaves
are also not linear
Each octave centre frequency is twice the
frequency of the one below it.
f2 = 2 f1
What does this mean?

## Slide 66: Weighted Sound Levels
Microphones and human ears have a different frequency response.
Several weighting networks (or frequency fliters) were designed to make the SLM respond to frequency like our ear.
The accepted frequency for occupational and environmental noise is the A weighting.
Common weightings are A, C & Z and linear

## Slide 67: Weighted Sound Levels
Frequency, Hz | A weighting | C weighting | Z weighting
16 | -56.7 | -8.5 | 
31.5 | -39.4 | -3.0 | 
63 | -26.2 | -0.8 | 
125 | -16.1 | -0.2 | 
250 | - 8.6 | -0.0 | Flat
500 | - 3.2 | -0.0 | from10Hz
1000 | 0 | 0 | to 20kHz
2000 | + 1.2 | -0.2 | 
4000 | + 1.0 | -0.8 | 
8000 | - 1.1 | -3.0 | 
16000 | - 6.6 | -8.5 | 

## Slide 68: Weighted Sound Levels

## Slide 69: The Human Audible Range of Hearing & Loudness
The nominal range in human hearing is 20 Hz up to 20,000 Hz.
However, it is a relatively small percentage of the population that can truly detect sounds at the outer edges of this range.
The threshold of hearing is that SPL that is just barely detected by a listener. Figure 2.9 depicts the equal-loudness contours for free-field conditions, with the minimum audible field (MAF), shown by the dashed line.

## Slide 71: The Human Audible Range of Hearing & Loudness
Human sensitivity is greatest from 2,000 to 5,000 Hz.
MAF the response in this most sensitive range is close to 0 dB, which is 20 µPa.
This is the principal reason 20 µPa has been designated the international reference pressure for determining SPL.

## Slide 72: The Human Audible Range of Hearing & Loudness
The nominal range in human hearing is 20 Hz up to 20,000 Hz.
Sound at higher frequencies is called Ultrasound
Sound at lower frequencies is called Infrasound

## Slide 73: Relationship Between Sound Pressure Level and Sound Power Level
SPL and PWL are related by the equation:
Lp = Lw + k
Where,
Lp is the sound pressure level (SPL) in dB,
Lw is the sound power level (PWL) in dB, and
k is a factor, dependent upon the acoustics of the environment, directivity of the source, and distance from the source.

## Slide 74: Time-Varying Noise Sources (cont)
Compressors, fans, electric motors etc generally produce sounds that are continuous or steady-state.
A steady-state sound remains relatively constant in time, varying by less than +/- 3 dB.
But what if they cycle off and on?

## Slide 75: Time-Varying Noise Sources (cont)
Sources with levels that fluctuate more than ±3 dB are generally classified as variable noise sources
Some have long quiet times then a loud part for example a brake press.
Which part of the noise should we measure?

## Slide 76: Time-Varying Noise Sources (cont)
Which part of the noise should we measure?

## Slide 77: Time-Varying Noise Sources (cont)
Another type of time varying noise is that produced as an impact or impulse.
An impact sound can be generated by the solid collision between two objects, such as hammering, dropped objects, a door slamming shut, metal-to-metal impacts, etc or by explosions such as gun fire or explosive tools.
Impulse sound is defined as an event having an exponential rise time constant of 35 milliseconds, and an asymmetric decay time constant of 1.5 seconds.

## Slide 78: Time-Varying Noise Sources (cont)
It is important to note the terms impulse and impact sound are commonly used interchangeably, despite the fact they have distinct characteristics.
These short-term events are also called transient sounds. However, for occupational noise assessment and from a practical standpoint, these terms may be considered the same.

## Slide 79
Human Response to Sound
The Structure and Function of the Ear
Outer (External) Ear
Middle Ear
Inner Ear
Central Auditory Pathway
Normal Hearing: Propagation of Sound through the Ear
Pitch and Loudness Perception
Audible Range

## Slide 80
Human Response to Sound (cont)
The Ear and its Response to Sound
Hearing is a critical human sense
Allows audible communication
with each other and our environment.

## Slide 81
Human Response to Sound (cont)
Sound adds richness to life:
subtleties of language and humour, the emotions instilled by music, or connection felt to our surroundings.
Unique and intricate anatomical and physiological design of the ear allows for the presence, clarity, and quality of sound to be experienced.
Incredibly complex, the auditory system is delicate, yet rugged; vulnerable yet remarkably resilient.

## Slide 82
Section through the ear

## Slide 83
Outer (External) Ear

## Slide 84
Outer (External) Ear
  Pinna:
  Collects sound waves and funnels them in
  two ears are better than one.
  Auditory Meatus or ear canal:
  Most illustrations depict the ear canal as being straight, it actually curved. The canal is a closed end tube and has resonance properties which amplify sounds between 2000 – 5000 Hz, an important feature for allowing soft sounds to be audible. The ear canal is approximately 24 mm (1 inch) in length.

## Slide 85
Outer (External) Ear
  Tympanic Membrane or Eardrum
  The eardrum is the terminal point of the outer ear.
  It seals the ear canal tube and connects at the umbo to the middle ear
  It is comprised of three layers of semi-transparent tissue, similar to skin, which grow continuously. The tympanic membrane must be intact for the normal transduction of sound.

## Slide 86
Outer (External) Ear
Sound is channeled into the ear and enhanced by characteristics of the ear canal.

## Slide 87
Outer (External) Ear
Video otoscope photo of normal eardrum looking down the ear canal to the transparent tympanic membrane.

## Slide 88
Middle Ear
The middle ear is the air-filled space between the eardrum and the bony inner ear.
It contains the
ossicles, muscles and the Eustachian tube

## Slide 89
Middle Ear
Ossicles
The three smallest bones in the human body, the malleus (hammer), incus (anvil), and stapes (stirrup) join to form the ossicular chain, suspended in the middle ear space by ligaments and muscles.
The malleus is attached to the tympanic membrane at the umbo.
The stapes footplate rests in the oval window of the cochlea in the inner ear at the other end.

## Slide 90
Middle Ear
Ossicles
The purpose of this delicate system is to overcome the impedance mismatch between the air and the fluid in the inner ear.
The orientation of the ossicular chain in combination with the surface area differential, creates a natural amplification of 15:1

## Slide 91
Middle Ear
Muscles: two tiny muscles
the tensor tympani muscle attaches to the handle of the malleus and
the stapedius muscle attaches to the neck of the stapes.
Contraction of these muscles pulls the malleus inward and the stapes away from the oval window. This temporarily changes the transmission path.

## Slide 92
Middle Ear
Muscles:
The acoustic or aural reflex refers to the immediate contraction of these muscles in response to a loud sound. It is more likely to be effective in younger than in older ears.
The reflex does not occur quickly enough to add significant protection from sudden burst of sound. It can reduce vibratory stimulation for sustained sound.
Don’t rely on it as it wont prevent loss of hearing due to long term exposure

## Slide 93
Middle Ear
Eustachian tube:
The Eustachian tube is an open tube, about 45 mm (1.75 inches) long, passing downward and inward from the middle ear space to the nasopharynx.
Its primary function is to equalize pressure differences between the outer and middle ear spaces; eg when in an airplane or diving.
Blockage of the tube is painful and can lead to burst eardrums

## Slide 94
Middle Ear
Close-up drawing
of the middle ear showing the
malleus,
incus and
stapes
connecting the
tympanic membrane to the inner ear

## Slide 95
Inner Ear

## Slide 96
Inner Ear

## Slide 97
Inner Ear

## Slide 98
Inner Ear
This electron micrograph shows the organ of Corti within the inner ear

## Slide 99
Inner Ear

## Slide 100
The supporting cells of the organ of Corti hold outer and inner hair cells in position.
There are approximately 12,000 to 20,000 outer hair cells organized in three rows.
On top of each outer hair cell are more than 100 stereocilia, arranged in a “W” shaped pattern, These are aligned from tallest to shortest: the shorter stereocilia are connected to the taller ones by tip-lengths, made up of protein substances. Tip-lengths also connect across bundles of stereocilia.
Outer Hair Cells

## Slide 101
The direction of stereocilia deflection, from the shortest to the tallest, or from the tallest to the shortest, is caused by either an excitatory or inhibitory response respectively.
The shearing of the stereocilia corresponds with the lengthening and shortening of the outer hair cells, an ability unique to these cells.
Outer Hair Cells

## Slide 102
Scanning electron microscopy shows the stair-step pattern of stereocilia.
Fluorescence microscopy image.
Outer Hair Cells

## Slide 103
Inner hair cells are arranged in one row on the spiral lamina.
There are approximately 3500 inner hair cells in each ear. They also have stereocilia, which are arranged in a “U” shaped pattern from short to tall.
Inner Hair Cells

## Slide 104
The primary difference between inner and outer hair cells is the motor function:
Unlike outer hair cells, inner hair cells are purely sensory and are not capable of movement.
Inner Hair Cells

## Slide 105
Central Auditory Pathway
Once sound passes through the peripheral auditory structures it has changed from vibratory energy to electrical stimulation and moves through the brainstem to the primary auditory cortex located on the temporal lobe of the brain.

## Slide 106
Central Auditory Pathway
Referred to as the central auditory pathway, the complex system of nerve fibres and synapses must be intact to make sound meaningful.
The central auditory pathway enables fine distinctions in timing which aid in sound localization and sophisticated perceptions of sound quality.

## Slide 107
Normal Hearing: Propagation of Sound through the Ear
Acoustical energy or sound waves set the tympanic membrane into vibration synchronous to the sound pressure
The eardrum responds and the acoustic energy is transduced to mechanical energy as the vibration is transmitted by the movement of the eardrum and the ossicular chain.
At the stapes footplate, energy is propagated from the air in the middle ear to the fluid contained in the chambers of the inner ear.

## Slide 108
Normal Hearing: Propagation of Sound through the Ear
In the cochlear chambers, as the oval window is pushed in, the perilymph in the scala vestibuli is displaced inward, sending a travelling wave, through the helicotrema into the scala tympani.
The movement of the fluid causes the membranous walls of the scala media, which houses the organ of Corti, to move as well.

## Slide 109
Normal Hearing: Propagation of Sound through the Ear
A schematic representation:
As the stapes footplate moves inward, the fluid in the inner ear is displaced creating the basilar membrane to move in a wave-like motion

## Slide 110
Normal Hearing: Propagation of Sound through the Ear (cont)
The mechanical motion of the fluid and membrane movement causes the stereocilia on top of the outer hair cells to deflect. This deflection opens a “trap door” and allows a chemical exchange inside the hair cells.
The depolarization of the hair cells causes the release of neurotransmitters at the base of the hair cells.
This chemical change creates an electrical signal that is sent to the auditory cortex, thus the energy is now biochemical.

## Slide 111
Normal Hearing: Propagation of Sound through
the Ear (cont)
This chemical change creates an electrical signal that is sent to the auditory cortex, thus the transmission is now biochemical.
Electrical difference endolymph to perilymph
Potassium flow between the cochlear fluids enhances sensitivity to minute pressure changes.

## Slide 112
Normal Hearing: Propagation of Sound through
the Ear (cont)
Active process of the outer hair cells, called the “silent cochlear amplifier” or “cochlear amplifier”
Enables fine distinctions between frequencies and process them separately, frequency selectivity, very soft sounds become audible.

## Slide 113
Normal Hearing: Propagation of Sound
through the Ear (cont)
The process also creates an energy flow from the cochlea outwards to the outer ear -called an otoacoustic emission (OAE).
OAEs are measured as acoustic energy in the outer ear canal. They are an important tool in clinical evaluation of hearing disorders.

## Slide 114
Pitch and Loudness Perception
Pitch is determined by the position on the basilar membrane of its maximum deflection in response to sound. The basilar membrane, (and in fact the auditory pathway) is “tonotopically” organized.
Like the keys on a piano, there is a progression from low pitch to high pitch from the apical end to the basal end. So, if the maximum deflection of the basilar membrane occurs in basal end, a high pitch tone is perceived.

## Slide 115
Pitch and Loudness Perception
The point at which the traveling wave peaks corresponds to the frequency of the sound.

## Slide 116
Pitch and Loudness Perception
The loudness of the sound is determined by the amplitude, or height of the wave-like motion of the basilar membrane.
The louder the sound, the greater is the mechanical vibration and movement of the basilar membrane, which increases both the number of hair cells that fire and the rate at which they fire.

## Slide 117
Pitch and Loudness Perception
The brain recognizes the pitch and the loudness of the sound by the place and the rate of the hair cell stimulation.
By measuring hearing sensitivity of various frequencies, the function of the ear can be assessed – audiometry. This is valuable for diagnosing ear pathologies from identifiable patterns of audiograms

## Slide 118
Audible Range
Pitch/Frequency
Human hearing ranges in frequency from approximately 20 Hz to 20,000 Hz
Hearing is most sensitive to the frequencies present in human speech, approximately 400 Hz – 5000 Hz.

## Slide 119
Vowel sounds tend to be lower in pitch while most consonant sounds tend to be higher in pitch.
The ability to understand speech requires the ability to discriminate between subtle differences in frequency
Audible Range

## Slide 120
Audible Range
Loudness/Intensity
The ear is very sensitive to changes in pressure, meaning it responds to an incredible range of intensities. The threshold of human hearing is equivalent to an intensity of 10-12 watts/m2.
This means the ear can detect a pressure change of less than one ten billionth of standard atmospheric pressure. On the other extreme, the threshold of pain is 1013 watts/m2 which is equivalent to 130 dB.

## Slide 121
Audible Range
Loudness/Intensity
The dynamic range of hearing, from barely perceptible to painful is so large due to the unique anatomical and physiological properties of the ear, which amplify extremely soft sounds as well as provides some inherent protective mechanisms against extremely loud sounds.

## Slide 122
3. RISK ASSESSMENT AND NOISE SURVEYS
  Occupational Noise Management
  Risk Assessment
  Exposure Limits for Noise
  Acoustical instrumentation
  Acoustic parameters and Measurement
  Assessment Surveys

## Slide 123
Occupational Noise Management
Noise and sound surround us - impact on an individual in an occupational environment depends on many factors.
The risk of excess exposure and the resultant adverse outcomes need to be controlled or managed to an acceptable level
The goal of legislation, regulations, codes etc, is to minimise the incidence of hearing loss or other problems caused by excessive noise.

## Slide 124
Occupational Noise Management (cont)
The mantra for the control of any occupational hazard is:
  Identify the Hazard
  Assess the Risk
  Control the Hazard or Exposure

## Slide 125
Occupational Noise Management (cont)
The elements of a noise management
programme include:
● Assess the risks to your employees from noise at work;
● Take action to reduce the noise exposure that produces those risks;
● Provide your employees with hearing protection if you cannot reduce the noise exposure enough using other methods;

## Slide 126
Occupational Noise Management (cont)
● Make sure the legal limits on noise exposure are not exceeded;
● Provide employees with information, instruction and training;
● Carry out health surveillance where there is a risk to health

## Slide 127
Exposure Levels Legislation for Noise
What is a “safe” level?
There is no simple answer as to what constitutes a “safe” noise exposure limit.
The answer is concealed in the intricate and diverse variables associated with an individual’s susceptibility to noise and with the characteristics and magnitude of the noise exposure.

## Slide 128
Exposure Levels and Legislation for Noise
How is exposure measured?
The A-weighted sound level is used in standards and regulations since it provides a single-number value (simple and fast) and it correlates well with hearing-damage risk due to long-term noise exposure.
The hearing damage risk from short impulsive noise like explosives or impacts is assessed in terms of the Peak noise level in dBC.

## Slide 129
Exposure Levels Legislation for Noise
What is a “safe” level? ------ Is it 85dBA?
In 1970s ISO and NIOSH estimates indicated,
10-15% of workers at risk for material
impairment if exposed to 8-hour average of 85
dBA over a 40-year working lifetime.
Material impairment was 25dB at 500, 1000,
and 2000 Hz.
But at that time the commonly used level was
90dBA

## Slide 130
Exposure Levels (cont)
In 1990, ISO 1999 used a different formula and put the excess risk for NIHL at 6% for workers exposed to 85 dBA on a daily basis
Further analysis of the original research, included non-linear effects of noise exposure, as well as alternative impairment formulae.
1997 NIOSH concludes the excess risk is 8% for workers with a noise exposure of 85 dBA over a 40-year working lifetime.

## Slide 131
Exposure Levels (cont)
From most studies, recommendations when hearing conservation measures need to be implemented are:
a noise exposure criteria of 85 dBA for the 8-hour workday noise exposure
AND
at no time during the day should the peak level exceed 140 dBC.
These are the criteria in national legislation or guidelines in most non EU countries

## Slide 132
Exposure Levels (cont)
In 2003 the European Union passed the directive [2003/10/EC of the European parliament and of the council] on the minimum health and safety requirements regarding the exposure of workers to the risks arising from physical agents (noise).
This directive included a staged approach with a lower and an upper action level and an exposure limit.

## Slide 133
Exposure Levels (cont) - EU Directive
Lower exposure action values:
Average exposure of 80 dB;
Peak sound pressure of 135 dB;
Upper exposure action values:
Average exposure of 85 dB;
Peak sound pressure of 137 dB.
How is exposure measured?
Averaged over a working day or week; and
Maximum noise (peak sound pressure)

## Slide 134
Exposure Levels (cont)
In the EU Directive there are also levels of
noise exposure which must not be exceeded:
Exposure limit values:
Daily or weekly exposure of 87 dB;
Peak sound pressure of 140 dB.

## Slide 135
Recommendation flow chart for managing the risks once a noise hazard has been identified
From HSE ‘Noise at Work’
Fig 3.1 of manual

## Slide 140
  Sound Level Meters
  Acoustical Calibrators
  Frequency Analysis
  Personal Noise Dosimeter
Acoustical Instrumentation

## Slide 141
Sound Level Meters

## Slide 142
Types of Sound Level Meters
There are two types or classes of SLMs
established by International Standards.
Class 1 - is a precision meter, and
Class 2 - is a general purpose instrument with
lower performance specifications than Class 1.
Legislation should be consulted to ensure that
the measurements are undertaken with the
appropriate class of SLM.

## Slide 143
Types of Microphones and Their Use
For occupational noise measurement there are
three types;
Random incidence microphones, (omni-directional)
Direct incidence microphones, (free-field),
Pressure microphones (pressure-response)
Most commonly used is the random incidence or omni-directional microphone.
BUT It is critical that you check!!

## Slide 146
Acoustical Instrumentation (cont)
Frequency analysis can be conducted using :
SLM with octave-band filter;
Recording and later analysis through filters or
Real Time Analyser (RTA)
SLMs generally can do only octave and third
octave whereas RTA’s also do what is known as
fine line of 400 to 800 separate bands.
Modern digital filtering has seen the capabilities
of SLM significantly enhanced while prices have
dropped.

## Slide 147
Modern digital filtering has seen the capabilities of SLM significantly enhanced while prices have dropped.

## Slide 148
Frequency analysis 1/3 octave-band spectral data for the
maximum sound levels generated by an internal
combustion engine.

## Slide 149
Personal Noise Dosimeter
A noise dosimeter (noise dose meter, personal
sound exposure meter) is an SLM designed to
measure a worker’s noise exposure over a
period of time.
The output is available as both noise dose and
noise exposure.
Noise exposure may be shown as an Leq,8h, LEX,8H, or TWA.
TWA - Time weighted average - is used
predominately in the USA, and implies an eight-
hour average.

## Slide 150
Personal Noise Dosimeter

## Slide 151
Acoustic Parameters and Measurement
A meter can be used to measure sound in different ways.
The number provided by the meter is not meaningful unless the meter has been set up in an appropriate manner for the purpose of the measurements.

## Slide 152
Acoustic Parameters and Measurement
There are two main types of weighting applied to the signal before a figure is displayed. They are;
frequency weighting and
time weighting.
Frequency Weighting:
For occupational assessments these
are A, C and Z

## Slide 153
Acoustic Parameters and Measurement
Time Weighting:
Typically meters will have selectable time
responses these are;
Slow,
Fast,
Max,
Impulse & Peak.
As this requires the meter to calculate the
sound levels by integration over differing time
intervals these are called time constants.

## Slide 154
Acoustic Parameters and Measurement
Time Weighting:
Fast and Slow time constants are
Slow 1 second
Fast 1/8th second
These dynamics determine how quickly the
instrument’s display is updated with sound
level data. In practice, the “slow” response
can be used for measuring relatively fast
changing sounds when an integrating meter is
not available.

## Slide 155
Acoustic Parameters and Measurement
Time Weighting:
Fast and Slow time constants
The “fast” response is used to obtain the limits of
a sound, such as the maximum or minimum, and
is preferred when using the integration function.
Some references and standards use subscripts
“S” and “F” for “slow” and “fast” and the levels
can be shown as LS and LF.
When no subscript is given, fast response is
assumed

## Slide 156
Acoustic Parameters and Measurement
Max:
The loudest excursion of the meter. This was regulated to be used with the Slow time weighting, but can be used with any reading.
Impulse SPL:
Defined as having an exponential rise time constant of 35 ms, and an asymmetric decay time constant of 1.5 s. It was thought that this could be used to describe impact sources, however it is no longer used for occupational noise

## Slide 157
Acoustic Parameters and Measurement
Peak SPL:
Peak has replaced impulse and max in the occupational environment.
The peak SPL, Lpk or Lpeak, is defined as the greatest value of the absolute instantaneous sound pressure - note this is the pressure and not the RMS pressure
For occupational noise measurements, the instrument must measure a pulse of 100 μs.

## Slide 158
Acoustic Parameters and Measurement
Equivalent Continuous Sound Level:
For the measurement of varying sound it
is necessary to average the energy over a
longer time period, a cycle of operation or the
whole work shift.
Equivalent continuous sound level, expressed
as Leq,T, is used to quantify the average SPL for
a given measurement period.

## Slide 159
Acoustic Parameters and Measurement
Equivalent Continuous Sound Level:
It is worth noting the term average sound level
is also used and for all practical purposes is
functionally identical.
To obtain an Leq,T, an integrating SLM
is used.

## Slide 160
Equivalent Continuous Sound Level

## Slide 161
Noise Exposure
To quantify the risk to workers it is necessary to determine their time-weighted average noise exposure.
Most regulations consider eight (8) hours to be a nominal workday. Therefore, the term “noise exposure normalized to a nominal 8-hour working day,” expressed as LEX,8h, or LAeq,8h is calculated.

## Slide 162: Today’s Learning Outcomes
Understand Sound
  Physics, descriptors and propagation
  Human response
Be familiar with Risk Assessment and Noise Surveys Instrumentation