## Slide 1
M503
Noise - Measurement & Its Effects
Day 3
Notes: <number>

## Slide 2: Today’s Learning Outcomes
Ch5 Understand hearing protector programs
Discuss the Selection of Hearing Protectors
Conduct measurements of a work environment,
analyse the data and develop a noise management plan

## Slide 3: 5. HEARING PROTECTOR Program

## Slide 4: OBJECTIVE
To understand how and why hearing protectors should be used as part of a noise exposure control strategy

## Slide 5: Hearing Protector Program
Treatment at source is most effective way to prevent hearing loss
Hearing protectors should only be used as interim measure or when there are no feasible engineering noise controls
Hearing protection devices (HPDs) consist of earplugs, earmuffs, canal caps helmets or combinations of these and are used to reduce the level of sound reaching the inner ear.

## Slide 6: Hearing Protector Program (cont)
HPDs should be used in designated high-noise areas until feasible engineering and/or administrative noise control measures effectively reduce work place noise
There are several broad types of hearing protectors and several methods of rating them for their comparative performance.
The quoted performance can differ significantly from the real world performance

## Slide 7: Understanding Required of:
How sound is generated, frequency and intensity
Likely exposure path
Communication
Necessity to wear ALL the TIME while exposed
Cleanliness and maintenance
Spare parts
Other methods available to reduce worker noise exposure.

## Slide 8: Effectiveness of Hearing Protectors

## Slide 9: Types of HPDs
Foam Insert Plugs
Both roll-down or push-in type, made from either polyvinyl chloride or polyurethane closed-cell material, and come in a variety of sizes and shapes.
Foam plugs are undoubtedly the most commonly used HPD

## Slide 10: Types of HPDs
Pre- molded Plugs
  Soft and/or flexible materials
  Variety of sizes.
  Comfortable for continuous use
  Easy to insert and remove
  Long lasting and easy to keep clean
  Can work loose during the day
  Generally have a lower noise reduction
  as they don’t always seal the canal well

## Slide 11: Types of HPDs
Custom-moulded Plugs
  Formed for individual’s ear canal using a malleable silicone putty or similar material.
  Fit and attenuation is dependent upon the expertise of the individual making the device.
  Can be ‘tuned’ to better
  cope with the noise and
  any special hearing
  requirements of the user.

## Slide 12: Types of HPDs
Semi-Insert or Canal Caps
Semi-insert type HPDs are essentially two soft earplugs or pods attached to a narrow spring-loaded band that presses them against the entrance to the ear canal.

## Slide 13: Types of HPDs
Ear Muffs
Rigid cups which completely cover the pinna
Headband provides clamping force
Soft cushions provide seal

## Slide 14: Types of HPDs
Combination of Ear Plugs and Ear Muffs
Used in very high noise areas
Performance of the combination of the ear plug and ear muff is not determined by simply adding the performance of each
Not easily to calculate the estimated performance
The effectiveness of the combination should be obtained from the manufacturer

## Slide 15: Types of HPDs
Helmets
Are very specialised and mostly used in extreme situations, generally military aircraft, helicopters or in some arc gouging operations

## Slide 16: Types of HPDs
Special Devices
 Radio communication
 Protection against extremely high noise environments
 Devices which turn off and on automatically
 Devices with particular frequency response or
 Choice for persons with pre-existing hearing loss.

## Slide 17: Types of HPDs
Linear ear protection
Most HPDs vary in performance across the frequency range and are unsuitable for use by musicians who need to hear the music in an undistorted manner.
Linear ear protection (usually in the form of ear plugs) are sometimes called musicians ear plugs or HiFi plugs.

## Slide 18: Types of HPDs
Linear ear protection (cont)
Designed specifically to have a flatter frequency response than normal ear plugs.
More relevant to classical or acoustic musicians as amplified musicians can utilise a controlled signal from the mixing desk.

## Slide 19: Types of HPDs
Non Linear or Combat Ear Plug
Schematic of a non linear combat ear plug.
Note the small delay unit in the stem of the plug
Constant sound can be transmitted down the tube to the ear but sharp rise time impulse noise is attenuated by this insert

## Slide 20: Types of HPDs
Electronic active ear muffs have good passive reduction and include a microphone and small loudspeaker speaker inside the cup for communication.
When a sudden loud noise or a sharp rise time impulse sound is detected, the amplification is cut and the passive protection of the ear muff utilised

## Slide 21: Types of HPDs
Active Noise Cancelling Headsets - use active noise
cancellation to attenuate noise in the lower frequencies.
This method produces a sound 180 deg out of phase to
cancel the noise
Useful when low frequency noise causes disturbance
to communication eg aircraft cockpits, passenger in
flight audio entertainment.
Active headsets and earplugs are coming for use with
MP3 players etc to screen out external noise.
These are not as yet certified for use in industrial
environments.

## Slide 22: Selection of HPDs
There is no such thing as a “best” hearing protector.
area noise levels,
worker noise exposures,
communication needs,
comfort,
hearing ability,
personal preference, and
interaction with other safety equipment

## Slide 23: Selection of HPDs
In reality, the “best” HPD is the one that will be
properly used by workers at ALL times when working
in high-noise areas.

## Slide 24: Selection of HPDs
Noise level under HPD
reduce to below 85dBA
overprotection is also bad
recommended levels are 70-80 dBA

## Slide 25: Selection of HPDs
Worker acceptance requires
Understanding of need
Choice
Comfort
Accessibility at the workplace
Accessibility to spare parts maintenance and storage

## Slide 26: HPD Selection Methods
All the following methods attempt to predict
population protection values achievable by the
majority of wearers, i.e. exposure control
Octave-band Method
Noise Reduction Rating
Noise Reduction Rating (Subject Fit)

## Slide 27: HPD Selection Methods
Noise Level Reduction Statistic
  Single Number Rating
  HML Method
Sound Level Conversion
Classification Method

## Slide 28: HPD Selection Methods
Some methods claim to be more precise than
others especially amongst the single number
ones
GIGO – “garbage in garbage out”
Don’t confuse Accuracy with Precision

## Slide 29: HPD Selection Methods
Not necessarily accurate as all the methods rely on
Accurate estimate of sound field,
Statistical sample of Laboratory test may not reflect the individual
Wearing habits differ from laboratory tests
Real world attenuation is often very different to Lab test
Real world exposure varies all the time

## Slide 30: Octave-band Method
The most precise method for estimating the
“protected” level
Remembered that even though the calculation method
may be precise, the resultant is only an estimated “in-
ear” level.

## Slide 31
Octave-band Method Example
line | Frequency (Hz): | 125 | 250 | 500 | 1000 | 2000 | 4000 | 8000 | Overall level
1 | Noise Level dB | 103 | 105 | 107 | 102 | 97 | 99 | 92 | 111
2 | A-weighting | -16.1 | -8.6 | -3.2 | 0 | +1.2 | +1.0 | -1.1 | --
3 | Noise Level dBA | 86.9 | 96.4 | 103.8 | 102 | 98.2 | 100 | 90.9 | 108
4 | Mean Attenuation of HPD | 12.8 | 19 | 28.5 | 36.1 | 38.1 | 38.3 | 26.7 | --
5 | Standard Deviation | 1.8 | 2.0 | 2.5 | 2.1 | 3.1 | 3.3 | 1.7 | --
6 | Mean – 1 SD | 11 | 17 | 26 | 34 | 35 | 35 | 25 | --
7 | Estimated in- ear level, dBA | 75.9 | 79 | 77.8 | 68 | 63.2 | 65 | 65.9 | 83

## Slide 32: Octave-band Method Example

## Slide 33: Noise Reduction Rating (NRR)
The NRR gained wide acceptance in the early 1980s
Simple and was Regulated - Occupational Noise
Exposure: Hearing Conservation Amendment; Final Rule
(OSHA, 1983)
Subtract the manufacturer’s published NRR value
from the C-weighted noise exposure to get the
estimated A-weighted protected level under the device.

## Slide 34: Noise Reduction Rating (NRR)
For real-world attenuation
LAeq,8 – [(NRR-7)x0.5] = Estimated LAeq,8 under the protector.
OR
For Earmuffs: Reduce the NRR by 25%,
For Formable plugs: Reduce the NRR by 50%,
For all other plugs: Reduce the NRR by 70%.

## Slide 35: Noise Reduction Rating (Subject Fit)
NRR(SF) better represents the real-world attenuation
achieved by groups of workers relative to the original
NRR
To estimate attenuation simply subtract the NRR(SF)
from the A-weighted noise exposure or worse-case
sound level to find the “protected” level under the
device.

## Slide 36: Noise Level Reduction Statistic
The most recent rating method to come out of the USA described in ANSI S12.68 (ANSI, 2007).
Recognises the problem that no single-number rating can accurately predict the range of performance achievable from HPDs

## Slide 37: Noise Level Reduction Statistic
Method A, NRSA80 (80 percentile value) – the protection that is possible for most individually trained persons to achieve or exceed.
Method B, NRSA80 (80 percentile value) – the protection that is possible for most users to achieve or exceed.
Method A or Method B, NRSA20 (20 percentile value) – the protection that is possible for a few motivated proficient users to achieve or exceed.

## Slide 38: Single Number Rating (SNR)
European Union and affiliated countries Single Number Rating (SNR) is used and specified for compliance
Again the C weighted exposure is used, but SNR numbers differ from NRR due to subject fit methods and frequencies used in testing

## Slide 39: HML Method (High Medium Low)
HPD may be labelled SNR 28, H=33, M=24, L=14; which means the estimated attenuation varies with the spectrum of the noise.
Since the HML method targets the noise spectrum it is potentially more accurate for predictive purposes than the SNR rating.
To use the HML ratings the user must know both the A-weighted and C-weighted sound pressure levels for the noise environment.

## Slide 40: Sound Level Conversion
Australia and New Zealand used the Sound Level Conversion (SLC80) rating, till 2005.
The SLC is an estimate of the attenuation achieved by 80 percent of well-managed and trained wearers
The C-weighted noise level is measured and the appropriate SLC value HPD is chosen to reduce the number to a suitable level.

## Slide 41: Classification Method
The simple method in AS/NZ Standard 1269 (2005) recognises that wearing time is the most critical parameter and variation in the noise environment will often render accurate calculation redundant.
LAeq,8h dB(A) | Class
Less than 90 90 to less than 95 95 to less than100 100 to less than105 105 to less than 110 Greater than 110 or equal to 110 | 1 2 3 4 5 requires specialist advice

## Slide 42: Classification Method
Comparison between class rating and SLC80

## Slide 43: Classification Method
If the noise environment is narrow band in character with significant tonality or has significant high or low frequency components or exhibits other complexities, then the octave-band method should be used.

## Slide 44: Fitting
All hearing protectors need to be fitted when initially
introduced to a worker.
A determination of ear health and physical attributes
should be undertaken to ensure a good seal is
achieved.
If multiple sizes are available they should be checked
to ensure the best fit for comfort and wear ability.

## Slide 45: Fitting Foam Earplugs
Pulling up on the Pinna (external ear) or pulling down on the lobe, you can straighten out your ear canal, allowing for the correct and full insertion of the plug into the canal. Each person needs to determine which method works best for him or her.

## Slide 46: Fitting Foam Earplugs
Proper versus Improper Insertion of Foam Plug

## Slide 47: Fitting Foam Earplugs
Left photo
shows a proper insertion of a formable earplug, which is fibreglass down in a sheathing material.
Right photo
is an improper insertion, as the device is too loose, or is not inserted deeply enough to be of benefit.

## Slide 48: Fitting Pre- moulded Earplugs
Varying sizes, such as small, medium, and large
Up to ten (10) percent of wearers can have two different size ear canals, each ear needs to be fit separately
HPD manufacturers provide ear gauges for sizing the ear canal. To obtain a proper fit on multi-flanged plugs at least one of the flanges should completely seal along the interior wall of the ear canal.
As with foam plugs, using the “pinna pull” is recommended for pre- moulded plugs.

## Slide 49: 5.4 Fitting Pre-moulded Earplugs
Proper Insertion: the end flange is just past the tragus.
Improper Insertion: the end flange extends past the tragus.

## Slide 50: Fitting Custom-Moulded Earplugs
Taking ear impressions for custom-moulded earplugs needs to be completed by a trained professional, such as an audiologist, or physician.
The wearer should receive one-on-one training from the professional on how to properly insert the custom-moulded plugs.

## Slide 51: Fitting Semi-Insert/Canal Caps
Are quick and easy to use but only recommended for short durations in high-noise areas
The pressure exerted by the band used to seal the earplug against the entrance to the ear canal means use can become uncomfortable, even painful (usually after 30 minutes).
To insert simply push the earplugs or pods into the entrance of the ear canal. The “pinna pull” technique is useful for effective seating at the entrance of the ear canal.

## Slide 52: Fitting Earmuffs
Most earmuffs can successfully fit a large percentage
of people BUT Check
Does the headband expand and contract enough to position the cups securely over each pinna?
Can the entire pinna comfortably fit inside the earmuff cup?
Does the cup’s cushion seal against the head all the way around the ear, or are there excessive gaps caused by bone structure, bulky eyeglass temples or facial hair?

## Slide 53: Fitting Earmuffs
If gaps are present, earmuffs can increase the level of noise reaching the eardrum through the “resonance effect” - especially for noise in the 125-250 Hz range
Best to have selection of muffs with easily adjustable bands and good cushioning.
Earmuffs should be checked regularly for
  Cracking and hardening of cushions
  Clamping band softening
  Internal absorber clean and in good condition
  Damage / modification of shell

## Slide 54: Fitting Earmuffs
Note how the ear lobe extends beyond the bottom of the earmuff cup, which will cause air leaks and a significant reduction in the delivered attenuation. This earmuff is not properly sized for this individual.

## Slide 55: Fitting Earmuffs
Excessive hair over the ears: can break the seal of the earmuff cups, significantly reducing the overall attenuation.
Same affect is true for safety glass temple bars.
All gaps or penetrations should be minimized as best as possible to achieve effective attenuation.

## Slide 56: Fitting Earmuffs
This earmuff is too big for this user.
The headband is fully closed, but does not rest on the top of the head, as it should.
Be careful to ensure HPDs are compatible with the wearer’s anatomy.

## Slide 57: Fitting Earmuffs
Left earmuff head band still maintains its original spring-loaded shape,
Right shows a head band that has been bent back enough over time to render this device less effective.
The earmuff on the right should be discarded.

## Slide 58: Fitting Earmuffs
Both earmuff cushions show permanent impressions, allows air leaks and reduces the attenuation.
The cushions need to be replaced.

## Slide 59: Fitting Earmuffs
These are the temples of doom.
The indentions of this person’s temples do not allow the earmuff cups to seal properly against the sides of the head, This person is not a good candidate for earmuffs

## Slide 60: Fitting Earmuffs
These muffs are the property of H.C.

## Slide 61: Wearer Field Test to Check Fitting
The Tug Test – Gently tug in and out on the end of the plug, handle, or cord.
 The Hum Test – After inserting one earplug, the wearer should hum or say “ahhh”. If one ear is properly sealed, creating the occlusion effect where bone conduction becomes noticeable, then the user’s voice will seem louder in the sealed ear.

## Slide 62: Wearer Field Test to Check Fitting
The Loudness Test – With earplugs inserted while standing in a noisy environment, the wearer should cup both hands over the ears. If there is a perceptible difference in noise level, the earplug is probably not inserted well enough
Break test- user breaks the seal of an earplug or cup of an earmuff when in noise, the noise level should increase markedly.

## Slide 63: Individual Hearing Protector Fit Testing
Even with appropriate focus on noise control,
reliance on HPDs as the last line of defence
against occupational noise exposure is inevitable.
One critical failure in this process has historically
been the fact the labelled protection values on HPD
are not reliable predictors of actual HPD performance.

## Slide 64: Individual Hearing Protector Fit Testing
Analysis of laboratory evaluations indicates individual variability in HPD performance is large enough to make any population-based, statistical assessment of HPD performance inappropriate for individual workers.

## Slide 65: Field Microphone in Real Ear (F-MIRE)
(Source: Courtesy of Aearo Technologies)
E-A-Rfit®, F-MIRE

## Slide 66: Real-Ear Attenuation at Threshold (REAT)
FitCheck Equipment
For earplugs

## Slide 67: HPD Requirements
MUST be used at all times
Must be readily available
Replacement parts and spare stock
must be available in suitable sizes
Warning signs MUST be at all
entrances to HPD required areas, not
“on the GATE”

## Slide 68: Training and Maintenance
HPD wearers should be trained in the proper use and care of their protectors during initial fitting, at the time of their annual hearing test, and whenever observed to be improperly wearing HPDs.

## Slide 69
Maintenance
Earplugs, primarily re-useable premolded and
custom plugs, should be routinely inspected to
ensure no damage or physical changes have
occurred to the device over time that would inhibit
the ability to obtain an airtight seal.
Plugs may be re-used if they are cleaned with a
mild soap and water between uses

## Slide 70
Maintenance
Earmuffs should be checked regularly for
impressions, cracking, and hardening of cushions
which can cause air leaks affecting the attenuation.
Replacement cushions are available from the
manufacturer
The headband should be routinely inspected to
ensure it still provides adequate pressure to seal
the ear cups against the side of the head.

## Slide 71: Today’s Learning Outcomes
Understand hearing protector programs
Discuss the Selection of Hearing Protectors
Conduct measurements of a work environment
Analyse data collected in work environment

## Slide 72
Afternoon Practical
Measurement in a work environment