## Slide 1
M503
Noise - Measurement & Its Effects
Day 4
Notes: <number>

## Slide 2: Today’s Learning Outcomes
Ch 6 To review employee education and training
Ch 7 To understand the principles of audiometric testing
Ch 8 To review reporting and record keeping
Ch 10 To understand the principles of environmental noise

## Slide 3
6. EDUCATION & TRAINING

## Slide 4
Education & Training
Once a noise hazard has been identified, some immediate action is required to protect employees.
Noise management programme must be holistically implemented.
It is important that everyone understands what's happening and why they have to follow new procedures

## Slide 5
Education & Training (cont)
Audio visual material can be used to cover most of the topics but it is essential to have ‘hands on’ demonstrations of the use of the types of hearing protection that are provided in the workplace.
Revision sessions need follow up on training, they need not be lengthy and can be in the form of informal ‘tool box’ OHS sessions.

## Slide 6: Basic Requirements
Essential part of overall noise management program
Required in stages as the program developed
Management must understand its responsibilities
Employees must understand the hazard and the safety systems

## Slide 7: Guidance for Training Content
Standards and codes of practice may include guidance on content
Different levels of training depending on the needs of the personnel:
  Management need overall understanding
  Those exposed to the noise need to understand the noise control measures
  Those recommending measures and reviewing and checking need detailed knowledge

## Slide 8: Training in Use of Hearing Protectors
Required as soon as hazard identified and hearing protectors provided
Training is an essential part of the overall hearing protector implementation and specific to the actual work environment
Need to know where to use them and how to use them so
Special emphasis on wearing all the time in the noise

## Slide 9: Training in Use of Hearing Protectors (cont)
1-2 hours sufficient in first instance
Hands on demonstrations
Audio visual material can assist
Regular follow up sessions to check proper use and maintain motivation
Good to coordinate with audiometric testing

## Slide 10
Ear and hearing
Noise – levels and effects
  Good to give examples from their workplace
Manager and worker responsibility
Importance of hearing protection
Explain control measures in place like covers, barriers, enclosures etc
Training in Use of Hearing Protectors (cont)

## Slide 11
Explain the noise levels and the remaining areas where hearing protectors required
Show the signage identifying the zones
Explain the process for supply and replacement of hearing protectors
Demonstrate the types of protection that are available – emphasize the importance of wearing all the time in the noise, accentuate the importance of comfort.
Training in Use of Hearing Protectors (cont)

## Slide 12
Demonstrate fitting techniques
Check that each employee can fit properly
Discuss good and bad practices with regard to use, care and maintenance of hearing protectors
Provide opportunity for discussion of individual concerns
Training in Use of Hearing Protectors (cont)

## Slide 13
Demonstrate cleaning and checking for defects
Show where supplies kept and explain processes for replacement
Explain procedure should there be a change or if something goes wrong
Training in Use of Hearing Protectors (cont)

## Slide 14: Training to Undertake Noise Assessments
Small and medium sized workplaces - more efficient to contract out
Larger companies may have personnel with the potential to develop the skills
Training course generally 2-3 days
Noise assessment should be followed by development or updating of noise management plan and implementation of noise control measures

## Slide 15: Training to Undertake Noise Assessments (cont)
In house staff need continuing training to update skills and awareness of advancements in instrumentation, options for noise control and hearing protectors
Need a thorough understanding of the noise assessment and the applicable noise exposure standards
Need to know their limits and when to call for further advice

## Slide 16
Explain basic acoustics and in particular the methods of measurement
Explain need for protection of hearing
Demonstrate requirement for accurate Measurement
Discuss procedures for workplace assessment in particular the time periods for accurate measurement of LAeq
Training to Undertake Noise Assessments (cont)

## Slide 17
Identify the applicable exposure standards
Discuss the range of options that should be considered when developing a noise management plan
Review the options for noise reduction
Training to Undertake Noise Assessments (cont)

## Slide 18: Training to Implement Noise Control Measures
Small and medium sized workplaces, often more efficient to contract out
Larger companies may have personnel with the potential to develop the skills
Based on the outcome of the noise assessment
Training course generally 2 to 3 days
Need to know their limits and when to call for further advice

## Slide 19
Prerequisite of the noise assessment training
Explain generation of sound from various noise sources
Review the basic options for noise reduction and control
Highlight the importance of considering each noise source
Training for Noise Control Measures (cont)

## Slide 20
Assess the options for control of noise from different types of sources
Discuss importance of vibration control
Emphasise that solutions need to be practical for effective implementation
Training for Noise Control Measures (cont)

## Slide 21: Conclusion
Different training programs needed for the different levels of involvement with the noise management program
Essential that management keeps a record of the training provided
There is always a need for ongoing training and refreshing as new techniques and products are developed

## Slide 22: 7. AUDIOMETRIC TESTING

## Slide 23: AUDIOMETRIC TESTING
Types of Hearing Loss:
Conductive
  Blockage or damage in the sound pathway to hair cells
  Diagnosed from bone conduction tests
  Loss similar across frequencies –
  effect is like turning down the volume on radio

## Slide 24: AUDIOMETRIC TESTING
Types of Hearing Loss:
Sensorineural
  Due to damage within the auditory nerve and/or central auditory pathway
  Loss differs across the frequency range
  Age-related hearing loss (ARHL), also called presbycusis,

## Slide 25: AUDIOMETRIC TESTING
Types of Hearing Loss:
Sensorineural (cont.)
  Noise-induced hearing loss (NIHL),
  Meniere’s Disease
  Vestibular schwannoma, which is a tumour on the auditory nerve
  Ototoxic drugs

## Slide 26: AUDIOMETRIC TESTING
Types of Hearing Loss:
Mixed
  Combination conductive and sensory neural includes chronic ear infection, trauma to the ear, and certain ear diseases

## Slide 27: Noise Induced Hearing Loss (NIHL)
Cause/Effect
Sound Exposure Intensity and duration
Relationship between the amount of noise exposure and hearing loss is not linear.
Genetic predisposition health diet and other factors
High Impulse/Impact Noise
Continuous and Intermittent Noise Exposure
Temporary and Permanent Threshold Shifts

## Slide 28: Auditory Effects of Excessive Noise Exposure
NIHL is a result of structural damage to the cochlea.
In general, the larger the hearing loss, the more
widespread the damage

## Slide 29: Auditory Effects of Excessive Noise Exposure
Intense blasts can cause such extreme vibration
that the eardrum may
  perforate and/or haemorrhage,
  the ossicles can fracture, and
  in severe cases, the organ of Corti can be torn off the basilar membrane
Hearing loss from this extensive damage would be
profound and affect multiple frequencies.

## Slide 30
Auditory Effects of Excessive Noise Exposure

## Slide 31
Progression of Noise Induced Hearing Loss

## Slide 32: Other Effects or Causes
Tinnitus – ‘ringing in the ears’
Common in the general population but more, likely to be bothersome for those with high occupational noise exposures.
Effects include difficulty falling asleep, reduced ability to concentrate, trouble relaxing, and experiencing annoyance, irritability, frustration, and/or despair.
Some treatments and coping strategies but no known cure.

## Slide 33: Other Effects or Causes
Age-Related Hearing Loss (ARHL) or Presbycusis
Due to the loss and deterioration of outer hair cells in the basal turn of the cochlea.
Audiometric pattern is a “sloping” audiogram: hearing is worse at higher frequency. The degree of change is highly individualized.
Differentiating between the aging affects and the noise affects can be problematic – methods given in Standards

## Slide 34: Other Effects or Causes
Non-organic Hearing Loss
When no apparent organic or physical cause for apparent hearing loss - individual is exaggerating to appear as if hearing loss exists . Also referred to as functional hearing loss or malingering
  In rare cases there is a psychological condition -clinical term is pseudohypacusis
  Legitimate results may be obtained with more time and special testing.

## Slide 35: Rehabilitation for Sensory Neural Hearing Loss
Hearing Aids – but limited effect
Lip reading
Headphones Aural Loops IR headsets
Partner coaching
Not Cochlear implant at this time

## Slide 36: Audiometric Program in Workplace
Program requires
Competent Testers
Database establishment and ongoing management
Privacy implications
Historical evaluation
Who is included
Benefits include:
Early identification of hearing damage
Compliment the hearing conservation program
Assist to identify where program not satisfactory or not followed

## Slide 37: AUDIOMETRY
Screening Audiometer:
Air only
Not so many frequencies
Lower dynamic range
Background noise not so critical
Operator training simpler
Simple results
Diagnostic Audiometer:
Air, bone, speech, narrow band, modulations etc.
Clinical setting
Background noise important
Professional evaluation

## Slide 38
Manual audiometer with air conduction threshold finding capability

## Slide 39
Example of a microprocessor audiometer with built‑in printer

## Slide 40
Computer-controlled audiometer:
The audiometer functions are accessed with the computer keyboard

## Slide 41
Bekesy Threshold Tracing at 3000 Hz

## Slide 42: Otoacoustic Emission (OAE)
This is a sound which is generated from within the inner ear.
OAEs disappear after the inner ear has been damaged and so can be used as a measure of inner ear health.
There are two general types of otoacoustic emissions: Spontaneous Otoacoustic Emissions and Evoked Otoacoustic Emissions.

## Slide 43: Otoacoustic Emission (OAE)
The click-evoked OAE is a non-invasive test for hearing defects and is now widely used for newborn babies
The test may well become more common for general audiometric screening.

## Slide 44: Audiometric Tests
  Basic requirement for booth - it must be quiet
  High noise reduction enclosure
  Good Seals around doors and joints
  Away from workplace noise
  Away from other noise like traffic, aircraft etc
  Basic requirement for equipment - must be accurate
Performance Checking - Bio-acoustic Simulator

## Slide 45: Otoscope
  Used to assess outer ear Otological Examination :
  Illuminator
  Viewer
  Can cause damage or other problems when not used professionally.

## Slide 46: Equipment Calibration
Annual and professionally outsourced
  Sound pressure output,
  Linearity of the attenuator,
  Harmonic distortion,
  Rise and decay time, and
  Overshoot and “off” levels.
Caution: Each set of headphones is calibrated to one audiometer. Headphones cannot be swapped or used with another audiometer without recalibration.

## Slide 47: Understanding the Audiogram
X- Left
O- Right
Red- Right
Blue- Left
……… But may differ so always check

## Slide 48
Normal
Mild
Moderate
Severe
Profound
Understanding the Audiogram

## Slide 49
Understanding the Audiogram

## Slide 50
Understanding the Audiogram

## Slide 51: Valid Audiometric Tests
Conducted by a competent person with calibrated and checked equipment
Test performed in controlled test environment which meets specified allowable ambient noise levels,
Baseline audiograms: no excessive noise exposure for a minimum of at least 14 hours prior to test,

## Slide 52: Valid Audiometric Tests
Require:
  employee identifying information,
  noise exposure information,
  job information on audiogram,
Thresholds that conform with standard audiometric configurations do not need additional audiological evaluation and
All required frequencies tested.

## Slide 53: Audiometric Testing Intervals and Conditions
  Baseline Test
  Annual Test
  Retest
  Transfer or Exit test

## Slide 54
Audiometric Testing Intervals and Conditions

## Slide 55: Audiometric Testing Intervals and Conditions
  Significant Threshold Shift Intervention
  Intervention Procedures
  Confirmation of STS
  Work-Related Determination
  STS Intervention Waived
  Recordable STS
  Workers’ Compensation

## Slide 56
8. REPORTING & RECORD KEEPING

## Slide 57
Reporting & Record Keeping
A proper risk management strategy must be:
Transparent
Documented and
Properly implemented.

## Slide 58
Reporting & Record Keeping
To ensure this occurs, a system of reporting
and documentation needs to be implemented
and maintained.
Responsibility must be assigned and
documented with key performance criteria
assigned to each level of management.

## Slide 59
Organizational Risk Management Plan Must Contain
The level at which noise exposure needs to be addressed within the organisation for both long and short term exposures.
The relationship of the organizational level to regulatory requirements.
The decision matrix for determining of implementation types of risk controls.
Long and short term strategies for risk control.

## Slide 60
Organizational Risk Management Plan Must Contain
Hazard identification assessments
Hazard control assessments
Hearing protector programmes
Audiometric monitoring and assessment program
Continuing risk identification and control strategy assessment

## Slide 61
An Organisational Chart can be Used to Show
The links between OH&S and finance, R&D sections production areas and senior management.
The roles and responsibilities for each part need to be incorporated into performance indicators, position statements and job descriptions.
In short unless a hazard management plan is seen as an essential part of the work function and culture it will not prosper.

## Slide 62: INTRODUCTION TO ENVIRONMENTAL NOISE

## Slide 63: Environmental Noise
Need to control noise in the environment to avoid annoyance as well as speech and sleep disturbance
Acceptable noise levels relate to expectations of what noise will exist in the area
Characteristics of the noise also important – frequency content, impulsive etc are more annoying than a constant noise

## Slide 64: Descriptors
A weighting used for most criteria
Percentile statistics over a time period
  LA10,T the level exceeded for 10% of the time used to describe the noise
  LA90,T the level exceeded for 90% of the time used to describe the background
Equivalent energy level LAeq,T

## Slide 65: Descriptors
LA10,T
LA90,T
18 hour for LA10

## Slide 66: Descriptors
LAeq ,T

## Slide 67: Descriptors
Sound exposure level, SEL for single events – normalises to 1 sec
Day night level, Ldn, combines the LAeq
  over the day, typically from 0700 to 2200
  over the night with a +10dB to allow for the extra annoyance

## Slide 68: European Union Directive
Environmental Noise Directive 2002/49/EC (EU, 2002)
Requires for any city >100,000, roads > 3,000,000 vehicles/ year, railways >30,000 train passages/ year and airports >50,000 flights/year
  noise contour mapping, information to public, development of local action plans, preserve areas with acceptable noise levels and collect data for future policy

## Slide 69
US Guidelines
  Based on Ldn which should be kept below 55 dB(A) in residential areas
Other approaches
  Specified zone noise standards based on type of area and time of day
  Comparison with existing background noise levels

## Slide 71
Table 10.1 | Guidance for Average Background Noise Levels, LA90,T |  | 
Type of Area | Time of Day |  | 
 | Day (0700-1800) | Evening (1800-2200) | Night (2200-0700)
Rural ie negligible transportation | 40 | 35 | 30
Semi rural and low density transportation | 45 | 40 | 35
Near some commerce or industry | 50 | 45 | 40
Near dense transportation | 55 | 50 | 45
Borders of industrial areas | 60 | 55 | 50
Within industrial areas | 65 | 60 | 55

## Slide 72: Factors Influencing Annoyance
Frequency content of the noise,
Duration of the noise,
Time of day noise occurs,
Time of year the noise occurs,
History of prior exposure to the noise source,
Perceived attitude of the noise source owner,
Special characteristics of the noise that make it especially irritating,
Ratio of intruding noise level to normal background noise level.

## Slide 73: Factors Influencing Annoyance
Unnecessary, or unnecessarily loud,
A threat to personal health or safety,
A threat to economic investment (property value),
 Beyond resident control.

## Slide 74: Sound Propagation Outdoors
Attenuation outdoors, Atotal, is determined by a number of factors:
Atotal = Adiv + Aair + Aenv + Amisc
Adiv attenuation due to geometrical divergence,
Aair due to air absorption,
Aenv due to the effects of the environment, and
Amisc due to all other factors, such as foliage, barriers, etc.

## Slide 75: Geometrical Divergence
Adiv due to the spreading from the source of the sound wave energy over large surface
Adiv = 20 log r/r0
r is the distance and r0 the reference of 1 m
For point source this results in 6 dB per doubling of
distance
For line source 3 dB per doubling of distance
In practice typically 3-5 dB per doubling of distance

## Slide 76: Air Absorption
Energy loss occurs from heat conduction and vibration of the air molecules
Depend on frequency, temperature and relative humidity
Relative humidity usually the dominant
This is usually only important over long distances

## Slide 77: Environmental Effects
Amount of reflected sound depends on the nature of the
surface – soft, rough etc

## Slide 78: Effect of Temperature
Temperature gradient leads to a bending up or down of
the sound wave
Daytime
Night and temperature inversion

## Slide 79: Effect of Wind
Wind gradient leads to a bending of the sound wave
depending on the direction

## Slide 80: Effect of Foliage
Very little effect on the noise level unless 100m dense forest!

## Slide 81: Measuring the Noise
Automatic noise loggers most convenient as can be
left in location BUT they measure all the noise so may
need to be supplemented with attended measurements

## Slide 82: Measuring the Noise

## Slide 83: Summary of Factors
Visibility of noise source
“foreign” noise
Tonal components
Impulsive noise
Noise that is random - unexpected
Low-frequency noise - resonances within residential structures.
Low pre-existing background noise level.

## Slide 84: Summary
The investigation process involves
Review of local criteria, guidelines etc
Property line sound level measurements.
Check for pure tones and other characteristics
Check times of noise occurrence.

## Slide 85: Summary (cont)
Follow-up actions may include the following:
Meet with the community/complainant.
Open Communications - "noise hot-line“
Inform the community of any unusual noise emissions
Beware that changes in the noise environment may lead to new complaints – an old noise may have masked a tone.

## Slide 86: Today’s Learning Outcomes
To understand the principles of audiometric testing
To review employee education and training
To review reporting and record keeping
To understand the principles of environmental noise