## Slide 1
M503
Noise - Measurement & Its Effects
Day 5
Notes: <number>

## Slide 2: Today’s Learning Outcomes
Write –up of Practical exercise
Discussion on practical aspects of noise assessments
Noise Control Program Evaluation
Mock Exam Review

## Slide 3: Guidelines For an Effective Hearing Conservation Programme
Outline “best practice” approach

## Slide 4: Best Practice
Procedures for measuring the noise
Determination of employee noise exposure
Noise controls – engineering and administrative
Provision of hearing protectors
Audiometric testing
Training

## Slide 5: Summary of Steps
Survey all work areas – identify >80 dBA.
Assessment noise exposures >80 dBA
Inform employees and management
Update noise surveys at least 2 years or when changes.
Noise control measures – if engineering and administrative controls insufficient then hearing protectors.

## Slide 6: Summary of Steps (cont)
Signage for all work areas ≥ 85 dBA
Hearing protection readily available signed areas
Training – initial and refresher- for all ≥ 85 dBA
Audiometric monitoring offered to all ≥ 85 dBA
Permanent threshold shifts reported

## Slide 7: Summary of Steps (cont)
Periodic evaluation of HCP s
Records of all components - area noise surveys, personal exposures hearing protection and audiometric testing - kept for legislative requirement or at least 30 years

## Slide 8: Noise Surveys
Identify who needs to be in HCP,
Determine area and equipment noise levels, and generate noise contour maps,
Collect acoustical data for noise control engineering purposes,
Identify all hearing protection required areas, and
Enable the selection of the appropriate hearing protection devices.

## Slide 9: Surveys
Instruments must meet standards and be properly maintained
Area surveys measure and document all areas >80 dBA,
Exposure surveys for all working >80 dBA
Training for those doing surveys
Re-evaluations every 2-5 years or when changes

## Slide 10: Survey Data
Area surveys as contours by machine, work area or map
Exposure survey data in terms of LAeq,8hr
Always check if LCPeak excess and document
Clear documentation for future reference

## Slide 11: Noise Control
Engineering noise control – at source by replacement or remedial measures
Administrative control – work practices to limit time of exposure

## Slide 12
Personal Hearing Protectors
Only reduce the noise at the ear when properly selected and properly worn
Provide adequate reduction - 75-80 dBA in ear
Avoid overprotection
Suitable for the work environment
Training in use and Motiviation

## Slide 13: Audiometric Monitoring
Baseline before exposure
Regular audiometric checks for those >85dBA
At termination of employment
Data analysed

## Slide 14: Intervention when Threshold Shift
Notify employee and counsel the employee.
If not using HPDs, provide and train in use.
If using HPDs, check, refit, retrain in use
Repeat audiometric check within 30 days

## Slide 15: Confirmed Threshold Shift
Investigation noise exposure,
Investigation of noise control options
Inform employee and advise follow-up actions

## Slide 16: Checking HCP Effectiveness
Individual – from audiometric checks
Overall –
  Noise control compliance audits
  Audiometric data base analysis
  Check for temporary threshold shifts

## Slide 17: Record Keeping
Noise measurements data
Noise exposure assessments
Employees included in the HCP
Audiometric testing and notifications
All HPDs available
Training records

## Slide 18: Record Keeping (cont)
Noise control studies,
HCP program and policy documents
Hearing protection effectiveness checks
Audits of HCP
Calibration of instruments.

## Slide 19: Intervention Strategies
Identify employees at risk
Identify problem job/work areas
Buy Quiet
Engineering solutions
Hearing protector refit/retrain

## Slide 20: Intervention Strategies (cont)
Audiometric test schedule
Special events motivation
Audits of hearing protector use
Training course
Encourage hearing protectors in non work

## Slide 21: Conclusion
“best practice” approach may be challenging in some workplaces
But there are many options
And proper implementation ► prevention hearing loss from occupational noise exposure

## Slide 22: Today’s Learning Outcomes
Write – up of practical exercise
Discussion on practical aspects of noise assessments
Noise Control Program Evaluation
Mock Exam Review