## Slide 1: M504 - Health hazards and exposure limits

## Slide 2: Health effects of asbestos
Asbestos fibres are a particular problem because of
  Their size
  Ability to split into finer fibres
  Their resistance to chemical attack
Fibres can remain airborne for long periods of time
When inhaled they are carried in the air-stream and can deposit within the respiratory system
  Large fibres (width greater than 3 microns) deposit in major airways of lungs, generally cleared by cilia and mucous
  Smaller fibres (width less than 3 microns) can reach the alveoli (gas-exchange region) of the lungs

## Slide 3: Health effects of asbestos
Doll and Peto (1985) report that
  “the hazard from airborne asbestos is greatest from fibres of between 5 and 100 micron in length, with diameters less than 1.5 or 2 micron, and with aspect ratios of more than 5 to 1”
  and
  “for asbestos fibres, length seems to be the (main) factor in health issues and very short fibres may not be carcinogenic at all. There is no evidence however of a cut off point for width or diameter.”

## Slide 4: Structure of the lungs
Trachea (windpipe)
Bronchi
Bronchioles
Alveolus
Diaphragm
Pleura & Pleural membrane

## Slide 5: Health effects of asbestos
Asbestosis
Mesothelioma
Lung cancer
Pleural plaques
  Thickening of the membrane lining the lungs
  Detected by chest X-ray, rarely of clinical significance as they are benign (do not become malignant)
  They indicate significant asbestos exposure
Asbestos warts
  Sometimes found on skin of workers, particularly hands
  Fibres lodge in skin and are overgrown causing benign growths

## Slide 6: Asbestosis
Disease first acknowledged in 1927
Is a scarring or fibrosis of the lungs
Severity depends on the amount of exposure and the duration of exposure (the dose)
  Asbestosis is a clear example of a dose-response relationship
Asbestosis can be caused by all forms of asbestos
Occurs after long-term, heavy exposure – high fibre concentrations over many years

## Slide 8: Asbestosis
Macrophage cells in alveoli unable to completely engulf the fibres
  As a result the macrophage cells die and release digestive enzymes and chemicals
  This attracts fibroblasts – cells responsible for ‘wound healing’ and creating fibrous tissue
  This causes a fibrosis or scarring of the lung tissue
Reduction in elasticity of lung tissue causes shortness of breath and reduced ability to take up oxygen
  Often leads to severe respiratory problems and heart failure

## Slide 9: Mesothelioma
Mesothelium
  Membrane lining of several body cavities and organs including
    lungs (pleural mesothelium)
    abdominal cavity (peritoneal mesothelium)
Mesothelioma
  Malignant tumour in which mesothelial cells become abnormal and divide without control
    These abnormal cells can metastasize (migrate) to other parts of the body
    Asbestos related mesothelioma usually occurs in the pleural mesothelium and may spread to other areas such as the peritoneum

## Slide 10: Mesothelioma
Very progressive disease
  Time from diagnosis to death is usually between 6 and 18 months
Long latent period
  Symptoms often do not appear until 20 to 30 years after exposure, sometimes even appearing up to 40 years later
No safe exposure limit
  There does not appear to be a threshold of exposure below which the disease will not occur
  Risk of developing the disease increases with the intensity and duration of exposure

## Slide 11: Mesothelioma
All types of asbestos have been shown to produce mesothelioma in animal experiments
Mesothelioma of the lung is almost always linked to asbestos exposure – mainly blue and brown
Hodgson and Darnton (2000) state that
“exposure specific risk of mesothelioma is in a ratio of 1:100:500 for chrysotile, amosite and crocidolite respectively”

## Slide 12: Lung cancer
Malignant growth of abnormal cells in the lungs
  Can be caused by asbestos as well as many other pollutants e.g. cigarette smoke, car exhausts
No safe exposure limit
  Determining risk of asbestos related lung cancer further complicated by the much higher number of lung cancers attributable to smoking
  Long latent period – usually at least 10 years and may be as much as 30 or 40 years after exposure before symptoms appear
  Mainly associated with exposure to blue and brown asbestos
  Risk of developing disease increases with intensity and duration of exposure
‘Synergistic’ with smoking – greatly increased risk

## Slide 13: Risk to health
Mortality rate
Death rate
Smoker
Asbestos worker
X 53
601.6
Yes
Yes
X 11
122.8
Yes
No
X 5
58.4
No
Yes
1
11.3
No
No
Asbestos and lung cancer
(Lung cancer death rates
per 100 000 person years)
NB: An example of synergism

## Slide 14: Quantitative risks from asbestos exposure
Difficult to determine precise levels of risk however the following general conclusions can be made
  Risks from crocidolite > amosite >> chrysotile
  At 0.01 fibres / ml.years risks from chrysotile are very low
  Studies show a wide range of estimates of risk
  Whatever exposure standard is used, it does not represent a ‘safe’ level and exposure to any form of asbestos should be prevented or reduced to as low a level as is practicable

## Slide 15: Quantitative risks from asbestos exposure
Estimation of risks from environmental exposure in buildings is even more difficult
  Levels of asbestos fibres in asbestos-containing buildings is usually below 0.0005 fibres/ml
  20 years exposure to chrysotile at this level for 40 hours a week produces a lifetime risk of death of 1 in 100,000
  This risk would be greater for continuous exposure or exposure to amosite or crocidolite

## Slide 16: Extent of asbestos related disease
Extensive use of asbestos in the past, with poor control, means that many people have developed asbestos related diseases.
  Long latent period means that in many countries deaths from asbestos related diseases are continuing to rise
USA – approximately 8,000 asbestos related deaths per year
UK – mesothelioma – 153 deaths in 1968, 1969 deaths in 2004, expected to rise to about 2450 deaths in about 2015
UK – total number of deaths due to asbestos in 2004 was about 4,000, expected to peak at about 6,000 a year between 2010 and 2015
Australia – mesothelioma deaths – about 200 per year in the mid-late 1980’s – reaching about 470 in 1999
The number of deaths in these countries should reduce in the next decade

## Slide 17: ‘Exposure limits’ for asbestos
Most countries have maximum permitted levels of exposure to asbestos
  As a ‘safe threshold level’ cannot be established these limits do not represent ‘safe’ levels of exposure and exposure should always be prevented or reduced to as low a level as reasonably practicable
National limits
  USA – ACGIH Threshold Limit Value (TLV) – 0.1 fibres / cm3 averaged over an 8-hour period
  UK – Control limit – 0.1 fibres / cm3 averaged over a 4-hour period
    (Peak exposure limit of 0.6 fibres / cm3 over a ten minute period)
  Australia – National Exposure Standard – 0.1 fibres / cm3 averaged over an 8-hour period

## Slide 18: Typical exposure levels for asbestos
HSG 247 gives the following estimates in fibres/cm3
  Well controlled work with ACMs
    Controlled wet stripping of lagging using manual tools up to 1
    Careful removal of AIB up to 3
    Drilling AIB with shadow vacuuming up to 1
  Poorly controlled work
    Partially wetted or dry stripping of lagging up to 100
    Partially wetted or dry stripping of spray coating up to 1000
    Drilling AIB without shadow vacuuming up to 10
    Power sawing AIB up to 20
    Hand sawing AIB up to 10

## Slide 19: Typical exposure levels for asbestos
As a comparison the DETR Asbestos and MMMF in buildings (1999) gives the following estimates in fibres/cm3
  Background (outdoor) concentration 0.000001 – 0.0001
  In buildings where ACMs are in good condition 0.0005
  Clearance indicator 0.01

## Slide 20: Inhalation studies for other fibres
Many synthetic fibrous materials have been developed as replacement materials for asbestos
  e.g. glass fibre, rock wool, slag wool, refractory ceramic fibres etc
  while these fibres are generally not crystalline and do not split lengthways to form thinner fibres, they can become airborne and may deposit somewhere in the respiratory system
Concerns have been raised over possible health effects, particularly if fibres are of a similar size to asbestos
  Many studies have been undertaken

## Slide 21: Inhalation studies for other fibres
Some animal studies have shown carcinogenicity when fibres directly implanted into lung tissue, however these effects have not been observed by fibre inhalation studies
Some studies have shown that more durable (or bio-persistent) fibres may cause greater health effects
  However, the effects were much less than those associated with asbestos
Many inhalation studies have been undertaken and generally do not indicate significant concerns with regard to lung diseases for most man-made mineral fibres
  However, refractory ceramic fibres appear to be of greater risk than glass fibre

## Slide 22: Health effects of other fibres
Most common effect of many man made mineral fibres is an acute irritation of the skin, eyes and upper respiratory tract
Glass fibre and some synthetic fibres have been classified by IARC as carcinogens since the late 1980’s.
  Originally, glass wool, rock wool and slag wool were placed in Category 2B
  These categories have now been reviewed and they are now placed in Category 3
However, evidence of carcinogenicity has been found for some refractory ceramic fibres that have high bio-persistence and also for some ‘special purpose’ or ‘superfine’ fibres.
  These are classified by the IARC as Category 2B carcinogens

## Slide 23: Health effects of other fibres
Carbon fibres are generally too large to reach the deep lung (alveoli)
  Tend to deposit further up the respiratory system
  Limited information on any fibrogenic or carcinogenic potential
Aramid fibrils have been shown to caused fibrosis in inhalation studies on rats
  Potential to cause cancer not confirmed

## Slide 24: ‘Exposure limits’ for man made mineral fibres
National limits
  UK – Workplace Exposure Limits defined in two ways – a gravimetric limit and a fibre count limit (depending on fibre type involved)
    Most man-made mineral fibres – 5 mg/m3 and 2 fibre/ml
    Refractory ceramic fibres and special purpose fibres – 5 mg/m3 and 1 fibre/ml
  USA – ACGIH Threshold Limit Values
    Most man-made mineral fibres – 1 fibre/ml
    Refractory ceramic fibres – 0.2 fibre/ml

## Slide 25: Typical exposures to MMMF
Exposure usually well controlled during manufacturing
High exposure levels can occur during installation, construction and removal activities
A particular problem can occur during furnace wrecking and demolition work involving refractory ceramic fibre products where these products have been heated to temperatures of 1000oC or above.
  At these temperatures these materials can be converted to cristobalite (a crystalline form of silica that is hazardous by inhalation)

## Slide 26: World Health Organisation approach to eliminating asbestos related diseases
Current estimates
  125 million people in world exposed to asbestos in the workplace
  90,000 people die each year from asbestos related diseases
Current use of asbestos
  Chrysotile still widely used
    90% used in asbestos-cement building materials
    7% used in friction materials
  More than 40 countries (including all of European Union) have banned use of all forms of asbestos
  World production of asbestos still exceeds 2 million tonnes per annum

## Slide 27: World Health Organisation approach to eliminating asbestos related diseases
Most efficient way to eliminate asbestos related disease is to stop using all types of asbestos
Continued use of asbestos in construction industry is a particular concern
Asbestos can be replaced by other materials that pose less risk
Materials containing asbestos should be encapsulated
Generally work should not be undertaken if likely to disturb asbestos
If necessary, work should only be undertaken with precautions such as
  Encapsulation
  Wet processes
  Local exhaust ventilation with filtration
  Regular cleaning
  Personal protective equipment
  Decontamination facilities

## Slide 28: Approaches to eliminating asbestos related diseases
Progressive legislative approach adopted in many countries as hazards became clearer
UK approach typical
  Progressive reduction in ‘control limits’
  Phasing out / banning of high risk products
  Phasing out / banning of types of asbestos
  Increasingly stringent requirements for working with / removing asbestos products
  Licensed contractors for work with asbestos

## Slide 29: Approaches to eliminating asbestos related diseases
Categories of people at risk
  Asbestos product manufacturers / installers
    Phased out in many countries
  Asbestos removal contractors
    Licensed, training, specified controls, minimise fibre release, decontamination procedures, personal protective equipment
  Workers who knowingly work on asbestos products
    Restrict work to lower risk materials, training, minimise fibre release, personal protective equipment
  Workers who unknowingly disturb asbestos products
    Asbestos register, management of asbestos containing materials, information available, permit to work