## Slide 1: M504 - Asbestos – personal protective equipment

## Slide 2: Respiratory protection
Exposure to asbestos should be prevented or reduced as far as reasonably practicable
Airborne fibre concentrations must be reduced to a minimum by means other than respiratory protection
  e.g. good work practices, engineering controls, wet removal, glove-bags, shadow vacuuming
However some processes e.g. asbestos removal may generate airborne fibre concentrations in excess of international and national standards
In these cases effective respiratory protection must be provided and worn correctly
  Respiratory protection can only reduce exposure, not stop exposure

## Slide 3: Respiratory protection
Whatever type of respiratory protection is chosen it should be
  Adequate i.e. capable of providing effective protection
  Suitable i.e. matched to the wearer, task and environment
  Correctly used
  Properly stored, maintained, examined and tested
  Of an appropriate standard e.g. ‘CE’ or ‘NIOSH/MSHA’ marked
  Chosen in consultation with the worker who is to use it

## Slide 6: Respiratory protection
The type of respiratory protection chosen will need to take into account
  Type of work to be done
  Expected fibre concentration
    May not be known in advance
    Often an order of magnitude estimate is made based on previous experience or air monitoring
  Respiratory protection with highest assigned protection factor considered first, then other factors such as working environment, wearer and the need for other personal protective equipment taken into account

## Slide 7: Assigned protection factors (APF)
Assigned protection factors used to predict if a particular type of respiratory protection is adequate to reduce the fibre concentration inside the mask to below the exposure standards
Variation in quoted factors between different countries / organisations
Example calculation:
Fibre concentration in work environment 1.2 fibres/cm3
APF (full face-piece air purifying mask UK) 40
Expected fibre concentration inside mask 1.2 / 40 = 0.03 fibres/cm3

## Slide 8: Respiratory protection – Face mask fit testing
Performance of tight-fitting face masks depends on achieving a good seal between the wearer and the face seal of the mask
Different people have different shapes and sizes of face so one particular type or size of mask will not fit all
Inadequate fit significantly reduces the protection provided to the wearer
To ensure a particular type of mask can provide adequate protection to the wearer a face-fit test should be carried out

## Slide 9: Respiratory protection – Face mask fit testing
Qualitative test
  Based on wearer’s subjective assessment of the leakage of a bitter or sweet tasting aerosol through the face seal
    Can be used for disposable or half-mask respirators
    Not sufficiently sensitive for full-face masks
Quantitative test – objective measure of face fit.
  Most common method measures concentration of particles within the mask relative to the concentration outside the mask under specified test conditions
    Should be used for full-face masks and is preferred method for testing half-masks

## Slide 10: Respiratory protective equipment (RPE) – Face mask fit testing
Face fit test should be undertaken in accordance with validated protocols and by a competent person
Face fit test should be repeated when the wearer
  Changes type, model or size of respirator
  Undergoes substantial dental work or develops facial changes e.g. scars around face seal area
  Significantly gains or loses weight
  In any case it is good practice to repeat test at suitable intervals, based on risk assessment – perhaps every year
  Repeat testing also has benefit of being a ‘refresher training’ on the correct fitting and use of respirator

## Slide 11: Use of respiratory protection
To achieve adequate performance
  Worn correctly – wearer should perform a ‘fit check’ before each use
  Beards or facial stubble will affect face seal of masks that rely on close contact between face and mask – therefore wearer must be clean shaven in face seal area for these types of mask
  Other items can affect seal including hair, jewellery and frames of glasses
Apart from face seal, the ability of a person to wear respiratory protection depends on other factors such as their health status
  Conditions such as asthma, emphysema, chronic airways disease and skin sensitivity may prevent use of respirator

## Slide 12: Personal protective clothing
Coveralls impervious to fibres should be worn
  No external pockets or velcro fastenings
  Disposable coveralls preferred – not re-used and should be disposed as asbestos waste
  Should have hoods – hood worn over any head straps of the respiratory protection
  Elasticated cuffs at wrist and ankle
  Worn over top of footwear to prevent dust / debris entering top of boot
Appropriate footwear
  Easily cleaned and decontaminated
Gloves

## Slide 14: Personal protective clothing
Risks from thermal stress must be taken into account when selecting personal protective equipment
  There may be heat related concerns for those wearing protective clothing, even in moderate thermal environments, if the work is strenuous
Whenever protective clothing is required, it is important to consider where and how the workers will decontaminate