## Slide 1
M504 Risk assessment of asbestos containing materials

## Slide 2: Risk assessment of ACMs
When asbestos containing materials are identified (or presumed to be present) an assessment of the risk they pose should be undertaken to
  Help decide what action is appropriate to deal with the asbestos containing materials
  Help decide which materials should be dealt with first
  Risk is dependent on
    how easily the asbestos containing material can release fibres
    whether the material is likely to be disturbed and
    whether people are likely to be exposed to the fibres
  A number of different risk assessment systems have been developed to take these factors into account

## Slide 3: Flow charts (e.g. HSG 227)
Based on series of flow charts or decision trees leading to a conclusion or action that should be undertaken to deal with an ACM
  These systems lead to consistent outcomes
  Flow charts generally more useful in developing control strategies than as a risk assessment system
  Generally not very good at prioritising which materials should be dealt with first

## Slide 4: Risk assessment systems – Australia (NOHSC 2018)
Provides a list of factors to take into account when undertaking the risk assessment of an asbestos containing material including
  Condition of material (friable, bonded)
  Whether they are liable to damage or deterioration
  Whether nature or location of any work to be carried out is likely to disturb the material
  Results from air monitoring

## Slide 5: Risk assessment systems – Australia (NOHSC 2018)
Does not provide guidance on the relative weighting that the various factors should be given
Relies on the competence of the person undertaking the risk assessment to take various factors into account
Tends to be incorporated into general risk assessment systems

## Slide 6: Risk assessment system (UK) – Algorithms (HSG 264 and HSG 227)
Algorithms are numerical ways of taking into account several factors by giving each factor a score
Scores added to give an overall score
Individual judgement is still required so the process is not exact
Assessment process is transparent so that it can be checked for any discrepancies at a later date

## Slide 7: Risk assessment system (UK) – Algorithms (HSG 264 and HSG 227)
HSE Guidance identifies two areas as
  Material assessment - Ability to release airborne fibres
    Documented in HSG 264
    Commonly used by many organisations in UK
    Completed as part of the survey
  Priority assessment - Human risk factors - needs detailed employer/premises manager input
    Documented in HSG 227
    Less widely used - many organisations have developed own systems
    More difficult to complete as part of the on-site survey

## Slide 8: Risk assessment system (UK) – Algorithms (HSG 264 and HSG 227)
Material risk assessment (potential of the asbestos containing material to release fibres) takes into account
  Product type
  Surface treatment
  Extent of damage/deterioration
  Asbestos type

## Slide 9: Material Assessment Algorithm
Product type (full list in HSG 264 Appendix 4)
  Score 3 Thermal insulation, sprayed asbestos, loose insulation etc
  Score 2 Insulation boards, millboards, textiles, gaskets, ropes etc
  Score 1 Asbestos cement, decorative coatings, composite materials (plastics, resins, roofing felt, vinyl floor tiles) etc

## Slide 10: Material Assessment Algorithm
Surface treatment (full list in MDHS 264 Appendix 4)
  Score 3 Unsealed thermal insulation, sprayed asbestos, loose insulation etc
  Score 2 Unsealed Insulation boards etc Sealed thermal insulation, sprayed coatings
  Score 1 Unsealed Asbestos cement Sealed Insulation boards etc
  Score 0 Composite materials (plastics, resins, vinyl floor tiles etc)

## Slide 11: Material Assessment Algorithm
Damage and deterioration (full list in MDHS 264 Appendix 4)
  Score 3 High damage or delamination, visible asbestos debris
  Score 2 Medium damage, significant breakage or several small areas of damage revealing asbestos fibres
  Score 1 Low damage, a few scratches or surface marks, a few broken edges on boards, tiles etc
  Score 0 No visible damage

## Slide 12: Material Assessment Algorithm
Asbestos type
  Score 3 Crocidolite
  Score 2 Amphibole asbestos excluding crocidolite
  Score 1 Chrysotile

## Slide 13: Material Assessment Algorithm
Additive score between 2 & 12
  10 + high risk
  7-9 medium risk
  5-6 low risk
  < 4 very low risk

## Slide 14: Priority risk assessment - HSG 227
Potential for people to be exposed to asbestos
  Note - criteria can be adapted to site circumstances
Four areas identified for assessment
  Occupant activity
  Likelihood of disturbance
  Human exposure potential
  Maintenance activity
Each of the four areas are sub-divided
  Each sub-division is given a score and the average for each area is calculated

## Slide 15: Priority risk assessment - HSG 227
Occupant activity
  Primary activity
    Score 3 - High disturbance - e.g. door with AIB panel in constant use
    Score 2 - Medium disturbance - e.g. industrial activity that may contact ACM’s
    Score 1 - Low disturbance - e.g. office type activities
    Score 0 - Rare disturbance - e.g. little used store room
  Secondary activity - consider above criteria

## Slide 16: Priority risk assessment - HSG 227
Likelihood of disturbance
  3 sub-divided categories
    Location
    Accessibility
    Extent / amount
  Location
    Score 3 - Confined spaces
    Score 2 - Room up to 100 m2
    Score 1 - Large rooms or well ventilated areas
    Score 0 - External

## Slide 17: Priority risk assessment - HSG 227
Likelihood of disturbance (continued)
  Accessibility
    Score 3 - Routinely disturbed
    Score 2 - Easily disturbed
    Score 1 - Occasionally likely to be disturbed
    Score 0 - Usually inaccessible or unlikely to be disturbed
  Extent / Amount
    Score 3 - > 50 m2 or > 50 m pipe run
    Score 2 - 10 - 50 m2 or 10 - 50 m pipe run
    Score 1 - < 10 m2 or < 10 m pipe run
    Score 0 - Small amounts or items e.g. gaskets

## Slide 18: Priority risk assessment - HSG 227
Human exposure potential
  3 sub-divided categories
    Number of occupants
    Frequency of use of area
    Average time area is in use
  Number of occupants
    Score 3 - > 10
    Score 2 - 4 to 10
    Score 1 - 1 to 3
    Score 0 - None

## Slide 19: Priority risk assessment - HSG 227
Human exposure potential (continued)
  Frequency of use of area
    Score 3 - Daily
    Score 2 - Weekly
    Score 1 - Monthly
    Score 0 - Infrequent
  Average time area is in use
    Score 3 - > 6 hours
    Score 2 - 3 - 6 hours
    Score 1 - 1 - 3 hours
    Score 0 - < 1 hour

## Slide 20: Priority risk assessment - HSG 227
Maintenance activity
  2 sub-divided categories
    Frequency of maintenance activity
    Type of maintenance activity
  Frequency of maintenance activity
    Score 3 - More than once per month
    Score 2 - More than once per year
    Score 1 - Once per year or less frequently
    Score 0 - ACM unlikely to be disturbed

## Slide 21: Priority risk assessment - HSG 227
Maintenance activity
  Type of maintenance activity
    Score 3 - High levels of disturbance e.g. moving a number of ceiling tiles for re-cabling
    Score 2 - Medium disturbance e.g. lifting a few ceiling tiles to access a valve
    Score 1 - Low disturbance e.g. changing light bulbs adjacent to asbestos insulation board ceiling
    Score 0 - Minor disturbance e.g. possibility of contact when gaining access

## Slide 22: Overall Risk Assessment (MDHS 100 and HSG 227)
Overall risk rating derived by adding the material risk assessment and the priority risk assessment
  Notes
    No official guidance to the significance of the total risk rating number - many organisations have developed in-house categories for subsequent action plans
    Some of the criteria used are subjective - so it is not an exact science
    Gives useful information on relative risk - but should not drive management actions purely based on numbers
    Can be used to demonstrate reduction in risk

## Slide 23: Risk assessment system (USA) – Environmental Protection Agency (EPA)
EPA document gives guidance on assessing need for abatement, determining its timing and choosing an abatement method
It considers three types of material
  Surfacing materials
  Pipe and boiler insulation
  Other materials
It assumes asbestos containing materials are included in a management programme
  Likelihood of fibre release determines the need and timing of additional action
  Nature and location of the asbestos containing material determines the abatement method

## Slide 24: Risk assessment system (USA) – Environmental Protection Agency (EPA)
Factors taken into account when assessing potential fibre release
  Current condition of asbestos containing material
    Evidence of deterioration or delamination
    Evidence of physical damage
    Evidence of water damage
  Potential for future disturbance, damage or erosion
    Proximity to air plenum or direct airstream
    Visibility, accessibility and degree of activity
    Change in building use
  Guidance given on each of the categories and simple ratings such as ‘present’, ‘absent’, ‘high’ or ‘low’ given. Numerical values are not given to each factor.

## Slide 25: Risk assessment systems
Whatever risk assessment system is used a number of general principles apply
  They should be appropriate for, and adapted if necessary for the specific situation of the organisation
  They should be undertaken by persons who are competent and have sufficient training
  They should be reviewed regularly in accordance with any National legislative requirements and whenever there have been significant changes