## Slide 1
M504 - Management of asbestos containing materials

## Slide 2: Management of asbestos containing materials
The potential hazards of asbestos can only occur if the fibres become airborne
  If asbestos containing materials are in good condition, well sealed and unlikely to be disturbed, it is better they are left in place and managed
  The control options for dealing with asbestos containing materials fall into 3 broad categories
    Manage the material to prevent fibre release
    Repair / seal the material and then manage to prevent fibre release
    Remove the material

## Slide 3: Management of asbestos containing materials
Develop, implement and maintain an asbestos management plan
Investigate if asbestos containing materials are present
Develop and maintain a register of asbestos containing materials, including details on locations, accessibility and condition
Develop measures to either remove the asbestos containing material or to minimise the risks and prevent exposure to asbestos
Ensure the control measures are implemented
Ensure the management plan is regularly reviewed

## Slide 4: Management of asbestos containing materials
If asbestos abatement work is not urgent it will be less costly if combined with other repair, renovation or maintenance work
Other factors that influence the timing of any asbestos abatement work include
  Pattern of normal work operations
  Any legal requirements / liabilities
  Expected useful life of the plant or building
  Pressures from building occupiers, users, public
Legislation in different countries should be checked to ensure compliance

## Slide 5: Management of asbestos containing materials
Information and training should be provided to workers, contractors and others who may come into contact with asbestos containing materials. This may include:
  Health risks of asbestos
  Types, uses and likely occurrence of asbestos containing materials
  Where the asbestos register is located and how to access it
  Procedures to prevent exposure to asbestos
  Where applicable, correct use of control measures, personal protective equipment and work methods to minimise risks
  Any applicable exposure standards
  Purpose of any air monitoring or health surveillance

## Slide 6: Development of an asbestos management plan
Purpose is to aid compliance with asbestos legislation and prevent exposure to asbestos fibres while asbestos containing materials remain in workplace
General principles that should be applied
  Aim should be for workplace to be free of asbestos. Consider removal of ACMs during refurbishment and/or maintenance
  Priority given to dealing with friable asbestos containing materials that are accessible
  Reasonable steps must be taken to label all ACMs. Locations of all ACMs recorded in register
  Risk assessment conducted for all ACMs

## Slide 7: Development of an asbestos management plan
General principles that should be applied (contd)
  Suitable controls implemented to prevent exposure to airborne asbestos
  Should be full consultation with workers during all stages of development of the management plan
  Identification of asbestos containing materials and subsequent risk assessments must be undertaken by competent persons
  Workers, contractors and others who may be exposed to asbestos, must be provided with information on health risks and appropriate control measures

## Slide 8: Content of an asbestos management plan
Should be comprehensive and include
  Asbestos register
  Mechanisms for providing all relevant people with information about
    location, type and condition of asbestos containing materials,
    risks they pose, and
    control measures to eliminate or minimise these risks
  Decisions about management options
  Timetable for action
  Arrangements for periodic inspections
  Monitoring arrangements
  Responsibilities of all persons involved
  Training arrangements
  Procedure and timetable for review of all aspects

## Slide 9: Content of an asbestos management plan
Should be clear and unambiguous
  Should set out aims of the plan, what is going to be done, when and how it is going to be done and by whom
  Clear lines of responsibility
  Person with overall responsibility identified
Asbestos register should be kept up to date and readily available
  Must be reviewed at suitable intervals e.g. annually
  If there have been significant changes, or
  If there is reason to believe it is no longer valid
Some materials present little hazard (e.g. mastics, roofing felts etc). These should still be included, to document they have been considered, found to be of minimal risk, with no specific actions required

## Slide 10: Control of risks from asbestos containing materials
Management actions
  Isolate / restrict access
    Restricted zones with controlled entry
    Permit to work system
  Information / training
    Suitable and sufficient labels / warning signs
    Awareness training, induction and refresher training
  Monitor condition of asbestos containing materials
    Periodic inspection
    System in place for reporting damage / deterioration
  Maintain and update asbestos register
    Formal system in place

## Slide 11: Control of risks from asbestos containing materials
Control actions
  Repair damaged asbestos containing materials
    Use appropriate fillers and coatings
  Encapsulate to prevent release of airborne fibres
    Alkali resistant paint for cement products
    High solids emulsion paint for insulating boards
    Proprietary bituminous or semi-flexible polymeric coatings
  Enclose / protect
    Physical barriers or covering panels
  Remove
    Competent persons, appropriate control measures

## Slide 12: Reviews of the asbestos management plan
Management plan should be reviewed at suitable intervals
  Annual review?
  Whenever there have been significant changes, or if it is believed the plan is no longer valid
  Review should critically examine effectiveness of asbestos management plan
Common problems relating to asbestos management