## Slide 1
M504 - Air sampling

## Slide 2: Air sampling – principle
Air drawn through a filter by means of a sampling pump
  at a known flow rate for a measured period of time
In the most commonly used method the filter is mounted on a slide and ‘cleared’ (made transparent)
  A proportion of the filter is examined using phase contrast optical microscopy and particles that conform to certain size criteria are counted
  Fibre concentration in fibres / cm3 of air is calculated
Other techniques such as electron microscopy are sometimes used

## Slide 3: Types of air monitoring
Personal sampling
  Undertaken within breathing zone of operative
    As close to mouth and nose as practicable (and in any case within 200 mm)
    Usually on upper lapel or shoulder of worker’s clothing
    Important to ensure that inlet to the sampling head is not obstructed by the clothing or protective clothing
Static sampling
  Usually undertaken with filter holder positioned between 1 and 2 metres above floor level

## Slide 4: Types of air monitoring
Personal sampling
  To assess the suitability of respiratory protective equipment being worn
  To check the effectiveness of control measures in place to control fibre release
  To assess compliance with relevant control limits or exposure standards

## Slide 5: Types of air monitoring
Static sampling
  Background sampling - to establish fibre concentrations prior to any activity that may lead to airborne fibre release
  Leak monitoring - to confirm that the controls in use are sufficient to prevent the spread of asbestos fibres and that the integrity of the enclosure is being maintained
  Clearance air monitoring - as part of a clearance certification procedure to verify an area is suitable for re-occupation
  Reassurance sampling - may be undertaken to confirm residual airborne fibre levels (e.g. after removal of an enclosure in a building or enclosed area)

## Slide 6: Air sampling procedures
The ‘membrane filter’ method is typically used to measure airborne fibre concentrations
  To obtain reliable and consistent results sampling and analysis should be undertaken by suitably trained persons who participate regularly in inter-laboratory quality control programmes
  Historically the membrane filter method has produced very unreliable results
    May still be a significant problem if analysis undertaken by non-accredited laboratories or by non-standard methods

## Slide 7: Air sampling procedures
Large differences in results between individual analysts and different testing laboratories can arise from
  Variations in sampling method and sample preparation
  Variations in quality, specification and set-up of microscope
  Particularly from subjective effects associated with the visual counting of fibres
Controlling these sources of error requires application of standard procedures and establishment of a reproducible routine
  Many countries have adopted the procedures set out in the WHO method

## Slide 8: Air sampling procedures
Comparability of results between different microscopists and laboratories can be improved by proper training and quality control systems
Microscopists should take part in intra-laboratory counting checks
Laboratories should take part in external proficiency testing programmes
Competence of testing laboratories can be demonstrated through National accreditation bodies such as UKAS, NATA and AIHA to the requirements of ISO 17025
Other potential problems with the method are:
  ‘Non-asbestos’ fibres of respirable size may be counted as asbestos
  Large amounts of ‘non-asbestos’ dust may overload the sampling filters, making microscopical examination difficult or impossible

## Slide 9: Sampling pumps
Sampling pumps should be capable of
  Providing a smooth airflow
  Having flow set to +/- 5% for flows of more than 2 litre/min
  Having flow set to +/- 10% for flows of 2 litres/min or less
  Maintaining this flow during period of sampling
    most modern pumps have built-in flow sensors that should ensure steady flow rates throughout sampling period
  Size and type of sampling pump depends on application

## Slide 10: Sampling pumps
Pumps for personal monitoring
  Should be light and portable enabling it to be worn on belt or in pocket
  Flow rates usually between 1 and 4 litres/minute
Pumps for static monitoring
  Can be much larger and pumps capable of flow rates up to 8 or even 16 litres/minute are available
    Higher flows enable sampling periods to be reduced
    Usually incorporate a means where the sampling head can be positioned between 1 and 2 metres above ground level

## Slide 11
Low flow pump and sampling head
High flow pump and sampling head on stand

## Slide 12: Sampling heads
WHO method requires sampling head to be
  Open faced filter holder with an electrically conducting cylindrical cowl
    Cowl to protect filter while still permitting a uniform deposit
    Cowl must point downwards during sampling
  Exposed part of filter at least 20 mm in diameter
  Cap or bung to protect filter from contamination during transport
  If re-used should be cleaned and dried prior to loading of new filters

## Slide 13
Filter head
Filter head (exploded view)
‘Gridded’ membrane filter

## Slide 14: Membrane filters
Mixed esters of cellulose or cellulose nitrate
Pore size of 0.8 to 1.2 micron
25mm diameter with printed grid
  Printed grid on sampling side of filter - grid lines will be in same plane as collected particles and will therefore provide a useful focussing aid
Filters should be loaded, unloaded and analysed in an area free from fibre contamination
Should be handled using flat-tipped tweezers
Filter blanks should be submitted with each batch of samples

## Slide 15: Flow measurement
Airflow measured using a flow meter
  Should be sensitive enough to measure flow to required tolerances
    Flow meters in sampling pumps generally not sufficiently accurate so a separate external ‘working’ flow meter used
  ‘Working’ flow meter should be calibrated against a ‘master’ or ‘reference’ flow meter that has been calibrated against a primary standard
    For convenience on-site working flow meter is often a ‘float’ type
    ‘Float’ type flow meters must be held vertically
    Master flow meter may be a float type, a bubble flow meter or a ‘dry-cal’ type

## Slide 16
‘Float’ type flow meter
‘Bubble’ flow meter

## Slide 17: Flow measurement
The inlet of the flow meter must be open to atmosphere
  i.e. it must be the first item in the sampling train
Temperature and pressure corrections generally not required
  unless conditions are significantly different from the calibration conditions (e.g. at least 20oC and / or at least 40 millibars from calibration conditions)
Master flowmeter must be traceable to National standards
  most laboratories send these to an accredited calibration laboratory for re-calibration every 12 months

## Slide 18: Sampling procedures
Taking the sample
  Remove entire protective cap or bung from the filter holder
  Start pump and record time
  Measure flow rate at start and end of sampling period
    The flow variation between the start and end of the sampling period should be within +/- 10% or the sample rejected
  Record time at end of sampling period
  Replace protective bung or cap
  Filter preferably transported for analysis in the capped filter holder

## Slide 19: Air sampling strategies
WHO method valid for determining fibre in air concentrations ranging from quantification limit (0.01 fibres/cm3) up to 100 fibres/cm3
For maximum accuracy the sampling strategy should aim to achieve the optimum density of fibres on the filter of between 100 and 650 fibres/mm2
  Therefore smaller volumes of air may be required for personal or compliance monitoring where airborne fibre concentrations are potentially higher than those likely to be found during background, leak or clearance monitoring

## Slide 20: Typical volumes etc table
Application | Sampling rate (litres/min) | Sample volume (litres) | Graticule areas examined | Limit of quantification (fibres/cm3)
Compliance sampling | 1 – 4 | 240 | 100 | 0.04
Assessment of respiratory protection | 1 – 4 | 240 | 100 | 0.04
Clearance sampling | 2 – 16 | 480 | 200 | 0.01
Background, leak, reassurance | 2 – 16 | 480 | 200 | 0.01
Limits of quantification based on sampling onto 25 mm filters

## Slide 21: Air sampling strategies
In general, the larger the volume of air sampled, the lower the concentration of fibres in air that can be reported
  However, practical limit to this approach as too dense deposits of dust on the filter makes examination of filter difficult or impossible
  Limit of quantification (LOQ) can be varied by changing the volume of air sampled or the number of graticule areas examined e.g.
    480 litre sample, 200 graticule areas – LOQ 0.01 fibre/cm3
    240 litre sample, 200 graticule areas – LOQ 0.02 fibre/cm3
    960 litre sample, 100 graticule areas – LOQ 0.01 fibre/cm3

## Slide 22: Sampling strategies
Personal sampling
  Filter holder positioned in breathing zone of worker
    it is important that the person being monitored is identified, together with at least the following information
      Work being undertaken at time of sampling
      Any environmental factors that may affect the result
      Type of protective equipment (particularly the type of respiratory protection) being used

## Slide 23: Types of air monitoring
Background or reassurance sampling
  The number and position of sampling points should cover likely sources of fibre release and areas where people are likely to be
  Fewer measurements may be appropriate for background or reassurance sampling than for clearance monitoring
  To achieve the limit of quantification of <0.01 fibres/ml each measurement typically results from a air sample of at least 480 litres with 200 graticules examined

## Slide 24: Types of air monitoring
Leak testing
  Measurement of fibre concentration outside the enclosure to check the integrity of the enclosure is being maintained
    Used to support initial smoke test and frequent thorough visual inspections of the enclosure during removal work
  Sample positions to consider would include
    Near openings such as the entry / exit airlocks
    Near the exhausts of air extraction equipment
    Near areas that may be difficult to seal completely
  It may be desirable to sample at higher flow rates or shorter periods to get a more rapid result
    Ensure the correct limit of quantification is applied if < 480 litres air sampled

## Slide 25: Recording calibration and sampling information
To ensure results are traceable and the purpose and outcome of sampling is clear it is important that sufficient information on the sampling and subsequent analysis is recorded
Sampling and analytical records should contain relevant site information and other information to
  establish traceability of any calibrations
  calculate the results and
  assure the quality of the sampling and analysis

## Slide 26: Recording calibration and sampling information
Details of the sampling that should be documented
  Date and location of sampling
  Type of sampling carried out
  Relevant environmental conditions and activities taking place during the sampling period
  Type and identification numbers of equipment including
    Sampling pumps
    Flow measurement devices
    Filters and sampling heads
  For each sample
    Unique identifier and specific sample position
    Start and finish time for each sample
    Flow checks at start of (during) and finish of sampling

## Slide 27: Recording calibration and sampling information
Details of the analysis that should be recorded
  Method of analysis
  The limit of quantification or limit of detection
  Details of the microscopical analysis including
    Measured diameter of the graticule
    Sets of lines visible on test slide
    Number of graticule areas examined
    Number of fibres counted
    Measured diameter of exposed area of filter
  Type and identification of equipment used including
    Microscopes
    Test slides and micrometers

## Slide 28: Clearance sampling and certification
Clearance inspection and sampling may be undertaken following removal of asbestos containing materials to determine if area is suitable for re-occupation
  Air samples taken and analysed to establish airborne fibre levels and compared with a ‘clearance indicator’
Requirement for clearance inspection and sampling determined by specific regulatory requirements or in their absence by normal risk assessment procedures
  Work with friable material that required an enclosure is likely to need independent clearance inspection and sampling
  Removal of lower risk materials such as asbestos cement or small amounts of asbestos in external locations may only require a visual inspection

## Slide 29: Clearance sampling and certification
  Competency of person conducting clearance inspection is critical to a credible programme
  Competent person should also be independent of those undertaking removal work
    In many countries there are specific regulatory requirements covering the above
  Air monitoring is only part of the clearance certification process. Of equal or greater importance is establishing the scope of work and undertaking a thorough visual inspection
  Any protective barriers or enclosures should remain in place until successful completion of the clearance inspection and monitoring

## Slide 30: Clearance sampling – visual inspection
Visual inspection is the most critical part of the clearance procedure
  Should verify that all of the work has been performed in manner specified
  Presence of visible asbestos debris after removal works have been ‘completed’ means further decontamination is required
  If either the work has not been fully completed or visible contamination remains the site is not ready
  Clearance air sampling should not be started until all visible deficiencies have been corrected

## Slide 31: Clearance sampling – visual inspection
Asbestos containing dust produced during the removal process will have spread inside the enclosure
  This and any residual dust on inadequately cleaned surfaces can present on-going risk to future users / occupants
Thorough visual inspection of all surfaces should be undertaken
  Close and detailed inspection
  Particular attention should be paid to areas where dust may have settled
  Areas that are difficult to reach should not be excluded
  Access equipment may be required
  Airlocks included in inspection

## Slide 32: Clearance sampling – visual inspection
Minor amounts of dust / debris may be cleaned by the removal workers at this stage
If amount of dust / debris remaining is more substantial and indicates that the area has not been thoroughly cleaned, the inspection should be stopped and the removal workers told to re-clean the whole area

## Slide 33: Clearance – air sampling
Undertaken after satisfactory visual inspection and when area is dry
  Most widely used method for determining fibre in air concentrations is the WHO method
  Limit of quantification of this method (based on 480 litre samples and counting 20 fibres) is 0.01 fibres/cm3
  This level has also been found to be reasonable to achieve with adequate cleaning and contamination
  0.01 fibres/cm3 has been widely adopted as a clearance indicator (e.g. UK, Australia, South Africa etc)
    USA has recommended volume of 3000 litres – however use 37mm filter instead of 25mm, and 100 graticule areas instead of 200 – limit of quantification is also usually 0.01 fibres / cm3

## Slide 34: Clearance – dust disturbance
To ensure air testing represents ‘worst-case’ situation
Purpose is to render airborne any traces of dust or debris that were not visible during the visual inspection
Duration and extent of dust disturbance affects amount of fibres rendered airborne
  Various attempts have been made to standardise dust disturbance protocol e.g.
  UK - brushing of surfaces where asbestos has been removed from as well as any surfaces that dust may have settled on. Duration of dust disturbance – undertaken for at least 1.5 minutes per measurement point at start of sampling period
  USA - utilise fans, compressed air or leaf blowers

## Slide 35: Clearance – air sampling
Samples distributed throughout the enclosure, with particular attention paid to areas where asbestos has been removed
Number of measurements (480 litres each) depends on size of the enclosure
  Larger enclosures require more measurements
  Except for very small enclosures there should always be at least measurements
  Guidance on the minimum numbers of measurements is given by the HSE (UK) – see next slide. More measurements may be required if the area is sub-divided e.g. a floor of a building divided into many rooms

## Slide 36: Clearance – typical minimum number of air sample measurements
Enclosure area (m2) | Enclosure volume (m3) | Minimum number of measurements
N/A | < 10 | 1
< 50 | 150 | 2
100 | 300 | 3
200 | 600 | 4
500 | 1500 | 6
1000 | 3000 | 9
5000 | 15000 | 16
10000 | 30000 | 20

## Slide 37: Multi-stage clearance certification
Many regulatory authorities require clearance certification for certain types of asbestos removal works
Multi-stage clearance certification is used in many countries to allow inspection and assessment to be performed in a structured, systematic and consistent manner
In UK four stages to the certification for reoccupation
  Stage 1 Preliminary check of site condition and job completeness
  Stage 2 Thorough visual inspection inside enclosure / work area
  Stage 3 Clearance air monitoring
  Stage 4 Final assessment after enclosure / work area dismantling

## Slide 38: 4-stage clearance certification (UK)
Stage 1 – preliminary check
  Establish the scope of work detailed in the plan of work has been carried out
  Diagram (or photos) of enclosure and surrounding areas prepared detailing main features and dimensions
  Analyst should check:
    Hygiene facilities intact, operational and clean
    Areas around enclosure free from obvious contamination
    Integrity of enclosure
    Any air extraction in place and operational
    Through viewing panels to gain initial impression of job completeness and suitability of area

## Slide 39: 4-stage clearance certification (UK)
Stage 2 – thorough visual inspection
Stage 3 – air monitoring
Stage 4 – final assessment (post-enclosure dismantling)
  Reassurance monitoring may be carried out during dismantling of enclosure
  After enclosure removed, visual inspection of area to ensure it is clean, as well as a re-inspection of waste routes and transit routes for debris

## Slide 40: Clearance certification
Important that person / organisation undertaking clearance certification is
  Competent
  Independent from organisation that undertook the asbestos removal
  In many countries should be accredited to ISO 17025 through their relevant National body
    e.g. UKAS in the UK, NATA in Australia
  The issue of a certificate by an independent and competent organisation provides crucial reassurance and security to subsequent building users

## Slide 41: Clearance certification
Certificate of reoccupation should
  Record completely and unambiguously sequence of events that have occurred
  Enable all parties to understand scope and extent of the clearance
  Enable all parties to be aware of issues identified and dealt with
  At each stage analyst and asbestos removal workers representative should sign to acknowledge outcome
  Certificate provides evidence of when outcome was communicated
  Each certificate should have unique reference number

## Slide 42: Inspection certificate for the hygiene facilities
On completion of removal works the hygiene facility should also be inspected and tested
Should be clean and dry before inspection and all potentially asbestos contaminated materials removed
Thorough visual inspection, dust disturbance and clearance air monitoring should be undertaken in shower and dirty end
Separate inspection certificate should be issued for the hygiene facility