## Slide 1
M504 - Asbestos removal

## Slide 2: Preparation of work specification
The decision to remove asbestos containing materials should be based on the application of the management plan
As part of the process the asbestos removal contractor or workers will need to be provided with details of the asbestos removal requirements
Whoever engages an asbestos removal contractor should either
  Have enough knowledge to critically assess contractor’s competency and plan of work, or
  Engage a separate and independent third party to provide this review

## Slide 3: Preparation of work specification
NOHSC: 2002 (2005) states that the work specification should include:
  Descriptions of asbestos containing materials to be removed, including type, condition and quantity
  Details of any section or materials to be left in place
  Areas to be cleaned or decontaminated
  Types of fittings / supports and if these are to be removed
  How the asbestos waste is to be disposed
  Arrangements for clearance inspections and air monitoring

## Slide 4: Preparation of work specification
NOHSC:2002 (2005) states work specification should include:
  Details of location of the removal
    Indoors, outdoors but protected, exposed to outside weather, enclosed in ducts or in trenches below ground level
  Difficult / unusual site conditions and access e.g. working at height
  Areas that are difficult to access e.g. wall and ceiling cavities
  Details of areas that have not been accessed but could contain asbestos
  Safe work procedures for dealing with any unexpected asbestos found during removal work

## Slide 5: Preparation of work specification
NOHSC: 2002 (2005) states that the work specification should include:
  Details of any residual heat in pipework, boilers, plant etc
  Other temperature considerations
  Location of electrical equipment and supplies that need to be isolated or protected
  Unusual or specific hazards associated with the removal area
  Site occupancy restrictions and conditions including access, egress and emergency arrangements

## Slide 6: Preparation of work specification
Other issues not specifically identified in NOHSC: 2002 (2005) include:
  Confined spaces (often an issue in asbestos removal work)
  Any hazardous chemicals or materials (other than asbestos) that might be present
  What provisions and procedures will be implemented for communications with the site manager / owner

## Slide 7: Preparation of job specification
Contractors / workers must be competent to undertake the removal work
In many countries asbestos removal contractors / workers have to be registered or licensed to work with the higher risk asbestos containing materials
  UK - the Health and Safety Executive issues licenses to work with asbestos coatings, asbestos insulation and asbestos insulating board
  Australia – the relevant State Occupational Health and Safety Authority issues licenses to asbestos removalists to remove friable asbestos containing materials and larger quantities of non-friable asbestos containing materials

## Slide 8: Preparation of job specification
The fact that a contractor holds a licence should ensure they meet certain minimum criteria
  However, this does not necessarily mean that
    They are competent for all types of removal work, or
    They will undertake the work correctly
  Therefore, it is important to
    Critically review their plan of work
    Critically review their competence
    Undertake audits of their work

## Slide 9: Preparation of job specification
  In many jurisdictions it is a requirement to notify work with asbestos to the relevant regulatory authority
  Depending on local requirements this duty may be placed on the site owner or on the removal contractors. It is important to establish who is responsible for any notifications
    In UK, for most work with asbestos insulation, asbestos spray coating and asbestos insulating board, the asbestos removal contractor must give 14 days notice to the enforcing authority prior to the commencement of the work
    Similarly, in Australia, notification to the relevant authority is also required.

## Slide 10: Asbestos removal – risk assessment
A risk assessment will need to be undertaken to establish
  risks associated with the work and
  the precautions needed to prevent or minimise the risks
This should ensure that
  Scope of the proposed work is fully considered
  Appropriate work methods are identified so that exposure to asbestos is adequately controlled and legal obligations satisfied
Carried out by a competent person and should describe the work, the expected exposures and the methods of control
Should be recorded in writing and form basis of plan of work
Should also include non-asbestos risks such as falls from height, electrical safety, heat stress, confined space work etc

## Slide 11: Asbestos removal – plan of work
Plan of work (often called method statement)
  Details the specific work methods and controls for a particular job at a particular location
  Source of reference for asbestos removal team
  Is an active document and if any significant changes on-site are necessary can be amended
    Changes communicated to employees
    Changes may need to be communicated to enforcing authorities
  Followed as far as reasonably practicable
    If cannot follow plan, stop work until new plan drawn up

## Slide 12: Asbestos removal – plan of work
Information to be included (NOHSC)
  Details of asbestos containing materials to be removed
    Location
    Whether friable or non-friable
    Type
    Condition
    Quantity

## Slide 13: Asbestos removal – plan of work
Information to be included (NOHSC)
  Preparation / planning
    Responsibilities assigned
    Commencement and completion dates
    Emergency plans
    Asbestos removal boundaries, type and level of isolation required, location of signs and barriers
    Control of electrical and lighting installations
    Personal protective equipment to be used
    Details of air monitoring
    Waste storage and disposal

## Slide 14: Asbestos removal – plan of work
Information to be included (NOHSC)
  Removal
    Methods to be used for removing asbestos
    Asbestos removal equipment
    Details on required enclosures
      size, shape and structure
      location of negative pressure exhaust units
    Decontamination units required
      Type, location, power and water requirements
    Other controls required

## Slide 15: Asbestos removal – plan of work
Information to be included (NOHSC)
  Decontamination and waste disposal
    Detailed procedures for
      Decontamination of workplace
      Decontamination of tools and equipment
      Personal decontamination
    Methods of disposal for asbestos wastes, including disposable personal protective equipment and structures used to enclose the removal area

## Slide 16: Asbestos removal – plan of work
Other considerations
  Should be kept on-site and available for anyone involved in the removal work including anyone involved in testing or monitoring of removal work
  Throughout the removal work, the site owner or operator should
    Have a competent representative checking the contractor to ensure work plan is being implemented
    Check that any site operations that may potentially affect the contractor are properly communicated and planned for
  Site specific emergency plan should be included
    Exit arrangements and emergency communications
    Decontamination procedures might need to be temporarily waived in event of an emergency

## Slide 17: Asbestos removal – plan of work
Other considerations
  Removal of asbestos from hot surfaces
    Work should be planned to avoid removal of asbestos from hot surfaces
    Scheduled and planned around shut-downs allowing sufficient time to cool
    Removal of friable asbestos from hot surfaces presents particular problems as wetting is ineffective
    Hot removal should only be used in emergency situations
  Heat stress
    Must be considered particularly in selection of protective equipment and work schedule
    Potential problems increased whenever work is contained within an enclosure

## Slide 18: Asbestos removal - enclosures
The need for and type of enclosure required depends on
  the type and quantity of materials being removed
  the location and the removal methods
These and any regulatory requirements are considered in the risk assessment when preparing the plan of work
Enclosure – a physical barrier around the asbestos work area to prevent spread of asbestos waste and dust to surrounding environment
  Access to enclosure regulated by entry and exit openings (airlocks) that also allow for decontamination of personnel and equipment
  Enclosure designed and constructed so that size and number of openings (and leaks) are minimised
  Enclosures should be under mechanical ventilation

## Slide 20: Asbestos removal - enclosures
Anybody entering enclosure should wear suitable personal protective equipment and decontaminate on leaving enclosure
Regulations frequently require an enclosure when working on most hazardous types of asbestos products
  Australia – friable asbestos containing materials
  UK – asbestos insulation, asbestos spray coating, asbestos insulating board

## Slide 22: Asbestos removal - enclosures
Enclosures may also be needed for lower risk materials such as asbestos cement if
  extensive breakage required or
  removal work is in a particularly sensitive area
However sometimes enclosures may not be practicable e.g.
  Working on high level pipework outside or
  Scale of work is very small and risk of fibre release is very low
In absence of enclosure, other measures must be in place e.g.
  Restricting access by barriers
  Work methods that minimise dust generation and prevent spread of contamination

## Slide 23: Asbestos removal - enclosures
Enclosure design and main features
  Suitable size taking into account working requirements and need for any plant or equipment to be used
    However, should not be over-sized as this increases potential for asbestos contamination and ventilation requirements. Also adds to cost of construction
  May make use of parts of existing structure e.g. walls, ceilings or may be free standing
  Surfaces smooth and impervious, usually achieved by use of lining material such as polythene
  Sealed as far as possible
    Particular attention paid to sealing around pipes, ducts etc that pass through into adjoining areas
    Openings sealed with tape, sheeting or expanding foam etc

## Slide 26: Asbestos removal - enclosures
Enclosure design and main features
  Sufficient negative pressure (mechanical ventilation)
    To provide additional control if any small or accidental leaks
    To avoid creating a confined space and to reduce exposure by reducing airborne fibre concentrations
    To control air movement during personnel and waste transfers to and from the enclosure
    More than one air extraction unit may be required
    For very large work areas it may be better to sub-divide it into a number of smaller enclosures

## Slide 28: Asbestos removal - enclosures
Enclosure design and main features
  Ideally access to the enclosure should be directly from the decontamination unit via a short space or tunnel
  However, often this is not practicable and a ‘transiting’ arrangement is used where workers enter and leave the enclosure via a three stage airlock
  Ideally enclosures should have separate airlock arrangements for removal of waste
  Should be able to see into the enclosure without the need to enter it. Sufficient viewing panels should be installed in the ‘walls’ of the enclosure or use of CCTV / webcam considered

## Slide 30: Asbestos removal - enclosures
Construction of enclosures
  Area may need pre-clean / preparation prior to construction of enclosure
    Remove non-asbestos dust and debris
    Removing movable items
    Sheeting over non-movable items
  Part or all of enclosure may require use of a temporary frame or structure to which impervious sheeting is securely fixed
    Timber most commonly used, may also use scaffolding
    Polythene sheeting is most widely used material
  Other factors to consider
    If external, wind and weather conditions
    If it is over permeable surfaces such as gravel or soil

## Slide 31: Asbestos removal - enclosures
Construction of enclosures
  Polythene sheeting must be of sufficient strength
    Australia (NOHSC) states for most jobs heavy duty plastic sheeting of 200 micron thickness suitable
    UK (HSE) states for most jobs sheeting of 250 micron thickness (1000 gauge) suitable
    Exposed locations may require stronger materials such as nylon mesh reinforced poly vinyl chloride (PVC) sheeting
    Where fire hazards occur, flame retardant polythene sheeting should be used

## Slide 32: Asbestos removal - enclosures
Construction of enclosures
  Airlocks / bag-locks sufficient size
    UK (HSE) requires minimum size of 1m x 1m x 2m
    Access openings constructed to prevent asbestos dust passing from one compartment to another
      Vertical slit in dividing panel
      Slit covered by flap on onside
      Flap weighted at the base
  Floor of enclosure covered by impervious material unless floor is impervious and easily cleaned
    Polythene sheeting or
    Polythene sheeting covered by hardboard or similar material

## Slide 33: Asbestos removal - enclosures
Air extraction equipment
  To provide negative pressure within enclosure
  Location of extraction equipment chosen to achieve effective airflow management through enclosure
    Make-up air mainly achieved by air flowing in through the airlocks
    Ideally inlet furthest from airlocks so air is purged through whole of enclosure
    May require use of additional flexible ducting to position inlet effectively
    Large areas may require more than one extraction unit

## Slide 34: Air extraction unit
Source: HSE Guidance Note HSG 247 – reproduced
under the terms of the click-use licence

## Slide 38: Asbestos removal - enclosures
Air extraction equipment
  Provides adequate filtration
    Should be fitted with high efficiency (HEPA) filter (Minimum 99.997% efficiency)
  Incorporates pre-filters to minimise dust build-up on main filter
    Pre-filters must be changed regularly
  Sufficient capacity
    UK (HSE) recommends a minimum of 8 air changes per hour for small / medium sized enclosures
  Discharge ducting
    Ideally extracted air should be vented to outside
  Make-up air
    May need cooling to minimise potential thermal stress issues

## Slide 39: Decontamination procedures
Anybody who enters an enclosure or designated work area may become contaminated with asbestos and will need to decontaminate themselves
  Purpose is to ensure that personal protective equipment as well as the person is cleaned to prevent further spread of contamination
All workers need to be properly trained including practical training
Emergency situations
  Site emergencies (fire, evacuation etc)
  Medical emergencies

## Slide 40: Decontamination procedures
Full decontamination
  Used in most situations where asbestos removal work is undertaken
    Full decontamination requires the use of a decontamination unit or hygiene facility
  Two different forms of full decontamination
    Hygiene facility directly connected via an intervening space or tunnel to the enclosure
    Use of transit facilities where the hygiene facility is physically separated from the enclosure

## Slide 42: Hygiene Facility
Source: HSE Guidance Note HSG 247 – reproduced
under the terms of the click-use licence

## Slide 43: Decontamination – hygiene unit attached to enclosure - entering
Enter hygiene unit via clean end door
Inspect, check respirator, undress. Put on clean personal protective equipment and respirator. Carry out fit check on respirator
Pass through shower area into ‘dirty’ end
Leave hygiene unit. Go through intervening airlock and enter enclosure

## Slide 44: Decontamination – hygiene unit attached to enclosure - leaving
Vacuum all visible dust from personal protective equipment
Leave enclosure and enter intervening airlock
Enter ‘dirty’ end of hygiene unit. Remove all footwear and clothing. Do not remove respirator
Enter shower area with respirator on, shower and use a sponge to clean respirator
Remove respirator, dispose of filters, finish showering
Move into clean area carrying respirator, dry off and dress
Exit hygiene facility via clean end external door

## Slide 45: Hygiene facility not attached directly to enclosure
Often ‘transit procedures’ are used when it is not practicable to connect the decontamination unit to the enclosure
Transit facilities provided to enable workers to carry out preliminary decontamination prior to travelling to the main hygiene facility
  Usually consists of a three-stage airlock of sufficient size attached to the enclosure
Object is to remove as much of the asbestos dust / debris acquired in the enclosure as possible
  To minimise spread of contamination transit footwear and transit coveralls are worn
  Transit routes should be away from occupied areas where practicable
On reaching hygiene facility full decontamination is undertaken

## Slide 46: Decontamination – transiting procedure – entering enclosure
Enter hygiene unit via clean end door
Inspect, check respirator, undress. Put on transit coveralls and footwear and respirator. Carry out fit check on respirator
Pass through shower area into ‘dirty’ end
Leave hygiene unit. Walk to transit facilities via designated transit route
Enter outer stage of transit airlock. Remove transit coveralls and footwear, put on working clothing and footwear
Go through intervening airlock and enter enclosure

## Slide 47: Decontamination – transiting procedure – leaving enclosure
Vacuum all visible dust from personal protective equipment
Leave enclosure and enter inner stage of transit airlock
Clean footwear with water, sponge down or wipe respirator
Enter middle stage of airlock, remove coveralls and footwear worn in enclosure. Do not remove respirator
Enter outer stage of airlock. Put on transit overalls and transit footwear. Walk to hygiene unit via designated transit route
Enter ‘dirty’ end of hygiene unit. Remove all footwear and clothing. Do not remove respirator
Enter shower area with respirator on, shower and use a sponge to clean respirator
Remove respirator, dispose of filters, finish showering
Move into clean area carrying respirator, dry off and dress
Exit hygiene facility via clean end external door

## Slide 48: Preliminary decontamination
In some situations (e.g. analyst undertaking clearance certification after asbestos removal) full decontamination may not be necessary
  The required decontamination level should be determined as part of the risk assessment for the work
On exiting, normal decontamination procedures should be followed
  Vacuum dust off protective equipment, wipe respirator, clean footwear
  Remove coveralls in middle stage of airlock
  Exit airlock system and remove respirator
Analysts entering areas where contamination is liable to be more significant should undertake full decontamination e.g.
  Entering a ‘live’ area to undertake supervisory duties
  Where there is greater potential for contamination during a clearance inspection such as crawling through roof void

## Slide 49: Preliminary decontamination
For building surveys decontamination of footwear is likely to be the most frequent activity
  This will be necessary in areas where asbestos dust and debris may be present on the floor
  If disposable overshoes are worn, these can be taken off, bagged as asbestos waste and replaced
  Otherwise, shoes can be wiped down
  In general, the coverall and respirator should be removed on completion of the survey (or at a break) in a safe area e.g. in the open air

## Slide 50: Removal procedures
A range of techniques can be used to minimise generation of airborne asbestos fibres. The chosen method will depend on a number of factors including:
  Type of asbestos product – insulation, spray coating, insulating board, cement etc
  The thickness of the asbestos containing material
  The presence and nature of any coating on the asbestos containing material
  The type and nature of any fixing – nailed, screwed etc
  Other factors e.g. whether pipework is redundant, the asbestos containing material is damaged, accessibility etc

## Slide 51: Removal procedures
Generation of airborne asbestos should be minimised e.g.
  Unscrewing and removing complete panels rather than breaking out
  Regular cleaning up and bagging of asbestos waste
  Use of high efficiency vacuum cleaners
  Remove whole sections of plant intact and transport to a ‘centralised’ asbestos removal site
  Wet down or damp down materials
    Particularly important for friable materials such as insulation and spray coating
    Removal of dry or poorly wetted insulation can lead to exposure levels of 100 fibres / cm3 or higher. Good wetting of the insulation should enable exposure levels to be reduced to much lower than 1 fibre / cm3

## Slide 52: Removal procedures - wetting
To achieve the most effective wetting
  Wetting agent applied at a rate at which it can be absorbed by the material
  Sufficient time allowed for wetting agent to thoroughly penetrate the material
    Porous materials will wet more quickly than some dense materials. Wetting times may be a few hours or even up to about a day
    Avoid over-wetting that may create slurry which may be difficult to deal with
    Degree of penetration checked before attempting removal, a dye may be added to the wetting agent to aid this examination
  Wetting may be less applicable (but still of benefit) for harder, dense materials such as friction products, cement products, waterproofed materials etc

## Slide 53: Removal procedures – controlled wetting by injection method
Material should be wetted through its full depth
  Water alone may not be very effective, so a wetting agent (surfactant) usually added
  Very effective method, particularly when outer surface is sealed or coated so wetting agent will be better retained within insulation
  Multipoint systems often have a ‘string’ of needles connected to a common injection pump
  Correct positioning of needles important as is allowing sufficient wetting time
  Wet injection carried out at low pressure to ensure controlled and uniform wetting. If higher pressures used, wetting may not be uniform and there is a greater risk of insulation breaking off

## Slide 54: Injection

## Slide 55: Removal procedures – controlled wetting by spray method
  Used where injection is inappropriate
    e.g. material too hard, unsealed, too thin etc
  Spraying generally wets outer surface and only penetrates thin porous materials
    Penetration and wetting can be improved by increasing number of ‘sprayings’ and allowing sufficient soak time
  Particularly suitable for:
    Unsealed, porous materials e.g. spray coatings
    Thin materials (less than 1 cm)
    Removal of asbestos insulating board
    Asbestos textiles, blankets, ropes
    In conjunction with glove-bags
    Removal of asbestos debris
    Work on asbestos cement

## Slide 56: Removal procedures – controlled wetting by spray method
  Water alone may not be very effective, so a wetting agent (surfactant) usually added
  For small applications hand pressurised equipment can be used. For larger applications, a low pressure spraying machine is more appropriate
  Spray applied so that the entire surface is saturated, but run-off is minimised

## Slide 59: Removal procedures – dry removal method
  Least preferred option – particularly for friable materials
    Only used if injection or wet spray methods are not suitable
  If dry removal method used the following factors should be considered and used, as determined by a risk assessment
    Work area fully enclosed and maintained at negative pressure
    Personnel involved in removal operation to wear respiratory protection with high assigned protection factor
    Material removed in small sections with minimal disturbance, to minimise fibre generation
    Waste material placed immediately in appropriate containers and wetted
    Vacuum cleaners used to minimise fibre generation by techniques such as ‘shadow vacuuming’

## Slide 60: Removal procedures – wrap and cut removal method
  Lagged pipework or assemblies wrapped in polyethylene sheeting before cutting out or disconnecting sections and either:
    Taken to separate area for controlled asbestos removal, after which underlying structure can be returned to service or disposed of as normal waste, or
    For redundant (small) pipework and vessels, the insulation is not removed from the underlying structure and all material disposed as asbestos waste

## Slide 61: Removal procedures – wrap and cut removal method
  Wrap and cut may be suitable when:
    The items are manageable in size
    The items have been emptied and cleaned where necessary to remove any residual hazardous materials
    The location of the item is such that building an enclosure is not practicable e.g. high level external pipework or remote locations
  The need for additional precautions such as enclosures should be considered in planning stage

## Slide 62: Removal procedures – glove-bag removal
  Glove-bags - single use bags, constructed of heavy-duty transparent polyethylene that allow stripping activities inside the bag by external operators
    Sealed at each end to include section of lagging to be removed
    Integral plastic arms and gloves together with access ports
    Range of sizes – typically about 1 metre wide x 1.5 metre deep
    Flexible, easily installed and quickly dismantled temporary enclosure for small asbestos removal jobs
    Particularly suited to removal of asbestos from individual valves, joints, pipe section etc.
      Can also be used to remove small sections from large assemblies to enable them to be broken down into sub-sections

## Slide 63: Glove bag

## Slide 64: Removal procedures – glove-bag removal
  Advantage
    All waste and contamination contained within bag reducing the need for extensive protective equipment and decontamination
  Limitations
    Bag can only contain a limited volume of material – care needs to be taken not to overfill bag with waste or water
    Potential that bag could split or seals fail – this possibility should be considered as part of risk assessment and if necessary an additional enclosure constructed
    If work is in area remote from other workers e.g. external pipework, additional enclosures may not be practicable and barriers / signs to restrict access may be sufficient

## Slide 65: Removal procedures – hot stripping of asbestos
Whenever possible removal of asbestos from hot metal or machinery should be avoided
  Plan removal work around shutdowns, with sufficient time allowed for metal / machinery to cool
If dry removal of asbestos from hot surfaces is the only option, particular attention should be paid to:
  Dust extraction equipment
  Appropriate personal protective equipment
  Potential for heat stress
    Design of work programme (work-rest regime)
    Fitness and acclimatisation of workers to heat
    Provision of adequate drinking water
    Workers trained to recognise symptoms of heat stress

## Slide 66: Asbestos waste removal procedures
Procedures developed that take into account
  Location of temporary waste storage on-site
  Transport of waste within the site and off-site
  Location of the waste disposal site
  Any local disposal authority requirements that apply
Loose asbestos waste should not be allowed to accumulate within the work area
  Regularly cleaned up and placed in bags / containers as work progresses

## Slide 67: Waste bags and containers and waste disposal
In many cases asbestos waste collected in heavy-duty polyethylene bags
  Bags labelled with appropriate warning stating they contain asbestos and inhalation should be avoided
  Waste should be ‘double-bagged’
  Waste should be wetted to minimise any potential fibre release
  Bags should not be overfilled
  Large pieces of asbestos should not be broken to fit into bag but should be wrapped or placed in drums that can be sealed

## Slide 69: Waste bags and containers and waste disposal
Routes for removing waste from work area should be designated in asbestos removal work plan
  In occupied buildings, where possible, movement of waste bags should be outside normal working hours
  Waste bags and containers removed from work area should be stored securely in skip or container until final disposal
Asbestos waste should be removed by a competent person and transported and disposed in accordance with National and local regulations and guidelines
  In some countries a licence from environmental and/or waste disposal authorities is required

## Slide 70: Enclosures – testing, monitoring and maintenance
The enclosure should
  Be constructed correctly and adequately sealed
  Remain in good condition and its effectiveness maintained
Various inspections, checks and tests may be required, and their outcome recorded e.g.
  Visual inspection prior to work commencing
  Smoke testing of enclosure
  Differential pressure monitoring
  Checks and inspections during work
  Air monitoring
  Testing and maintenance of air extraction equipment

## Slide 71: Enclosures – testing, monitoring and maintenance
Visual inspection prior to work
  Thorough inspection, particular attention paid to seals, airlocks, joints and sealing of sheeting around pipes and conduits etc
Smoke testing
  Enclosure filled with smoke prior to work commencing to check for any leaks in enclosure. Any gaps / leaks should be rectified
  Procedure in UK – extraction units switched off
  Procedure in USA – extraction units switched on
  For large enclosures and enclosures in external or remote areas use of smoke testing may be of limited use

## Slide 73: Enclosures – testing, monitoring and maintenance
Differential pressure monitors
  Provide continuous indication of ‘negative pressure’ within enclosure
  Not particularly reliable particularly with external enclosures
Checks and inspections during removal work
  Thorough visual inspection of enclosure at start of each shift to check for any defects and check that negative pressure is being maintained
  Air extraction units also checked to confirm it is operating within normal operating parameters
  (Check screening / flaps being pulled inwards)

## Slide 74: Enclosures – testing, monitoring and maintenance
Air monitoring
  May be carried out at start of work and periodically to confirm that asbestos release is adequately controlled
    Near airlocks, air extraction equipment and particularly in occupied or sensitive areas
    Monitoring may be undertaken within enclosure to verify that respiratory protection is adequate
Testing and maintenance of air extraction equipment
  Air extraction units should be left running continuously during removal work
  Schedule for checking that they are operating correctly included in plan of work (should be at least every shift)
  Air extraction equipment should also be thoroughly examined and tested at suitable intervals