## Slide 1
M506
Ergonomic Essentials
Day 2

## Slide 2: ERGONOMICS METHODS & TECHNIQUES

## Slide 3: Work design (1)
Allocation of functions
Task analysis
Work organisation factors
Issues of poor work design
User trials
Problem solving
Notes: Discuss general concepts to be covered in this section

## Slide 4: Work design (2)
‘Allocation of functions’
Human only
Computer only
Human & computer - human in control
Human & computer – computer in control
Notes: When designing systems, and deciding whether or not a function should be either automated or performed by a human, there are three possible function outcomes:
1. Functions that must be carried out by machines
2. Functions that must be carried out by humans
3. Functions that could be carried out by humans or machines, or a combination of both

## Slide 5: Work design (3)
Requirements:
1. Formulation of goals
2. Analysis and allocation of functions
3. Design concept
4. Detailed design
5. Realisation, implementation and validation
6. Evaluation
ISO 6385:2004
‘Ergonomic principles in the design of work’
Notes: Explain the concept
Use the ISO info to elaborate on the principles in design of work systems.

## Slide 6: Work design (4)
Worker health & wellbeing
Safety
Performance
How do you evaluate these categories?
ISO 6385:2004 Evaluating the system design
Medical / physiological
Subjective measures
Psychological measures
Reliability measures
Errors
Unsafe behaviours
Near misses
Accidents
Quality
Quantity
Cost benefit
Notes: Ask people to suggest evaluation techniques for each category on the LHS of slide.

## Slide 7: Work design (5)
Hierarchical task analysis
  Specify system purpose
  Identify tasks/components required for system
  Identify goals of each task/component
  Determine sub-tasks and then sub-tasks etc, until finish pathway….
Notes: Explain HTA and differentiate this system analysis with a task analysis of job
Ask for examples
Break into groups of 3 and Conduct a relevant HTA
Feedback to large group
Identify ways in which the usefulness of the HTA could be maximised.

## Slide 8: Work organisation (1)
Fragmentation of work / Taylorism
  Complex jobs broken down into simpler components
  The components are repeated
  e.g. Production lines in early 1900s
What are possible advantages of this allocation of work functions?
What are possible disadvantages?
Notes: Explain Taylorism
Ask people to list potential ads and disads from this work fragmentation

## Slide 9: Work organisation (2)
Task variation
A range of tasks
Workers are multi-skilled
A range of physical and cognitive demands
e.g. Job enlargement,
Task rotation, or
Self directed work teams
Reduced risk of occupationally related disorders (eg cumulative trauma)
Notes: Discuss the 3 ways of achieving task variation and the benefits from this (refer to manual).

## Slide 10: Work organisation (3)
Work Load
Notes: At extremely low levels of workload boredom may set in resulting in missed signals and a poor performance
Medium levels of workload are optimal and performance remains high, however further increases in workload may result in overload and a marked decline in performance.

## Slide 11: Work organisation (4)
Job satisfaction
What factors contribute to an individuals’ work satisfaction?
Consider:
Organisational aspects
General work aspects &
Personal aspects
Notes: Job satisfaction refers to an individual’s general attitude or feelings toward their work and work experiences
There can be major differences in job satisfaction between individuals and even between individuals performing the same job
Ask for experiences from participants.

## Slide 12: Work organisation (5)
DEMANDS
 |  | Low | High
CONTROL | H i g h | Low demand High control (low strain) | High demand High control (active)
 | L o w | Low demand Low control (passive) | High demand Low control (high strain)
SUPPORT
(can assist people to manage)
Notes: Job demands need to be balanced with a degree of control by the worker over how the work will be done
Those employees who have high demands placed on them but who have little job control (decision latitude) are the most likely to be at risk of developing psychological or physical disorders
Ask for examples from participant’s workplaces
This is illustrated in the diagram. (Employees who have low demand and low control are by definition in a passive position)

## Slide 13: Poor work design problems….
Examples:
Sedentary work
Computer work
Repetitive work
Notes: Explore issues with computer, sedentary and repetitive work
Ask why Participants think these may be an issue – consider yesterday’s session content.

## Slide 14: User trials
Purpose
Task
HTA
Participants
Trial
Measure
Feedback
Improve
Re-test
Notes: User trials are often used to test equipment, products or devices with the potential user group
The purpose of the trial is to review and improve the design of the product by asking the potential end user their views and observe their interaction with the device, review, improve and retest.

## Slide 15: Problem solving
Determine criteria
to be assessed
Review methods against criteria
Use chosen methods to assess issue
Determine ergonomics intervention
Implement ergonomics intervention
Evaluate intervention
Notes: Explore the scientific approach to problem solving for Ergonomics
Link User Trial with concepts of ergonomics intervention
Discuss each step with Participants. Link with Risk Management – monitoring interventions...

## Slide 16: ERGONOMICS RISK MANAGEMENT

## Slide 17: Ergonomics Risk Management
BP
Notes: Provide overview of risk management approach

## Slide 18: Hazards & risks
Hazard – potential for harm
Risk – the probability that the hazard will cause injury or harm

## Slide 19: Ergonomics hazard identification
Records
  Statistics
  Near misses
  Hazard reports
  OHS minutes
Consultation
  Formal surveys
  Tool box talks
  OHS reps
  Meetings
  Informal chats
Observation
  Direct viewing inspections
  audits
  walk through surveys
Notes: Ask for examples of each method from participants’ workplaces.

## Slide 20: Ergonomics risk assessment
Frequency
Severity of risk
Work factors
Individual factors
When would you do this?
Notes: Ask when this would be undertaken – experience from Participants’ workplaces?

## Slide 21: Ergonomics risk management (1)
‘Hierarchy of controls’
Eliminate
Substitute
Engineering / design
Administration
PPE

## Slide 22: Ergonomics risk management (2)
Match controls with level of risk
  Eliminate
  Substitute
  Engineer HARD BARRIERS
  Administration
  PPE SOFT BARRIERS
Notes: Matching controls with level of risk
Discuss examples of each

## Slide 23: Ergonomics risk management (3)
Evaluate controls
  Effectiveness
  Availability
  Cost benefit/cost effectiveness
Notes: Link with risk management cycle
Discuss evaluation in terms of effectiveness – does it actually control the problem , does control create more problems (unanticipated)
Availability of controls ongoing
Cost benefit.
Discuss cost benefit in general terms – what would Participants consider when measuring cost benefits of interventions (NB further detail on this later in day).

## Slide 24: MEASUREMENTS & INFORMATION GATHERING

## Slide 25: Ergonomics Standards
ISO
Notes: Inform re the main sources of information: Standards, guidelines (e.g. from ILO and country OHS bodies).

## Slide 26: Ergonomics guidance
ILO’s vision of decent work
“Work is central to people's well-being.
In addition to providing income, work can pave the way for broader social and economic advancement…...
Such progress, however, hinges on work that is decent….”
Notes: Explain role of ILO and guidance data

## Slide 27: Ergonomics guidance
Notes: Ask about the guidance Participants currently use– inc country / state/organisation specific – and its value.

## Slide 28: Ergonomics Standards
Technical committees for ergonomics standards.
Guiding principles
Anthropometry & biomechanics
Human-system interaction
Physical environment
ISO
Notes: Provide more detail on ISO & explain the aim of ISO and the standards with ergo input.

## Slide 29: Which ergonomic assessment method?
Considerations:
Criteria to be evaluated
Accuracy required
Ability to involve key personnel
Acceptability
Cost benefit
Notes: Use these standards as benchmarks for ergonomics (or as minimum standards)
Ergonomists need to measure what is happening in the workplace to compare to these standards, and need to choose an appropriate measuring method.

## Slide 30: Ergonomic assessment methods
Observational
Rating scales, questionnaires & checklists
Models & simulation
Notes: Explore these types of assessment methods
Discussion regarding Participant experience with each type of assessment method.