## Slide 1
M506
Ergonomic Essentials
Day 4

## Slide 2: WORKPLACE, JOB & PRODUCT DESIGN
BP

## Slide 3: Outline
Work Environment
  Design of work systems
  Workspace/workstation design
  Equipment design
Information, Displays & Controls
  Design principles
  Visual, auditory displays
  Controls
    Layout, shape, size, movement, effort, resistance, feedback, stereotyping
  Principles of software ergonomics

## Slide 4: Chairs & Seating
Arrange work to combine seated and standing postures
Considerations for work chairs:
  Adjustability of chair (suit 90% workforce)
  Posture of spine
  Amount of static and active muscle work
  Compression of tissues
    Thighs
    Behind knees
Notes: Revisit principle of alternating work postures
Discuss considerations for work chairs.

## Slide 5: Optimum sitting position
McPhee
Notes: Discuss slide in detail
Exercise: Review chairs.

## Slide 6: Vehicle cab design
Ingress/egress
Operator space
  Comfort (physical, environmental)
  Visibility
  Operation
Seats
  Adjustable
  Designed for 97% operators
Displays & Controls
Notes: Discuss considerations for other common seated workstation: the vehicle cab.

## Slide 7: Vehicle cab design - seats
Driver/Operator Seat Dimensions | 
Seat | Seat depth -- 380–480 mm Seat width – 450 mm (min) Angle -- 5-10o backwards The seat may be slightly dished (raised sides - max 25 mm transverse, 40 mm lengthways) Height adjustment in the seat (at least 130 mm, 200 mm preferred) Height adjustment range above floor level- - 370–500 mm At least 150 mm of travel fore/aft adjustment of seat (AS 2956.5) Front edge and sides of the seat--- well rounded to avoid pressure on the underside of the operators' thighs (approx. 60 mm radius)
Backrest including Lumbar Support | Height above seat -- approx 200–250 mm (position of mid lumbar support above seat) Angle adjustment of backrest -- 95-120o to horizontal
UOW
Notes: Discuss slide
Ask for examples from participant workplaces – how do they think the seats would ‘measure up’ to these guidelines?

## Slide 8: Computer (VDT) Workstations
Design to consider:
  Users
    Age, anthropometrics, etc
  Type of computer equipment
    Size, shape, requirements to operate
  Tasks to be performed
    Lighting, glare, space, document holders, etc
Seated vdu workstation, note adjustable
chair, and use of footrest. Source: ASCC
Notes: Discuss VDT (VDU) workstations
Explore issues under each heading, ask for examples…

## Slide 9: Computer Equipment
Screen image
  Colours
  Clarity
  Adjust for older users
Keyboard
  Thin
  Dished keys
  Feedback from keys
Mouse
  Appropriate shape
  Easily grasped by hand
  Feedback
Screen
  Height, angle and tilt adjustable
  Appropriate distance
Document holders
  To raise source document allowing neutral neck posture
ASCC, 2007
Notes: Outline computer equipment requirements (NB very brief, great deal of ergonomic research in these areas).

## Slide 10: Assessing Computer (VDT) Workstations
HSE checklist
  http://www.hse.gov.uk/campaigns/euroweek/pdfs/vduchecklist.pdf
WorkSafe Victoria
  http://www.workcover.vic.gov.au/wps/wcm/resources/file/ebcb9c435c881f7/officewise.pdf
Notes: Useful checklists for computer workstations…
Activity: Work area for review; or use video clip.
  Divide into groups of 3
  Review chosen checklist
  Observe worker
  Audit workstation with checklist
  Feedback to large group.

## Slide 11: INFORMATION, DISPLAYS & CONTROLS
Human-machine interaction
  Machine displays information to the operator
  Operator provides information to the machine
  Machine provides feedback to the operator
BP
Notes: Discuss slide
Ask for examples of each dot point.

## Slide 12: Information, Displays & Controls – Design principles
Consider:
  Suitability for task
    Function allocation, grouping, operational relationship
  Self descriptiveness
    Information availability
  Controllability
    Redundancy, accessibility, movement space
  Conformity with user expectations
    Compatibility with learning and practice
  Error tolerances
    Error correction, error handling time
  Suitability for individualisation and learning
    flexibility.
  IS EN 894-1
Notes: Outline design principles and describe each point.
Aim of information, displays and controls is to have:
  Detectability -- the intended receiver can sense the signal
  Recognisability -- the intended receiver can tell what the signal is
  Intelligibility -- the intended receiver can tell what the signal means
  Conspicuousness -- signal is attention-getting

## Slide 13: Visual Displays
Design
Location
Lighting
Line of sight
volkswagon.com.au
Notes: Most common form of display as best way for human to gain simultaneous perception of a large amount of information
Visual information displays should be clear, concise and precise.

## Slide 14: Auditory Displays
Intensity, frequency, duration, timbre, time between specific sounds
Used when:
  Operator’s vision already occupied
  Immediate action required
  Simple, short message
  Working in dark or dull environment
  Operator moving around workplace due to task requirements.
Notes: Design of auditory displays must consider the operator’s ability to detect, identify and interpret the sound
Mention tactile displays.

## Slide 15: Quantitative & Qualitative Displays
Data can be presented in a variety of ways.
Decision based on
  Level of detail needed
  Speed of response required
This submarine display clearly demonstrates
the position of the vessel in it’s dive. (Stevenson)
Notes: Ask for difference between quantitative and qualitative displays
Discuss the slide
Discuss combination displays – this representational and quantitative.

## Slide 16: Danger & Information Signals
Auditory or Visual, or combination
ISO 11429 provides preferred characteristics of signals
Yellow
Blue
Red
Green
Notes: Discuss
Refer to handout – characteristics of signals.

## Slide 17: Safety Signs & Labels
Conspicuousness
Emphasis
Legibility
Simplicity
Intelligibility
Visibility
Permanence
standardisation
Notes: Discuss
Ask for good and poor examples of signs & labels.

## Slide 18: Controls (1)
Layout
  Easy & safe operation
  Primary & secondary groupings
  Function groupings
  Backlit for dark conditions
  Safeguards against accidental operation
lg.com
Notes: Controls provide a method for workers to change the status and operations of a machine
The control actuator may be operated by light touch on a button, grasping and moving a lever, turning a dial, using a foot on a pedal, or other means
Layout is an important consideration for controls – discuss slide.

## Slide 19: Controls (2)
Shape & Size
  Easily distinguished by location, type, shape, feel
  Size, shape, colour, location matched to usage and importance
  Account for anthropometric variability and wearing of PPE
Sifam.com
Notes: Each control should be readily distinguished by its location, type, shape, feel
The size, shape, colour and location of knobs and switches and other controls must be matched to usage and their importance
Size should accommodate large feet (pedals) or small/large hands and account for the need to wear protective clothing like gloves or safety shoes.

## Slide 20: Controls (3)
Movement, Effort, Resistance & Feedback
  Movement should produce consistent & expected effect
  Stereotypical directions and movements (push control forward to raise forklift tines, pull back to lower)
  Sensitivity related to force
UOW
Notes: Discuss slide
Ask for examples: e.g. excessive force to slightly increase volume, etc.

## Slide 21: Controls (4) - Controls & Compatibility
Stevenson
Notes: Discuss the recommendations;
Highlight the issue of stereotyping: use the L hand drive vehicle being driven by R hand drive vehicle operator.
Activity: Divide into groups of 4
  Consider the principles of controls just discussed
  Discuss own experience of controls in workplace – as a group provide one example of an issue with controls in each of the overheads:
  Layout
  Shape & Size
  Movement etc
  Controls & compatibility
  Feedback to large group.

## Slide 22: Principles of Software Ergonomics
ISO 13407
User-centred approach
  Understand & specify the context of use
  Specify the user & organisational requirements
  Produce designs & prototypes
  Conduct user-based assessment
Notes: Software ergonomics refers to the interface and interaction between the human and machine in terms of the software
The ergonomic design of software aims to enhance the user’s ability to operate applications effectively, efficiently and with satisfaction
Consideration must be given to the user characteristics, the tasks to be performed and the environment in which the system will be used.

## Slide 23: Summary
Work Environment
  Design of work systems
  Workspace/workstation design
  Equipment design
Information, Displays & Controls
  Design principles
  Visual, auditory displays
  Controls
    Layout, shape, size, movement, effort, resistance, feedback, stereotyping
  Principles of software ergonomics
Notes: Summarise section
Clarify any questions.