## Slide 1: WORKPLACE, JOB & PRODUCT DESIGN
BP
Notes: <number>
In ergonomic work system design, the person is the focus, with the aim of optimising human performance and well-being.

## Slide 2: Outline
Work Environment
  Design of work systems
  Workspace/workstation design
  Equipment design
Information, Displays & Controls
  Design principles
  Visual, auditory displays
  Controls
    Layout, shape, size, movement, effort, resistance, feedback, stereotyping
  Principles of software ergonomics
Notes: <number>

## Slide 3: Work Environment Introduction & Definition
Work system (ISO 6385):
  “A system comprising one or more workers and work equipment acting together to perform the system function, in the workspace, in the work environment, under the conditions imposed by the work tasks”
  Physical ergonomics
  Organisational ergonomics
  Cognitive ergonomics
Notes: <number>
To optimise human performance, all 3 domains of ergonomics must be considered in the design of the work system.

## Slide 4: Principles of Work System Design
Consider the WHOLE work system,
  Formulate goals
  Analyse and allocate functions
  Draw up design concept
  Determine detailed design
  Implement and validate
  Evaluate
  NB design process is iterative
  and consultative
  (ISO 6385)
Notes: <number>
This design process must take into consideration multiple users with different characteristics, including people with special requirements
It must also include the interaction between the user or users and all the components of the work system such as the tasks, equipment, workspaces and the work environment and the movement of people and materials
Ask if any Participants have been involved in ‘green field’ site & gone through the process
Ask them to outline for group.

## Slide 5: Layout of Workspaces
Workspace size
  Suitable for functions to be performed (incl. maintenance tasks)
  Lighting, tempt appropriate for functions to be performed
  Review needs with changing/evolving functions and equipment
Workspace arrangements
  Facilitates appropriate work postures
  Adequate space for all equipment
Notes: <number>
Discuss layout of workspaces and workstations.

## Slide 6: General considerations
Access
Size of work area
Design & selection of tools
Environmental conditions
Visual requirements of task
Noise levels
PPE
Bluescope Steel
Notes: <number>
Explore each dot point on slide and ask for examples.

## Slide 7: Workstation & Equipment Design
Workstation design:
“The combination & spatial arrangement of work equipment, surrounded by the work environment under the conditions imposed by the work tasks.”
Work equipment:
  “Tools, including hardware & software, machine, vehicles, devices, furniture, installations & other components used in the work system.”
  ISO 6385
Notes: <number>

## Slide 8: Workstation Design - Principles
Horizontal work area
Working position
Work heights
Viewing distances & angles
Reach distances
Access & clearance
BP
Notes: <number>
Discuss principles of workstation design
Link with anthropometry section
Describe task in slide and ask re dot points – what particular aspects need attention?

## Slide 9: Workstation Design - Horizontal Work Area
Use of materials & work equipment in the primary and secondary
work areas; infrequent activities in the tertiary work area.
McPhee
Notes: <number>
Demonstrate horizontal work area in terms of Primary, Secondary and Tertiary work areas.

## Slide 10: Workstation Design – Work position
Different work tasks have different requirements for working positions:
  Sitting: fine, manipulative work
  Standing: heavier manual work
Combination of sitting and standing postures over shift preferable.
Bluescope Steel
Notes: <number>
Discuss work position principles: sitting/standing; sit/stand stations.

## Slide 11: Workstation Design – Working height
Working height is task dependent:
  Visual requirements
  Manual precision
  Strength
Backwatch collections, WorkCover NSW
Notes: <number>
Make distinction between different working heights for different tasks: inspection or precision V strength requirements
Ask participants for examples.

## Slide 12: Workstation Design – Viewing distances & angles
Viewing distances proportional to size of work object
  Small object, shorter viewing distance, higher work surface
Ensure viewing distances cater for all ages
Viewing angles vary from 15o-45o
McPhee
McPhee
Notes: <number>
Ask for examples from participant workplaces.

## Slide 13: Workstation Design – anthropometric requirements
Reach
Access & Clearance
ASCC, 2007
ASCC, 2007
Notes: <number>
Emphasise anthropometric requirements of reach & clearance
Use examples.

## Slide 14: Equipment Design - Tools
Handles
Forces
Design
Type of operation
Weight
Controls
Mechanical aids
Bluescope Steel
Stevenson
Notes: <number>
Examples of good and bad tool designs: e.g. handles, forces, controls
Have 3 poorly designed tools, divide into 3 groups, 1 tool per group and ask to identify the problem with the design and suggested controls.