## Slide 1: M507 – Introduction to Toxicology – Case Study
Notes: <number>

## Slide 2: Nitroglycerin use in industry
  Explosives Industry
      Defence
      Quarrying
      Demolition
  Pharmaceutical Industry
      Tablets
      Patches
      Sprays
Notes: <number>

## Slide 3: Health Effects
Vasodilator
“NG Headache”
Withdrawal Symptoms
    Headache (short term)
    Heart Problems (long term)
Notes: <number>

## Slide 4: Pharmaceutical Process
© Crown Copyright
Notes: <number>
Pharmaceutical plant - can say a little more about this - this is the schematic of an aerosol filling line - it is designed to fill the small aerosol cans angina sufferers use.
it is a continuous process with lots of women doing very repetitive tasks - to relieve boredom they rotate jobs frequently - HSE called in due to complaints of headaches
we turned up after some improvements made - ventilation system designed to protect the product from the workers not the other way round - workers wore protective equipment for the same reason

## Slide 5: Putting valves on
© Crown Copyright
Notes: <number>
Pharmaceutical plant - can say a little more about this - this is the schematic of an aerosol filling line - it is designed to fill the small aerosol cans angina sufferers use.
it is a continuous process with lots of women doing very repetitive tasks - to relieve boredom they rotate jobs frequently - HSE called in due to complaints of headaches
we turned up after some improvements made - ventilation system designed to protect the product from the workers not the other way round - workers wore protective equipment for the same reason
This is where the nozzles are put on - note the local exhaust and gloves.
when the nozzle is put on some of the contents are released - sometimes into the gloves, sometimes towards the person sitting opposite

## Slide 6: Fitting Nozzles
© Crown Copyright
Notes: <number>
Pharmaceutical plant - can say a little more about this - this is the schematic of an aerosol filling line - it is designed to fill the small aerosol cans angina sufferers use.
it is a continuous process with lots of women doing very repetitive tasks - to relieve boredom they rotate jobs frequently - HSE called in due to complaints of headaches
we turned up after some improvements made - ventilation system designed to protect the product from the workers not the other way round - workers wore protective equipment for the same reason
This is where the nozzles are put on - note the local exhaust and gloves.
when the nozzle is put on some of the contents are released - sometimes into the gloves, sometimes towards the person sitting opposite

## Slide 7: Exposures by Task
© Crown Copyright
Notes: <number>
average values from several people - because of the frequent changes of job we usually got two jobs between tea breaks and voidings
no NG in air samples
Two sources of exposure:
the filling station which sometimes did not seal the top properly and then blew the contents out
the nozzling point where NG was being squirted at the fingers of the workers - latex gloves not good for stopping NG

## Slide 8: Skin Absorption & Gloves
Urine samples detected exposure but air measurements did not, indicating skin absorption.
Exposure shows that glove type unsuitable.
Tasks (fitting nozzles) and practices (location of work stations) causing exposure were identified.
© Crown Copyright
Notes: <number>