## Slide 1: M507 – Common industrial processes

## Slide 2: Materials handling
Materials handling operations are common to many industries
  Often the source of exposure to hazardous substances
Good industrial hygiene practice means consideration should be given to prevention of exposure
  Elimination or substitution
  Engineering controls
  Process and operational controls
  Local exhaust ventilation
  Personal protective equipment

## Slide 3: Handling of solids and powders
Selection of materials to reduce or eliminate dust generation
  Powder supplied as ‘dust-reduced’ form
  Pellets, granules or flakes instead of powders
  Pastes or powders dispersed in liquids
  All above are dependent on compatibility with process requirements

## Slide 4: Bulk powder delivery and transfer
Bulk powders may be supplied by tankers or in tote bins
  May be transferred to silos by pneumatic transfer which is clean and efficient
  However seals and flexible ducting need to be maintained in good condition as ducting may be at positive pressure
Direct feed from storage silos to mixing vessel may avoid need to handle powder
  Generally totally enclosed, but will need vents for air displaced during filling and transfer
  Discharged air will need cleaning prior to discharge

## Slide 5: Bulk powder delivery and transfer
Bulk powder transfer often undertaken by moving belt conveyor systems
  Dust can become airborne at transfer points
  Dust generation can be minimised by reducing height of drop and any cross-draughts
  Transfer points may need partial enclosure and local exhaust ventilation

## Slide 6: Bulk powder delivery and transfer
Bulk powders may be delivered in
  paper or plastic bags
  intermediate bulk containers or
  woven plastic sacks
Whenever dusty materials are transferred, handled or used, spillages may occur
  Good standards of housekeeping and clean up of spillages required
  Wet wiping and / or use of industrial vacuum cleaners should be used rather than dry brushing

## Slide 7
Split bag containing sodium carbonate
Source: Steve Bailey – reproduced with permission

## Slide 8: Dust generation at powder handling processes
Dust generation can occur at many processes
  Filling containers with powders can displace dust laden air
    Full or partial enclosure with local exhaust ventilation may be required
  Opening, emptying and disposal of bags
    Automated units are widely available
  Weighing of mix ingredients
    Automated weighing
    If manual weighing ventilated booths or cabinets may be required for hazardous material

## Slide 9: Dust generation at powder handling processes
Dust generation can occur at many processes
  Mixing (formulation) of powders
    Powders can be made airborne by the mixing action
  Sieving
  Maintenance tasks
    Changing filters
    Emptying bins

## Slide 10
Manual loading of open mixer from drum
Source: Steve Bailey – reproduced with permission

## Slide 11
Sieving of process samples - (Reproduced with permission)

## Slide 12: Bulk liquid delivery and transfer
Bulk liquids may be supplied by tankers or in drums
  May be transferred to storage tanks by enclosed transfer which is clean and efficient
  However seals, joints and pipes need to be maintained in good condition to prevent leaks and fugitive emissions
Direct feed from storage tanks to point of use may avoid need to come into contact with liquid
  Generally totally enclosed, but will need vents for air displaced during filling and transfer
  Displaced air may contain high vapour levels which may need recovering or capturing prior to discharge

## Slide 13
Delivery of methanol from a tanker
Source: Steve Bailey – reproduced with permission

## Slide 14: Exposure to liquids during handling
Exposure can occur at many processes
  Cleaning and maintenance of pipework and vessels
    Systems need to be in place to ensure they are effectively purged of hazardous materials
  Filling containers with liquids such as solvents can displace solvent vapour laden air
    Full or partial enclosure with local exhaust ventilation may be required
  Transferring of liquids from containers has the potential for spills or splashes
  Simple precautions such as lidded containers and closing containers can reduce exposure from evaporation of liquids

## Slide 15
Paint bench – open tins and rags soaked in thinners can be a source of exposure
Source: Steve Bailey – reproduced with permission

## Slide 16: Grinding of metals
Uses bonded abrasive (grinding wheels, discs and belts) to wear away parts of a work piece
  Historically sandstone and diamonds used
    High incidence of silicosis from sandstone
  Replaced by artificial abrasives e.g. aluminium oxide, silicon carbide and synthetic diamonds
    Local exhaust ventilation required for most grinding operations
    Also high noise and vibration levels

## Slide 17
Grinding
Source: HSE: Working with us on Noise and Hand-Arm Vibration – reproduced under the terms
of the Click-Use Licence

## Slide 18
Grinding wheels fitted with local exhaust ventilation
Source: Steve Bailey – reproduced with permission

## Slide 19
Grinding of metal components - (Reproduced with permission)

## Slide 20: Machining of metals
Many machines e.g. lathes, drills, saws produce larger particles than from grinding so airborne generation low
  Main health hazard is from cutting fluids
    Mineral oils, soluble oils and synthetic fluids
  Skin contact with cutting fluids may cause contact dermatitis, skin infections and de-fatting
    Prolonged exposure to oil-based cutting fluids can cause folliculitis
  Inhalation of oil mists may cause range of respiratory effects
  High levels of bacterial growth may occur in some cutting fluids

## Slide 21: Welding of metals
Welding – process by which metals are joined together
  Usually achieved by melting the metal and a filler material to form a pool of molten metal that solidifies on cooling to form a strong joint
  Sources of heat include
    gas flame e.g. oxy-acetylene
    electric arc between an electrode and the work piece
    resistance to passage of electric current

## Slide 22: Gas welding
Generally uses oxygen and acetylene or air and propane fed to a hand-held welding torch to produce a flame
  Melts the surfaces of the metal parts to be joined
  A filler metal or alloy is usually added
  Chemical fluxes used to prevent oxidation

## Slide 23: Arc welding
Electric current used to strike an arc between an electrode and the materials to be welded
  Temperature up to about 4000oC
  Melts the surfaces of the metal parts to be joined
  A filler metal or alloy is usually added – either by melting the electrode (consumable electrode process) or by melting a separate filler rod (non-consumable electrode process)

## Slide 24
Arc welding
Source: Steve Bailey – reproduced with permission

## Slide 25: Arc welding
To achieve a strong weld, weld area must be shielded from atmosphere to prevent oxidation and contamination
  Flux shielded arc welding – consumable electrode consists of a metal core surrounded by the flux as a coating.
    Metal core acts as the filler material for the weld
    Flux coating also melts covering the molten metal with slag and generates a protective covering of carbon dioxide
  Gas-shielded arc welding – blanket of inert gas (e.g. argon, helium, nitrogen) covers the weld area
    Most common types are MIG (metal inert gas) welding and TIG (tungsten inert gas) welding

## Slide 26
Arc gouging or cutting
Source: Steve Bailey – reproduced with permission

## Slide 27: Resistance welding
Heat generated by resistance to flow of electric current through components to be welded
  Small areas of molten metal formed at interface of components to be welded
  Commonly used for ‘spot-welding’ of thin metal sheets – two electrodes clamp sheets together and pass electric current through
  Low weld strength but easily automated – widely used in car manufacturing

## Slide 28: Health hazards of welding
Airborne contaminants can come from a number of sources
  Metal being welded and metal filler rod being used
    Chromium, nickel, manganese, iron etc
  Metallic coatings on article being welded
    Zinc, cadmium etc
  Any paint, grease or dirt on article being welded
  Flux coatings on the filler rod
    Fluorides
  Breakdown of surrounding air by heat or ultra-violet light
    Ozone, oxides of nitrogen
  Inert gas being used

## Slide 29: Health hazards of welding
Additional hazards can occur when welding undertaken in a confined space
  Important that good ventilation of area is achieved, together with permit to work system
  May require an external air supply to welder
Physical hazards include
  High noise levels
  Intense ultra-violet light from arc welding
    Momentary exposure may cause painful irritation - ‘arc-eye’
  Infra-red radiation

## Slide 30
Welding of mild steel - (Reproduced with permission)

## Slide 31
Welding - (Reproduced
with permission)

## Slide 32
Welding - (Reproduced with permission)

## Slide 33: Electroplating and galvanizing
Electroplating applies a metallic layer (e.g. nickel, chromium) to a product
  Product wired as the cathode
  Metal to be applied wired as anode
  Electric current passed through electrolyte solution and metal ions migrate from anode to cathode where they deposit as a thin layer
  (Product must be thoroughly cleaned prior to plating)
Galvanising is a similar process that applies a zinc coating to steel products for corrosion protection

## Slide 34
Electroplating bath with detergent foam
Source: Steve Bailey – reproduced with permission

## Slide 35
Electroplating bath fitted with local exhaust ventilation
Source: Steve Bailey – reproduced with permission

## Slide 36: Electroplating and galvanizing
Chemical hazards
  Heated acid and alkali solutions used in cleaning and treating metals are corrosive
    Burns, irritation to skin, eyes and mucous membranes
  Cyanide solutions often used in electrolytic degreasing and electroplating
  Chromium compounds usually as chromic acid (hexavalent chromium)
    Burns, ulceration of skin, perforation of nasal septum
  Nickel salts can cause allergic dermatitis and irritation
  Chromium and nickel compounds may be carcinogenic

## Slide 37: Soldering and brazing
Metal items joined by melting a filler metal or alloy with a flux that flows into the joint
  Differs from welding in that temperatures are much lower and metals being joined do not melt
  Soldering temperatures below 450oC
  Brazing temperatures above 450oC
  Hazards depend on metals or alloys being melted and the type of flux used

## Slide 38: Soldering and brazing
Soldering using lead / tin alloy based solders widely used in electrical and electronics industry to make electrical connections
  As soldering is at lower temperatures metal fumes generally of little concern
  Main risk from soldering is from breakdown (or pyrolysis) products of the flux
  Flux is commonly rosin based and breakdown products are potent respiratory sensitisers

## Slide 39
Soldering
Source: Steve Bailey – reproduced with permission

## Slide 40
Fumes from soldering
Source: HSE Rosin-cored solder fume assessment – reproduced under the terms of the Click-Use licence

## Slide 41: Soldering and brazing
Rosin-based solder flux fume can lead to occupational asthma – effects are permanent and irreversible
  Not possible to identify safe level of exposure
  Exposure should be avoided or kept as low as reasonably practicable
  Lower temperatures can significantly reduce the amount of fume produced
  Adequate control often requires use of local exhaust ventilation
Brazing often uses fluoride based fluxes
  ‘Silver soldering’ (a type of brazing) the metal alloy sometimes contains cadmium (cadmium free alternatives available)

## Slide 42: Degreasing
Many industrial components need to be cleaned to remove unwanted dirt and grease that would interfere with subsequent processes such as painting, plating, soldering
Two main types of solvent degreasing
  Cold degreasing – a range of techniques that use solvent at ambient temperature
  Vapour degreasing – solvent heated to generate vapour

## Slide 43: Cold degreasing
Dip cleaning
  Articles immersed in solvent in tank
  Lifted out slowly – preferably in wire baskets
  Cover kept on dip tanks as far as practicable
  Sometimes uses ultrasonic cleaning
Wiping
  Large items cleaned with solvent using cloths - used cloths stored in lidded containers and disposed safely
Brushing
  Care needed to minimise splashing
Spraying
  Can lead to high solvent concentrations

## Slide 44: Vapour degreasing
Effective and widely used technique
  Tank partly filled with solvent with heater in base
  Solvent heated – vapour rises to fill tank up to a level at which cooling coils act as condensers
  Tank usually fitted with slot extraction at the rim of the tank to prevent escape of solvent vapour from tank

## Slide 45
Conventional top loading vapour degreasing tank
Source: Envirowise – reproduced with permission

## Slide 46: Vapour degreasing
‘Dirty’ component lowered into vapour layer
  Vapour condenses onto the cold surface and dissolves soluble contaminants
  Solvent (and contaminant) drains back into the base of the tank
  Process continues until temperature of component reaches that of the vapour
Cleaned component then lifted slowly above vapour level to drain fully while still within tank
  Component then removed from tank and allowed to cool to ambient temperature
Whole process may be partly or fully automated

## Slide 47
Large vapour degreasing tank fitted with cooling coils and slot extraction at the rim
Source: Steve Bailey – reproduced with permission

## Slide 48: Vapour degreasing
Soluble and insoluble dirt collects in sump at the bottom of the tank
  Periodically this needs clearing and disposing
  Tank may be considered a confined space and high concentrations of solvent vapour may be present
  Safe systems of work and permit to work may be required
Solvents commonly used include trichloroethylene and tetrachloroethylene
  Some applications may require specific solvents or mixtures of solvents

## Slide 49: Vapour degreasing
Common operating errors that may increase solvent emission include
  Poor stacking of components (particularly hollow components)
  Insufficient drying time within the freeboard above vapour layer
  Components lifted at too high a speed
  Excessive movement of components in the bath
Note: chlorinated solvents are readily decomposed by hot surfaces and open flames
  Decomposition products include phosgene, hydrogen chloride and carbon monoxide
  Smoking and hot processes such as welding should be prohibited in the vicinity of degreasing operations

## Slide 50: Painting
Main health risks is usually from solvents
  Wide range of solvents may be used e.g. aliphatic and aromatic hydrocarbons, ketones, alcohols, glycols and glycol ethers
  Use of low solvent content paints is becoming more widespread
  Solvent content may vary from about 5 – 50%
  May also use solvent based paint thinner
Other health risks can arise from additives, and in particular, from isocyanates in polyurethane paints

## Slide 51: Painting
Three main categories
  Paint applied by brush or roller
    Relatively slow rates of application
    Operator moves away from recently painted areas
    Exposure mainly dependent on level of general ventilation
  Surface immersed in paint and allowed to drain
    Dipping, flow coating
  Spray painting

## Slide 52: Spray painting
Generally higher exposure potential
  Paint for spray application usually contains more solvent than paint for brushing
  Higher rates of application
  Spraying of liquids containing solvents can produce high levels of solvent vapours as the fine spray allows rapid evaporation of the solvent
  Conventional air spraying is the most common method, however,
    large quantities of solvent vapour may be generated
    overspray of paint is common

## Slide 53
Spraying isocyanate based paint in paint spray booth
Source: HSE LEV Trainer Adviser Briefing Days – reproduced with permission

## Slide 54: Spray painting
Spray painting may be automated or manual
Most industrial spray painting applications require local exhaust ventilation at point of application and also during drying and baking operations
  Usually in the form of ventilated enclosures or open-fronted booths
Automation allows greater use of ventilated enclosures and can reduce worker exposure

## Slide 55: Spray painting
Electrostatic spray painting
  Electric charge placed on paint mist particle so it is attracted to part to be painted
  Reduces rebound and overspray so can reduce mist and solvent exposure to operator
Powder coating
  Electric charge placed on paint particles.
  Powder sprayed onto electrically grounded item to be coated
  Item baked to fuse the powder into a continuous coating

## Slide 56: Spray painting
Particular care needed with polyurethane and epoxy paints that contain isocyanates – potent respiratory sensitisers
  Effective enclosures fitted with extract ventilation
  Protective clothing
  Air-fed respiratory protective equipment
  Medical surveillance
  (Note: isocyanates also skin sensitisers)
Dermatitis from irritation and de-fatting of skin from solvents
  Skin contact must be minimised
Other hazards include lead, cadmium and chromium based pigments and additives such as fungicides and pesticides

## Slide 57
Paint mixing – skin and airborne exposure can occur to solvents and pigments
Source: Steve Bailey – reproduced with permission

## Slide 58: Confined spaces
Not an industrial process as such but a common cause of potential problems e.g.
  High concentrations of heavier than air solvent vapours in tanks, pits etc
  Oxygen replaced by inert gases during purging of vessels that contained flammable liquids
  Build up of methane from anaerobic decay of organic material e.g. in sewers or mines
  Build up of carbon dioxide from brewing processes
Controls include permit to work, testing of atmosphere etc

## Slide 59: M507 – Group work – Health Effects

## Slide 60: Group work – health effects
Each group will be given a scenario involving an industrial process or type of work
You are required to anticipate hazardous substances that the workers are likely to be exposed to – for each substance identify
  Health effects of the substance (acute and chronic)
  Likely routes of entry
  Typical controls that you would expect to see in place
Concentrate on occupational hygiene issues – ignore ‘pure safety issues’ such as working at height etc
Report back to the whole class

## Slide 61: Scenario (1)
Dismantling of a large factory that had previously been used for electroplating of metal products
Structure of building
  Large steel girders supporting wall and ceiling panels
Tanks / vessels containing residues remain on-site

## Slide 65
Electroplating bath
Source: Steve Bailey – reproduced with permission

## Slide 66
Electroplating bath fitted with local exhaust ventilation
Source: Steve Bailey – reproduced with permission

## Slide 67
Large vapour degreasing tank
Source: Steve Bailey – reproduced with permission