## Slide 1: M507 Overview of health effects

## Slide 2: Overview of health effects of selected substances
Gases
Organic solvents and vapours
Other selected organic liquids
Metals and metal compounds
Dusts and particulate materials
Mineral fibres

## Slide 3: Gases
Gases may be grouped as:
  simple asphyxiants
    e.g. nitrogen, methane, helium etc
  chemical asphyxiants
    e.g. carbon dioxide, carbon monoxide, hydrogen sulphide, hydrogen cyanide
  irritants
    upper respiratory tract irritants – e.g. ammonia, sulphur dioxide
    lower respiratory tract irritants – e.g. oxides of nitrogen, phosgene
Notes: <number>

## Slide 4: Simple asphyxiants
Act on the body by replacing or diluting oxygen in the air we breathe
21% O2
Unconscious
Death?
19%
ALARMS
ON GAS DETECTORS
<16%
Notes: <number>

## Slide 5: Simple asphyxiants
Nitrogen
  Main constituent of air
  Used in ammonia production, as inert atmosphere and as a freezing agent
Helium and argon
  Inert gases
  Used as shielding gases in welding, purging chemical plant
Methane
  Product of anaerobic decay of organic matter, constituent of fossil fuel reserves
Notes: <number>

## Slide 6: Chemical asphyxiants
Chemical asphyxiants act by reacting with blood or tissue so that the blood or tissue is unable to make use of the available oxygen and chemical asphyxiation occurs
  i.e. body shows signs of being deprived of oxygen
Notes: <number>

## Slide 7: Carbon dioxide
Causes heart and breathing changes
  at 3% - breathing becomes deeper
  at 6% - heart and pulse rate increases
  at 10% - DANGER TO LIFE
  (Occupational Exposure Limit (OEL) is 0.5%)
Occurs as a product of combustion
  Petrol and diesel engines
  Blast furnaces, coke ovens
Other industrial occurrences include
  By-product of brewing
  Carbonisation of drinks
  Refrigeration
Notes: <number>

## Slide 8: Carbon monoxide
Binds strongly to haemoglobin and so reduces oxygen carrying capacity of blood
  30 ppm – occupational exposure limit
  ~ 300 ppm - acute symptoms – giddiness, headache, drowsiness
  3500ppm and above – rapid loss of consciousness – danger to life
Odourless and non-irritant
Occurs from incomplete combustion of carbonaceous compounds
  Gas heaters, petrol engines, blast furnaces, mining, smelting
Notes: <number>

## Slide 9: Hydrogen cyanide
Fast acting and fatal poison
  Short-term exposure limit – 10 ppm for 15 minutes
  Acute effects – rapid onset of headache, convulsions and death
  Inhibits cytochrome oxidase action within cells – causes a chemical asphyxiant action
Colourless gas with ‘almond - like’ odour
Produced by contact of cyanide salts with acid
  Used in precious metal extraction, plating industry
  Used as fumigant
Notes: <number>

## Slide 10: Hydrogen sulphide
Colourless gas with odour of ‘rotten eggs’
Inhibits cytochrome oxidase action in cells (similar to hydrogen cyanide)
Acute health effects include
  Irritation of eyes and mucous membranes at low concentrations
  Unconsciousness, respiratory paralysis, death at higher concentrations
  0.025 ppm - odour threshold
  5 ppm – occupational exposure limit
  20-30 ppm - intense smell
  100-200 ppm - olfactory sense fatigue occurs
  1000 ppm- respiratory paralysis / death
Occurrences: sewers, mining, gas and oil refining
Notes: <number>

## Slide 11: Respiratory tract irritants
Generally divided between upper and lower respiratory tract irritants
  Somewhat arbitrary division based largely on water solubility
  Highly water soluble gases e.g. ammonia, chlorine, sulphur dioxide and hydrogen chloride primarily affect the upper respiratory tract
  Low water solubility gases e.g. oxides of nitrogen and primarily affect the lungs
Notes: <number>

## Slide 12: Ammonia (NH3)
Colourless gas with pungent odour
  Very soluble in water producing strongly alkali solution
  Irritant to eyes, mucous membranes and upper respiratory tract
  At high concentrations severe, and often fatal respiratory / lung damage can occur
Used in manufacture of fertilisers, as a refrigerant gas and as chemical reagent
Notes: <number>

## Slide 13: Chlorine (Cl2)
Dense greenish- yellow gas with pungent odour
  Very soluble in water forming strongly acidic solution
  Acute and severe irritant to mucous membranes, respiratory system and lungs – can lead to pulmonary oedema and death in severe exposures
  Chronic lung damage including bronchitis can occur
Used in chemical and pharmaceutical production, water disinfection, bleaching and plastics manufacture
Notes: <number>

## Slide 14: Hydrogen chloride (HCl)
Colourless gas with strong irritating odour
  Can also occur as liquid acid
  Acute and severe irritant to eyes, mucous membranes and upper respiratory tract
  At higher concentrations severe and often fatal damage occurs with pulmonary oedema
  Chronic lung damage including bronchitis can occur
Uses include metal cleaning, electroplating, manufacture of fertilisers
Notes: <number>

## Slide 15: Sulphur dioxide (SO2)
Dense, colourless gas with pungent odour
  Produces sulphuric acid on contact with water
  Acute effects include severe irritation of mucous membranes and upper respiratory tract
  Exposure to higher levels can rapidly lead to pulmonary oedema and death
  Chronic effects include bronchitis
  Effects may be enhanced by absorption onto fine particulates which can then reach the deep lung
Used in chemical industry and paper manufacturing. Also used as a fumigant and as a preservative
Notes: <number>

## Slide 16: Oxides of nitrogen
Nitrogen dioxide (NO2) is a reddish-brown gas with a pungent odour
  Acute effects include pulmonary irritation some 8 – 24 hours after exposure
  Severe exposure can result in death from pulmonary oedema
  Chronic lung damage including emphysema can occur
Uses include manufacturing of nitric acid, explosives and jet fuel
  Can be generated during arc welding and from diesel engines
Notes: <number>

## Slide 17: Organic solvents and vapours
The term ‘organic’ refers to substances whose molecular structure is based on carbon atoms
Most organic solvents are volatile liquids with boiling points ranging from about 35oC to 200oC
Solvent vapours are produced from the liquid at temperatures below the boiling points
Many are also toxic and flammable
Widely used in chemical manufacturing and many processes
Notes: <number>
Biotransformation - idea is to change compound to form that can be excreted - water soluble and less toxic - sometimes metabolite more toxic

## Slide 18: Organic solvents and vapours
Generally absorbed by two main routes of entry
  Inhalation
  Skin absorption
Solvent vapours rapidly absorbed through the lungs and enter the bloodstream causing systemic effects
Solvents in contact with skin can cause local effects as well as being absorbed through the skin
Cover a wide range of substances including
  Aliphatic hydrocarbons
  Aromatic hydrocarbons
  Halogenated hydrocarbons
  Others including alcohols, ethers, esters and ketones
Notes: <number>
Principle routes of entry - examples
Acute / chronic - differences / typical effects
Local / systemic - examples

## Slide 19: Aliphatic hydrocarbons
Based on straight chain carbon atoms
  Examples - pentane, hexane, heptane
Used in fuels and also as solvents
Widely used in inks, surface coatings and adhesives
Hexane used as chemical feedstock and for extraction of oils and fats from natural products
Notes: <number>

## Slide 20: Aromatic hydrocarbons
Based on ‘benzene ring’ structure
  Examples - benzene, toluene, xylene
Benzene
  Found in petrol (typically 1% or less)
  Excellent solvent but its use has reduced due to its toxicity
  Major use as chemical feedstock
Toluene
  Constituent of petrol
  Chemical feedstock
  Solvent, widely used in adhesives, inks and surface coatings
Xylene
  Solvent for paints, adhesives, rubber solutions and pesticides
Notes: <number>

## Slide 21: Other organic solvents
Halogenated hydrocarbons
  Examples include carbon tetrachloride, trichloroethylene, trichloroethane, tetrachloroethylene, dichloromethane
Other solvents
  Alcohols
  Ethers
  Esters
  Ketones
Notes: <number>

## Slide 22: Organic solvents and vapours
Solvents may encountered as single substances, mixtures or in formulated products
Risk to health depends on many factors including toxicity, exposure level and volatility
  Rate of evaporation varies widely
  Indication of volatility given by vapour pressure
Solvent vapours are heavier than air and in a still environment will tend to sink to floor – where air movement is restricted high concentrations can build up in tanks, pits, sumps etc
  However, for low solvent vapour concentrations density difference is not significant and normal air movement is sufficient to disperse and dilute these vapours
Notes: <number>
Principle routes of entry - examples
Acute / chronic - differences / typical effects
Local / systemic - examples

## Slide 23: Typical exposures to organic solvents and vapours
Closed plant
  Production and use in chemical processing usually in closed plant, however, exposure can occur in a number of situations
  Maintenance work – when pipework is opened or valves, pumps removed for repair
  Fugitive emissions – emissions during normal operations
  Contact from spillages
Transfer of solvents
  Exposure to solvent vapours during transfer of solvents between vessels, tanks and drums
  Vapour produced from solvent being transferred and displacement of solvent laden air from vessel being filled
Use of solvent based products
  Evaporation of solvent during painting, printing and surface coating
  Maintenance and cleaning operations using solvents
Notes: <number>
Principle routes of entry - examples
Acute / chronic - differences / typical effects
Local / systemic - examples

## Slide 24: General health effects of solvents
Acute
  Headache
  Drowsiness
  Nausea
  Narcosis (euphoria)
  Dizziness
  Unconsciousness
  Death
De-fatting of skin / irritation
Notes: <number>

## Slide 25: Common health effects of solvents
Chronic
  Dermatitis
  Liver damage (Hepatotoxicity)
  Kidney damage (Nephrotoxicity)
  Brain and central nervous system effects
    Irritability, sleep disorders, dementia
  Possible effects on foetus and reproductive systems
Notes: <number>

## Slide 26: Specific health effects for some organic solvents
Benzene
  Known human carcinogen, affects bone marrow causing anaemia and can cause leukaemia
Carbon tetrachloride, chloroform, tetrachloroethylene
  Liver and kidney damage
Glycol ethers (some)
  Possible reproductive effects
n-Hexane
  Can cause nerve damage – peripheral neuropathy – thought to be caused by a metabolite
Notes: <number>

## Slide 27: Other selected organic liquids
Styrene
  Readily absorbed by inhalation and through skin
  Acute effects – irritant and narcotic
Major uses
  Production of styrene-butadiene rubber
  Solvent for resin in glass reinforced plastics manufacture
    Particular problems arise when working on large structures where operator has to work in relatively confined area
Notes: <number>

## Slide 28: Other selected organic liquids
Isocyanates
  Main examples – toluene di-isocyanate (TDI) and diphenylmethane di-isocyanate (MDI)
  Supplied as 2-part polyurethane systems comprising a di-isocyanate and a resin. Components mixed together by the user and quickly sets to form the finished product
  Main uses
    Flexible foams (usually TDI based)
    Rigid foams (usually MDI based)
    MDI also used as a binder in products such as particle boards and foundry sand moulds
    2-part polyurethane paints
Notes: <number>

## Slide 29: Other selected organic liquids
Isocyanates
  Irritant to eyes, skin, respiratory tract
    Very high exposure can cause pulmonary oedema
  Main concern is allergic reaction
    Respiratory sensitisation may occur after single peak exposure
    Once sensitised asthmatic attacks may occur even at extremely low exposure levels
    May result in permanent pulmonary disability
    Good control systems, LEV, RPE and health surveillance may be required
  Use of MDI may be preferred to TDI as it is less volatile
Notes: <number>

## Slide 30: Other selected organic liquids
Aniline
  Converts haemoglobin to methaemoglobin which reduces the oxygen carrying capacity of the blood
Formaldehyde
  Severe irritant, possible respiratory sensitiser, possible carcinogen
Vinyl chloride monomer
  Raynaud’s phenomenum, angiosarcoma (cancer) of the liver, irritant, narcotic
Notes: <number>

## Slide 31: Metals and compounds - introduction
Exposure to metals from industrial processes can occur in many ways and produce acute and chronic health effects
Inhalation of dust (e.g. from grinding and machining) and fume (e.g. from smelting and welding as metal or metal oxide) are usually the main routes of exposure
Several metals can produce effects through skin contact or even ingestion
Notes: <number>

## Slide 32: Cadmium (Cd)
Used for plating of steel to impart corrosion resistance properties, in steel alloys, in nickel / cadmium batteries and as pigments in the paint and plastics industries
Exposure usually by inhalation –
  Dust from machining and processing of cadmium containing materials
  Fume - most likely as cadmium oxide (often seen as a brown fume) from the zinc smelting process, burning or welding of plated materials, from smelting of scrap metal
Cadmium has long half-life in the body (10 – 30 years)
Notes: <number>

## Slide 33: Cadmium (Cd)
Acute health effects
  irritation of respiratory system
  high exposure can cause severe pneumonitis and oedema which can be fatal
Chronic health effects
  lung emphysema
  Main effect is kidney damage – resulting in loss of kidney filtration function leading to presence of low molecular weight proteins in the urine
  Cadmium may also cause cancer in the kidney
Notes: <number>

## Slide 34: Chromium (Cr)
Can exist in different forms (valencies)
  the metal, chromium (III) – trivalent, and chromium (VI) – hexavalent. In terms of health effects the hexavalent state is of most concern
Chromium – uses
  In stainless steel, other corrosion resistant alloys, chrome plating, as pigment, as wood preservative and in some cements
Exposure to dust and fume can occur in production, machining and welding of chromium metals and alloys.
  Note: Welding can produce Chromium (VI)
  Chromic acid mist (also chromium (VI) can be produced during electroplating processes)
  Also skin contact can occur when using pigments and cement
Notes: <number>

## Slide 35: Chromium (Cr)
Acute health effects
  Mainly caused by irritant and corrosive effects of chromic acid and its salts
  Main effects are skin irritation and ulceration
Chronic health effects
  Main concern is lung cancer (from hexavalent chromium)
  Contact dermatitis and sensitisation
Notes: <number>

## Slide 36: Copper (Cu)
Copper has been widely used due to its excellent thermal and electrical conductivity. It is also corrosion resistant.
  Uses include electrical and electronic products, pipework, alloys e.g. beryllium/copper, brass (copper/zinc), bronze (copper/tin), in electroplating and in wood preservatives, pesticides and fungicides
Exposure to copper is mainly as dust or as oxide fume
Health effects – mainly acute effects
  Irritation of nasal mucous membranes and the eyes
  Fumes from hot processes such as welding and brazing can cause metal fume fever. Symptoms include flu-like symptoms that occur particularly at the start of a week or on return from a period away. The effects usually last about 24-48 hours
Notes: <number>

## Slide 37: Lead (Pb)
In terms of industrial hygiene two categories of lead are considered
  Lead and inorganic lead compounds
    Used in metal products, sheet metal, solders, pigments, batteries, pottery glazes, lead crystal glass
  Organic lead compounds
    Additive in petrol (tetra ethyl lead)
Notes: <number>

## Slide 38: Lead (Pb)
Lead and inorganic lead compounds
  Main routes of entry are by inhalation of dust or oxide fume and by ingestion where hygiene standards are poor
  Significant levels of lead fume can be produced at temperatures above 450oC
  Handling of molten lead or lead alloys is the most likely source of inhaling lead oxide fume
  Lead has been used in paints, and any mechanical activity (e.g. grinding or sanding) or hot work (e.g. cutting or welding) on these painted surfaces may result in exposure to dust or fume respectively
  Gas cutting of painted steelwork during demolition of buildings, bridges and ships are examples where exposures to lead fume has occurred
Notes: <number>

## Slide 39: Lead (Pb)
Health effects of lead and inorganic lead compounds
Lead is readily absorbed through the lungs and once absorbed is transported by the red blood cells and stored in the bone marrow where it interferes with haemoglobin production
Effects include anaemia, fatigue, abdominal pain, loss of appetite, muscular weakness (peripheral neuropathy) and possible brain damage
Lead can also enter a foetus through the placenta of the mother and damage the nervous system and brain. Lead can also impair male fertility
Notes: <number>

## Slide 40: Lead (Pb)
Health effects of organic lead compounds
  Exposure to organic lead compounds is through vapour inhalation and are also readily absorbed through the skin – significantly different to inorganic lead
  Psychiatric disturbances such as insomnia, hyperactivity, tremor and mania
Notes: <number>

## Slide 41: Mercury (Hg)
Mercury - the only metal that is liquid at room temperature
  Mercury vapour is produced at room temperature - at higher temperatures significant concentrations can be produced
  Exposure to mercury metal is usually via inhalation of vapour - often from spillages that are not cleaned effectively – (metallic mercury is poorly absorbed by ingestion)
  Exposure to mercury salts is usually by inhalation of dusts
Uses include
  Thermometers and barometers
  Batteries
  Mercury vapour lamps
  Pharmaceuticals
Notes: <number>

## Slide 42: Mercury (Hg)
Health effects
  Chronic exposure to all forms of mercury can cause damage to the brain, disruption of the central nervous system, neuro-psychiatric disorders with symptoms including neurosis and paranoia
  Organic mercury compounds e.g. methyl mercuric chloride are generally more toxic than inorganic mercury salts
  Motor neurone disturbances and visual field constriction more commonly associated with organic mercury compounds
  Historically mercury poisoning was seen in the felt hat industry where mercury salts were used and classic mercury CNS effects were observed
Notes: <number>

## Slide 43: Nickel (Ni)
Nickel - refined from sulphide ores by the Mond process.
  Nickel sulphides converted to oxides and reacted with carbon monoxide to form volatile nickel carbonyl (a known carcinogen) as an intermediate in the production of nickel metal
Uses of Nickel – range of alloys including stainless steels, nickel / cadmium batteries, in electroplating and in ceramics
Exposure to nickel - usually inhalation of dust and fume from metal processing, grinding and welding
Acute health effects
  Allergic dermatitis and sensitisation (‘nickel itch’)
  Pneumonitis from nickel oxide fume
Chronic health effects
  Cancer of nasal sinuses and lung cancer
Notes: <number>

## Slide 44: Zinc (Zn)
Zinc used as an electroplated coating (galvanised steel), in brass and other alloys and in soldering fluxes (zinc chloride)
Exposure to zinc usually by inhalation of dust and fume from metal processing, grinding and welding
  Gas cutting of galvanised steel, zinc metal spraying, and some welding operations are likely to present the highest potential exposure to zinc oxide fume
Acute health effects
  Inhalation of oxide fume from hot processes such as welding can produce metal fume fever. Effects usually last 24-48 hours
  Zinc chloride is irritating and corrosive to skin and lungs
Notes: <number>

## Slide 45: Dusts and particulate materials
Wide range of substances that may be present as a significant dust hazard in industry
  The following examples are used to illustrate some of the hazardous properties and health effects
    Crystalline silica
    Nanoparticles
    Diesel engine exhaust
    Latex
    Enzymes
    Flour and other food components
    Asbestos
    Machine-made mineral fibres

## Slide 46: Crystalline silica
Crystalline silica (silicon dioxide) is the most abundant compound in earth’s crust and is a common airborne contaminant in many industrial processes
Two forms of silica - crystalline and amorphous
Crystalline silica of much more concern - particularly the respirable (less than 10 micron) dust fraction that can reach the alveoli
Crystalline silica
  quartz - most common - wide variety of sources
  cristobalite – can be formed from quartz at high temperatures

## Slide 47: Crystalline silica
With sufficient exposure crystalline silica can cause silicosis, a typical pneumoconiosis
  Chronic disease that develops after many years exposure
  Reduction in lung function due to production of fibrosis (scar tissue) in the lungs
  Also increased risk of lung cancer in silicosis sufferers
  Exceptionally high exposure can lead to acute silicosis within months, with progressive massive fibrosis causing severe impairment or death within a few years
Possibly greater risks with cristobalite than with quartz

## Slide 48: Crystalline silica
Respirable dust particles may be formed whenever silica containing rock is drilled, blasted, cut or crushed
  Different rock types contain different amounts of silica e.g.
    Sand and sandstone >90%
    Granite and slate up to 40%
    Ball clays 25%
    Limestone <1%
  Exposure may occur in mining and quarrying as well as in a wide range of industries

## Slide 49
Disc cutting of stone block
(Source: HSE LEV Trainer Adviser Briefing Days – reproduced with permission)

## Slide 50: Crystalline silica
Occurrences in industry
  Mining and quarrying
  Sand moulds in metal casting and foundry work
  Pottery and ceramics industry
  Brick manufacture
  Refractory materials lining ovens, kilns and furnaces
    E.g. blast furnaces, gas and coke plants, cement and lime works, ceramics, glass manufacturing
    Refractory materials may contain high levels of quartz which may be converted to cristobalite at high temperatures
    Replacement of furnace linings may be a particular problem

## Slide 51: Nanoparticles
Particles with at least one dimension <100 nm
  Small size gives specific or enhanced properties compared with same materials at the macro scale
  Have very high surface area to volume ratio
  Too small for macrophage cells to detect and small enough to penetrate cell membranes and be transported around body
  Possibly increased health risks – relative lack of toxicological information
  Difficulties in monitoring and assessing risk
  Examples include nanosilver, metal oxide nanoparticles, carbon nanotubes and fullerenes

## Slide 52: Diesel engine exhaust
Complex mixture of gases, vapours and particulates
  Contains products of combustion including carbon (soot), carbon monoxide, aldehydes, nitrogen dioxide, sulphur dioxide and a range of organic breakdown products
  Most contaminants absorbed onto the carbon particles which are small enough to reach the alveoli
Acute health effects
  Irritation of nose, eyes and respiratory tract, headache, fatigue
Chronic health effects
  Bronchitis, can also exacerbate symptoms of asthma
  Classified by IARC as probably carcinogenic to humans

## Slide 53: Latex
Natural rubber latex contains proteins to which people may be allergic
  Main categories of workers most at risk include
    Healthcare workers – surgeons, nurses, dentists etc
    Other groups e.g. car mechanics, catering and electronics trades
    Industrial rubber manufacturing workers

## Slide 54: Enzymes
Enzymes are specific types of proteins that occur in all living cells
  Metabolic enzymes
    catalyse and regulate biochemical reactions that occur within the cell
  Digestive enzymes
    e.g. pepsin, lipase, protease and amylase – catalyse the breakdown of proteins, fats and carbohydrates in food
  Enzymes widely used in detergent, food and brewing industries
  Enzymes are potential allergens and can have particularly severe effects if inhaled as a dust

## Slide 55: Flour and other food components
Many food and food components may cause allergic response
  e.g. flour, grain dust, bakery dust, egg protein, fish protein
  Flour extensively used, can generate a fine dust
    Health effects include rhinitis, occupational asthma as well as dermatitis
    Allergic response may be from the flour itself, from amylase enzyme or other ingredients such as egg powder

## Slide 56: Asbestos
Naturally occurring fibrous silicate minerals – three types have been widely used
  Chrysotile (white asbestos)
  Amosite (brown asbestos)
  Crocidolite (blue asbestos)
Can split lengthways into finer fibres
  Often much less than 3 micron in width – typically less than 1 micron. This size of fibre can reach the alveoli
Wide range of useful properties including
  Good thermal and electrical insulator, flexibility, strength, resistance to chemical attack, non-combustibility
Extensively used in many building materials and in vehicles, domestic and industrial items

## Slide 57: Asbestos – main uses
Pipe and boiler insulation (lagging)
Spray coatings
  Thermal and acoustic insulation, fire protection to ceilings and structural steel
Asbestos insulation boards
  Fire protection as wall and ceiling panels, lining panels to ducts and lift shafts
Asbestos cement products
  Corrugated and flat sheeting, rainwater goods, tiles, flues
Others including:
  Friction materials, protective clothing, rope insulation, gaskets, floor tiles and textured coatings (‘Artex’)

## Slide 58
Insulation (lagging) to pipework and calorifiers
(Source: Gully Howard Technical Ltd)

## Slide 59
Asbestos insulating board ceiling tiles
(Source: Gully Howard Technical Ltd)

## Slide 60: Asbestos – health effects
Three main health effects are asbestosis, lung cancer and mesothelioma
Asbestos only a health risk in situations when asbestos fibres become airborne and can be inhaled
In many countries, asbestos is the largest occupational cause of death
  In the UK about 4,500 people die each year from asbestos related disease
  Expected to rise to 6 – 8,000 per year by 2015 before starting to reduce

## Slide 61: Asbestosis
Fibrotic pneumoconiosis that causes a progressive loss of elasticity and lung function
Only occurs after high exposures, usually over many years
Fine fibres that reach the alveoli not readily removed and macrophage cells that are unable to remove them are damaged releasing enzymes that cause scarring of the lung tissue
All types of asbestos can cause asbestosis
Example of a clear ‘dose-response’ relationship

## Slide 62: Asbestos related lung cancer
No known safe level of exposure
  Risk of developing lung cancer increases with exposure to asbestos
  Risk of developing lung cancer increases with smoking
  Risk of developing lung cancer is greatly increased with exposure to asbestos and smoking – a ‘synergistic’ effect
All forms of asbestos can cause lung cancer - blue and brown asbestos much more likely than white asbestos
Long latent period for effects to occur – typically 15 to 50 years

## Slide 63: Asbestos - mesothelioma
No known safe level of exposure
Risk of developing mesothelioma increases with exposure to asbestos
All forms of asbestos can cause mesothelioma - blue and brown asbestos much more likely than white asbestos
Long latent period for effects to occur – typically 15 to 50 years

## Slide 64: Machine made mineral fibres (MMMF)
Also termed synthetic vitreous fibres or man made mineral fibres and include
  Continuous glass fibres
    Relatively large diameter (usually 5 – 15 micron) meaning that they are too large to reach alveoli
  Insulation wools made of glass, rock or slag fibres
    Wider range of fibre diameters including some less than 3 micron which are respirable
  Refractory ceramic fibres (usually aluminium silicates)
    Wider range of fibre diameters including some less than 3 micron which are respirable

## Slide 65
Re-lining a furnace with refractory ceramic fibre blocks
(Source: Steve Bailey – reproduced with permission)

## Slide 66
Re-lining a furnace with refractory ceramic fibre blocks
(Source: Steve Bailey – reproduced with permission)

## Slide 67: Machine made mineral fibres (MMMF)
Chronic health effects
  Continuous glass fibres, insulation wools made of glass, rock or slag fibres classified by IARC as Group 3 (not classifiable as to carcinogenicity to humans)
  Refractory ceramic fibres classified by IARC as Group 2B (possibly carcinogenic to humans)
    Additional problem associated with refractory ceramic fibre products is the possible conversion to cristobalite after exposure to high temperatures
Acute health effects
  Irritation of skin, eyes, upper respiratory tract

## Slide 68: M507 – ‘Paint manufacture’ case studies

## Slide 69: Paint manufacture (1)
Process information
  Addition of bulk powder (Titanium dioxide) through inlet (sieve) into mixing vessel
  Brushing down powder from surfaces into mixing vessel
Other information
  Material safety data sheet – see separate sheets
  Other bulk powders and pigments added depending on paint specification

## Slide 70: Case study – general information
Operating conditions
  Normal production
Who is being exposed
  Machine operators (Male (6))
Pattern of exposure
  Batch process over 8 hour shift

## Slide 71: Case study – video (0 – 54 seconds)
Identify sources of exposure
  Inhalation
  Skin absorption
  Ingestion
Look for evidence of exposure
Comment on existing controls and procedures
What other information would you require
Notes: <number>
UK 1980’s. 0.18 Sack – someone else clear away? 0.30 other person. Static / flammability issues?

## Slide 72: Paint formulation (2)
Process information
  Mixing of paint
  Bulk powders, pigments, 2-ethoxyethanol solvent
  After mixing stored in drums – surface covered with polythene to minimise evaporation and prevent formation of ‘skin’ on paint
  Mixed batches poured through sieve to remove larger solids
Pattern of exposure
  Batch processes
  Continuous manufacture of batches over 8 hour working day
Other information
  Material safety data sheets – see separate sheets

## Slide 73: Case study – video (0.54 – 1.46)
Identify sources of exposure
  Inhalation
  Skin absorption
  Ingestion
Look for evidence of exposure
Comment on existing controls and procedures
Notes: <number>
0.58 organic vapour analyser (OVA), 1.04 polythene skin. Std overalls

## Slide 74: Paint formulation (3)
Process information
  Cleaning of paint residues from mixing vessels using spatula and brushes
Pattern of exposure
  20 litres of methyl ethyl ketone (MEK) used per batch
  Cleaning takes place 3 times per day for about 20 minutes each time
  Solvent / paint residues within vessel
Other information
  Material safety data sheet – see separate sheets

## Slide 75: Case study – video (1.46 to end)
Identify sources of exposure
  Inhalation
  Skin absorption
  Ingestion
Look for evidence of exposure
Comment on existing controls and procedures
Notes: <number>
3.07 gap in LEV. Process replaced by automated washer – saved money due to reduced solvent use and disposal costs.