## Slide 1: M507 – Specific industry profiles

## Slide 2: Smelting and refining of iron and steel
Smelting and refining industries process metal ores and scrap metal to produce pure metals and metal alloys (mixtures of different metals)
Metals and alloys then processed further to manufacture structural components, machinery, instruments and tools etc

## Slide 3: Iron and steel industry
Iron ore melted in blast furnace
  Iron ore (+ scrap), limestone and coke added from top
  Hot air (+ oxygen) blown in from bottom
  Carbon monoxide produced converts iron ore to iron (still contains large amount of impurities)
  Limestone added as flux – forms slag with other contaminants
  Molten iron tapped from base for later use in foundries or transferred directly to a steel making plant
Notes: <number>

## Slide 4
Notes: <number>

## Slide 5
Blast furnace
(Source: Wolverhampton Archives – reproduced with permission)

## Slide 6: Steel making
Iron from blast furnace contains large amounts of impurities
  Carbon (+ others such as sulphur and phosphorus)
  These must be removed / reduced to produce steel
Main types of steel making furnaces
  Basic oxygen converters
  Electric arc
Special steel alloys contain other metals e.g.
  chromium and nickel in stainless steel
  tungsten and cobalt for hardened steels
Notes: <number>

## Slide 7
Tapping of blast furnace - (Reproduced with permission)

## Slide 8: Chemical hazards of smelting and refining
Metal oxide fumes from molten metal (particular metal depends on metals being worked and impurities)
Silica and metal dusts during crushing and grinding of ores
Silica dust from furnace maintenance
Notes: <number>

## Slide 9: Chemical hazards of smelting and refining
Sulphur dioxide produced from sulphide ores
Carbon monoxide produced by combustion processes
Specific hazards include
  Production of nickel carbonyl in nickel refining
  Arsenic in copper and lead refining and smelting
  Mercury and cyanide exposure in gold refining
Notes: <number>

## Slide 10
Pouring molten gold - (Source: Brian Davies – reproduced with permission)

## Slide 11: Other hazards of smelting and refining
Thermal stress issues common in metal smelting and refining industry from high levels of infra-red radiation from furnaces and hot metal
Infra-red radiation can also cause eye damage including cataracts
High noise levels
Notes: <number>

## Slide 12
Steel works rolling mill - (Reproduced with permission)

## Slide 13: Foundries
Two main categories foundries
  Ferrous (iron and steel) foundries
  Non-ferrous foundries (e.g. aluminium, brass, bronze)
Main processes
  Pouring molten metal into a heat-resistant mould
    Range of different types of mould but the most common iron foundry processes use sand moulds
  Cooling of metal casting and removal from mould
  Finishing and cleaning of casting
Notes: <number>

## Slide 14
Foundry furnace - (Source: HSE (UK) – reproduced with permission)

## Slide 15: Ferrous foundry - melting
Iron or scrap melted in furnace
  Types include cupola, electric arc, electric induction and crucible furnaces
Health hazards
  Iron and other metal oxide fume / dust
  Carbon monoxide (particularly from cupola furnaces and crucible furnaces)
  Impurities in scrap - lead, zinc etc
  Also noise, heat, hot metal
Notes: <number>

## Slide 16: Ferrous foundries - mould preparation
Mould prepared to form the desired shape of the casting
  Include cores if required to form hollow internal areas of the casting
Iron foundries usually use traditional sand moulds
  Contain crystalline silica - quartz
  Also contain clay and other binders e.g. isocyanates, phenol-formaldehyde or urea-formaldehyde resins
  Sand used damp - hazard arises when sand becomes dry
Notes: <number>

## Slide 17: Ferrous foundries – melting and pouring
Main hazards - heat and fumes
  Metal oxide fumes, carbon monoxide
  Decomposition products from binders e.g. isocyanates, formaldehyde and amines
  Control is usually by local exhaust ventilation or hood at the pouring station with direct air supply at the operator position
Refractory linings of cupola furnaces have to be periodically renewed
  Potential heat stress as furnace cannot be allowed to cool completely and involves working inside furnace
  Also high dust levels – crystalline silica
Notes: <number>

## Slide 18
Foundry work - (Source: HSE (UK) – reproduced with permission)

## Slide 19: Ferrous foundries
Shake-out, casting extraction and core knockout
  After cooling, rough casting removed from mould by impact onto a vibrating grid to dislodge the sand
  Sand drops through grid for cleaning and recycling
  High potential dust levels as the sand is very dry and still hot
Health hazards include
  Airborne dust from sand (quartz)
  Thermal stress
  Noise
Notes: <number>

## Slide 20: Ferrous foundries – fettling (cleaning) of casting
Initial cleaning involves removal of mould sand and easily removed material
Fettling includes removal of residual sand, rough edges, surplus metal etc
  Tools include abrasive wheels and grinders
Higher levels of airborne silica dust are likely where controls or housekeeping are poor
Silicosis or mixed dust pneumoconiosis are common health effects
Notes: <number>

## Slide 21
Casting before and after fettling
(Source: HSE (UK) – reproduced
with permission)

## Slide 22: Non-ferrous foundries
Steel foundries
  Very similar to ferrous foundries - processes are same
  However higher temperatures so quartz in sand moulds more likely to be converted to cristobalite and sand residues on castings may be more difficult to remove
Light alloy foundries
  Mainly aluminium and magnesium
  Fluoride based fluxes
  Metal moulds
Notes: <number>

## Slide 23: Non-ferrous foundries
Brass and bronze foundries
  Hazards mainly related to metal oxide dusts and fumes during melting, pouring and finishing
  Copper and zinc metal fume fever – flu-like symptoms
  Lead – particularly during melting and pouring
  Cadmium – acute pneumonitis and chronic kidney damage
Precision foundries
  Use investment or ‘lost-wax’ process
  Wax patterns prepared and coated with fine refractory powder before building up rest of mould
  Wax melted out prior to or during casting
  Fumes from decomposition of wax
Notes: <number>

## Slide 24: Mining and quarrying
Wide range of health hazards
  Particulates
    Crystalline silica
  Diesel exhaust
  Gases
    e.g. methane, hydrogen sulphide
  Noise and vibration
  Thermal stress
  Ionising radiation
  Hazards will depend on type of mine or quarry, its depth, composition of ore or surrounding rock and work methods
Notes: <number>

## Slide 25: Mining and quarrying
Airborne particulate hazards
  Crystalline silica (quartz) is the most common compound in the earth’s crust and is the most common dust that workers are exposed to in mining and quarrying industries
  Airborne dust produced by a wide range of processes
    Drilling, blasting, cutting of rocks
    Crushing, grading (sieving)
    Conveyor transfer
    Loading and transportation
Notes: <number>

## Slide 26
Crawler mounted drill with
no dust control
(Source: HSE (UK) – reproduced
with permission)

## Slide 27
Loading lorry using mechanical arm
(Source: HSE (UK) – reproduced with permission)

## Slide 28
Mobile jaw crusher and conveyors
(Source: HSE (UK) – reproduced with permission)

## Slide 29: Mining and quarrying
Airborne particulate hazards
  Coal mining – coal mine dust is a mixture of coal, crystalline silica and other mineral dusts
  Composition varies with the coal seam, surrounding rock strata and mining method
  Coal mine dust can cause coal worker’s pneumoconiosis as well as chronic bronchitis and emphysema
  Dust generation can be reduced by changes in coal cutting techniques and by using adequate mechanical ventilation and water sprays
Notes: <number>

## Slide 30
Longwall coal mining with water sprays
(Source: NIOSH (US) – reproduced with permission)

## Slide 31: Mining and quarrying
Other health hazards
  Diesel engine exhaust
    Complex mixture of gases, vapours and particulates
    Carbon monoxide, nitrogen dioxide, sulphur dioxide
    Volatile organic compounds (VOC’s)
      e.g. unburned hydrocarbons, aldehydes and polycyclic aromatic hydrocarbons (PAH’s)
      These may be absorbed onto the diesel particulate
    IARC considers diesel particulate to be a probable carcinogen
Notes: <number>

## Slide 32: Mining and quarrying
Other health hazards
  Naturally occurring gases
    Methane – simple asphyxiant (and combustible and may cause explosions)
    Hydrogen sulphide – chemical asphyxiant
  Oxygen deficiency
  Other specific exposure hazards
    Mercury vapour in gold and mercury mining
    Arsenic in gold and lead mining
    Radon gas in uranium and other mines
  Noise
  Heat stress (particularly in deep mines)
Notes: <number>

## Slide 33: Oil and petroleum industry
Crude oil
  Complex mixture of paraffins (alkanes), naphthenes (cycloalkanes) aromatic hydrocarbons and other organic compounds
    Varies greatly from one oil field to another
    Little use in raw state – needs to be processed to produce commercial products of value
Notes: <number>

## Slide 34: Petroleum refining
Hydrocarbons in crude oil are separated by distillation into different fractions with specified boiling point ranges
  Light gases, gasoline, naphtha, kerosene, gas oil, fuel oil and higher boiling residues
To produce required quantities of different products, each fraction may be further processed e.g.
  Cracking – using heat and catalysts to break down higher boiling point hydrocarbons into lighter products
  Reforming – using heat, pressure and catalysts to convert paraffins and naphthenes to iso-paraffins and aromatics
  Alkylation – conversion of alkanes to iso-paraffins
Contaminants such as metals, nitrogen compounds and sulphur compounds need to be removed
Notes: <number>

## Slide 35: Petroleum refining
Fugitive emissions of hydrocarbon vapours are always of concern. Controls include:-
  Floating roofs on storage tanks to prevent evaporation
  Vapours from tanks collected in a vapour recovery system and returned to the product stream
  Pumps / valves / seals etc regularly checked for vapour emissions and repaired if necessary
Notes: <number>

## Slide 36: Pharmaceutical industry
A particular issue in the pharmaceutical industry is that the products are designed to be physiologically active i.e.
  They are designed to impact on human health at very low doses
  This may be desirable if you require the medication but clearly it is undesirable for the worker to be exposed to the medication or active ingredient in the workplace
Notes: <number>

## Slide 37: Pharmaceutical industry
Primary manufacture
  Production of the active ingredient by chemical reaction. This is usually undertaken in closed systems
Secondary manufacture (or formulation)
  Mixing the active ingredient with other materials to form a suitable product
  Often mixed with excipients (inert bulking materials such as starch or magnesium stearate) to allow very low doses of active ingredients to be administered (e.g. there may only be a few milligrams of active ingredient in a tablet)
Notes: <number>

## Slide 38
Addition of sack of powder to reactor
(Source: Steve Bailey – reproduced with permission)

## Slide 39
Fully enclosed tablet press with extraction
(Source: Steve Bailey – reproduced with permission)

## Slide 40: Pharmaceutical industry
As well as active ingredients being physiologically active they may have other effects such as respiratory sensitisation or be teratogenic
Exposure limits for active ingredients often in microgram (or even nanogram) per cubic metre range
  Controls therefore need to be stringent e.g.
    Total containment commonplace
    Segregated work areas
    Local exhaust ventilation with HEPA filtration
    Disposable coveralls
    High standards of respiratory protective equipment
Notes: <number>

## Slide 41: M507 – ‘Wonderdrug’ case study

## Slide 42: ‘Wonderdrug’ information
Formulation
  Aspirin 53.5%
  Paracetamol 38.3%
  Caffeine 7.6%
Processes
  Filling of hoppers from bulk container
  Packing / filling of product
Other information
  Material safety data sheets – see separate sheets

## Slide 43: Case study – general information
Operating conditions
  Normal, nearly all workstations running
Who is being exposed
  Machine operators (Female (50) some < 18 years)
  Machine fillers (Male (2))
  Maintenance personnel during changeover / cleaning
Pattern of exposure
  Continuous over 8 hour shift
  High levels during changeover / cleaning

## Slide 44: Case study - video
Identify sources of exposure
  Inhalation
  Skin absorption
  Ingestion
Look for evidence of exposure
Comment on existing controls and procedures
Comment on any particular health issues