## Slide 1: Polyurethane polymer manufacturing - Case study
Notes: <number>
Biological monitoring is a tool for assessing exposure by all routes. It has a particular role where substances can be absorbed through the skin or where control of an inhalation hazards relies o respiratory protective equipment. MbOCA is a model compound for biological monitoring – both to demonstrate the utility of biological monitoring and for a type of biological monitoring guidance value based on good occupational hygiene practice rather than health.
HSL has been monitoring exposure to MbOCA for many years – the message from the following slides is that biological monitoring or exposure assessment is useful for interventions to reduce exposure at the industry level, the level of the individual company and for the individual worker.

## Slide 2: A Hypothetical Polyurethane Manufacturer
You are contacted by the owner of a small business
  A Government Inspector told him to get help
  An occupational health provider visits once a year and has not reported any problems
The company employs 10 people,
  4 in the office (Owner/Manager, Sales, Accounts)
  6 in the factory making polyurethane seals, gaskets and coating metal parts with wear resistant polyurethane
Crown Copyright 2009
Notes: <number>
MbOCA is a model compound for biological monitoring, guidance values and for demonstrating the results of HSE’s attempts to reduce exposure and risk of ill-health.

## Slide 3: A Hypothetical Polyurethane Manufacturer
The process:
  Weighing a known quantity of hardener
  Mixing the hardener with a known quantity of resin
  Mixing & degassing
  Pouring the mixture into heated moulds
  Leaving to cure overnight
  Getting the articles out of the moulds and trimming
Crown Copyright 2009
Notes: <number>
MbOCA is a model compound for biological monitoring, guidance values and for demonstrating the results of HSE’s attempts to reduce exposure and risk of ill-health.

## Slide 4: Safety Data
Hardener
  Aromatic amine
  Suspect Carcinogen
  Melting point 100oC
  UK Airborne exposure limit 0.005 mg.m-3
  ‘Skin notation’
  UK Biological monitoring guidance value 15 µmol/mol
Resin
  Di-Isocyanates
  ‘Sensitiser’
    Skin and Respiratory
  Melting point 40 - 67oC
  UK Airborne exposure limit 0.02 mg.m-3
Crown Copyright 2009

## Slide 5: Historical Data
Air monitoring data:
  Exposure to isocyanates below the UK Workplace Exposure Limit
Occupational health data:
  No evidence of asthma (but staff turnover is about 3 per year)
  One case of dermatitis
Crown Copyright 2009
Notes: <number>
MbOCA is a model compound for biological monitoring, guidance values and for demonstrating the results of HSE’s attempts to reduce exposure and risk of ill-health.

## Slide 6: Site visit: heating/weighing
Crown Copyright 2009

## Slide 7: Site visit: Pouring
Crown Copyright 2009

## Slide 8: Site visit: Mixing
Crown Copyright 2009

## Slide 9: Site visit: Moulding
Crown Copyright 2009

## Slide 10: Site visit: Protective Equipment
Crown Copyright 2009

## Slide 11: Monitoring results
Air monitoring for isocyanates
  All personal inhalation exposures less than WEL (0.005 mg/m3)
Biological monitoring for amines (urine)
  About half the samples showed detectable levels of diamines (some above BMGV)
  Not clear if metabolites are from inhalation of isocyanate or dermal absorption of di-amine breakdown products
  If inhalation of isocyanate – need better control (asthma risk)
  If dermal absorption of di-amine need better control of dermal exposure (carcinogen & skin sensitiser risk)
Crown Copyright 2009
Notes: <number>

## Slide 12: Feedback
Crown Copyright 2009
Notes: <number>

## Slide 13
Processes look poorly controlled
  LEV poorly positioned
  Poor housekeeping
  Visible surface contamination
  Low technology work practices
LEV provided but is it appropriate and well-maintained?
PPE (gloves, overalls, masks) provided
  No evidence of masks being worn
  Overalls show visible contamination
  Gloves seem to be heatproof in design – could absorb and transfer contamination
Crown Copyright 2009

## Slide 14
Evidence of exposure to both hardener and resin
Appear to be obvious areas of improvement
Carcinogen and sensitiser so regular monitoring required
Air monitoring, biological monitoring and LEV testing appropriate
Crown Copyright 2009

## Slide 15
Medical surveillance required
  Questionnaire, Lung Function, Skin Surveillance
High staff turnover means asthma cases may be overlooked due to ‘healthy worker effect’. Improving working conditions may reduce turnover, reducing recruitment/training costs.
Crown Copyright 2009

## Slide 16: Next Steps
Revisit workplace to:
  See if controls can be improved & exposure reduced
  Investigate exposure to isocyanates
    Inhalation of isocyanates or diamines
    Dermal absorption of isocyanates or diamines
Crown Copyright 2009
Notes: <number>