## Slide 1
M501 - Case Study 2
Supplementary Information for Course Presenter
Notes: <number>

## Slide 2
Rice-growers Co-operative Limited
Double Fatality
Notes: <number>
This is a real incident study which unfortunately resulted in the deaths of two workers. The aim is to demonstrate the potential for very high concentrations of toxic gases to be present in what appears to be an otherwise normal work situation.

## Slide 3
The Site
Notes: <number>
The scenario:
You receive a late afternoon phone call that two employees have died in a rice elevator pit located in a rice storage shed.
The bodies have been removed by the first response group ( Fire Brigade) and the area has been cordoned off awaiting your investigation. No other information was available at this stage.
You have to travel to the site (approximately 300km from your office) the next morning to carry out the scientific investigation.
As the distances involved are significant there is a need to make plans for your investigation. Discuss what equipment you would consider taking and how you would go about such an investigation.

## Slide 4
The Rice Shed
Notes: <number>
On arrival at site you are told that trucks bring rice to the storage sheds where it is tipped into a road level intake grill of a receiving bin. A horizontal drag conveyor is used to move the rice from the receiving bin to the “boot” or bottom of a vertical bucket conveyor or vertical elevator where it is lifted up to the top of the shed & transferred to a horizontal conveyor from which it is discharged into the storage shed.

## Slide 5
The Elevator Pit
Notes: <number>
The bottom of the vertical elevator is in a cast concrete pit approximately 2.8 metres x 2.3 metres x 4.2 metres deep. A fixed steel access ladder is mounted on the wall and adjacent to the elevator.
Rice and water had accumulated at the bottom of the pit and is a “murky” colour.
The installed electrical sump pump used to clear this material could not be started by the two employees even after working on it from the ladder in the pit.
After a break they positioned a portable petrol driven engine on the top edge of the pit and lowered a pump into the water and commenced to pump out the accumulated rice and water. The pump malfunctioned after several minutes causing a violent agitation of the water and rice sludge and a person entered the pit by the access ladder to clear a suspected blockage. He collapsed and a second person when attempting his rescue also collapsed into the water at the bottom of the pit.
A third person alerted to the incident saw one employee laying face up in the water and the other face down. In an attempt to save this person from drowning quickly went down into the pit holding his breath, but firstly tied a rope to himself (held by other employees at the top of the pit), and turned the person face up. When ascending the ladder he too would have collapsed except he was pulled up by his colleagues to safety.
Local fire brigade personnel wearing self contained breathing apparatus later entered the pit and removed the bodies of the deceased persons on the day of the accident.

## Slide 6: Initial On Site Analysis
Combustible gases Not Detected (ND)
Carbon dioxide 0.06 % ES 0.5%
IDLH 5 %
Carbon monoxide ND ES 25 ppm
IDLH 1500 ppm
Hydrogen sulphide 15 ppm ES 10 ppm
IDLH 300 ppm
ES Exposure Standard
IDLH Immediately Dangerous to Life & Health
Notes: <number>
The above results are a summary of the maximum direct reading instantaneous results obtained directly above the surface of the water in the pit.
Levels as such were not considered to be of concern, albeit H2S was above the TWA ES.

## Slide 7: Gas Bag Analysis
Normal Atmospheric Gases
Oxygen 20.7 % (20.9%)
Carbon dioxide Trace (0.04%)
Nitrogen 79.2 % (78 %)
Asphyxiants
Methane Trace
Ethane ND
Propane ND
Contaminant Gases
Carbon monoxide ND (ES 25 ppm)
Hydrogen sulphide Trace (ES 10 ppm)
Notes: <number>
Similarly Laboratory results from gas bag samples collected just above the surface of the water and indicated that the atmospheric constituents were at normal levels and the toxic or contaminant gases were not detected or at trace levels.

## Slide 8: Head Space Gas Analysis
Hydrogen sulphide
Wine flagon 540 ppm
Soft drink bottle 450 ppm
ES 10 ppm
IDLH 300 ppm
Notes: <number>
On the day of the incident a member of the fire brigade when in the pit collected two samples of the water. Both water samples occupied approximately one quarter of the volume of their respective containers.
Results for hydrogen sulphide in the “head space” of the containers were well above the IDLH level for hydrogen sulphide.

## Slide 9: Microbiological / Water analysis
Pit Brew Water 9000 H2S producers/ml
Bore (seepage) water 1000 - 4000 ”
Hydrogen sulphide (eg clostridium) formers reduce sulphur compounds to sulphides causing a blackening of the colonies as exhibited by
the water in the pit.
Notes: <number>
Microbiology analysis of the water samples collected showed the presence of hydrogen sulphide forming bacteria

## Slide 10: Hydrogen Sulphide – Health Effects
ppm Effect
0.1 - 30 Odour of rotten eggs - obvious & unpleasant
50-100 Marked dryness & irritation nose & throat
100-150 Temporary loss of smell - olfactory fatigue
200-250 Severe irritation, headache, nausea - exposure for
4 hours can cause death
500+ Rapidly unconscious & respiratory failure in 5 mins
1000 + May cause coma after a single breath & rapidly fatal
Notes: <number>
After reviewing the literature it was postulated that hydrogen sulphide was produced by anaerobic bacteria and retained in the murky water. It was further postulated that when the pit contents were violently disturbed by the malfunctioning pump, a high concentration of hydrogen sulphide was released, resulting in the almost immediate collapse of the employee who entered the pit to service the pump, the second employee and also affected the third employee who was saved.
Carbon monoxide asphyxiation from the exhaust of the portable petrol driven engine was also postulated as a possible cause of death of the two employees. It was considered that due to the immediate effect on the employees it was not likely to be carbon monoxide.

## Slide 11: HYPOTHESIS
Hydrogen sulphide from anaerobic bacteria action in pits & released by violent agitation
NOT Carbon monoxide from combustion engine
Plan to simulate events
Notes: <number>
Thus the above hypothesis was formed and a plan to simulate the events of the incident constructed.

## Slide 12: Simulation of Events
Prior to agitation
Oxygen 20.8 %
Carbon monoxide ND
Carbon dioxide 0.06 %
Combustible gases ND
Hydrogen sulphide ND
Notes: <number>
These levels taken at face value on their own would indicate that it would be “safe” to enter the confined space.
BUT !!!

## Slide 13: Simulation of Events (cont)
Agitation of the pit by malfunctioning pump
Oxygen 20.8 %
Carbon monoxide ND
Carbon dioxide 0.06 %
Combustible gases ND
Hydrogen sulphide 300 ppm
Notes: <number>
With the agitation of the contents of the pit hydrogen sulphide levels were measured of the order of 300 ppm and no carbon monoxide was detected.
At the subsequent Coroners inquest hydrogen sulphide was found to be the cause of the deaths of the two employees.

## Slide 14: Hydrogen Sulphide Incidents
Similar hydrogen sulphide incidents have been reported in the following industries
  Meat processing
  Chicken processing
  Leather processing
Notes: <number>
A review of the literature established that similar incidents had occurred in the meat, chicken & leather processing industries indicating that such incidents are not “rare’ events.
Discuss what the operators/management should have done to prevent such an incident.